## Slide 1: Triggers in Charging Stage 2 and Stage 3 (SA5 #149)
Chen Shan Huawei

## Slide 2: The triggers in Charging Data Message Stage2
Triggers in the charging Stage 2
  TS 32.255: SMF triggers for PDU session, quota management.
  TS 32.254: NEF triggers for API invocation/notification.
  TS 32.256: AMF triggers for registration, location, N2 connection…
  …. SMSF, Prose charging trigger, Network slice charging trigger

## Slide 3: The Triggers in the CHF CDRs in Stage2
Triggers in the CHF CDRs Stage 2
  TS 32.254: NEF triggers in NEF CHF CDR.
  TS 32.257: EAS Deployment in CHF CDRs ….

## Slide 4: The Triggers in the Open API in the Stage3
Triggers in the Stage 3
  TS 32.291: The “Triggers” is reported in the Charging Data Request in the message
  TS 32.291: “TriggerType” is the Enumeration data type, which specify the Triggers defined in the Service Charging Specifications in the Stage 2 , such as the 32.255.

## Slide 5: The Triggers in the CHF CDRs in Stage2
Triggers in the Common charging data in CHF-CDR
  5G Common charging data in CHF-CDR specified in TS 32.298 describes the two level trigger.
Source: TS 32.290 V18.0.0
  UUC level triggers
  Message/Main level

## Slide 6: Summary
Problems:
    The relationship of Triggers in CHF CDR between TS 32.298 and TS 32.XXX service charging specifications
      Every service charging specifications includes the clause for the CHF record data, including the triggers such as SMF triggers in data connectivity CHF CDR in the TS 32.255, NEF triggers in exposure CHF CDR in the TS 32.254.
      The CHF record data in service charging specification stage 2 should be aligned with the TS 32.298 Stage 3.
      In the TS 32.298, Only SMF triggers is included.
    The relationship of Triggers in message between TS 32.291 and TS 32.XXX service charging specifications
      The triggers is transferred in the charging data request/response specified in service charging specifications, including such as SMF triggers in the TS 32.255, NEF triggers in the TS 32.254.
      The triggers in service charging specification Stage 2 should be aligned with the TS 32.291 Stage 3.
      In the TS 32.291, Only SMF triggers is included.
Two Opinions for the corrections.
  Remove all the triggers in the message level and CHF CDR in the stage 2 if Stage 3 is not supported.
  Add the trigger type definition and binding in the 32.291 and add the NF triggers in the and CHF parameters and ASN.1 in the TS 32.298. ---- Proposed in the CRs as the example.

## Slide 7: Thank you!