## Slide 1: Charging Triggers in Stage 2 and Stage 3 (SA5 #151)
Chen Shan
Huawei

## Slide 2: The triggers in Charging Data Message Stage2
Triggers in the charging Stage 2
  TS 32.255: SMF triggers for PDU session, quota management.
  TS 32.254: NEF triggers for API invocation/notification.
  TS 32.256: AMF triggers for registration, location, N2 connection…
  …. SMSF, Prose charging trigger, Network slice charging trigger

## Slide 3: The Triggers in the CHF CDRs in Stage2
Triggers in the CHF CDRs Stage 2
  TS 32.254: NEF triggers in NEF CHF CDR.
  TS 32.257: EAS Deployment in CHF CDRs ….

## Slide 4: The Triggers in the Open API in the Stage3
Triggers in the Stage 3
  TS 32.291: The “Triggers” is reported in the Charging Data Request in the message
  TS 32.291: “TriggerType” is the Enumeration data type, which specify the Triggers defined in the Service Charging Specifications in the Stage 2 , I.e. the 32.255.

## Slide 5: The Triggers in the CHF CDRs in Stage3
Triggers in the Common Field of CHF-CDR
  5G Common charging data in CHF-CDR specified in TS 32.298 clause 5.1.5.0
Source: TS 32.290 V18.0.0
  UUC level triggers
  Message/Main level
  In the TS 32.298 CHF CDR and the corresponding ASN.1
  “Trigger” only covers SMF Triggers which specify the Triggers defined in the Service Charging Specifications in the Stage 2 , i.e. the 32.255.
  “sMFTrigger” is aligned with the data type “ TriggerType“ specified in the TS 32.291.
  ASN.1 for CHF CDRs

## Slide 6: Summary
Problems
    The relationship of Triggers in CHF CDR between TS 32.298 and TS 32.XXX service charging specifications
      Every service charging specifications includes the clause for the CHF record data, including the triggers such as SMF triggers in data connectivity CHF CDR in the TS 32.255, NEF triggers in exposure CHF CDR in the TS 32.254.
      The CHF record data in service charging specification stage 2 should be aligned with the TS 32.298 Stage 3.
      In the TS 32.298, Only SMF triggers are included.
    The relationship of Triggers in message between TS 32.291 and TS 32.XXX service charging specifications
      The triggers is transferred in the charging data request/response specified in service charging specifications, including such as SMF triggers in the TS 32.255, NEF triggers in the TS 32.254.
      The triggers in service charging specification Stage 2 should be aligned with the TS 32.291 Stage 3.
      In the TS 32.291, Only SMF triggers are included.
Meeting | CR | Title
SA5 #148 | S5-233451 | Rel-17 CR 32.298 Addition of the Triggers in the CHF CDR
 | S5-233452 | Rel-18 CR 32.298 Addition of the Triggers in the CHF CDR
SA5 #149 | S5-234287 | Rel-17 CR 32.298 Addition of the NF Triggers in the CHF CDR
 | S5-234288 | Rel-18 CR 32.298 Addition of the NF Triggers in the CHF CDR
SA5 #150 | S5-235476 | Rel-17 CR 32.298 Addition of the NF Triggers in the CHF CDR
 | S5-235479 | Rel-18 CR 32.291Correction on the TriggerType
 | S5-235477 | Rel-18 CR 32.298 Addition of the NF Triggers in the CHF CDR
 | S5-235478 | Rel-17 CR 32.291Correction on the Trigger Type
SA5 #151 | S5-236XXX | Rel-18 CR 32.254 Remove the Triggers in Charging Data message Rel-18 CR 32.256 Remove the Triggers in Charging Data message Rel-17 CR 28.201 Remove the Triggers in Charging Data message Rel-17 CR 32.257 Remove the Triggers in Charging Data message
Two Opinions for the corrections
    Determine whether the triggers should be reported in the Charging Data Request Message
      Option A: If required, add the NF triggers in the CHF CDR TS 32.298.----Proposed in the CRs at SA5 #148 and 149.
      Option B: If required, add the trigger type definition and binding in the 32.291 and add the all NF triggers in the and CHF parameters and ASN.1 in the TS 32.298. ---- Proposed in the CRs at SA5 #150.
      Option C: If not required, remove all the triggers in the message level and CHF CDR in the stage 2 because Stage 3 is not supported. The SMF trigger is an exception because SMF triggers are already covered.--- Proposed in the CRs at SA5 #151.

## Slide 7: Option A --- Add NF triggers
Add the special triggers in the CHF CDR
Add the general NF triggers in the CHF CDR
  To keep alignment with the CHF CDRs specified in the service specifications, the following item should be added.
    For NEF charging, the message level triggers is specified in the TS 32.254
    For Edge computing charging, the message level triggers is specified in the TS 32.257.
    For NSPA charging, the triggers in Used Unit Container is specified in the TS 28.202.
  Other NF consumers which not specify the trigger in the CHF CDR will not present in the CHF CDR.
  Add the NF triggers in the CHF CDR which can be used for any NF consumer (e.g. AMF, NEF), except SMF.

## Slide 8: Option B --- Add the triggers in TS 32.291
…
…
Add the detailed trigger types for SMSF, AMF, NEF…and other NF consumers
  Take the SMSF as the example
  Stage 2 TS 32.274
  Stage 3 TS 32.291
  Other Trigger Type are added.
  IMS Nodes
  AMF
  NEF
  NSPA
  NSM

## Slide 9: Option B --- Add the triggers in TS 32.298
…
Add the detailed trigger Type for SMSF, AMF, NEF…and other NF consumers
  Take the SMSF as the example
  Stage 2 TS 32.274
  Stage 3 TS 32.298
  SMF
  Extend the Trigger and the sMFTrigger is not used.
  Define new trigger types for all NF consumers.
  Define new data type of trigger types “string” for all NF consumers and reference to the TS 32.291.
TriggerType ::= OCTET STRING

## Slide 10: Option C --- Remove the triggers in the Stage2
  In the Stage 2, the following triggers have been specified.
    For NEF charging, the message level triggers is specified in the TS 32.254
    For Edge computing charging, the message level triggers is specified in the TS 32.257.
    For NSPA charging, the triggers in Used Unit Container is specified in the TS 28.202.
  Remove the triggers in the service specifications stage2 .Take NSPA triggers as the example
Remove the triggers in the charging data message and CHF CDR
  NSPA
  AMF
  NEF

## Slide 11: Thank you!