## Slide 1: OpenAPI SS: SubNetwork and ManagedElement Schema definition Issues (revision of S5-237498)
Nokia, Nokia Shanghai Bell

## Slide 2: Background/Problem
For OpenAPI SS, Generic NRM (TS28.623) does not define SubNetwork-Single, instead
All the following OpenAPI files defined a separate SubNetwork-Single:
  TS28104_MdaNrm.yaml: SubNetwork-Single:
  TS28105_AiMlNrm.yaml: SubNetwork-Single:
  TS28312_IntentNrm.yaml: SubNetwork-Single:
  TS28536_CoslaNrm.yaml: SubNetwork-Single:
  TS28538_EdgeNrm.yaml: SubNetwork-Single:
  TS28541_5GcNrm.yaml: SubNetwork-Single:
  TS28541_NrNrm.yaml: SubNetwork-Single:
  TS28541_SliceNrm.yaml: SubNetwork-Single:
  Issue 1: Not possible to instantiate a complete SubNetwork
  Some attributes (e.g., in blue rectangle in above diagram) in the SubNetwork-Single is common to all the SubNetwork-Single definitions
  The Service specific attribute (e.g., Intent in above diagram) is not reachable by SubNetwork instance instantiated from SubNetwork-Single defined in other OpenAPI.
  Hence, it’s not possible to instantiate a SubNetwork MOI with all MOI contained by SubNetwork, e.g. A SubNetwork MOI with both Intent MOI and NetworkSlice MOI.
  Issue 2: Semantic issue
  the schema of Resource is anyOf (TS28532_ProvMnS.yaml) resources from all service specific NRM, it leads to confusion. (Imaging a scenario: the Provisioning MnS instances two SubNetwork-Single MOI, with the same class type [same value for objectClass], but different content of MOI, especially from same version of TS28.541– which defines 3 different variants of SubNetwork-Single)
TS28312_IntentNrm.yaml： Example

## Slide 3: TS28623_GenericNrm.yaml (SubNetwork definitions)
Same issue for ManagedElement IOC
Other issues observed:
> The self containment is missing (in red)
> MnsAgent is name contained by 3 IOC, which is mis-leading, a XOR indication shall be added to diagram or add description in note.
Domain_ IOC defined in TS28.620
TS28.622 Figure 4.2.1-1: NRM fragment

## Slide 4: TS28532_ProvMnS.yaml: Resource
Defined a few variants of SubNetwork-Single
Each these SubNetwork-Single dose not include the name contained IOC which is name contained by SubNetwork-Single from other scheme.
For example, SubNetwork-Single defined in “TS28541_NrNrm.yaml” does not include name containment IOC defined in SubNetwork-Single from TS28541_5GcNrm.yaml.
Same issue for ManagedElement IOC.

## Slide 5: Example of two SubNetwork-single IOC definition
TS28541_5GcNrm.yaml
TS28541_NrNrm.yaml
Repeated definition in all domain specific OpenAPI files.

## Slide 6: Solution 1 (Top-down)
# in TS28623_GenericNrm.yaml: to implement new IOC (SubNetwork-Single)
# in TS28541_5GcNrm.yaml: (current stage3)
# in TS28541_5GcNrm.yaml: to change SubNetwork-Single to SubNetwork-ncO-5gcNrm
With the changes to all other yaml files, there will be only one SubNetwork-Single IOC definition in TS28.623
Pros: straightforward changes,
Cons: The SubNetwork-Single shall always instantiated from Generic NRM instead of from bottom yaml file (i.e. from TS28541_SliceNrm.yaml). A quick fix is to add a simple schema definition in bottom yaml file (one line reference of the SubNetwork-Single) like below:
Main idea:
1) Only define SubNetwork-Single in Generic NRM (TS28.623),
2) all service OpenAPI only implement the name containment relationship.
3) Same fix also for ManagedElement-Single
Solution 1 example
This Commented out part is to be removed in actual CR
Note: the tag ‘-ncO-’ indicates name contained Object

## Slide 7: Solution 2: bottom up
Main idea: define a SubNetwork-Single in each Service OpenAPI file, but with the same definition.
Step1: Define a common service level name containment schema in generic NRM (TS28.623)
Step2: update the SubNetwork-Single definition in service NRM as below
With the changes to all other YAML files, there will be a few (the same) SubNetwork-Single IOC definition
Cons: duplicated definition (but contents are the same),
Pros: The SubNetwork-Single shall always be instantiated from bottom YAML file (i.e. from TS28541_SliceNrm.yaml), and each subnetwork-single definition is complete.
Existing stage 3 example
Solution 2 example (part 1 out of 2)
Solution 2 example (part 2 out of 2)

## Slide 8: Endorsement proposal
Endorse the solution 1 to fix the issue for Rel-18 (not for early releases)

## Slide 9: Thanks