## Slide 1: Cloud Native Data Streaming
15 May, 24
Source: Rakuten Mobile Inc [RMI]

## Slide 2: Background
  Large scale cloud native deployment requires
                Moving massive amount of data from microservices at NF side to the management system.
                Data sharing among multiple data consumers microservices in the management system.
                High availability with strong resiliency and fault protection.
                Dynamic scaling and load balancing
Conventional data streaming pattern and architecture for PM/trace/analytics are not suitable anymore.
Efficient, high throughput, highly scalable, and fault-tolerant data streaming framework is needed for sharing data between cloud native network functions and management system.
Management service
Management service
NF workload
NF workload
NF
3GPP Management System
MnF
WebSocket
Node
NF workload
Node
Node
Node cluster
Management workload
NF
…
…
Cloud site
Cloud site
Cloud site
Convention streaming architecture
Cloud-native streaming architecture
storage
storage
…
Single point-to-point connection based.
Traffic aggregation point is difficult to scale dynamically and to be efficient for cloud-native environment.
No data sharing.
Limited transport resiliency and fault tolerance.
Application layer manage all connection aspects for connections, parallel streaming, scaling, resiliency, load balancing etc -> huge development and maintenance cost for it to be adapted to cloud environment.
Multipoints-to-multipoints streaming with data sharing removing performance bottle neck at the aggregation point and improve efficiency.
High scalability.
Highly distributed.
High availability with strong transport resiliency and fault tolerance.
Messaging framework and orchestration tools from 3rd party and open-source handles most of the complexities for managing connections, parallel streaming, scaling, resiliency, load balancing etc.
Messaging framework

## Slide 3
Feature | Conventional Streaming (3GPP 28.532 ) | Cloud-Native Streaming
Infrastructure | Dedicated Servers: Network operators manage their own physical servers for data processing and storage. This requires upfront investment in hardware, ongoing maintenance, and manual provisioning of additional resources during peak loads. | Cloud-Based Resources: Data processing and storage leverage virtual servers within a cloud platform. This eliminates the need for upfront hardware costs and allows for automatic scaling based on data volume. You only pay for the resources you use, leading to potentially lower overall costs.
Architecture | Monolithic Application or Point-to-Point Integrations: A single, large application might handle data ingestion, processing, and reporting. Modifying functionalities within this application can be complex and require changes to the entire system. Alternatively, point-to-point integrations might be used, where each data source has a custom connection to the processing application. This creates a tightly coupled system that's difficult to modify or scale. | Microservices Architecture with Streaming Platform: The system is broken down into smaller, independent services that handle specific tasks (e.g., data ingestion, processing, reporting). This allows for easier development, deployment, and updates. A dedicated streaming platform, like Apache Kafka, acts as a central hub for data flow. Data sources publish data to the platform, and processing services subscribe to relevant data streams. This decoupled architecture promotes flexibility and independent scaling of services.
Integration | Proprietary Protocols or Custom Integrations: Data exchange between network elements and the processing system might rely on proprietary protocols specific to the network vendor. Alternatively, custom integrations might be developed to connect different elements. This approach can be complex to manage and maintain, especially when integrating new network equipment. | Standardized APIs and Event-Driven Architecture: APIs (Application Programming Interfaces) act as standardized communication channels between network elements and the streaming platform. This approach simplifies integration and ensures compatibility with a wider range of equipment. Event-driven architecture allows for loosely coupled communication – network elements publish events (data updates) to the platform, and processing services subscribe to receive relevant events when they occur. This improves scalability and simplifies adding new data sources.
Scalability | Manual Scaling: Adding or removing dedicated servers to handle fluctuations in data volume is a manual process that requires planning and downtime. This can lead to inefficiencies, as underutilized servers during low traffic periods increase costs, while insufficient resources during peak times can lead to performance issues. | Automatic Scaling: Cloud platforms offer automatic scaling based on real-time data flow. Additional virtual servers are automatically provisioned when needed and de-provisioned when traffic subsides. This ensures optimal resource utilization and avoids performance bottlenecks during peak loads.
Real-time Processing | Limited Capabilities: Traditional systems might have limited real-time processing capabilities due to the architecture and the overhead of data processing within a monolithic application or point-to-point integrations. Delays in data processing can lead to outdated insights and slower response times to network issues. | Enabled through Streaming Platform: Streaming platforms like Kafka are specifically designed for handling large volumes of data in real-time. Data is processed as it arrives, enabling faster analysis and quicker identification of network performance problems. This allows for proactive troubleshooting and minimizes potential disruptions.

## Slide 4: Cloud-Native Streaming with Message Bus Solution – Concept
Partitions
parallel contribution of data pieces
of the same topic
parallel consuming of data pieces of the same topic with data isolation
Producers , consumers and data bus workloads are distributed across multiple server nodes and node clusters
Redundant message bus instances and connections for load balancing and failure protection
Data Bus
Producer
Producer
Producer
Producer
Consumer
Producer
publish
Producer
publish
Producer
publish
Consumer
subscribe
Consumer
subscribe
Msg. Bus
Distributed Cloud Infrastructure
Dynamic horizontal scaling of data producers and transport capacity
Publish-Subscription based streaming mode designed for cloud-native applications – micro-service architecture, parallel streaming, data sharing, distributed, scaling
Stream/top A
Stream/top B
Stream/top C
Data bus handling data distribution, routing, subscription management etc
Data bus workload can scale horizontally also

## Slide 5: 3GPP Management System to Support Message Bus Solution
The workloads producing data in a Cloudified NF (data producers) connect to and produce the streaming data in parallel to the message bus/brokers
Instead of establishing direct connections between streaming data reporting MnS producer and consumer based on WebSocket, a message bus/broker is introduced in between to handle the data streaming for cloudified NF.
Microservices consuming data in a 3GPP management system (data consumers) may consume the streaming data in parallel from the message bus/broker.
The number of parallel connections may scale in and out dynamically as the workloads of the cloudified NF scales.
Multiple message bus/broker instances may exist to duplicate the connections with data procedures and consumers for connectivity resiliency and load balancing
A generic interface may be introduced for managing the data streaming jobs for e.g. connection establishment and data subscriptions, i.e. the relationships between data producers, consumers, message buses/brokers and the streaming data contents.

## Slide 6: Generic Data Job Control API
A generic API solution set can be introduced to support data job management for any types of data bus implementation, e.g. Kafka and others.
The API solution support generic operations common for types message bus technology, e.g. :
establishStreamingTopic: Setup up a streaming topic. A topic is a logical streaming channel (rather than real socket connection) allow MnS producer to stream all or a portion of the PM metrics and KPIs collected by a measurement job (TS 28.550) to the management system via the channel. Multiple data producers can stream data to the same topic in parallel. A streaming topic can be optionally configured with partitions which further partition the logical streaming channel in to sub channels and isolate the traffics between them.
The topicId and streamInfo are conveyed from MnS producer to the MnS consumer to establish the logical channel and make MnS producer knowing which logical channel to send the traffic to and what to be sent. Message bus/broker URIs are sent along with the operation which allow MnS producer to setup the connection with the message bus.
Input parameters:
TopicList
>TopicInfo
>>TopicId
>> BrokerURIs
>> PartitionConfiguration (optional)
>> StreamInfo
>>> Parameters defined in Table 12.5.1.4.2.5-1 of 3GPP TS28.532
addStream: Add more stream to topic
deleteStream: Delete a stream from topic
getTopicInfo
getStreamInfo
VS
Currently solution set in 28.532 for Websocket based streaming job control
Any message bus implementation is allowed, e.g. Kafka
Setup up logical streaming channel between MnS producer and consumer instead of connection.
The actual connection is with the message bus as the middle layer.
Setup up direct connection between MnS consumer and MnS producer

## Slide 7: Co-existence with Other Cloud Native Streaming Solutions