3GPP TSG-SA5 (Telecom Management)	(S5-070177

# Meeting SA5#51, 22 - 26 Jan 2007, Seville, SPAIN

| CR-Form-v9.3 |
| --- |
| CHANGE REQUEST |
| ( | 32.633 | CR | 0019 | ( rev | - | ( Current version: | 7.0.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Removing IMS related links from the CN NRM |
| --- | --- |
| Source to WG: ( | Nokia, Ericsson (Gyula.bodog@nokia.com) |
| Source to TSG: ( | S5 |
| Work item code: ( | OAM7-NIM |  | Date: ( | 26/01/2007 |
| Category: ( | F |  | Release: ( | Rel-7 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) |
| Reason for change: ( | The link between HSS and the IMS NEs are defined in the IMS NRM. No need to define links between HLR and IMS NEs |
| Summary of change: ( | Removing from the modelling the following links: Link_Hlr_Scscf, Link_Cscf_Hlr, Link_As_Auc and Link_As_Hlr according to the IS specification |
| Consequences if ( not approved: | Not existing and not correct links are defined in the specification, which can lead to wrong implementation. |
| Clauses affected: ( | Section 1, 5.2.41, 5.2.42, 5.2.48, 5.2.62, Annex A |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  | x |  | O&M Specifications | 32.632, 32.635, 32.732, 32.733, 32.735 |
| Other comments: ( | Related R7 CR to 32.732 is in S5-070173 CR to 32.733 is in S5-070174 CR to 32.735 is in S5-070175 CR to 32.632 is in S5-070176 and CR to 32.635 is in S5-070178 |

1st Modified Section

# 1	Scope

The purpose of the present document is to define the mapping of the IRP information model (see TS 32.632 [3]) to the protocol specific details necessary for implementation of this IRP in a CORBA/IDL environment.

This Solution Set specification is related to 3GPP TS 32.632 V7.1.X.

Next Modified Section

## 5.2	Information Object Class (IOC) mapping

### 5.2.1	IOC MscServerFunction

Mapping from NRM IOC MscServerFunction attributes to SS equivalent MOC MscServerFunction attributes

| Attributes of IOC MscFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| mscServerFunctionId | mscServerFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |
| mccList | mccList | GenericNetworkResourcesIRPSystem::AttributeTypes:: LongSet | Read-Write, M |
| mncList | mncList | GenericNetworkResourcesIRPSystem::AttributeTypes:: LongSet | Read-Write, M |
| lacList | lacList | GenericNetworkResourcesIRPSystem::AttributeTypes:: LongSet | Read-Write, M |
| sacList | sacList | GenericNetworkResourcesIRPSystem::AttributeTypes:: LongSet | Read-Write, M |
| gcaList | gcaList | GenericNetworkResourcesIRPSystem::AttributeTypes:: LongSet | Read-Write, M |
| mscId | mscId | long | Read-Write, M |
| Associated With/mscServerFunction-GsmCell | mscServerFunction-GsmCell | GenericNetworkResourcesIRPSystem::AttributeTypes::MOReferenceSet | Read-Only, M |
| Associated With/mscServerFunction-ExternalGsmCell | mscServerFunction-ExternalGsmCell | GenericNetworkResourcesIRPSystem::AttributeTypes::MOReferenceSet | Read-Only, M |
| Associated With/mscServerFunction-CsMgwFunction | mscServerFunction-CsMgwFunction | GenericNetworkResourcesIRPSystem::AttributeTypes::MOReferenceSet | Read-Only, M |

### 5.2.2	IOC HlrFunction

Mapping from NRM IOC HlrFunction attributes to SS equivalent MOC HlrFunction attributes

| Attributes of IOC HlrFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| hlrFunctionId | hlrFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.3	IOC VlrFunction

Mapping from NRM IOC VlrFunction attributes to SS equivalent MOC VlrFunction attributes

| Attributes of IOC VlrFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| vlrFunctionId | vlrFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.4	IOC AucFunction

Mapping from NRM IOC AucFunction attributes to SS equivalent MOC AucFunction attributes

| Attributes of IOC AucFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| aucFunctionId | aucFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.5	IOC EirFunction

Mapping from NRM IOC EirFunction attributes to SS equivalent MOC EirFunction attributes

| Attributes of IOC EirFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| eirFunctionId | eirFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.6	IOC SmsIwmscFunction

Mapping from NRM IOC SmsIwmscFunction attributes to SS equivalent MOC SmsIwmscFunction attributes

| Attributes of IOC SmsIwmscFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| smsIwmscFunctionId | smsIwmscFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.7	IOC SmsGmscFunction

Mapping from NRM IOC SmsGmscFunction attributes to SS equivalent MOC SmsGmscFunction attributes

| Attributes of IOC SmsGmscFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| smsGmscFunctionId | smsGmscFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.8	IOC SgsnFunction

Mapping from NRM IOC SgsnFunction attributes to SS equivalent MOC SgsnFunction attributes

| Attributes of IOC SgsnFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| sgsnFunctionId | sgsnFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read-Write, M |
| mccList | mccList | GenericNetworkResourcesIRPSystem::AttributeTypes:: LongSet | Read-Write, M |
| mncList | mncList | GenericNetworkResourcesIRPSystem::AttributeTypes:: LongSet | Read-Write, M |
| lacList | lacList | GenericNetworkResourcesIRPSystem::AttributeTypes:: LongSet | Read-Write, M |
| racList | racList | GenericNetworkResourcesIRPSystem::AttributeTypes:: LongSet | Read-Write, M |
| sacList | sacList | GenericNetworkResourcesIRPSystem::AttributeTypes:: LongSet | Read-Write, M |
| sgsnId | sgsnId | long | Read-Write, M |
| Associated With/sgsnFunction-GsmCell | sgsnFunction-GsmCell | GenericNetworkResourcesIRPSystem::AttributeTypes::MOReferenceSet | Read-Only, M |
| Associated With/sgsnFunction-ExternalGsmCell | sgsnFunction-ExternalGsmCell | GenericNetworkResourcesIRPSystem::AttributeTypes::MOReferenceSet | Read-Only, M |
| proceduralStatus | There is no corresponding SS attribute. |  |  |

### 5.2.9	IOC GgsnFunction

Mapping from NRM IOC GgsnFunction attributes to SS equivalent MOC GgsnFunction attributes

| Attributes of IOC GgsnFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| ggsnFunctionId | ggsnFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |
| proceduralStatus | There is no corresponding SS attribute. |  |  |

### 5.2.10	IOC BgFunction

Mapping from NRM IOC BgFunction attributes to SS equivalent MOC BgFunction attributes

| Attributes of IOC BgFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| bgFunctionId | bgFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.11	IOC GmscFunction

Mapping from NRM IOC GmscFunction attributes to SS equivalent MOC GmscFunction attributes

| Attributes of IOC GmscFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| gmscFunctionId | gmscFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.12	IOC SmlcFunction

Mapping from NRM IOC SmlcFunction attributes to SS equivalent MOC SmlcFunction attributes

| Attributes of IOC SmlcFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| smlcFunctionId | smlcFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.13	IOC GmlcFunction

Mapping from NRM IOC GmlcFunction attributes to SS equivalent MOC GmlcFunction attributes

| Attributes of IOC GmlcFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| gmlcFunctionId | gmlcFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.14	IOC ScfFunction

Mapping from NRM IOC ScfFunction attributes to SS equivalent MOC ScfFunction attributes

| Attributes of IOC ScfFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| scfFunctionId | scfFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.15	IOC SrfFunction

Mapping from NRM IOC SrfFunction attributes to SS equivalent MOC SrfFunction attributes

| Attributes of IOC SrfFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| srfFunctionId | srfFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.16	IOC CbcFunction

Mapping from NRM IOC CbcFunction attributes to SS equivalent MOC CbcFunction attributes

| Attributes of IOC CbcFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| cbcFunctionId | cbcFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.17	IOC CgfFunction

Mapping from NRM IOC CgfFunction attributes to SS equivalent MOC CgfFunction attributes

| Attributes of IOC CgfFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| cgfFunctionId | cgfFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.18	Void

### 5.2.19	IOC GmscServerFunction

Mapping from NRM IOC GmscServerFunction attributes to SS equivalent MOC GmscServerFunction attributes

| Attributes of IOC GmscServerFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| gmscServerFunctionId | gmscServerFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.20	IOC IwfFunction

Mapping from NRM IOC IwfFunction attributes to SS equivalent MOC IwfFunction attributes

| Attributes of IOC IwfFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| iwfFunctionId | iwfFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.21	IOC MnpSrfFunction

Mapping from NRM IOC MnpSrfFunction attributes to SS equivalent MOC IwfFunction attributes

| Attributes of IOC MnpSrfFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| mnpSrfFunctionId | mnpSrfFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.22	IOC NpdbFunction

Mapping from NRM IOC NpdbFunction attributes to SS equivalent MOC NpdbFunction attributes

| Attributes of IOC NpdbFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| npdbFunctionId | npdbFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.23	IOC SgwFunction

Mapping from NRM IOC SgwFunction attributes to SS equivalent MOC SgwFunction attributes

| Attributes of IOC SgwFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| sgwFunctionId | sgwFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.24	IOC SsfFunction

Mapping from NRM IOC SsfFunction attributes to SS equivalent MOC SsfFunction attributes

| Attributes of IOC SsfFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| ssfFunctionId | ssfFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.25	IOC BsFunction

Mapping from NRM IOC BsFunction attributes to SS equivalent MOC BsFunction attributes

| Attributes of IOC BsFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| bsFunctionId | bsFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |

### 5.2.26	IOC IucsLink

Mapping from NRM IOC IucsLink attributes to SS equivalent MOC IucsLink attributes

| Attributes of IOC IucsLink in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| iucsLinkId | iucsLinkId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |
| Connected To/connectedRnc | connectedRnc | GenericNetworkResourcesIRPSystem::AttributeTypes::MOReference | Read-Only, M |
| Connected To/connectedBss | connectedBss | GenericNetworkResourcesIRPSystem::AttributeTypes::MOReference | Read-Only, M |

### 5.2.27	IOC IupsLink

Mapping from NRM IOC IupsLink attributes to SS equivalent MOC IupsLink attributes

| Attributes of IOC IucsLink in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| iupsLinkId | iupsLinkId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |
| Connected To/connectedRnc | connectedRnc | GenericNetworkResourcesIRPSystem::AttributeTypes::MOReference | Read-Only, O |
| Connected To/connectedBss | connectedBss | GenericNetworkResourcesIRPSystem::AttributeTypes::MOReference | Read-Only, O |

### 5.2.28	IOC IubcLink

Mapping from NRM IOC IubcLink attributes to SS equivalent MOC IubcLink attributes

| Attributes of IOC IucsLink in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| iubcLinkId | iubcLinkId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |
| Connected To/connectedRnc | connectedRnc | GenericNetworkResourcesIRPSystem::AttributeTypes::MOReference | Read-Only, M |

### 5.2.29	IOC ALink

Mapping from NRM IOC ALink attributes to SS equivalent MOC ALink attributes

| Attributes of IOC IucsLink in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| aLinkId | aLinkId | string | Read-Only, M |
| userLabel | userLabel | string | Read- Write, M |
| Connected To/connectedBss | connectedBss | GenericNetworkResourcesIRPSystem::AttributeTypes::MOReference | Read-Only, M |

### 5.2.30	IOC GbLink

Mapping from NRM IOC GbLink attributes to SS equivalent MOC GbLink attributes

| Attributes of IOC IucsLink in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| gbLinkId | gbLinkId | string | Read-Only, M |
| userLabel | userLabel | string | Read-Write, M |
| Connected To/connectedBss | connectedBss | GenericNetworkResourcesIRPSystem::AttributeTypes::MOReference | Read-Only, M |

### 5.2.31	IOC CsMgwFunction

Mapping from NRM IOC CsMgwFunction attributes to SS equivalent MOC CsMgwFunction attributes

| Attributes of IOC MgwFunction in TS 32.632 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| csMgwFunctionId | csMgwFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read-Write, M |
| Associated With/csMgwFunction-MscServerFunction | csMgwFunction-MscServerFunction | GenericNetworkResourcesIRPSystem::AttributeTypes::MOReference | Read-Only, M |
| Connected To/csMgwFunction-IucsLink | csMgwFunction-IucsLink | GenericNetworkResourcesIRPSystem::AttributeTypes::MOReferenceSet | Read-Only, M |
| Connected To /csMgwFunction-ALink | csMgwFunction-ALink | GenericNetworkResourcesIRPSystem::AttributeTypes::MOReferenceSet | Read-Only, M |

### 5.2.32	Void

### 5.2.33	Void

### 5.2.34	Void

### 5.2.35	Void

### 5.2.36	Void

### 5.2.37	Void

### 5.2.38	Void

### 5.2.39	Void

### 5.2.40	Void

### 5.2.41	Void

### 5.2.42	Void

### 5.2.43	Void

### 5.2.44	Void

### 5.2.45	Void

### 5.2.46	Void

### 5.2.47	Void

### 5.2.48	Void

### 5.2.49	Void

### 5.2.50	Void

### 5.2.51	Void

### 5.2.52	Void

### 5.2.53	Void

### 5.2.54	Void

### 5.2.55	Void

### 5.2.56	Void

### 5.2.57	Void

### 5.2.58	Void

### 5.2.59	Void

### 5.2.60	Void

### 5.2.61	Void

### 5.2.62	Void

### 5.2.63	Void

### 5.2.64	Void

### 5.2.65	Void

Next Modified Section

Annex A (normative):
CORBA IDL, NRM Definitions

# A.1	IDL specification (file name "CoreNetworkResourcesNRMDefs.idl")

// File: CoreNetworkResourcesNRMDefs.idl

#ifndef _CORENETWORKRESOURCESNRMDEFS_IDL_

#define _CORENETWORKRESOURCESNRMDEFS_IDL_

#include "GenericNetworkResourcesNRMDefs.idl"

#pragma prefix "3gppsa5.org"

/**

* This module defines constants for each MO class name and

* the attribute names for each defined MO class.

*/

module CoreNetworkResourcesNRMDefs

{

/**

*  Definitions for MO class MscServerFunction

*/

interface MscServerFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "MscServerFunction";

// Attribute Names

//

const string mscServerFunctionId = "mscServerFunctionId";

const string mccList = "mccList";

const string mncList = "mncList";

const string lacList = "lacList";

const string sacList = "sacList";

const string gcaList = "gcaList";

const string mscId = "mscId";

const string mscServerFunctionGsmCell = "mscServerFunctionGsmCell";

const string mscServerFunctionExternalGsmCell = "mscServerFunctionExternalGsmCell";

const string mscServerFunctionCsMgwFunction = "mscServerFunctionCsMgwFunction";

};

/**

*  Definitions for MO class HlrFunction

*/

interface HlrFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "HlrFunction";

// Attribute Names

//

const string hlrFunctionId = "hlrFunctionId";

};

/**

*  Definitions for MO class VlrFunction

*/

interface VlrFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "VlrFunction";

// Attribute Names

//

const string vlrFunctionId = "vlrFunctionId";

};

/**

*  Definitions for MO class AucFunction

*/

interface AucFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "AucFunction";

// Attribute Names

//

const string aucFunctionId = "aucFunctionId";

};

/**

*  Definitions for MO class EirFunction

*/

interface EirFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "EirFunction";

// Attribute Names

//

const string eirFunctionId = "eirFunctionId";

};

/**

*  Definitions for MO class SmsIwmscFunction

*/

interface SmsIwmscFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "SmsIwmscFunction";

// Attribute Names

//

const string smsIwmscFunctionId = "smsIwmscFunctionId";

};

/**

*  Definitions for MO class SmsGmscFunction

*/

interface SmsGmscFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "SmsGmscFunction";

// Attribute Names

//

const string smsGmscFunctionId = "smsGmscFunctionId";

};

/**

*  Definitions for MO class SgsnFunction

*/

interface SgsnFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "SgsnFunction";

// Attribute Names

//

const string sgsnFunctionId = "sgsnFunctionId";

const string mccList = "mccList";

const string mncList = "mncList";

const string lacList = "lacList";

const string racList = "racList";

const string sacList = "sacList";

const string sgsnId = "sgsnId";

const string sgsnFunctionGsmCell = "sgsnFunctionGsmCell";

const string sgsnFunctionExternalGsmCell = "sgsnFunctionExternalGsmCell";

};

/**

*  Definitions for MO class GgsnFunction

*/

interface GgsnFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "GgsnFunction";

// Attribute Names

//

const string ggsnFunctionId = "ggsnFunctionId";

};

/**

*  Definitions for MO class BgFunction

*/

interface BgFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "BgFunction";

// Attribute Names

//

const string bgFunctionId = "bgFunctionId";

};

/**

*  Definitions for MO class GmscFunction

*/

interface GmscFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "GmscFunction";

// Attribute Names

//

const string gmscFunctionId = "gmscFunctionId";

};

/**

*  Definitions for MO class SmlcFunction

*/

interface SmlcFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "SmlcFunction";

// Attribute Names

//

const string smlcFunctionId = "smlcFunctionId";

};

/**

*  Definitions for MO class GmlcFunction

*/

interface GmlcFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "GmlcFunction";

// Attribute Names

//

const string gmlcFunctionId = "gmlcFunctionId";

};

/**

*  Definitions for MO class ScfFunction

*/

interface ScfFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "ScfFunction";

// Attribute Names

//

const string scfFunctionId = "scfFunctionId";

};

/**

*  Definitions for MO class SrfFunction

*/

interface SrfFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "SrfFunction";

// Attribute Names

//

const string srfFunctionId = "srfFunctionId";

};

/**

*  Definitions for MO class CbcFunction

*/

interface CbcFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "CbcFunction";

// Attribute Names

//

const string cbcFunctionId = "cbcFunctionId";

};

/**

*  Definitions for MO class CgfFunction

*/

interface CgfFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "CgfFunction";

// Attribute Names

//

const string cgfFunctionId = "cgfFunctionId";

};

/**

*  Definitions for MO class GmscServerFunction

*/

interface GmscServerFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "GmscServerFunction";

// Attribute Names

//

const string gmscServerFunctionId = "gmscServerFunctionId";

};

/**

*  Definitions for MO class IwfFunction

*/

interface IwfFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "IwfFunction";

// Attribute Names

//

const string iwfFunctionId = "iwfFunctionId";

};

/**

*  Definitions for MO class MnpSrfFunction

*/

interface MnpSrfFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "MnpSrfFunction";

// Attribute Names

//

const string mnpSrfFunctionId = "mnpSrfFunctionId";

};

/**

*  Definitions for MO class NpdbFunction

*/

interface NpdbFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "NpdbFunction";

// Attribute Names

//

const string npdbFunctionId = "npdbFunctionId";

};

/**

*  Definitions for MO class SgwFunction

*/

interface SgwFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "SgwFunction";

// Attribute Names

//

const string sgwFunctionId = "sgwFunctionId";

};

/**

*  Definitions for MO class SsfFunction

*/

interface SsfFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "SsfFunction";

// Attribute Names

//

const string ssfFunctionId = "ssfFunctionId";

};

/**

*  Definitions for MO class BsFunction

*/

interface BsFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "BsFunction";

// Attribute Names

//

const string bsFunctionId = "bsFunctionId";

};

/**

*  Definitions for MO class IucsLink

*/

interface IucsLink : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "IucsLink";

// Attribute Names

//

const string iucsLinkId = "iucsLinkId";

const string connectedRnc = "connectedRnc";

const string connectedBss = "connectedBss";

};

/**

*  Definitions for MO class IupsLink

*/

interface IupsLink : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "IupsLink";

// Attribute Names

//

const string iupsLinkId = "iupsLinkId";

const string connectedRnc = "connectedRnc";

const string connectedBss = "connectedBss";

};

/**

*  Definitions for MO class IubcLink

*/

interface IubcLink : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "IubcLink";

// Attribute Names

//

const string iubcLinkId = "iubcLinkId";

const string connectedRnc = "connectedRnc";

};

/**

*  Definitions for MO class ALink

*/

interface ALink : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "ALink";

// Attribute Names

//

const string aLinkId = "aLinkId";

const string connectedBss = "connectedBss";

};

/**

*  Definitions for MO class GbLink

*/

interface GbLink : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "GbLink";

// Attribute Names

//

const string gbLinkId = "gbLinkId";

const string connectedBss = "connectedBss";

};

/**

*  Definitions for MO class CsMgwFunction

*/

interface CsMgwFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "CsMgwFunction";

// Attribute Names

//

const string csMgwFunctionId = "csMgwFunctionId";

const string csMgwFunctionMscServerFunction = "csMgwFunctionMscServerFunction";

const string csMgwFunctionIucsLink = "csMgwFunctionIucsLink";

const string csMgwFunctionALink = "csMgwFunctionALink";

};

};

#endif // _CORENETWORKRESOURCESNRMDEFS_IDL_

End of modifications

Annex B (informative):
Change history

| Change history |
| --- |
| Date | TSG # | TSG Doc. | CR | Rev | Subject/Comment | Cat | Old | New |
| Jun 2001 | SA_12 | SP-010283 | -- | -- | Approved at TSG SA #12 and placed under Change Control | -- | 2.0.0 | 4.0.0 |
| Jun 2002 | SA_16 | SP-020302 | 0001 | -- | Align with Rel-4 Network Architecture (23.002) by changing Roaming Signalling Gateway (R-SGW) to Signalling Gateway (SGW) | F | 4.0.0 | 4.1.0 |
| Sep 2002 | SA_17 | SP-020489 | 0002 | -- | Upgrade to Rel-5 the CORBA SS for Core Network NRM (add Managed Object Classes (MOCs) | C | 4.1.0 | 5.0.0 |
| Dec 2002 | SA_18 | SP-020747 | 0003 | -- | Removal of faulty attribute uraList (alignment with Rel-5 32.632 Network Resource Model) | F | 5.0.0 | 5.1.0 |
| Sep 2004 | SA_25 | SP-040567 | 0004 | -- | Correction in Rules for NRM extensions - Align with 32.622 (Generic NRM IS) | F | 5.1.0 | 5.2.0 |
| Sep 2004 | SA_25 | SP-040582 | 0005 | -- | Correction of modelling of Media GateWay (MGW) | F | 5.1.0 | 5.2.0 |
| Sep 2004 | SA_25 | SP-040581 | 0006 | -- | Add Inheritance in CORBA IDL | B | 5.2.0 | 6.0.0 |
| Dec 2004 | SA_26 | SP-040809 | 0007 | -- | Add new IMS Entities | B | 6.0.0 | 6.1.0 |
| Dec 2004 | SA_26 | SP-040809 | 0008 | -- | Add restart notification to GSN objects using “proceduralStatus” attribute - Align with IS in 32.632 | B | 6.0.0 | 6.1.0 |
| Mar 2005 | SA_27 | SP-050047 | 0011 | -- | Align with 32.632, regarding the IS template and UML repertoire | F | 6.1.0 | 6.2.0 |
| Mar 2005 | SA_27 | SP-050047 | 0012 | -- | Correct List of Long Attributes | A | 6.1.0 | 6.2.0 |
| Mar 2005 | SA_27 | SP-050047 | 0013 | -- | Add IMS links to CN NRM CORBA SS | B | 6.1.0 | 6.2.0 |
| Mar 2006 | SA_31 | SP-060103 | 0014 | -- | Name correction of BgcfFunction - Align with 32.632 Information Service (IS) | F | 6.2.0 | 6.3.0 |
| Sep 2006 | SA_33 | SP-060611 | 0015 | -- | Add missing CscfFunction to CN NRM - Align with 32.632 | F | 6.3.0 | 6.4.0 |
| Dec 2006 | SA_34 | SP-060712 | 0016 | -- | Correct the Link subclasses to model Mg and Mj reference points - Align with 32.632 | F | 6.4.0 | 6.5.0 |
| Dec 2006 | SA_34 | SP-060731 | 0017 | -- | Move IMS part to new IMS NRM (32.733) | C | 6.5.0 | 7.0.0 |

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.