3GPP TSG-SA5 (Telecom Management)	(S5-070201

# Meeting SA5#51, 22 - 26 Jan 2007, Seville, SPAIN

| CR-Form-v9.3 |
| --- |
| CHANGE REQUEST |
| ( | 32.298 | CR | 0063 | ( rev | - | ( Current version: | 7.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Add PoC session initiation type into PoC-information - Align with 32.272 |
| --- | --- |
| Source to WG: ( | Huawei (Cloud.zhao@huawei.com) |
| Source to TSG: ( | S5 |
| Work item code: ( | CH7-PoC-CH |  | Date: ( | 26/01/2007 |
| Category: ( | C |  | Release: ( | Rel-7 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) |
| Reason for change: ( | As described in 32.272 Sec.5.1.1 (“PoC session related charging”), two session establishment types are supported, which can provide different call latency, QoE, etc. This should be considered in charging. See details in OMA-TS-PoC-ControlPlane-V1_0. |
| Summary of change: ( | Add PoC Session Initiation Type to identify the initiation type each participant chooses when initiating session.The value type can be: Pre-established or On-demand. |
| Consequences if ( not approved: | Inability to identify which type of session a PoC subscriber uses to initiate a PoC session. Misalignment with 32.272 |
| Clauses affected: ( | 5.1.4.3.7A (new), 5.2.4.3 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  | X |  | O&M Specifications | 32.272, 32.299 |
| Other comments: ( | Related R7 CR 32.272 in S5-070200 Related R7CR 32.299 in S5-070203 |

1st Modified Section

##### 5.1.4.3.7A	PoC session initiation type

The field is of type Enumerated. It identifies the type of the PoC session initiation.

The identifier can be one of the following:

- Pre-established

- On-demand

Next Modified Section

#### 5.2.4.3	PoC CDRs

This subclause contains the abstract syntax definitions that are specific to the CDR types defined in TS 32.272 [32].

POCChargingDataTypes {itu-t (0) identified-organization (4) etsi(0) mobileDomain (0) charging (5) pocChargingDataTypes (7) asn1Module (0) version1 (0)}

DEFINITIONS IMPLICIT TAGS	::=

BEGIN

-- EXPORTS everything

IMPORTS

CallDuration, RecordType, Diagnostics, IMSI, IMEI, IPAddress, ISDN-AddressString, LocalSequenceNumber, ManagementExtensions, MSISDN, NodeAddress, RecordingEntity, ServiceKey, TimeStamp, ServiceContextID

FROM GenericChargingDataTypes {itu-t (0) identified-organization (4) etsi(0) mobileDomain (0) charging (5) genericChargingDataTypes (0) asn1Module (0) version1 (0)}

GSNAddress, NodeID, SGSNPLMNIdentifier

FROM GPRSChargingDataTypes {itu-t (0) identified-organization (4) etsi(0) mobileDomain (0) charging (5) genericChargingDataTypes (2) asn1Module (0) version1 (0)}

IMS-Charging-Identifier, Incomplete-CDR-Indication, InterOperatorIdentifiers, InvolvedParty, MessageBody, Media-Components-List, Session-Id, SIP-Method

FROM IMSChargingDataTypes {itu-t (0) identified-organization (4) etsi(0) mobileDomain (0) charging (5) imsChargingDataTypes (4) asn1Module (0) version1 (0)}

;

------------------------------------------------------------------------------

--

--  POC RECORDS

--

------------------------------------------------------------------------------

POCRecord	::= CHOICE

{

--

-- Record values 80..81 are PoC specific

--

pPFRecord			[80] PPFRecord,

cPFRecord			[81] CPFRecord

}

PPFRecord 	::= SET

{

recordType						[0] RecordType,

retransmission					[1] NULL OPTIONAL,

sIP-Method						[2] SIP-Method	OPTIONAL,

nodeAddress						[3] NodeAddress	OPTIONAL,

session-Id						[4] Session-Id	OPTIONAL,

calling-Party-Address			[5] InvolvedParty	OPTIONAL,

called-Party-Address			[6] InvolvedParty	OPTIONAL,

servedParty					[7] GraphicString	OPTIONAL,

serviceRequestTimeStamp			[8] TimeStamp	OPTIONAL,

serviceDeliveryStartTimeStamp	[9] TimeStamp	OPTIONAL,

serviceDeliveryEndTimeStamp		[10] TimeStamp	OPTIONAL,

recordOpeningTime				[11] TimeStamp	OPTIONAL,

recordClosureTime				[12] TimeStamp OPTIONAL,

interOperatorIdentifiers		[13] InterOperatorIdentifiers OPTIONAL,

localRecordSequenceNumber		[14] LocalSequenceNumber OPTIONAL,

recordSequenceNumber			[15] INTEGER	OPTIONAL,

causeForRecordClosing			[16] CauseForRecordClosing	OPTIONAL,

incomplete-CDR-Indication		[17] Incomplete-CDR-Indication	OPTIONAL,

iMS-Charging-Identifier			[18] IMS-Charging-Identifier	OPTIONAL,

list-Of-SDP-Media-Components	[19] SEQUENCE	OF	Media-Components-List	OPTIONAL,

gGSNaddress						[20] NodeAddress	OPTIONAL,

serviceReasonReturnCode			[21] UTF8String	OPTIONAL,

list-Of-Message-Bodies			[22] SEQUENCE	OF	MessageBody	OPTIONAL,

userLocationInfo				[23] OctetString	OPTIONAl,

poCInformation					[24] POCInformation	OPTIONAL,

recordExtensions				[25] RecordExtensions	OPTIONAL,

serviceContextID				[26] ServiceContextID OPTIONAL

}

CPFRecord		::=	SET

{

recordType						[0] RecordType,

retransmission					[1] NULL	OPTIONAL,

sIP-Method						[2] SIP-Method	OPTIONAL,

nodeAddress						[3] NodeAddress	OPTIONAL,

session-Id						[4] Session-Id	OPTIONAL,

calling-Party-Address			[5] InvolvedParty	OPTIONAL,

called-Party-Address			[6] InvolvedParty	OPTIONAL,

servedParty					[7] GraphicString	OPTIONAL,

serviceRequestTimeStamp			[8] TimeStamp	OPTIONAL,

serviceDeliveryStartTimeStamp	[9] TimeStamp	OPTIONAL,

serviceDeliveryEndTimeStamp		[10] TimeStamp	OPTIONAL,

recordOpeningTime				[11] TimeStamp	OPTIONAL,

recordClosureTime				[12] TimeStamp	OPTIONAL,

interOperatorIdentifiers		[13] InterOperatorIdentifiers	OPTIONAL,

localRecordSequenceNumber		[14] LocalSequenceNumber	OPTIONAL,

recordSequenceNumber			[15] INTEGER	OPTIONAL,

causeForRecordClosing			[16] CauseForRecordClosing	OPTIONAL,

incomplete-CDR-Indication		[17] Incomplete-CDR-Indication	OPTIONAL,

iMS-Charging-Identifier			[18] IMS-Charging-Identifier	OPTIONAL,

list-Of-SDP-Media-Components	[19] SEQUENCE	OF	Media-Components-List	OPTIONAL,

gGSNaddress						[20] NodeAddress	OPTIONAL,

serviceReasonReturnCode			[21] UTF8String	OPTIONAL,

list-Of-Message-Bodies			[22] SEQUENCE	OF	MessageBody	OPTIONAL,

userLocationInfo				[23] OctetString	OPTIONAl,

poCInformation					[24] POCInformation	OPTIONAL,

recordExtensions				[25] RecordExtensions	OPTIONAL,

serviceContextID				[26] ServiceContextID OPTIONAL

}

------------------------------------------------------------------------------

--

--  PoC DATA TYPES

--

------------------------------------------------------------------------------

CauseForRecordClosing	::= ENUMERATED

{

normalRelease					(0),

abnormalRelease					(1),

serviceChange					(2), -- e.g. change in media due to Re-Invite

volumeLimit						(3),

timeLimit						(4),

numberofTalkBurstLimit			(5),

maxChangeCond					(6),

sessionTypeChange				(7),

managementIntervention			(8)

}

ChangeCondition			::= ENUMERATED

{

serviceChange					(0), -- e.g. change in media due to Re-Invite

volumeLimit						(1),

timeLimit						(2),

numberofTalkBurstLimit			(3),

numberofActiveParticipants		(4),

tariffTime						(5)

}

ListofTalkBurstExchange			::= SET

{

number-Of-Talk-Bursts				 [1] INTEGER OPTIONAL,

talk-Burst-Volume					 [2] INTEGER OPTIONAL,		-- measured in octets

talk-Bursts-Time					 [3] CallDuration OPTIONAL,

number-Of-Received-Talk-Bursts		 [4] INTEGER OPTIONAL,

received-Talk-Burst-Volume			 [5] INTEGER OPTIONAL,		-- measured in octets

received-Talk-Burst-Time			 [6] CallDuration OPTIONAL,

changeCondition						 [7] ChangeCondition OPTIONAL,

changeTime							 [8] TimeStamp,

numberofParticipants				 [9] INTEGER OPTIONAL

}

POCInformation			::= SET

{

pOCSessionType					 [1] POCSessionType OPTIONAL,

numberofParticipants			 [2] INTEGER OPTIONAL,

listofParticipants				 [3] SEQUENCE OF InvolvedParty OPTIONAL,

listofTalkBurstExchange			 [4] SEQUENCE OF ListofTalkBurstExchange OPTIONAL,

pOCControllingAddress			 [5] UTF8String OPTIONAL,

pOCGroupName					 [6] UTF8String OPTIONAL,

pOCSessionId					 [7] UTF8String OPTIONAL,

pOCSessionInitiationType		 [8] POCSessionInitType OPTIONAL

}

POCSessionInitType		::= ENUMERATED

{

pre-established			   (0),

on-demand	  			   (1)

}

POCSessionType			::= ENUMERATED

{

1-to-1session              (0),

chat-group-session         (1),

pre-arranged-group-session (2),

ad-hoc-group-session       (3)

}

End of modifications

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.