3GPP TSG-SA5 (Telecom Management)	( S5-070214

# Meeting SA5#51, 22 - 26 Jan 2007, Seville, SPAIN

| CR-Form-v9.3 |
| --- |
| CHANGE REQUEST |
| ( | 32.335 | CR | 0003 | ( rev | - | ( Current version: | 6.2.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network | X | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Add Notification XML definition in NotificationLogIRP |
| --- | --- |
| Source to WG: ( | Huawei, Yangli (afi@huawei.com) |
| Source to TSG: ( | S5 |
| Work item code: ( | OAM7-NIM |  | Date: ( | 26/01/2007 |
| Category: ( | B |  | Release: ( | Rel-7 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) |
| Reason for change: ( | Notification XML definition is missing in 32.335. |
| Summary of change: ( | Add NotificationLogIRP Notification XML Definitions |
| Consequences if ( not approved: | Notification of NotificationLogIRP can’t be logged. |
| Clauses affected: ( | 4.6, Annex C |
|  | Y | N |  |  |
| Other specs ( |  | x | Other core specifications ( |  |
| affected: |  | x | Test specifications |  |
|  |  | x | O&M Specifications |  |
| Other comments: ( |  |

1st Modified Section

## 4.6	NL IRP Notification XML Definitions

This clause provides XML definitions of Notification Log IRP notifications as defined in [4].

The structure of the NotificationLogIRP Notification XML Definitions is shown in graphical depiction below:

Note: The use of XML schema key word “sequence” to support IS-defined set (not sequence) is for the purpose of XML processor efficiency. This shall not imply the use of “sequence” in other technology.

Next Modified Section

Annex C (normative):
NotificationLogIRP Notification XML schema (file name "ntfLogNotif.xsd")

<?xml version="1.0" encoding="UTF-8"?>

<!--

3GPP TS 32.335 NotificationLogIRP Notification XML Schema

ntfLogIRPNotif.xsd

-->

<schema xmlns:xl="http://www.3gpp.org/ftp/specs/archive/32_series/32.335#ntfLogIRPNotif" xmlns:xe="http://www.3gpp.org/ftp/specs/archive/32_series/32.305#notification" xmlns="http://www.w3.org/2001/XMLSchema" targetNamespace="http://www.3gpp.org/ftp/specs/archive/32_series/32.335#ntfLogIRPNotif" elementFormDefault="qualified" attributeFormDefault="unqualified">

<import namespace="http://www.3gpp.org/ftp/specs/archive/32_series/32.305#notification"/>

<simpleType name="LogSubscriptionId">

<restriction base="string">

<minLength value="1"/>

</restriction>

</simpleType>

<simpleType name="CurrentOccupancyLevel">

<restriction base="short">

<maxInclusive value="100"/>

<minInclusive value="0"/>

</restriction>

</simpleType>

<simpleType name="LogFullAction">

<restriction base="string">

<enumeration value="Wrap"/>

<enumeration value="Halt"/>

</restriction>

</simpleType>

<complexType name="NotificationCategories">

<sequence>

<element name="IRPVersion" type="string" maxOccurs="unbounded"/>

</sequence>

</complexType>

<complexType name="NotifyLogSubscribed">

<complexContent>

<extension base="xe:Notification">

<sequence>

<element name="body">

<complexType>

<sequence>

<element name="LogSubscriptionId" type="xl:LogSubscriptionId"/>

<element name="LoggingEndTime" type="dateTime" minOccurs="0"/>

<element name="NotificationCategories" type="xl:NotificationCategories" minOccurs="0"/>

<element name="Filter" type="string" minOccurs="0"/>

</sequence>

</complexType>

</element>

</sequence>

</extension>

</complexContent>

</complexType>

<complexType name="NotifyLogUnsubscribed">

<complexContent>

<extension base="xe:Notification">

<sequence>

<element name="body">

<complexType>

<sequence>

<element name="LogSubscriptionId" type="xl:LogSubscriptionId"/>

</sequence>

</complexType>

</element>

</sequence>

</extension>

</complexContent>

</complexType>

<complexType name="NotifyOccupancyLevelCrossed">

<complexContent>

<extension base="xe:Notification">

<sequence>

<element name="body">

<complexType>

<sequence>

<element name="LogSubscriptionId" type="xl:LogSubscriptionId"/>

<element name="CurrentOccupancyLevel" type="xl:CurrentOccupancyLevel"/>

<element name="LogFullAction" type="xl:LogFullAction" minOccurs="0"/>

</sequence>

</complexType>

</element>

</sequence>

</extension>

</complexContent>

</complexType>

<complexType name="NotifyLoggingResumed">

<complexContent>

<extension base="xe:Notification">

<sequence>

<element name="body">

<complexType>

<sequence>

<element name="LogSubscriptionId" type="xl:LogSubscriptionId"/>

</sequence>

</complexType>

</element>

</sequence>

</extension>

</complexContent>

</complexType>

<element name="NotifyLogSubscribed" type="xl:NotifyLogSubscribed"/>

<element name="NotifyLogUnsubscribed" type="xl:NotifyLogUnsubscribed"/>

<element name="NotifyOccupancyLevelCrossed" type="xl:NotifyOccupancyLevelCrossed"/>

<element name="NotifyLoggingResumed" type="xl:NotifyLoggingResumed"/>

</schema>

End of modifications

Annex D (informative):
Change history

| Change history |
| --- |
| Date | TSG # | TSG Doc. | CR | Rev | Subject/Comment | Cat | Old | New |
| Sep 2004 | S_25 | SP-040564 | -- | -- | Submitted to TSG SA#25 for Information | -- | 1.0.0 |  |
| Jun 2005 | S_28 | SP-050291 | -- | -- | Submitted to TSG SA#28 for Approval | -- | 2.0.0 | 6.0.0 |
| Mar 2006 | SA_31 | SP-060091 | 0001 | -- | Correct a validating error in notificationLog.xsd | F | 6.0.0 | 6.1.0 |
| Dec 2006 | SA_34 | SP-060709 | 0002 | -- | Correct XML schema | F | 6.1.0 | 6.2.0 |

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.