3GPP TSG-SA5 (Telecom Management)	(S5-070227

# Meeting SA5#51, 22 - 26 Jan 2007, Seville, SPAIN

| CR-Form-v9.3 |
| --- |
| CHANGE REQUEST |
| ( | 32.251 | CR | 0045 | ( rev | - | ( Current version: | 7.2.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Introduce support for Network Requested Secondary PDP Context Activation for online charging |
| --- | --- |
| Source to WG: ( | Vodafone (gavin.wong (at) vodafone.com) |
| Source to TSG: ( | S5 |
| Work item code: ( | PCC-CH |  | Date: ( | 26/01/2007 |
| Category: ( | B |  | Release: ( | Rel-7 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) |
| Reason for change: ( | Network requested secondary PDP context activation (NRSPCA) was added to the GPRS stage 2 and the charging triggers associated with this procedure needs to be updated. Network requested secondary PDP context activation is applicable only to PCC where the bearer control mode is NW_Only. In practise, the GGSN/PCEF should seek authorisation from OCS before proceeding with the GPRS session management signalling as per the flow described in clause 7.4.2 and A.1.4.4.2 of TS 23.203. |
| Summary of change: ( | Add trigger for CCR initial to be on determination of the need for a NRSPCA and a CCR update when the activation procedures are complete from a PCEF/GGSN perspective to provide any missing information from the CCR initial. |
| Consequences if ( not approved: | Incorrect handling of the network requested secondary PDP context activation leading possibly to excessive rejections of the PDP context activations due to the nature of the GPRS signalling procedure. |
| Clauses affected: ( | 5.3.1.2, 5.3.2.2.1, 5.3.2.2.2, 6.3.1.2 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

1st Modified Section

#### 5.3.1.2	Flow Based Bearer Charging

PDP context charging allows the GGSN to collect charging information related to data volumes sent to and received by the UE/MS, categorised by the QoS applied to the PDP context. FBC is supported by the GGSN by the integrated PCEF. When the PCEF is present, the normal PDP context charging is enhanced by the capability to categorise the PDP context data traffic by specific service data flows. I.e., while there is only one uplink an one downlink data volume count per PDP context in PDP context charging, FBC may provide several service data flow counts per defined service data flow. The default service data flow is the wildcard, i.e. all traffic for all IP addresses, all TCP ports, etc.; when no other, specific service data flows are configured, the behaviour of FBC is identical to the normal PDP context charging on the GGSN. When further service data flows are specified, traffic is categorised, and counted, according to the service data flow specification, and the wildcard service data flow applies to all traffic that does not match any of the specific service data flows. Details of this functionality are specified in TS 23.203 [72] and TS 32.240 [1].

According to TS23.203 [72], FBC shall support different charging models per service data flow. These charging models may be based on volume and/or time and on number of events matching a specific service data flow template. In general the charging of a service data flow shall be linked to the PDP Context under which the service data flow has been activated.  In this scenario the PCEF shall request the reservation of units (number of events) prior to service delivery.

The following chargeable events are defined for FBC:

- Network request for PDP context activation. Associated with the network requested secondary PDP context activation procedure, as defined in TS 23.203 [72] and 23.060 [201], upon encountering this event, a CCR initial, indicating the request for activation of secondary PDP context is sent toward the OCS.

- Start of PDP context. Upon encountering this event, a CCR initial, indicating the start of the PDP context, is sent towards the OCS, and the data volume and/or elapsed time is captured per PDP Context. For network requested secondary PDP context activation, this event triggers a CCR update, when the PCEF receives an Update PDP Context Request message with the RAN Procedures Ready flag, and the data volume and/or elapsed time for the PDP context begins at this point.

- Start of service data flow. A CCR update is generated for the PDP context, indicating the start of a new service data flow, and new counts for this service data flow are started. The type of counters shall depend on the charging model configured for the service data flow. When event based charging applies, the first occurrence of an event matching a service data flow template shall be considered as the start of a service.

- Termination of service data flow. The service data flow counters are closed, and a CCR update is generated towards the OCS, indicating the end of the service data flow and the final counts for this service data flow. For information on how the termination of service data flows is detected, refer to TS 23.203 [72]. Additionally when event based charging applies, service termination shall also occur when the event service units granted by the OCS are exhausted.

- End of PDP context. Upon encountering this event, a CCR termination, indicating the end of the PDP context, is sent towards the OCS together with the final counts for the PDP context and all service data flows.

- Expiry of an operator configured time limit per PDP context. This event triggers the emission of a CCR update, indicating the elapsed time and the accrued data volume for the PDP context since the last report.

- Expiry of an operator configured time limit per service data flow. The service data flow counters are closed and a CCR update is sent to the OCS, indicating the accrued counts since the last report for that service data flow. A new service data flow container is opened if the service data flow is still active.

- Expiry of an operator configured data volume limit per PDP context. This event triggers the emission of a CCR update, indicating the elapsed time and the accrued data volume for the PDP context since the last report.

- Expiry of an operator configured data volume limit per service data flow. The service data flow counters are closed and a CCR update is sent to the OCS, indicating the accrued counts since the last report for that service data flow. A new service data flow container is opened if the service data flow is still active.

- Expiry of an operator configured data event limit per service data flow. The service data flow counters are closed and a CCR update is sent to the OCS, indicating the accrued counts since the last report for that service data flow.  A new service data flow container is opened if the service data flow is still active.

- Change of charging condition: QoS change, tariff time change, location change (CGI/SAI or RAI). When this event is encountered, all current counts are captured and sent towards the OCS with a CCR update. New counts for PDP Context and/or all active service data flows are started.

Management intervention may also force trigger a chargeable event.

Next Modified Section

##### 5.3.2.2.1	Triggers for starting and stopping an FBC Credit Control session

CCR initial is sent to OCS when PDP context is activated. For network requested secondary PDP context activation, the CCR initial is sent to the OCS when the PCEF determines a need for the PDP context and before any GPRS signalling is initiated.

CCR terminate is sent to OCS when:

- PDP context is deactivated

- Session termination is indicated by the OCS (e.g. Credit Limit Reached)

- Abort-Session-Request is received from the OCS, this also results in network initiated PDP context deactivation.

Next Modified Section

##### 5.3.2.2.2	Triggers for providing interim information for an FBC Credit Control session

CCR update is sent to OCS when:

- User starts to use certain service

- Active service is removed from the allowed services (e.g. charging rule is removed)

- Granted quota runs out

- Validity time for granted quota expires

- Update is requested by the OCS

- Change of charging conditions occur and according re-authorisation trigger re-authorisation is needed.

- Management intervention

- Provision of a charging rule

- For network requested secondary PDP context activation, reception of an Update PDP Context Request message with the RAN Procedures Ready flag.

Next Modified Section

#### 6.3.1.2	Definition of the PS Information

PS specific charging information is provided within the PS Information.

The detailed structure of the PS Information can be found in the table 6.3.1.2.

Table 6.3.1.2 : Structure of the PS Information

| Field | Category | Description |
| --- | --- | --- |
| Charging Id | OC | This field holds the Charging Id for this PDP context (this together with the GGSN-Address constitutes a unique identifier for the PDP context). |
| PDP Type | OC | This field holds the type of PDP context, e.g. IP or PPP. |
| PDP Address | OC | This field holds the PDP address of the served IMSI, i.e. IPv4 or IPv6. This parameter shall be present except when both the PDP type is PPP and dynamic PDP address assignment is used. |
| Negotiated QoS Profile | OC | This field holds the QoS profile applied by GGSN. See NOTE. |
| SGSN Address | OC | This field holds the SGSN IP address that is used by the GTP control plane for the handling of control messages. It may be used to identify the PLMN to which the user is attached. |
| GGSN Address | OC | This field holds the IP-address of the GGSN that generated the Charging Id. |
| CG Address | OC | This field holds the Charging Gateway IP address. |
| IMSI MCC MNC | OC | This field holds the MCC and MNC extracted from the user's IMSI (first 5 or 6 digits, as applicable from the presented IMSI). |
| GGSN MCC MNC | OC | This field holds the MCC-MNC of the network the GGSN belongs to. |
| NSAPI | OC | This field Identifies a particular PDP context for the associated PDN and MSISDN/IMSI from creation to deletion. See NOTE. |
| Called Station Id | OC | This field contains the identifier of the access point (APN) the user is connected to. |
| Session Stop Indicator | OC | This field indicates to the AAA server that the last PDP context of a session is released and that the PDP session has been terminated. |
| Selection Mode | OC | This field contains the Selection mode for this PDP Context received in the Create PDP Context Request Message. |
| Charging Characteristics | OC | This field contains the charging characteristics for this PDP Context received in the Create PDP Context Request Message (only available in R99 and later releases). |
| SGSN MCC MNC | OC | This field holds the MCC and MNC extracted from the RAI within the Create PDP Context Request or Update PDP Context Request message. |
| MS Time Zone | OC | This field indicates the offset between universal time and local time in steps of 15 minutes of where the MS currently resides. |
| CAMEL Charging Info | OC | This field holds the copy of any CAMEL Information present in S-CDR(s). |
| Rule Base Name | OC | This field holds the MCC and MNC extracted from the RAI within the Create PDP Context Request or Update PDP Context Request message. |
| User Location Info | OC | This field indicates details of where the UE is currently located (e.g. RAI, SAI or CGI). |
| RAT Type | OC | This field indicates which Radio Access Technology is currently serving the UE. |
| Furnish Charging Information | OC | This field contains the PS Furnish Information Elements. |

NOTE:	For Network Requested Secondary PDP Context Activation, the CCR Initial does not contain a value of NSAPI, whilst the Negotiated QoS profile reflects the requested QoS profile used in the activation request.

End of Modifications

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.