3GPP TSG-SA5 (Telecom Management)	(S5-070292

# Meeting SA5#51, 22 - 26 Jan 2007, Seville, SPAIN

| CR-Form-v9.3 |
| --- |
| CHANGE REQUEST |
| ( | 32.313 | CR | 0004 | ( rev | - | ( Current version: | 6.3.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Correct the compiling errors in the CORBA IDL |
| --- | --- |
| Source to WG: ( | ZTE(huangsq@zte.com.cn) |
| Source to TSG: ( | S5 |
| Work item code: ( | OAM-NIM |  | Date: ( | 26/01/2007 |
| Category: ( | F |  | Release: ( | Rel-6 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) |
| Reason for change: ( | There are two enum values of “FAILURE” in the same name space. This would make the IDL unavailable. |
| Summary of change: ( | Change one of the “FAILURE” to “FULL_FAILURE” to avoid the name conflict in a name space. |
| Consequences if ( not approved: | The IDL can not be compiled successfully. |
| Clauses affected: ( | 12.3, 14.4, Annex A |
|  | Y | N |  |  |
| Other specs ( |  | x | Other core specifications ( |  |
| affected: |  | x | Test specifications |  |
|  |  | x | O&M Specifications |  |
| Other comments: ( |  |

1st Modified Section

# A.1	IDL specification (file name “GenericIRPManagementConstDefs.idl”)

//File: GenericIRPManagementConstDefs.idl

#ifndef _GENERIC_IRP_MANAGEMENT_CONST_DEFS_IDL_

#define _GENERIC_IRP_MANAGEMENT_CONST_DEFS_IDL_

#include <TimeBase.idl>

// This statement must appear after all include statements

#pragma prefix "3gppsa5.org"

/* ## Module: GenericIRPManagementConstDefs

This module contains definitions commonly used among all IRPs.

==============================================================

*/

module GenericIRPManagementConstDefs

{

/*

* Definition imported from CosTime.

* The time refers to time in Greenwich Time Zone.

* It also consists of a time displacement factor in the form of minutes of

* displacement from the Greenwich Meridian.

*/

typedef TimeBase::UtcT IRPTime;

typedef string DN;

typedef sequence <DN> DNList;

enum Signal {OK, FULL_FAILURE, PARTIAL_FAILURE};

enum Result {SUCCESS, FAILURE};

/*

* This holds a list of notification Ids

*/

typedef sequence <long> NotifIdSet;

/*

* This holds identifiers of notifications that are correlated.

*/

struct CorrelatedNotification

{

DN source;// Contains DN of MO that emitted the set of notifications

// DN string format in compliance with Name Convention for

// Managed Object.

// This may be a zero-length string. In this case, the MO

// is identified by the value of the MOI attribute

// of the Structured Event, i.e., the notification.

NotifIdSet notif_id_set;  // Set of related notification ids

};

/*

* The VersionNumber is a string that identifies the IRP specification name

* and its version number. See definition "IRP document version number

* string" or "IRPVersion".

* The VersionNumberSet is a sequence of such VersionNumber. It is returned

* by get_XXX_IRP_versions(). The sequence order has no significance.

*/

typedef string VersionNumber;

typedef sequence <VersionNumber> VersionNumberSet;

typedef string MethodName;

typedef string ParameterName;

typedef sequence <ParameterName> ParameterList;

/*

* The Method defines the structure to be returned as part of

* get_supported_operations_profile(). The name shall be the actual method

* name (ex. "attach_push", "change_subscription_filter", etc.)

* The parameter_list contains a list of strings. Each string shall be

* the actual parameter name (ex. "manager_reference", "filter", etc.)

*/

struct Method

{

MethodName name;

ParameterList parameter_list;

};

/*

* List of all methods and their associated parameters.

*/

typedef sequence <Method> MethodList;

typedef string NotificationName;

struct Notification

{

NotificationName name;

ParameterList parameter_list;

};

typedef sequence <Notification> NotificationList;

/*

* Defines the name of an attribute of a Managed Object

*/

typedef string MOAttributeName;

/*

* Defines the value of an attribute of a Managed Object in form of a CORBA

* Any. Apart from basic datatypes already defined in CORBA, the allowed

* attribute value types are defined in the AttributeTypes module.

*/

typedef any MOAttributeValue;

/*

* Represents an attribute: "name" is the attribute name

* and "value" is the attribute value.

*/

struct MOAttribute

{

MOAttributeName name;

MOAttributeValue value;

};

typedef sequence <MOAttribute> MOAttributeSet;

typedef string ManagerIdentifier;

/*

* The following are types carrying an optional parameter.

* If the boolean is TRUE, then the value is present.

* Otherwise the value is absent.

*/

union StringOpt switch (boolean)

{

case TRUE: string value;

};

union ShortOpt switch (boolean)

{

case TRUE: short value;

};

union UnsignedShortOpt switch (boolean)

{

case TRUE: unsigned short value;

};

union LongOpt switch (boolean)

{

case TRUE: long value;

};

union UnsignedLongOpt switch (boolean)

{

case TRUE: unsigned long value;

};

union IRPTimeOpt switch (boolean)

{

case TRUE: GenericIRPManagementConstDefs::IRPTime value;

};};

#endif // _GENERIC_IRP_MANAGEMENT_CONST_DEFS_IDL_

End of modifications

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.