3GPP TSG-SA5 (Telecom Management)	(S5-080930

Meeting SA5#59, 21 - 25 April 2008, Chengdu, CHINA 	revision of S5-080677

| CR-Form-v9.4 |
| --- |
| CHANGE REQUEST |
| ( | 32.240 | CR | 0016 | ( rev | - | ( Current version: | 8.3.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Implication on overall Charging description for Common IMS |
| --- | --- |
| Source to WG: ( | Nokia Siemens Networks |
| Source to TSG: ( | S5 |
| Work item code: ( | CH8 |  | Date: ( | 25/04/08 |
| Category: ( | B |  | Release: ( | Rel-8 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) |
| Reason for change: ( | In Rel-8 Common IMS Introduction on IMS Multimedia Telephony and Supplementary Service is also considering Advice of Charge but currently not mentioned in the overall Charging description. |
| Summary of change: ( | The TS for MMTel Charging and AoC service added with the corresponding refinements. |
| Consequences if ( not approved: | TS 32.240 not refers the Rel-8 specifications TS 32.275 and TS 32.280. |
| Clauses affected: ( | 1, 2, 5.5, 5.5.4 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

1st Modified Section

# 1	Scope

The present document is part of a series of documents that specify charging functionality and charging management in GSM/UMTS networks. The GSM/UMTS core network charging architecture and principles are specified in the present document, which thus provides an umbrella for other charging management TSs that specify:

- the content of the CDRs per domain / subsystem /service (offline charging);

- the content of real-time charging events per domain / subsystem /service (online charging);

- the functionality of online and offline charging for those domains / subsystems / services;

- the interfaces that are used in the charging framework to transfer the charging information (i.e. CDRs or charging events).

The purposes of the present document are:

- to lay down common principles of charging in the network; and

- to specify a logical common charging architecture that applies to all 3GPP domains, subsystems and services.

A set of domain/subsystem/service specific TSs covers the bearer (CS, PS, WLAN domains), subsystem (IMS) and service (MMS, LCS, etc.) levels, respectively, in the 32.25x, 32.26x and 32.27x TS number range. These TSs describe the mapping of the common architecture specified in the present document onto the specific domain/subsystem/service and the scenarios and information for online and offline charging that are specific to the domain/subsystem/service. They are commonly referred to as the “middle tier (charging) TSs”.

A set of TSs in the 32.280 and 32.29x range cover common aspects such as the Advice of Charge service,  CDR parameter and syntax descriptions, online and offline charging applications, and the charging interactions within the network (CDR transfer) as well as between the network and the Billing Domain (CDR file transfer).

The complete document structure for these TSs is outlined in the following figure.

Figure 1: Charging specifications structure

All terms, definitions and abbreviations used in the present document, that are common across 3GPP TSs, are defined in the 3GPP Vocabulary, 3GPP TR 21.905 [100]. Those that are common across charging management in GSM/UMTS domains, services or subsystems are provided in the present document (umbrella TS), and are copied into clause 3 of the other TSs depicted in the figure, for ease of reading. Finally, those items that are specific to the present document are defined exclusively in the present document.

Furthermore, requirements that govern the charging work are specified in 3GPP TS 22.115 [101].

Next Modified Section

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]- [9]	Void.

[10]	3GPP TS 32.250: "Telecommunication management; Charging management; Circuit Switched (CS) domain charging".

[11]	3GPP TS 32.251: "Telecommunication management; Charging management; Packet Switched (PS) domain charging".

[12]- [29]	Void.

[30]	3GPP TS 32.270: "Telecommunication management; Charging management; Multimedia Messaging Service (MMS) charging".

[31]- [49]	Void.

[50]	3GPP TS 32.299: "Telecommunication management; Charging management; Diameter charging application".

[51]	3GPP TS 32.298: "Telecommunication management; Charging management; Charging Data Record (CDR) parameter description".

[52]	3GPP TS 32.297: "Telecommunication management; Charging management; Charging Data Record (CDR) file format and transfer".

[53]	3GPP TS 32.296: "Telecommunication management; Charging management; Online Charging System (OCS) applications and interfaces".

[54]	3GPP TS 32.295: "Telecommunication management; Charging management; Charging Data Record (CDR) transfer".

[55]- [68]	Void.

[69]	3GPP TS 32.280: "Telecommunication management; Charging management; Advice of Charge (AoC) service".

[70]	Void.

[71]	3GPP TS 23.203: "Policy and charging control architecture".

[72]- [99]	Void.

[100]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[101]	3GPP TS 22.115 "Service aspects; Charging and billing".

[102]- [199]	Void.

[200]- [206]	Void.

[207]	3GPP TS 23.078: "Customized Applications for Mobile network Enhanced Logic (CAMEL); Stage 2".

[208]- [209]	Void.

[210]	3GPP TS 23.234: "3GPP system to Wireless Local Area Network (WLAN) interworking; System description".

[211]- [299]	Void.

[300]	ITU-T Recommendation D.93: "Charging and accounting in the international land mobile telephone service (provided via cellular radio systems)".

[301]- [399]	Void.

[400]- [401]	Void.

[402]	IETF RFC 4006: "Diameter Credit Control Application".

Next Modified Section

## 5.5	Charging information utilisation

To be completed. This clause should be separated between offline charging / CDRs / billing and online charging / credit control. OCS aspects will also be included (e.g. OCS CDRs), e.g. the following text: “It is important to note that also in the online charging case, operators may wish to apply similar billing analyses (e.g. statistics) and, obviously, inter-operator accounting, as in the offline charging case. If this is required, the OCS is responsible to generate CDRs similar in scope to the ones described in offline charging above.”

The MSC server and Gateway MSC server are responsible for the collection of all charging relevant information for each MS and PSTN connection and for the storage of this information in the form of CDRs.

Circuit switched calls can be charged in one MSC server (the anchor MSC server) where all relevant data is available. That is guaranteed by routing all signalling information though the anchor MSC server even if the traffic channel of a call is routed through another MSC server due to handover.

The Gateway MSC server acts as a gateway into other PLMN or fixed networks. Within the PLMN, the GMSC server is responsible for the generation of CDRs for calls routed from or into other networks.

If subscribed CAMEL services apply to MS, the (G)MSC servers contain CAMEL subscription data providing the information required for invocation of the CAMEL dialogues for controlling the MS terminating and MS originating calls. Charging data record parameters resulting from the CAMEL treatment applying to MS calls is derived from the CAMEL subscription data.

In addition to user subscribed services, specific dialled CAMEL services might be invoked which also influence existing records or even trigger the generation of separate records steered by service logic.

In addition to the information collected from these network elements, network management functions are required for the administration of online charging data stored in the network nodes. This data is employed to drive the charge display on the User Equipment (UE) as required by the Advice of Charge (AoC) service in TS 22.115 [101] and charging perspective of AoC is defined by 3GPP TS 32.280 [69].

Next Modified Section

### 5.5.4	Advice of Charge

The charging data collected from the network elements may be used to provide tariff information concerning the use of services, by both home and visiting subscribers, within the network. The appropriate tariff information to the network elements is distributed by the Advice of Charge supplementary service. The function is specified in TS 32.280 [69].

An alternative mode of AoC can also be used to indicate the occurrence of new charges to the user, e.g. when a monthly allowance is being exceeded, or when a service is requested that is not included in the subscription fees, while others are. This topic is for further study.

End of modifications

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.