Third Generation Partnership Project (3GPP™)

DRAFT Meeting Report
for
3GPP WG SA5
meeting: 62bis OAM

Sophia-Antipolis, France, 14/01/2008 to 16/01/2008

1	Opening	3

2	Approval of the agenda	3

3	Registration of new documents	3

4	IPR declaration	3

5	E-UTRAN & EPC OAM	3

5.1	UID_380036 E-UTRAN NRM IRP	3

5.2	UID_390002 Performance measurements for E-UTRAN	6

5.3	UID_390003 Key Performance Indicators (KPIs) for E-UTRAN	9

5.4	UID_380037 EPC NRM IRP	10

5.5	UID_390011 Performance measurements for EPC (EPC-OAM)	11

5.6	UID_370001 Subscriber and Equipment Trace for E-UTRAN and EPC (32.423)	12

5.7	Rel-8 Maintenance for SON, E-UTRAN & EPC OAM	14

6	HNB OAM	15

6.1	UID_ 420037 3G Home NodeB OAM&P Interface Type 1 Management	16

6.2	UID_360007 Study on SON related OAM interfaces for Home NodeB	23

7	Review of outputs and liaisons to other groups	23

8	Any other business	23

9	Closing	23

Annex A: List of contribution documents	25

Annex B: List of action items	31

Annex C: List of participants	32

## 1	Opening

The SA5 Chairman, Christian Toche of Huawei Technologies, welcomed the OAM delegates to the SA5#62bis OAM meeting, hosted by ETSI in Sophia Antipolis, France.

## 2	Approval of the agenda

S5-090501	Meeting Schedule
					Source: WG Chairman

Discussion:

The SA5 Chairman presented the contribution.

Decision: 		The document was agreed.

S5-090512	Agenda (revised)
					Source: WG Chairman

Discussion:

The SA5 Chairman presented the agenda. There were no objections and the agenda was agreed.

Decision: 		The document was agreed.

S5-090502	Document List
					Source: WG Secretary

Decision: 		The document was noted.

## 3	Registration of new documents

The late contributions were identified.

## 4	IPR declaration

## 5	E-UTRAN & EPC OAM

### 5.1	UID_380036 E-UTRAN NRM IRP

S5-090511	E TD Modelling of antenna tma sector
					Source: Ericsson

Decision: 		The document was revised to S5-090608.

S5-090608	E TD Modelling of antenna tma sector
					Source: Ericsson

(Replaces S5-090511)

Decision: 		The document was revised to S5-090626.

S5-090626	E TD Modelling of antenna tma sector
					Source: Ericsson

(Replaces S5-090608)

Discussion:

A working agreement is present in S5-090629.

Decision: 		The document was noted.

S5-090542	E-UTRAN NRM IS cleanup
					Source: Ericsson

Decision: 		The document was agreed.

S5-090543	32.763 E-UTRAN NRM Corba SS skeleton
					Source: Ericsson

Decision: 		The document was agreed.

S5-090544	32.763 E-UTRAN NRM Corba SS Rapporteur's proposal
					Source: Ericsson

Decision: 		The document was revised to S5-090600.

S5-090600	32.763 E-UTRAN NRM Corba SS Rapporteur's proposal
					Source: Ericsson

(Replaces S5-090544)

Decision: 		The document was agreed.

S5-090545	32.763 E-UTRAN NRM Corba SS Mappings
					Source: Ericsson

Decision: 		The document was agreed.

S5-090546	32.765 E-UTRAN NRM XML skeleton
					Source: Ericsson

Decision: 		The document was agreed.

S5-090547	32.765 E-UTRAN NRM XML Rapporteur's proposal
					Source: Ericsson

Decision: 		The document was revised to S5-090601.

S5-090601	32.765 E-UTRAN NRM XML Rapporteur's proposal
					Source: Ericsson

(Replaces S5-090547)

Decision: 		The document was agreed.

S5-090585	M pseudo CR add the missing definitions for end point models in E-UTRAN NRM IRP
					Source: Motorola

Decision: 		The document was noted.

S5-090587	Support/Read/Write Qualifiers for pciList Attribute of EUtranGenricCell IOC (Replaces S5-090586)
					Source: Qualcomm Europe, Orange

Decision: 		The document was agreed.

S5-090598	Adding IP address of X2 interface of eNB to E-UTRAN NRM
					Source: Nokia Siemens Networks, Huawei

Decision: 		The document was revised to S5-090609.

S5-090609	Adding IP address of X2 interface of eNB to E-UTRAN NRM
					Source: Nokia Siemens Networks, Huawei

(Replaces S5-090598)

Decision: 		The document was revised to S5-090627.

S5-090627	Adding IP address of X2 interface of eNB to E-UTRAN NRM
					Source: Nokia Siemens Networks, Huawei

(Replaces S5-090609)

Decision: 		The document was revised to S5-090628.

S5-090628	Adding IP address of X2 interface of eNB to E-UTRAN NRM
					Source: Nokia Siemens Networks, Huawei

(Replaces S5-090627)

Decision: 		The document was agreed.

S5-090629	Working assumption concerning S5-080626
					Source: SA5 OAM

Decision: 		The document was agreed.

### 5.2	UID_390002 Performance measurements for E-UTRAN

S5-090509	Handover measurements for E-UTRAN
					Source: Nokia Siemens Networks

Decision: 		The document was revised to S5-090605.

S5-090605	Handover measurements for E-UTRAN
					Source: Nokia Siemens Networks

(Replaces S5-090509)

Decision: 		The document was agreed.

S5-090510	Handover measurements for E-UTRAN - use cases
					Source: Nokia Siemens Networks

Decision: 		The document was agreed.

S5-090514	Cell counters for Availability KPI
					Source: Ericsson, T-Mobile

Decision: 		The document was revised to S5-090606.

S5-090606	Cell counters for Availability KPI
					Source: Ericsson, T-Mobile

(Replaces S5-090514)

Decision: 		The document was agreed.

S5-090516	EPS Bearer counters for Accessibility KPI
					Source: Ericsson

Decision: 		The document was agreed.

S5-090517	S1Sig counters for Accessibility KPI
					Source: Ericsson

Decision: 		The document was agreed.

S5-090520	EPS Bearer counters for Retainability KPI
					Source: Ericsson

Decision: 		The document was revised to S5-090607.

S5-090607	EPS Bearer counters for Retainability KPI
					Source: Ericsson

(Replaces S5-090520)

Decision: 		The document was agreed.

S5-090554	Revision of cause values for counters using S1-protocol procedures
					Source: Huawei Technologies

Decision: 		The document was noted.

S5-090555	Revison of cell bit-rate
					Source: Huawei Technologies

Discussion:

There will be an updated version in the next meeting.

Decision: 		The document was noted.

S5-090556	Revison of use case for cell bit-rate
					Source: Huawei Technologies

Decision: 		The document was agreed.

S5-090557	Cleanup to active UE counter
					Source: Huawei Technologies

Decision: 		The document was agreed.

S5-090558	Cleanup to DL packet delay counter
					Source: Huawei Technologies

Decision: 		The document was agreed.

S5-090576	Enhancement of Use case on cell throughput
					Source: Motorola

Discussion:

More discussion is necessary.

Decision: 		The document was noted.

S5-090577	Measurements related to PDCP bit rate and SDU
					Source: Motorola

Discussion:

Will be resubmitted to next meeting.

Decision: 		The document was postponed.

S5-090578	Use case on RF Performance
					Source: Motorola

Discussion:

More discussion is necessary.

Decision: 		The document was noted.

S5-090579	Measurements related to FR performance
					Source: Motorola

Decision: 		The document was noted.

S5-090580	Enhanced Use case on PRB usage
					Source: Motorola

Decision: 		The document was noted.

S5-090581	Measurements related to PRB usage for signalling
					Source: Motorola

Discussion:

Will be resubmitted to next meeting.

Decision: 		The document was postponed.

S5-090582	Use case on ARQ and HARQ performance
					Source: Motorola

Decision: 		The document was noted.

S5-090583	Measurements related to ARQ and HARQ
					Source: Motorola

Discussion:

Will be resubmitted to next meeting.

Decision: 		The document was postponed.

### 5.3	UID_390003 Key Performance Indicators (KPIs) for E-UTRAN

S5-090513	Availability Formula in KPI definition for E-UTRAN
					Source: Ericsson, T-Mobile

Decision: 		The document was revised to S5-090602.

S5-090602	Availability Formula in KPI definition for E-UTRAN
					Source: Ericsson, T-Mobile

(Replaces S5-090513)

Decision: 		The document was agreed.

S5-090515	Accessibility Formula in KPI definition for E-UTRAN
					Source: Ericsson

Decision: 		The document was revised to S5-090603.

S5-090603	Accessibility Formula in KPI definition for E-UTRAN
					Source: Ericsson

(Replaces S5-090515)

Decision: 		The document was agreed.

S5-090519	Retainability Formula in KPI definition for E-UTRAN
					Source: Ericsson

Decision: 		The document was agreed.

S5-090521	Update EPS Bearer to E-RAB
					Source: Ericsson

Decision: 		The document was noted.

S5-090552	Pseudo CR to TS 32.410 -Additional KPI
					Source: Vodafone

Decision: 		The document was revised to S5-090604.

S5-090604	Pseudo CR to TS 32.410 -Additional KPI
					Source: Vodafone

(Replaces S5-090552)

Decision: 		The document was noted.

### 5.4	UID_380037 EPC NRM IRP

S5-090559	Remove one requirement related with E-MBMS for EPC NRM IRP
					Source: Huawei Technologies

Decision: 		The document was revised to S5-090620.

S5-090620	Remove one requirement related with E-MBMS for EPC NRM IRP
					Source: Huawei Technologies

(Replaces S5-090559)

Decision: 		The document was agreed.

S5-090560	Rapporteur clean up suggestion for draft TS32.752 EPC NRM IRP IS
					Source: Huawei Technologies

Decision: 		The document was revised to S5-090610.

S5-090610	Rapporteur clean up suggestion for draft TS32.752 EPC NRM IRP IS
					Source: Huawei Technologies

(Replaces S5-090560)

Decision: 		The document was agreed.

S5-090561	Revise the attribute of IOC MMEFunction
					Source: Huawei Technologies

Decision: 		The document was revised to S5-090611.

S5-090611	Revise the attribute of IOC MMEFunction
					Source: Huawei Technologies

(Replaces S5-090561)

Decision: 		The document was noted.

S5-090562	Add the attribute weightFactor to IOC MMEFunction
					Source: Huawei Technologies

Decision: 		The document was noted.

S5-090563	Proposal on IOC MMEPool and MMEPoolArea
					Source: Huawei Technologies

Decision: 		The document was noted.

S5-090564	Discuss the write qualifier of yellow items in TS32.752
					Source: Huawei Technologies

Decision: 		The document was revised to S5-090612.

S5-090612	Discuss the write qualifier of yellow items in TS32.752
					Source: Huawei Technologies

(Replaces S5-090564)

Decision: 		The document was agreed.

S5-090584	M pseudo CR end point models for EPC
					Source: Motorola

Decision: 		The document was noted.

### 5.5	UID_390011 Performance measurements for EPC (EPC-OAM)

S5-090532	Measurement related to PDN-GW
					Source: Samsung, China Mobile

Decision: 		The document was revised to S5-090613.

S5-090613	Measurement related to PDN-GW
					Source: Samsung, China Mobile

(Replaces S5-090532)

Decision: 		The document was noted.

S5-090533	proposal of PDN-GW initiated Dedicated Bearer Creatation related measurements for EPC
					Source: Samsung, China Mobile

Decision: 		The document was revised to S5-090613.

S5-090534	proposal of PDN-GW initiated Dedicated Bearer Modification with QoS update related measurements for EPC
					Source: Samsung, China Mobile

Decision: 		The document was revised.

S5-090614	proposal of PDN-GW initiated Dedicated Bearer Modification with QoS update related measurements for EPC
					Source: Samsung, China Mobile

(Replaces S5-090534)

Decision: 		The document was withdrawn.

S5-090535	proposal of PDN-GW initiated Dedicated Bearer Modification without QoS update related measurements for EPC
					Source: Samsung, China Mobile

Decision: 		The document was revised to S5-090615.

S5-090615	proposal of PDN-GW initiated Dedicated Bearer Modification without QoS update related measurements for EPC
					Source: Samsung, China Mobile

(Replaces S5-090535)

Decision: 		The document was withdrawn.

S5-090536	proposal of PDN-GW initiated Dedicated Bearer Deletion related measurements for EPC
					Source: Samsung, China Mobile

Decision: 		The document was revised to S5-090616.

S5-090616	proposal of PDN-GW initiated Dedicated Bearer Deletion related measurements for EPC
					Source: Samsung, China Mobile

(Replaces S5-090536)

Decision: 		The document was withdrawn.

### 5.6	UID_370001 Subscriber and Equipment Trace for E-UTRAN and EPC (32.423)

S5-090588	CR R8 EPC signalling activation mechanisms û align with 29.274 and 29.272
					Source: Motorola, Vodafone, T-Mobile

Decision: 		The document was revised to S5-090621.

S5-090621	CR R8 EPC signalling activation mechanisms û align with 29.274 and 29.272
					Source: Motorola, Vodafone, T-Mobile

(Replaces S5-090588)

Decision: 		The document was sent for email approval.

S5-090589	CR EPC and E-UTRAN signalling deactivation mechanisms û align with 29.274, 29.272 and 36.413
					Source: Motorola, Vodafone, T-Mobile

Decision: 		The document was revised to S5-090622.

S5-090622	CR EPC and E-UTRAN signalling deactivation mechanisms û align with 29.274, 29.272 and 36.413
					Source: Motorola, Vodafone, T-Mobile

(Replaces S5-090589)

Decision: 		The document was sent for email approval.

S5-090590	CR R8 EPC and E-UTRAN trace recording session starting mechanisms û align with 36.413, 36.423
					Source: Motorola, Vodafone, T-Mobile

Decision: 		The document was revised to S5-090623.

S5-090623	CR R8 EPC and E-UTRAN trace recording session starting mechanisms û align with 36.413, 36.423
					Source: Motorola, Vodafone, T-Mobile

(Replaces S5-090590)

Decision: 		The document was sent for email approval.

S5-090591	CR R8 Add the missing PGW to EPC trace recording session stopping mechanism
					Source: Motorola, Vodafone, T-Mobile

Decision: 		The document was revised to S5-090624.

S5-090624	CR R8 Add the missing PGW to EPC trace recording session stopping mechanism
					Source: Motorola, Vodafone, T-Mobile

(Replaces S5-090591)

Decision: 		The document was sent for email approval.

S5-090592	CR R8 Enhancement of trigger events in 3GPP TS 32.423 û align with 29.274, 29.272
					Source: Motorola, Vodafone, T-Mobile

Decision: 		The document was revised to S5-090625.

S5-090625	CR R8 Enhancement of trigger events in 3GPP TS 32.423 û align with 29.274, 29.272
					Source: Motorola, Vodafone, T-Mobile

(Replaces S5-090592)

Decision: 		The document was withdrawn.

S5-090593	CR R8 refinement of the Trace Reference
					Source: Motorola, Vodafone, T-Mobile

Decision: 		The document was noted.

S5-090594	CR Mechnisms for Management activation in E-UTRAN
					Source: Motorola, Vodafone, T-Mobile

Decision: 		The document was noted.

S5-090595	Discussion paper on Trace failure report
					Source: Motorola, Vodafone, T-Mobile

Decision: 		The document was noted.

S5-090596	CR R8 enhance the XML schema to support failure report in 32 423
					Source: Motorola, Vodafone, T-Mobile

Decision: 		The document was withdrawn.

### 5.7	Rel-8 Maintenance for SON, E-UTRAN & EPC OAM

S5-090537	E Qc CR Rel-8 TS 32511
					Source: Ericsson, Qualcomm

Decision: 		The document was revised to S5-090617.

S5-090617	E Qc CR Rel-8 TS 32511
					Source: Ericsson, Qualcomm

(Replaces S5-090537)

Decision: 		The document was agreed.

S5-090540	ZTE CR R8 32.531 Correct the errors in the use case
					Source: ZTE

Decision: 		The document was revised to S5-090618.

S5-090618	ZTE CR R8 32.531 Correct the errors in the use case
					Source: ZTE

(Replaces S5-090540)

Decision: 		The document was agreed.

S5-090548	Traceability for ANR Use Cases
					Source: Ericsson

Decision: 		The document was revised to S5-090619.

S5-090619	Traceability for ANR Use Cases
					Source: Ericsson

(Replaces S5-090548)

Decision: 		The document was agreed.

## 6	HNB OAM

S5-090701	32.xx1-001
					Source: Rapporteur

Decision: 		The document was agreed.

S5-090702	32.xx2-001
					Source: Rapporteur

Discussion:

Alcatel-Lucent presented the document.

Decision: 		The document was agreed.

S5-090703	32.xx3-001
					Source: Rapporteur

Discussion:

Alcatel-Lucent presented the document.

Decision: 		The document was agreed.

S5-090704	32.xx4-001
					Source: Rapporteur

Decision: 		The document was not addressed due to lack of time.

### 6.1	UID_ 420037 3G Home NodeB OAM&P Interface Type 1 Management

S5-090505	Use of TR-069 for HNB Management
					Source: bbf2008.958

Discussion:

The SA5 Chairman presented the LS.

Qualcomm suggested that the LS addresses an issue that for R8 will be handled proprietarily, but may be standardized in R9.

ACTION:	Put the issue of northbound interface from TR-069 ACS in the agenda for the next call with the BBF.
	(action on: Chairman)

ACTION:	A formal LS reply will be sent from the SA5#63 meeting on BBF LS on northbound interface.
	(action on: Zou Lan)

Decision: 		The document was postponed.

S5-090506	Response liaison from FF to BBF ''Femtocell Access Point Data Model''
					Source: Liaison_FF_to_BBF_20081210

Discussion:

The SA5 Chairman presented the LS.

Decision: 		The document was noted.

S5-090549	E TD Record of email discussion on work expected from BBF re HNB Mgmt
					Source: Ericsson

Discussion:

Ericsson presented the contribution. There was no objection to proceed with the approach proposed in the contribution.

Decision: 		The document was noted.

S5-090522	3G Home NodeB OAM&P Requirements
					Source: ip.access

Discussion:

ip.access presented the contribution. Some revisions were applied based on comments made during the meeting. The figure is for guidance and not considered a requirement.

For CM-003 it was agreed and also to be added in the security section, with the modification of the phrase to indicate the 'support of one of the two security mechanisms'.

Some more discussion is necessary on CM-004 but the requirement is added.

CM-005 is deleted.

PM-001 was agreed to be changed from shall to may.

PM-003: was rephrased to state that the HNB will support PM utilising the file transfer option of TR-069. T-Mobile, Huawei, NSN, Telefonica, Ericsson, ZTE, TeliaSonera supported this while Alcatel-Lucent objected to this change.

PM-004 was agreed with some rewording.

PM-005 was agreed.

PM-006 was agreed with the addition of FTPS with/without username/password.

PM-007: there was some discussion whether the requirement is necessary. Alcatel-Lucent that the performance would be degraded. NSN suggested that the change of performance would be negligible. It was decided to remove the requirement for the time being.

PM-008 was agreed.

PM-009 it was agreed to remove the reference to TR-069 RPC.

FM-001 was discussed. FM-007 was removed. FM-008 was shortened to be a stage 1 requirement.

Decision: 		The document was agreed with modifications.

S5-090530	HNB OAM&P Requirements (result of phone conference #2)
					Source: Ericsson

Discussion:

Ericsson presented the contribution. CM requirements were agreed and will be business level requirements. PM requirements were modified online. X1 agreed with Editor's Note (highlighted)

x.1.1 was agreed

x.1.2 second sentence was deleted

x.1.3 first sentence of the first requirement was agreed with 'may'; the rest was deleted.

x.1.4 was removed.

Decision: 		The document was agreed with modifications.

S5-090706	HNB OAM&P Requirements revision
					Source: Ericsson

Decision: 		The document was not addressed due to lack of time.

S5-090566	Add 3G Home NodeB OAM&P business level requirements
					Source: Huawei Technologies

Discussion:

Huawei presented the contribution.

CM-CON-001 was removed. CM-CON-002 was agreed. CM-CON-003 was rephrasedd to mention radio environment instead of surrounding HNBs/Macro eNBs, and was agreed as such. CM-CON-004 was agreed with minor changes (remotely reboot). CM-CON-005 was rephrased similarly and agreed. There was some discussion on the fact that the licensed frequencies should not be mentioned; it was agreed to remove the licensed term. Contributions are needed to develop on other cases (e.g. handling a HNB transmitting on a side band).

PM-CON-001 was removed. PM-CON-002 was removed. PM-CON-003 was changed from may to shall and some further rewording was applied. PM-CON-004 was agreed after it was changed from may to shall and manually was removed.

FM-CON-001 was agreed with the removal of Network and the change of may to shall. Airvana objected to this but did not sustain the objection. FM-CON-002 was agreed with some changes.

Decision: 		The document was agreed with modifications.

S5-090550	Add Business-level Requirements for Autoconfiguration (Configuration Management Section)
					Source: Qualcomm Europe

Discussion:

Not presented as 566 covers this.

Decision: 		The document was withdrawn.

S5-090567	Add 3G Home NodeB OAM&P specification level requirements
					Source: Huawei Technologies

Discussion:

Huawei presented the contribution.

CM-FUN-001 was agreed. CM-FUN-002 was added and CM-FUN-002 was renamed to bis, but these will have to be renumbered. There were agreed.

CM-FUN-003 was agreed to be split in two requirements.

PM-FUN-001 was removed. PM-FUN-002 was revised online and agreed. PM-FUN-003 was revised online and agreed. PM-FUN-004 was revised online and agreed.

FM-FUN-001 was agreed. FM-FUN-002 was removed. FM-FUN-003 was revised online and agreed.

FM-FUN-002b: Vodafone, ip.access, Alcatel-Lucent, T-Mobile, Telefonica,Telecom Italia, Thomson, Huawei, ZTE supported having both solutions for alarms (file transfer and notification). Ericsson, NSN supported having only file transfer. The Chairman suggested that the group took this option (both possibilities) as a working assumption. Ericsson proposed that companies came with contributions showing the advantages of active VS passive solution. Vodafone suggested that to have HNB in Rel-8, as Vodafone wishes, this would slow things down too much. NSN suggested that arguments have not been given on the dual solution's advantages. The Chairman suggested the timeline is defined and it is too late to start producing use cases; it was decided that either or both possibilities may be supported (periodic file transfer and RPC notification) in order for the work to progress; this can change during discussions in the future meetings. This decision was captured also in S5-090707. Based on this 002b was agreed.

FM-004 was removed. FM-005 was removed.

FM-006:

Decision: 		The document was agreed with modifications.

S5-090525	TR-069 Connection Requests to HNB
					Source: Cisco, IP.Access

Decision: 		The document was revised to S5-090527.

S5-090527	Connection Requests to HNB Further Analysis
					Source: Cisco, Ip.Access

(Replaces S5-090525)

Discussion:

ip.access presented the contribution.

Some discussion on IP Sec followed. It was also pointed out that there is no ongoing work in SA2 or SA3 on Rel-8 HNB. More discussion is necessary.

Decision: 		The document was noted.

S5-090574	Discussion on HNB IP updating
					Source: Huawei Technologies

Discussion:

Huawei presented the contribution. 1 is not considered a requirement and was removed. 2 was reworded and agreed. 3 was agreed.

Decision: 		The document was agreed with modifications.

S5-090531	32.xx1 Add requirements to Fault management Section
					Source: Alcatel-Lucent

Discussion:

Alcatel Lucent presented the contribution. The general feeling is that this is a very generic requirement; nevertheless some more analysis is necessary as there could be compliance issues.

Xx1-2 was removed. Xx1-3 was agreed with some rephrasing.

Xx1-4 was removed. Xx1-5 was agreed with some rephrasing.

S5-080731 was agreed as in revision 3.

Decision: 		The document was noted.

S5-090551	Add Specification-level Requirements for Autoconfiguration (Configuration Management Section)
					Source: Qualcomm Europe

Discussion:

Qualcomm presented the contribution. Agreed as in revision 1.

Decision: 		The document was agreed.

S5-090528	3G HNB Data Model Document Content and Scope
					Source: Thomson

Discussion:

Thomson presented the contribution. It was agreed to include the draft TS and continue the discussion on the subject in the conference calls.

Qualcomm, Alcatel-Lucent, Thomson, Huawei, ip.access, Telefonica, T-Mobile, Airvana supported the insertion of the contribution. Ericsson did not object to the proposal.

It was decided to insert the contribution in the proposal.

Decision: 		The document was agreed.

S5-090523	Home NodeB to HMS Procedure Flows
					Source: ip.access

Decision: 		The document was not presented.

S5-090524	Data Format for CM, FM & PM
					Source: ip.access

Decision: 		The document was not presented.

S5-090573	Add 3G Home NodeB Registration Procedure Flow
					Source: Huawei Technologies

Decision: 		The document was revised to S5-090712.

S5-090712	Add 3G Home NodeB Registration Procedure Flow
					Source: Huawei Technologies

(Replaces S5-090573)

Decision: 		The document was not addressed due to lack of time.

S5-090538	32.XX3 Discussion on the Usage of a File for FM & PM
					Source: Alcatel-Lucent

Discussion:

Alcatel-Lucent presented the contribution. More discussion is necessary.

Decision: 		The document was noted.

S5-090539	32.xx3 Updates to HNB Management Proc Flows
					Source: Alcatel-Lucent, T-Mobile, VF, Telecom Italia, Thomson, AT&T

Discussion:

Alcatel-Lucent presented the contribution. 6.1.1 should not be introduced in an Annex. Some more review of the document is necessary.

Decision: 		The document was noted.

S5-090541	32.xx3 Update to Architecture for HNB Management Section
					Source: Alcatel-Lucent

Discussion:

Alcatel-Lucent presented the contribution.

Decision: 		The document was agreed with modifications.

S5-090553	HNB FM and PM data model definition (xx2)
					Source: Alcatel-Lucent

Discussion:

Alcatel-Lucent presented the contirbution. Some comments were made that were taken into account for the next conference call.

Decision: 		The document was noted.

S5-090568	Add 3G Home NodeB OAM&P General Data Model Overview
					Source: Huawei Technologies

Decision: 		The document was revised to S5-090709.

S5-090709	Add 3G Home NodeB OAM&P General Data Model Overview
					Source: Huawei Technologies

(Replaces S5-090568)

Discussion:

Needs to be updated for the next conference call to improve readability and avoid incompatibilities with other sections.

Decision: 		The document was noted.

S5-090569	Add 3G Home NodeB Alarm Reporting Procedure Flow
					Source: Huawei Technologies

Decision: 		The document was not addressed due to lack of time.

S5-090570	Add 3G Home NodeB FM File Update Procedure Flow
					Source: Huawei Technologies

Decision: 		The document was not addressed due to lack of time.

S5-090571	Add 3G Home NodeB PM File Update Procedure Flow
					Source: Huawei Technologies

Decision: 		The document was revised to S5-090710.

S5-090710	Add 3G Home NodeB PM File Update Procedure Flow
					Source: Huawei Technologies

(Replaces S5-090571)

Decision: 		The document was not addressed due to lack of time.

S5-090572	Add 3G Home NodeB Gateway Discovery Procedure Flow
					Source: Huawei Technologies

Decision: 		The document was revised to S5-090711.

S5-090711	Add 3G Home NodeB Gateway Discovery Procedure Flow
					Source: Huawei Technologies

(Replaces S5-090572)

Decision: 		The document was not addressed due to lack of time.

S5-090708	Revision of FM-006
					Source: ip.access

Discussion:

ip.access presented the contribution.

It was agreed that the english of the text must be revised at a later time. This will be handled by the Rapporteur.

708 was agreed as in revision 1.

Decision: 		The document was agreed with modifications.

S5-090597	Minutes of the January 9th phone meeting on work split BBF - 3GPP SA5 for HNB OAM
					Source: WG Chairman

Discussion:

The WG Chairman presented the contribution.

SA5 agreed on data model definition in R8:

1. CM parti is driven by BBF;

2. FM/PM are driven by SA5.

Decision: 		The document was noted.

S5-090707	Working assumption on alarm handling in HNB
					Source: SA5

Decision: 		The document was agreed.

S5-080713	T-069 enabled data model for 3GPP
					Source: Ericsson, NSN, Huawei

Discussion:

Ericsson presented the contribution. There was some discussion and it was decided to note the contribution.

Decision: 		The document was noted.

### 6.2	UID_360007 Study on SON related OAM interfaces for Home NodeB

## 7	Review of outputs and liaisons to other groups

S5-090503	Meeting Report
					Source: TB Officer

## 8	Any other business

The conference calls for HNB will proceed and information will be provided on the list. The conference calls with BBF will also proceed and the invitation will be extended to all SA5: the next conference call with BBF is on 19 January.

It was decided to re-structure the weekly SA5 HNB weekly calls: subsequent meetings will focus more on 32.582, 32.583 and 32.584. 32.581 will be handled with email discussion.

It was also suggested to have two HNB SA5 confcalls per week. There was no support for this. 32.581 will not be in the agenda of the next conference calls unless really necessary (requirement impacting subsequent calls).

The working assumptions will be kept within SA5 and will be rediscussed in the Prague meeting. It was also decided to prepare a technical vote on S5-090707. This will be reflected in the agenda for SA5#63. MCC will handle the preparation of the possible technical vote.

S5-090507	LS on ''intention to create a new version of the DM enabler''
					Source: SP-080868

Decision: 		The document was not addressed.

## 9	Closing

The SA5 Chairman thanked the Officials, the Delegates and MCC for their support, hard work and contribution and closed the meeting.

## Annex A: List of contribution documents

| Document | Title | Source | Decision | Replaces | Replaced by |
| --- | --- | --- | --- | --- | --- |
| S5-080713 | T-069 enabled data model for 3GPP | Ericsson, NSN, Huawei | noted | - | - |
| S5-090501 | Meeting Schedule | WG Chairman | agreed | - | - |
| S5-090502 | Document List | WG Secretary | noted | - | - |
| S5-090503 | Meeting Report | TB Officer |  | - | - |
| S5-090505 | Use of TR-069 for HNB Management | bbf2008.958 | postponed | - | - |
| S5-090506 | Response liaison from FF to BBF ''Femtocell Access Point Data Model'' | Liaison_FF_to_BBF_20081210 | noted | - | - |
| S5-090507 | LS on ''intention to create a new version of the DM enabler'' | SP-080868 | not addressed | - | - |
| S5-090509 | Handover measurements for E-UTRAN | Nokia Siemens Networks | revised | - | S5-090605 |
| S5-090510 | Handover measurements for E-UTRAN - use cases | Nokia Siemens Networks | agreed | - | - |
| S5-090511 | E TD Modelling of antenna tma sector | Ericsson | revised | - | S5-090608 |
| S5-090512 | Agenda (revised) | WG Chairman | agreed | - | - |
| S5-090513 | Availability Formula in KPI definition for E-UTRAN | Ericsson, T-Mobile | revised | - | S5-090602 |
| S5-090514 | Cell counters for Availability KPI | Ericsson, T-Mobile | revised | - | S5-090606 |
| S5-090515 | Accessibility Formula in KPI definition for E-UTRAN | Ericsson | revised | - | S5-090603 |
| S5-090516 | EPS Bearer counters for Accessibility KPI | Ericsson | agreed | - | - |
| S5-090517 | S1Sig counters for Accessibility KPI | Ericsson | agreed | - | - |
| S5-090519 | Retainability Formula in KPI definition for E-UTRAN | Ericsson | agreed | - | - |
| S5-090520 | EPS Bearer counters for Retainability KPI | Ericsson | revised | - | S5-090607 |
| S5-090521 | Update EPS Bearer to E-RAB | Ericsson | noted | - | - |
| S5-090522 | 3G Home NodeB OAM&P Requirements | ip.access | agreed with modifications | - | - |
| S5-090523 | Home NodeB to HMS Procedure Flows | ip.access | not presented | - | - |
| S5-090524 | Data Format for CM, FM & PM | ip.access | not presented | - | - |
| S5-090525 | TR-069 Connection Requests to HNB | Cisco, IP.Access | revised | - | S5-090527 |
| S5-090527 | Connection Requests to HNB Further Analysis | Cisco, Ip.Access | noted | S5-090525 | - |
| S5-090528 | 3G HNB Data Model Document Content and Scope | Thomson | agreed | - | - |
| S5-090530 | HNB OAM&P Requirements (result of phone conference #2) | Ericsson | agreed with modifications | - | - |
| S5-090531 | 32.xx1 Add requirements to Fault management Section | Alcatel-Lucent | noted | - | - |
| S5-090532 | Measurement related to PDN-GW | Samsung, China Mobile | revised | - | S5-090613 |
| S5-090533 | proposal of PDN-GW initiated Dedicated Bearer Creatation related measurements for EPC | Samsung, China Mobile | revised | - | S5-090613 |
| S5-090534 | proposal of PDN-GW initiated Dedicated Bearer Modification with QoS update related measurements for EPC | Samsung, China Mobile | revised | - | - |
| S5-090535 | proposal of PDN-GW initiated Dedicated Bearer Modification without QoS update related measurements for EPC | Samsung, China Mobile | revised | - | S5-090615 |
| S5-090536 | proposal of PDN-GW initiated Dedicated Bearer Deletion related measurements for EPC | Samsung, China Mobile | revised | - | S5-090616 |
| S5-090537 | E Qc CR Rel-8 TS 32511 | Ericsson, Qualcomm | revised | - | S5-090617 |
| S5-090538 | 32.XX3 Discussion on the Usage of a File for FM & PM | Alcatel-Lucent | noted | - | - |
| S5-090539 | 32.xx3 Updates to HNB Management Proc Flows | Alcatel-Lucent, T-Mobile, VF, Telecom Italia, Thomson, AT&T | noted | - | - |
| S5-090540 | ZTE CR R8 32.531 Correct the errors in the use case | ZTE | revised | - | S5-090618 |
| S5-090541 | 32.xx3 Update to Architecture for HNB Management Section | Alcatel-Lucent | agreed with modifications | - | - |
| S5-090542 | E-UTRAN NRM IS cleanup | Ericsson | agreed | - | - |
| S5-090543 | 32.763 E-UTRAN NRM Corba SS skeleton | Ericsson | agreed | - | - |
| S5-090544 | 32.763 E-UTRAN NRM Corba SS Rapporteur's proposal | Ericsson | revised | - | S5-090600 |
| S5-090545 | 32.763 E-UTRAN NRM Corba SS Mappings | Ericsson | agreed | - | - |
| S5-090546 | 32.765 E-UTRAN NRM XML skeleton | Ericsson | agreed | - | - |
| S5-090547 | 32.765 E-UTRAN NRM XML Rapporteur's proposal | Ericsson | revised | - | S5-090601 |
| S5-090548 | Traceability for ANR Use Cases | Ericsson | revised | - | S5-090619 |
| S5-090549 | E TD Record of email discussion on work expected from BBF re HNB Mgmt | Ericsson | noted | - | - |
| S5-090550 | Add Business-level Requirements for Autoconfiguration (Configuration Management Section) | Qualcomm Europe | withdrawn | - | - |
| S5-090551 | Add Specification-level Requirements for Autoconfiguration (Configuration Management Section) | Qualcomm Europe | agreed | - | - |
| S5-090552 | Pseudo CR to TS 32.410 -Additional KPI | Vodafone | revised | - | S5-090604 |
| S5-090553 | HNB FM and PM data model definition (xx2) | Alcatel-Lucent | noted | - | - |
| S5-090554 | Revision of cause values for counters using S1-protocol procedures | Huawei Technologies | noted | - | - |
| S5-090555 | Revison of cell bit-rate | Huawei Technologies | noted | - | - |
| S5-090556 | Revison of use case for cell bit-rate | Huawei Technologies | agreed | - | - |
| S5-090557 | Cleanup to active UE counter | Huawei Technologies | agreed | - | - |
| S5-090558 | Cleanup to DL packet delay counter | Huawei Technologies | agreed | - | - |
| S5-090559 | Remove one requirement related with E-MBMS for EPC NRM IRP | Huawei Technologies | revised | - | S5-090620 |
| S5-090560 | Rapporteur clean up suggestion for draft TS32.752 EPC NRM IRP IS | Huawei Technologies | revised | - | S5-090610 |
| S5-090561 | Revise the attribute of IOC MMEFunction | Huawei Technologies | revised | - | S5-090611 |
| S5-090562 | Add the attribute weightFactor to IOC MMEFunction | Huawei Technologies | noted | - | - |
| S5-090563 | Proposal on IOC MMEPool and MMEPoolArea | Huawei Technologies | noted | - | - |
| S5-090564 | Discuss the write qualifier of yellow items in TS32.752 | Huawei Technologies | revised | - | S5-090612 |
| S5-090566 | Add 3G Home NodeB OAM&P business level requirements | Huawei Technologies | agreed with modifications | - | - |
| S5-090567 | Add 3G Home NodeB OAM&P specification level requirements | Huawei Technologies | agreed with modifications | - | - |
| S5-090568 | Add 3G Home NodeB OAM&P General Data Model Overview | Huawei Technologies | revised | - | S5-090709 |
| S5-090569 | Add 3G Home NodeB Alarm Reporting Procedure Flow | Huawei Technologies | not addressed due to lack of time | - | - |
| S5-090570 | Add 3G Home NodeB FM File Update Procedure Flow | Huawei Technologies | not addressed due to lack of time | - | - |
| S5-090571 | Add 3G Home NodeB PM File Update Procedure Flow | Huawei Technologies | revised | - | S5-090710 |
| S5-090572 | Add 3G Home NodeB Gateway Discovery Procedure Flow | Huawei Technologies | revised | - | S5-090711 |
| S5-090573 | Add 3G Home NodeB Registration Procedure Flow | Huawei Technologies | revised | - | S5-090712 |
| S5-090574 | Discussion on HNB IP updating | Huawei Technologies | agreed with modifications | - | - |
| S5-090576 | Enhancement of Use case on cell throughput | Motorola | noted | - | - |
| S5-090577 | Measurements related to PDCP bit rate and SDU | Motorola | postponed | - | - |
| S5-090578 | Use case on RF Performance | Motorola | noted | - | - |
| S5-090579 | Measurements related to FR performance | Motorola | noted | - | - |
| S5-090580 | Enhanced Use case on PRB usage | Motorola | noted | - | - |
| S5-090581 | Measurements related to PRB usage for signalling | Motorola | postponed | - | - |
| S5-090582 | Use case on ARQ and HARQ performance | Motorola | noted | - | - |
| S5-090583 | Measurements related to ARQ and HARQ | Motorola | postponed | - | - |
| S5-090584 | M pseudo CR end point models for EPC | Motorola | noted | - | - |
| S5-090585 | M pseudo CR add the missing definitions for end point models in E-UTRAN NRM IRP | Motorola | noted | - | - |
| S5-090587 | Support/Read/Write Qualifiers for pciList Attribute of EUtranGenricCell IOC (Replaces S5-090586) | Qualcomm Europe, Orange | agreed | - | - |
| S5-090588 | CR R8 EPC signalling activation mechanisms û align with 29.274 and 29.272 | Motorola, Vodafone, T-Mobile | revised | - | S5-090621 |
| S5-090589 | CR EPC and E-UTRAN signalling deactivation mechanisms û align with 29.274, 29.272 and 36.413 | Motorola, Vodafone, T-Mobile | revised | - | S5-090622 |
| S5-090590 | CR R8 EPC and E-UTRAN trace recording session starting mechanisms û align with 36.413, 36.423 | Motorola, Vodafone, T-Mobile | revised | - | S5-090623 |
| S5-090591 | CR R8 Add the missing PGW to EPC trace recording session stopping mechanism | Motorola, Vodafone, T-Mobile | revised | - | S5-090624 |
| S5-090592 | CR R8 Enhancement of trigger events in 3GPP TS 32.423 û align with 29.274, 29.272 | Motorola, Vodafone, T-Mobile | revised | - | S5-090625 |
| S5-090593 | CR R8 refinement of the Trace Reference | Motorola, Vodafone, T-Mobile | noted | - | S5-090621 |
| S5-090594 | CR Mechnisms for Management activation in E-UTRAN | Motorola, Vodafone, T-Mobile | noted | - | - |
| S5-090595 | Discussion paper on Trace failure report | Motorola, Vodafone, T-Mobile | noted | - | - |
| S5-090596 | CR R8 enhance the XML schema to support failure report in 32 423 | Motorola, Vodafone, T-Mobile | withdrawn | - | - |
| S5-090597 | Minutes of the January 9th phone meeting on work split BBF - 3GPP SA5 for HNB OAM | WG Chairman | noted | - | - |
| S5-090598 | Adding IP address of X2 interface of eNB to E-UTRAN NRM | Nokia Siemens Networks, Huawei | revised | - | S5-090609 |
| S5-090600 | 32.763 E-UTRAN NRM Corba SS Rapporteur's proposal | Ericsson | agreed | S5-090544 | - |
| S5-090601 | 32.765 E-UTRAN NRM XML Rapporteur's proposal | Ericsson | agreed | S5-090547 | - |
| S5-090602 | Availability Formula in KPI definition for E-UTRAN | Ericsson, T-Mobile | agreed | S5-090513 | - |
| S5-090603 | Accessibility Formula in KPI definition for E-UTRAN | Ericsson | agreed | S5-090515 | - |
| S5-090604 | Pseudo CR to TS 32.410 -Additional KPI | Vodafone | noted | S5-090552 | - |
| S5-090605 | Handover measurements for E-UTRAN | Nokia Siemens Networks | agreed | S5-090509 | - |
| S5-090606 | Cell counters for Availability KPI | Ericsson, T-Mobile | agreed | S5-090514 | - |
| S5-090607 | EPS Bearer counters for Retainability KPI | Ericsson | agreed | S5-090520 | - |
| S5-090608 | E TD Modelling of antenna tma sector | Ericsson | revised | S5-090511 | S5-090626 |
| S5-090609 | Adding IP address of X2 interface of eNB to E-UTRAN NRM | Nokia Siemens Networks, Huawei | revised | S5-090598 | S5-090627 |
| S5-090610 | Rapporteur clean up suggestion for draft TS32.752 EPC NRM IRP IS | Huawei Technologies | agreed | S5-090560 | - |
| S5-090611 | Revise the attribute of IOC MMEFunction | Huawei Technologies | noted | S5-090561 | - |
| S5-090612 | Discuss the write qualifier of yellow items in TS32.752 | Huawei Technologies | agreed | S5-090564 | - |
| S5-090613 | Measurement related to PDN-GW | Samsung, China Mobile | noted | S5-090532 | - |
| S5-090614 | proposal of PDN-GW initiated Dedicated Bearer Modification with QoS update related measurements for EPC | Samsung, China Mobile | withdrawn | S5-090534 | - |
| S5-090615 | proposal of PDN-GW initiated Dedicated Bearer Modification without QoS update related measurements for EPC | Samsung, China Mobile | withdrawn | S5-090535 | - |
| S5-090616 | proposal of PDN-GW initiated Dedicated Bearer Deletion related measurements for EPC | Samsung, China Mobile | withdrawn | S5-090536 | - |
| S5-090617 | E Qc CR Rel-8 TS 32511 | Ericsson, Qualcomm | agreed | S5-090537 | - |
| S5-090618 | ZTE CR R8 32.531 Correct the errors in the use case | ZTE | agreed | S5-090540 | - |
| S5-090619 | Traceability for ANR Use Cases | Ericsson | agreed | S5-090548 | - |
| S5-090620 | Remove one requirement related with E-MBMS for EPC NRM IRP | Huawei Technologies | agreed | S5-090559 | - |
| S5-090621 | CR R8 EPC signalling activation mechanisms û align with 29.274 and 29.272 | Motorola, Vodafone, T-Mobile | sent for email approval | S5-090588 | - |
| S5-090622 | CR EPC and E-UTRAN signalling deactivation mechanisms û align with 29.274, 29.272 and 36.413 | Motorola, Vodafone, T-Mobile | sent for email approval | S5-090589 | - |
| S5-090623 | CR R8 EPC and E-UTRAN trace recording session starting mechanisms û align with 36.413, 36.423 | Motorola, Vodafone, T-Mobile | sent for email approval | S5-090590 | - |
| S5-090624 | CR R8 Add the missing PGW to EPC trace recording session stopping mechanism | Motorola, Vodafone, T-Mobile | sent for email approval | S5-090591 | - |
| S5-090625 | CR R8 Enhancement of trigger events in 3GPP TS 32.423 û align with 29.274, 29.272 | Motorola, Vodafone, T-Mobile | withdrawn | S5-090592 | - |
| S5-090626 | E TD Modelling of antenna tma sector | Ericsson | noted | S5-090608 | - |
| S5-090627 | Adding IP address of X2 interface of eNB to E-UTRAN NRM | Nokia Siemens Networks, Huawei | revised | S5-090609 | S5-090628 |
| S5-090628 | Adding IP address of X2 interface of eNB to E-UTRAN NRM | Nokia Siemens Networks, Huawei | agreed | S5-090627 | - |
| S5-090629 | Working assumption concerning S5-080626 | SA5 OAM | agreed | - | - |
| S5-090701 | 32.xx1-001 | Rapporteur | agreed | - | - |
| S5-090702 | 32.xx2-001 | Rapporteur | agreed | - | - |
| S5-090703 | 32.xx3-001 | Rapporteur | agreed | - | - |
| S5-090704 | 32.xx4-001 | Rapporteur | not addressed due to lack of time | - | - |
| S5-090705 | nn | nn | [not addressed] | - | - |
| S5-090706 | HNB OAM&P Requirements revision | Ericsson | not addressed due to lack of time | - | - |
| S5-090707 | Working assumption on alarm handling in HNB | SA5 | agreed | - | - |
| S5-090708 | Revision of FM-006 | ip.access | agreed with modifications | - | - |
| S5-090709 | Add 3G Home NodeB OAM&P General Data Model Overview | Huawei Technologies | noted | S5-090568 | - |
| S5-090710 | Add 3G Home NodeB PM File Update Procedure Flow | Huawei Technologies | not addressed due to lack of time | S5-090571 | - |
| S5-090711 | Add 3G Home NodeB Gateway Discovery Procedure Flow | Huawei Technologies | not addressed due to lack of time | S5-090572 | - |
| S5-090712 | Add 3G Home NodeB Registration Procedure Flow | Huawei Technologies | not addressed due to lack of time | S5-090573 | - |

## Annex B: List of action items

| Meeting/Number | Agenda item | Document | Details | Responsible |
| --- | --- | --- | --- | --- |
| S5-62bis OAM/8 | 6.1 | S5-090505 | Put the issue of northbound interface from TR-069 ACS in the agenda for the next call with the BBF. | Chairman |
| S5-62bis OAM/9 | 6.1 | S5-090505 | A formal LS reply will be sent from the SA5#63 meeting on BBF LS on northbound interface. | Zou Lan |

## Annex C: List of participants

| Lastname | Firstname | Role | Organization Represented | SDO |
| --- | --- | --- | --- | --- |
| Aba | Istvan | ViceChairman | T-Mobile Austria GmbH | ETSI |
| Amirijoo | Mehdi | Attendee | Telefon AB LM Ericsson | ETSI |
| Andrianov | Anatoly | Attendee | MOTOROLA GmbH | ETSI |
| Berggren | Tommy | Attendee | TeliaSonera AB | ETSI |
| Bizzarri | Simone | Attendee | TELECOM ITALIA S.p.A. | ETSI |
| Bódog | Gyula | Attendee | Nokia Siemens Networks Oy | ETSI |
| Catovic | Amer | Attendee | QUALCOMM EUROPE S.A.R.L. | ETSI |
| Chen | Zhe | Attendee | SAMSUNG Electronics Co. | ARIB |
| Cornily | Jean Michel | Attendee | ORANGE SA | ETSI |
| Cristallo | Geoffrey | Attendee | Alcatel-Lucent | ETSI |
| Cruz | Manuel | Attendee | TELEFONICA S.A. | ETSI |
| Divialle | Marie | Attendee | NORTEL NETWORKS (EUROPE) | ETSI |
| Elmdahl | Per | Attendee | Nanjing Ericsson Panda Com Ltd | CCSA |
| Gompakis | Panagiotis | Attendee | Vodafone D2 GmbH | ETSI |
| Gupta | Rajarshi | Attendee | Qualcomm Incorporated | ATIS |
| Huang | Shuqiang | Attendee | ZTE Corporation | CCSA |
| Li | Rong | Attendee | CCSA | CCSA |
| Li | Gang | Attendee | Nokia Siemens Networks | ETSI |
| Li | Yunxi | Chairman | Nanjing Ericsson Panda Com Ltd | CCSA |
| Liminiana | Marta | Attendee | TELEFONICA S.A. | ETSI |
| MacPherson | Ian | Attendee | ip.access Ltd. | ETSI |
| Malviya | Manish | Attendee | Alcatel-Lucent Telecom Limited | ETSI |
| Murphy | Chris | Attendee | MOTOROLA Ltd | ETSI |
| Neal | Adrian | Attendee | Vodafone Teknoloji Hizmetleri | ETSI |
| Nunzi | Giorgio | Attendee | NEC EUROPE LTD | ETSI |
| Pan | Feng | Attendee | HuaWei Technologies Co., Ltd | CCSA |
| Petersen | Robert | Attendee | Nippon Ericsson K.K. | ARIB |
| Romero | Ramon | Attendee | TELEFONICA S.A. | ETSI |
| Schmidt | Jörg | Member | Nokia Siemens Networks | ETSI |
| Shibata | Takeshi | Attendee | Hitachi Ltd. | ARIB |
| Stephens | Paul | Attendee | MOTOROLA Ltd | ETSI |
| Sudarsan | Padma | Attendee | Alcatel-Lucent | ATIS |
| Suerbaum | Clemens | Attendee | Nokia Siemens Networks | ETSI |
| Toche | Christian | WG_Chairman | HUAWEI TECHNOLOGIES Co. Ltd. | ETSI |
| Tovinger | Thomas | ViceChairman | Telefon AB LM Ericsson | ETSI |
| Tse | Edwin | Attendee | Ericsson Inc. | ATIS |
| Xia | Haitao | Attendee | HuaWei Technologies Co., Ltd | CCSA |
| Yoshizawa | Taka | Attendee | Thomson | ETSI |
| Zhang | Kai | Attendee | HuaWei Technologies Co., Ltd | CCSA |
| Zhu | Weihong | Attendee | ZTE Corporation | CCSA |
| Zou | Lan | Attendee | HuaWei Technologies Co., Ltd | ATIS |
| Zuo | Zhisong | Attendee | ZTE Corporation | CCSA |