c3GPP TSG-SA5 (Telecom Management)

Meeting SA5#63, 16 - 20 February 2008, Prague, CZ

Source:		Peter Legg, Huawei

Title:		UID_390002 Performance measurements for E-UTRAN Rapporteur Report

Document for:		Approval

Agenda Item:		<x.y.z>

# Progress status

Percentage of completion: 100% (previously 80%)

Summary of progress: limited progress.

Outstanding issues: several documents are to be revisited after revision later this week.

# Minutes

The RG session was held on Wednesday 18th February, Quarters 2-4

| Tdoc | Title/Discussion/Conclusion | Source |
| --- | --- | --- |
| S5-091158 | Triggered HO events presented by Peter Legg, Huawei. Conclusion, no need to reply. No restriction on PM, but will be difficult to introduce CM to achieve Handover Parameter Optimisation because handover measurement usage is expected to vary between vendors. | R2-090833 |
| S5-091235 | Editorial update to the PDCP delay measurement name presented by Ulf Hubinette, E///. Agreed. | Ericsson |
| S5-091236 | Removal of Tx bit-rate measurements presented by Ulf Hubinette, E///. Agreed. | Ericsson |
| S5-091238 | IP Latency measurements presented by Ulf Hubinette, E///. Huawei: need to add buffer in x.1. Moto: change to EUTRANgenericcellTDD etc as agreed at this meeting. Moto: 4.4.x.3: how does this work? Same UE different QCI. E/// just consider UE. Moto: dont think this is useful. UE part is not agreed, take offline. Moto: why do we need t wo measurements ? revisit kpi document. update to 1651. not agreed | Ericsson |
| S5-091240 | IP throughput measurements presented by Ulf Hubinette, E///. not agreed. Measurements are at layer 2, need discussion in RAN2. | Ericsson |
| S5-091244 | Mobility KPI measurements presented by Ulf Hubinette, E///. These are linked to revised mobility kpis. It was questioned why qci is relevant here, by Huawei and Moto. CMO said it was interested to see different performance of handover for different services. There was a consensus that preparation was the most important aspect. the mobility kpi should reflect this - prep per qci and execution not qci specific. not agreed (noted) | Ericsson |
| S5-091245 | Updates on measurements names according to naming conventions presented by Ulf Hubinette, E///. Remove exe in handover counters. Need "tot" in 4.5.3 and 4.5.4, 4.3.2.1.1.HO.IratAtt.cause. 4.3.1.5.3 needs to be reordered to HO.NoDRXOutAtt. Need "out" , do not delete. Noted, as info for rapporteur to update the specification. Action to rapporteur to fix this. | Ericsson |
| S5-091246 | Background/use case for re-structuring of Release measurements presented by Ulf Hubinette, E///. Moto: current counters support abnormal release, eNB releases are abnormal unless cause value is ue inactivity. Structure change not agreed. not agreed Noted. | Ericsson |
| S5-091247 | Use case for SAE Bearer release presented by Ulf Hubinette, E///. not agreed Noted | Ericsson |
| S5-091264 | Use case for air interace packet loss presented by Peter Legg, Huawei. The author stated that the use-case needs revision because ran2 was unable to define a pure air interface packet loss counter on the uplink. Moto suggested that the final sentence should be clarified (showing that an offline calculation is suggested). The proposed use-case should be specified as DL only and new text is needed for the UL. revision in 1264 to be addressed later in the week. not agreed | Huawei Technologies |
| S5-091267 | Counter for air interace packet loss presented by Peter Legg, Huawei. Moto: commented that we need EUTRANgenericcell, not EUTRANcell. The author stated that the uplink counter needs to be revised according to ran2 definition of uplink packet loss. Revision in 1267. not agreed | Huawei Technologies |
| S5-091269 | Revison of cell bit-rate counter presented by Peter Legg, Huawei. Moto: commented that the data forwarding over S1 should be checked. Huawei agreed to do this. document is agreed.. | Huawei Technologies |
| S5-091286 | Clearance of 32.425-050 presented by Yao Yizhi,Moto. Bullet d, E///. Why is e-utran generic cell used ? Moto: this makes it applicable to tdd or fdd. E/// OK. CMO: keep consistency with 32.405. Moto: need another editorial update. Now EUTRANcellTDD and FDD are now agreed in principal (at this meeting). Update into next version. agreed with modifications. | Rapporteur |
| S5-091287 | Enhancement of Use case on cell throughput presented by Yizhi. E/// did not see the justification for the measurements. Isnt the prb usage enough. Needs rwork New tdoc 1670. not agreed | Motorola |
| S5-091288 | Measurements related to PDCP bit rate and SDU presented by Yizhi. Comments were collected for information. Huawei said bit-rate counters were not clear, need to measure DCCH from RRC and NAS. Tdoc 1671 for any revision. not agreed | Motorola |
| S5-091289 | Use case on RF Performance presented by Yizhi. Huawei argued that sir is difficult to measure and may not be the best measure of cell edge bit-rate. NSN thought mean and worst-case sir would be OK. Motorola agreed to remove sir from use case. E/// said all these RF should be referred to RAN. update in 1673, keeping dl power only. not agreed | Motorola |
| S5-091290 | Measurements related to RF performance withdrawn. Need ran input (definition of dl power measurement) | Motorola |
| S5-091291 | Use case on ARQ and HARQ performance presented by Yizhi. Agreed. | Motorola |
| S5-091292 | Measurements related to ARQ and HARQ presented by Yizhi. Needs ran2 to define layer 2 measurements. Late for rel-8. Noted. not agreed | Motorola |
| S5-091293 | Enhanced Use case on PRB usage presented by Yizhi. Huawei stated that total prb usage and dtch usage is sufficient. Huawei (action) to check if measurement allows a mixed dcch and dtch mac pdu to be well weighted E/// do not understand the use-case reason. not agreed Noted | Motorola |
| S5-091294 | Measurements related to PRB usage for control channels noted without discussion. not agreed | Motorola |
| S5-091307 | M Presentation of 32.425-060 for information and approval presented by Yizhi. Which version number ? Ask MCC. Agreed to be sent to SA for approval. | Rapporteur |
| S5-091407 | Structure changes to SAE Bearer Release measurements (revised S5-091248) noted without discussion. | Ericsson |

# Action items

| Item | Description | Release | Owner | Status | Target |
| --- | --- | --- | --- | --- | --- |
| 63.1 | Update spec measurement names | Rel-8 | Rapporteur | New | Next SA |
| 63.2 | Check detail of dtch prb usage | Rel-8 | Huawei | New | SA5 #64 |