3GPP TSG-SA5 (Telecom Management)	S5-094301

Meeting SA5#68, 09 -13 Nov 2009, Shanghai, PRC	revision of S5-09154

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 32.260 | CR | 0080 | ( rev | - | ( Current version: | 9.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Account Expiration Information from OCS to IMS Application Servers |
| --- | --- |
| Source to WG: ( | AT&T, Ericsson |
| Source to TSG: ( | SA5 |
| Work item code: ( | CH9 |  | Date: ( | 13/11/2009 |
| Category: ( | B |  | Release: ( | Rel-9 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | In On-Line Charging scenarios, allows the application providing service to the end-user to take into consideration account expiration information. |
| Summary of change: ( | OCS may include account date & time expiration information in the CCA response to a CCR request, using a new AVP. |
| Consequences if ( not approved: | Inferior service experience provided to the end-user in some cases where impending account expiration may be a factor. |
| Clauses affected: ( | 6.3.1.2, 6.3.3 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  | X |  | O&M Specifications | 32.299 |
| Other comments: ( |  |

1st Modified Section

#### 6.3.1.2	Definition of the IMS Information

IMS specific charging information is provided within the IMS Information. The fields of the IMS Information which are different coved in several IMS network nodes are indicated by the node specific type.

The detailed structure of the IMS Information can be found in table 6.3.1.2.

Table 6.3.1.2: Structure of the IMS Information

| Field | Category | Description | Provided by IMS NE |
| --- | --- | --- | --- |
| Event Type | OC | This field holds the SIP Method, the content of the SIP “Event” header and the content of the SIP “expires” header when present in the SIP request. | All |
| Node Functionality | M | This field contains the function of the node. | All |
| Role of Node | OM | This field specifies the role of the AS/CSCF. | All |
| User Session ID | OM | This field holds the session identifier. For a SIP session the Session-ID contains the SIP Call ID. | All |
| Calling Party Address | OM | This field holds the address (SIP URI or TEL URI)URI of the party (Public User Identity or Public Service Identity) initiating a session or requesting a service. | All |
| Called Party Address | OM | For SIP transactions, except for registration, this field holds the address of the party (Public User ID or Public Service ID) to whom the SIP transaction is posted. For registration transactions, this field holds the Public User ID under registration. | All |
| Number Portability routing information | OC | This field includes information on number portability after DNS/ENUM request from S-CSCF in the calling user’s home network. | S-CSCF, I-CSCF, AS, MGCF, BGCF |
| Carrier Select routing information | OC | This field includes information on carrier select after DNS/ENUM request from S-CSCF in the calling user’s home network. | S-CSCF, i_CSCF, AS, MGCF, BGCF |
| Alternate Charged Party Address | OC | The address of an alternate party that is identified by the AS at session initiation, and is charged in place of the calling party. | AS only |
| Requested Party Address | OC | For SIP transactions this field holds the address of the party (Public User ID or Public Service ID) to whom the SIP transaction was originally posted. This field is only present if different from the Called Party Address parameter. | S-CSCF and AS/MRFC |
| Called Asserted Identity | OC | The address of the final asserted identity. Present if the final asserted identity is available in the SIP 2xx response. | S-CSCF and AS/MRFC |
| Associated URI | OC | This field holds a non-barred public user identity (SIP URI or TEL URI) associated to the public user identity under registration. | S-CSCF, P-CSCF, I-CSCF, IBCF |
| Time Stamps | OC | This field holds the time of the SIP REQUEST and the time of the response to the SIP REQUEST. | All |
| Application Server Information | OC | This field holds the SIP URI(s) of the AS(s) addressed during the session and the called party number (SIP URI, E.164), if an application server determines it. | S-CSCF and MRFC |
| Inter Operator Identifier | OC | This field holds the identification of the network neighbours (originating and terminating) as exchanged via SIP signalling if available. | All |
| IMS Charging Identifier | OM | This field holds the IMS Charging Identifier (ICID) as generated by a IMS node for a SIP session. | All |
| Early Media Description | OC | This field holds session and media parameters related to media components set to active during the SIP session establishment and before a final successful or unsuccessful SIP answer to the initial SIP INVITE request is received. Once a media component is set to active, subsequent status changes shall be registered. Since several SDP negotiations may occur during the SIP session establishment, this field may occur several times. | Not in I-CSCF |
| SDP Session Description | OC | This field holds the content of an "attribute-line" (i=, c=, b=, k=, a=, etc.) related to a session. | Not in I-CSCF |
| SDP Media Component | OC | This is a grouped field comprising several sub-fields associated with one media component. Since several media components may exist for a session in parallel these sub-fields may occur several times. | Not in I-CSCF |
| Served Party IP Address | OC | This field holds the IP address of either the calling or called party, depending on whether the P-CSCF is in touch with the calling or the called party. | P-CSCF |
| Server Capabilities | OC | This field contains the server capabilities as described in 3GPP TS 29.229 [205]. | I-CSCF |
| Trunk Group ID | OC | This field identifies the incoming and outgoing PSTN legs. | MGCF |
| Bearer Service | OC | This field holds the used bearer service for the PSTN leg. | MGCF |
| Service Id | OC | This field identifies the service the MRFC is hosting. For conferences the conference ID is used as the value of this parameter. | MRFC |
| Service Specific Info | OC | This field contains service specific data if and as provided by an Application Server. | AS |
| Message Bodies | OC | This field holds information about the Message body, Content-Type, Content-Length, Content-Disposition and Originator if available. | P-CSCF, S-CSCF, MGCF, IBCF and AS |
| Access Network Information | OC | This field contains the content of the P-header P-Access-Network-Info. | All |
| IMS Communication Service ID | OC | This field contains the IMS communication service identifier if received in the P-Asserted-Service header in the SIP request. | S-CSCF, IBCF, and AS |
| Cause Code | OC | This field contains the cause value. | All |
| Real Time Tariff Information | Oc | This field holds the tariff/add-on charge received. | S-CSCF, IBCF, MGCF and AS |
| Online Charging Flag | OC | This field indicates the Online Charging Request was sent based on the provided ECF address from the SIP P-header “P-Charging-Function-Addresses”. NOTE: No proof that online charging action has been taken | S-CSCF and AS/MRFC |
| Account Expiration | OC | This field indicates the subscriber account expiration date and time of day. | OCS |

Next modification

### 6.3.3	Detailed Message Format for online charging

The following table specifies per Operation type the charging data that are sent by each of the IMS network elements for:

- IMS session and IMS event (I/U/T/E)

- IMS-GWF, AS

- IMS session only (I/U/T)

- MRFC

The Operation types are listed in the following order: I (initial)/U (update)/T (terminate)/E (event). Therefore, when all Operation types are possible it is marked as IUTE. If only some Operation types are allowed for a node, only the appropriate letters are used (i.e. IUT or E) as indicated in the table heading. The omission of an Operation type for a particular field is marked with "-" (i.e. IU-E). Also, when an entire filed is not allowed in a node the entire cell is marked as "-".

Note that not for all structured fields the individual field members are listed in the table. Detailed descriptions of the fields are provided in TS 32.299 [50].

Table 6.3.3.1 illustrates the basic structure of the supported fields in the Debit and Reserve Units Request for IMS online charging.

Table 6.3.3.1: Supported fields in Debit and Reserve Units Request Message

| Field | Node Type | IMS-GWF | MRFC | AS |
| --- | --- | --- | --- | --- |
|  | Supported Operation Types | I/U/T/E | I/U/T | I/U/T/E |
| Session Identifier | IUTE | IUT | IUTE |
| Originator Host | IUTE | IUT | IUTE |
| Originator Domain | IUTE | IUT | IUTE |
| Destination Domain | IUTE | IUT | IUTE |
| Operation Identifier | IUTE | IUT | IUTE |
| Operation Token | IUTE | IUT | IUTE |
| Operation Type | IUTE | IUT | IUTE |
| Operation Number | IUTE | IUT | IUTE |
| Destination Host | IUTE | IUT | IUTE |
| User Name | IUTE | IUT | IUTE |
| Origination State | IUTE | IUT | IUTE |
| Origination Timestamp | IUTE | IUT | IUTE |
| Subscriber Identifier | IUTE | IUT | IUTE |
| Termination Cause | —T- | —T | —T- |
| Requested Action | IUTE | IUT | IUTE |
| Multiple Operation | IU-E | IU- | IU-E |
| Multiple Unit Operation | IU-E | IU- | IU-E |
| Service Units Requested | IU-E | IU- | IU-E |
| Action Requested | ---E | - | ---E |
| Service Units Used | -UT- | -UT | -UT- |
| Subscriber Equipment Number | IUTE | IUT | IUTE |
| Proxy Information | IUTE | IUT | IUTE |
| Route Information | IUTE | IUT | IUTE |
| Extended Information | IUTE | IUT | IUTE |
| Service Information with PS and IMS Information |
| Event Type | IUTE | IUT | IUTE |
| Role Of Node | IUTE | IUT | IUTE |
| Node Functionality | IUTE | IUT | IUTE |
| User Session Id | IUTE | IUT | IUTE |
| Calling Party Address | IUTE | IUT | IUTE |
| Called Party Address | IUTE | IUT | IUTE |
| Number Portability routing information | I--E | - | I--E |
| Carrier Select routing information | I--E | - | I--E |
| Requested Party Address | I--E | I-- | I--E |
| Called Asserted Identity | -UTE | -UT | -UTE |
| Associated URI | --TE | - | - |
| Application Server Information | IUTE | IUT | - |
| Inter Operator Identifier | IUTE | IUT | IUTE |
| IMS Charging Identifier | IUTE | IUT | IUTE |
| SDP Session Description | IU-- | IU- | IU-- |
| SDP Media Component | IU-- | IU- | IU-- |
| GGSN Address | IU-- | IU- | IU-- |
| Served Party | - | - | - |
| Server Capabilities | - | - | - |
| Trunk Group ID | - | - | - |
| Bearer Service | - | - | - |
| Service Id | - | IUT | - |
| Service Specific Info | - | - | - |
| Messages Bodies | IUTE | - | IUTE |
| Cause Code | --TE | --T | --TE |
| Access Network Information | IUTE | IUT | IUTE |
| IMS Communication Service ID | I--E | - | I--E |

Table 6.3.3.2 illustrates the basic structure of the supported fields in the Debit and Reserve Units Response for IMS online charging.

Table 6.3.3.2: Supported fields in Debit and Reserve Units Response Message

| Field | Node Type | IMS-GWF | MRFC | AS |
| --- | --- | --- | --- | --- |
|  | Supported Operation Types | I/U/T/E | I/U/T | I/U/T/E |
| Session Identifier | IUTE | IUT | IUTE |
| Operation Result | IUTE | IUT | IUTE |
| Originator Host | IUTE | IUT | IUTE |
| Originator Domain | IUTE | IUT | IUTE |
| Operation Identifier | IUTE | IUT | IUTE |
| Operation Type | IUTE | IUT | IUTE |
| Operation Number | IUTE | IUT | IUTE |
| Operation Failover | IUTE | IUT | IUTE |
| Multiple Unit Operation | IUTE | IUT | IUTE |
| Operation Failure Action | - | - | - |
| Redirection Host | - | - | - |
| Redirection Host Usage | - | - | - |
| Redirection Cache Time | - | - | - |
| Proxy Information | - | - | - |
| Route Information | - | - | - |
| Failed parameter | - | - | - |
| Extended Information | IUTE | IUT | IUTE |
| Service Information with IMS Information |
| Account Expiration | - | - | IUTE |

End of modifications

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.