3GPP TSG-SA5 (Telecom Management)	S5-094177

Meeting SA5#68, 09 -13 Nov 2009, Shanghai, PRC	revision of S5-093853

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 32.275 | CR | 0023 | ( rev | - | ( Current version: | 9.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | MMTel Online charging scenarios simplification – IMS-GWF interaction removal |
| --- | --- |
| Source to WG: ( | Alcatel-Lucent |
| Source to TSG: ( | SA5 |
| Work item code: ( | eMMTel-SS-CH |  | Date: ( | 13/11/2009 |
| Category: ( | C |  | Release: ( | Rel-9 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | Generic “AS implementing supplementary services” interaction with IMS-GWF is no longer needed for each MMTel supplementary service Online Charging as it is already described separately. |
| Summary of change: ( | Remove interaction with IMS-GWF description for following online charging scenarios : CDIV, FA, CUG. |
| Consequences if ( not approved: | Redondant generic description within online charging description for each supplementary service. |
| Clauses affected: ( | 5.3.2.1.1, 5.3.2.1.2, 5.3.2.1.3 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

1st Modified Section

##### 5.3.2.1.1	Communications Diversion (CDIV)

###### 5.3.2.1.1.1	Communications Diversion (CDIV) – successful establishment

The following figure shows the Diameter transactions that are required between Application Server implementing the CDIV service and OCS, when online charging is applied to a successful CFU communication.

Figure 5.3.2.1.1.1-1: Message Sequence Chart for online charging of CDIV service - establishment

A communication is requested towards User B: CFU and online-based charging activated for user B.

1) INVITE request incoming for User B. Based on the iFC, indicating that User B is subscribed to the CDIV supplementary service, the communication is forwarded to AS implementing CDIV, where CFU is detected.

2)  As the subscriber is “online charging”, the AS sends a Credit-Control-Request (INITIAL_REQUEST, service CDIV, ICID..) to the OCS for requesting units for the CDIV (CFU) supplementary service.

3)  The OCS grants units in the Credit-Control-Answer response for this request.

4) The CDIV (CFU) can now be delivered: an Invite is sent towards user C via the S-CSCF.

5-6) On answer from User-C (200 OK), the AS sends a Credit-Control-Request (UPDATE, USU) with possible already used units and requests new units to continue.

7) New units are granted via Credit-Control-Answer and the 200 OK is propagated.

###### 5.3.2.1.1.2	Communications Diversion (CDIV) – release

The next figure shows the Diameter transactions occurring on release of the previous established communication, initiated by user C:

Figure 5.3.2.1.1.2-1: Message Sequence Chart for Offline charging of CDIV service -release

1) User C initiates release of the communication

2) At session termination the AS implementing the CDIV service, sends a Credit-Control-Request (TERMINATION_REQUEST, used service units) for ending credit control.

Next Modified Section

##### 5.3.2.1.2	Flexible Alerting (FA)

The following figure shows the Diameter transactions that are required between Application Server implementing the FA service and OCS, when online charging is applied to a successful FA communication.

Figure 5.3.2.1.2-1: Message Sequence Chart for Online charging of FA service

UE-B and UE-C are FA group members of the FA group identified by the “Pilot Identity”.

A communication is requested from UE-A towards the “Pilot Identity”.

1) INVITE request incoming for “Pilot Identity”. Based on the Initial Filter Criteria (IFC), indicating the request must be forwarded to an AS implementing FA for this “Pilot Identity”.

2) As “online charging” is activated for the “Pilot Identity”, the AS implementing FA has to initiate parallel Invite towards each of FA group members.

3) For FA member User B, the AS sends a Credit-Control-Request (INITIAL_REQUEST, service FA, ICID-B) to the OCS for requesting units for the FA supplementary service.

4) The OCS grants units in the Credit-Control-Answer response for this request.

5) INVITE is sent towards User B via the S-CSCF.

6) Alerting phase signalling occurs with UE-A.

7) A parallel (from step 3 to step 6) scenario occurs towards User-C with session identified by ICID-C.

8-9) Upon reception of the 200 OK answer from UE-C, AS sends CANCEL to other FA group member being alerted (UE-B).

10) More signalling for CANCEL transactions

11-13) When the last CANCEL transaction is terminated, AS sends a Credit-Control-Request (UPDATE, USU) with possible already used units, and requests new units to continue the communication between User A and User C.

14) New units are granted via Credit-Control-Answer

15) 200 OK is propagated towards User A.

Next Modified Section

##### 5.3.2.1.3	Closed User Group (CUG)

###### 5.3.2.1.3.1	Closed User Group (CUG): Originating

The following figure shows the Diameter transactions that are required between Application Server implementing the CUG service and OCS, when online charging is applied to a successful originating communication from User-A CUG member.

Figure 5.3.2.1.3.1-1: Message Sequence Chart for Online charging of CUG service - originating call

User-A is subscribed to CUG service, and initiates a communication towards User B.

1) User-A initiates a communication towards User B sending INVITE request. Based on the Initial Filter Criteria (IFC) Rules, indicating that User A is subscribed to the CUG supplementary service, the communication is forwarded to an AS implementing CUG.

2) AS performs checks from the request received regarding User A CUG subscription profile, and determines the CUG-communication is allowed for CUG member User-A towards User-B.

3-4) As “online charging” is activated for User A, the AS sends a Credit-Control-Request (INITIAL_REQUEST, service CUG, ICID.) to the OCS for requesting units for the CUG supplementary service.The OCS grants units in the Credit-Control-Answer response for this request. The AS forwards INVITE via the S-CSCF towards User-B with CUG information included.

Note: In case the result from AS checks indicates non-CUG communication behaviour (for CUG communication with outgoing access…), non-CUG communication charging applies, and CUG information is not included in the forwarded Invite.

5) SIP signalling for communication establishment.

6-8) 200 OK answer received from User B, and AS sends a Credit-Control-Request (UPDATE, USU) with possible already used units, and requests new units to continue the CUG communication between User A and User B. New units are granted via Credit-Control-Answer, and 200 OK is propagated towards User A.

###### 5.3.2.1.3.2	Closed User Group (CUG): Terminating

The following figure shows the Diameter transactions that are required between Application Server implementing the CUG service and OCS, when online charging is applied to a successful terminating communication towards User-B CUG member.

Figure 5.3.2.1.3.2-1: Message Sequence Chart for Online charging of CUG service - terminating call

User-B is subscribed to CUG service.

1) Incoming INVITE request with CUG information towards User-B.Based on the Initial Filter Criteria (IFC) Rules, indicating that User B is subscribed to the CUG supplementary services, the communication is forwarded to an AS implementing CUG.

2) AS performs checks from the request received regarding User B CUG subscription profile, and determines the CUG-communication is allowed for CUG member User-B from User A.

3-4) As “online charging” is activated for User B, the AS sends a Credit-Control-Request (INITIAL_REQUEST, service CUG, ICID.) to the OCS for requesting units for the CUG supplementary service.The OCS grants units in the Credit-Control-Answer response for this request. The AS forwards INVITE via the S-CSCF towards User-B.

Note: In case the result from AS checks indicates non-CUG communication behaviour (incoming access from non-CUG member…), non-CUG communication charging applies.

5) SIP signalling for communication establishment.

6-8) 200 OK answer received from User B, and AS sends a Credit-Control-Request (UPDATE, USU) with possible already used units, and requests new units to continue the CUG communication between User B and User A. New units are granted via Credit-Control-Answer, and 200 OK is propagated towards User A.

End of modifications

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

# Text boxes

5. 200 OK

10. More SIP signalling

2. UE-B and UE-C members of  FA group “Pilot Identity”

4. INVITE (user C)

4. INVITE (user C)

new Units requested

More SIP signalling

1. INVITE (User B, CUG Information)

UE B

Terminating UE-B Home Network

SIP signalling

9. 200 OK

new Units requested

10. CCR (update, USU)

11. CCA (update, GSU)

9. 200 OK

1. INVITE (User B)

8. SIP signalling

6. CCR (update, USU)

9. 200 OK

1. INVITE (User B)

6. Reserve units for incoming session for User B (same ICID).

7. CCA (Initial, CC_not_applicable)

5. CCR (initial,  ICID, RSU )

1. INVITE (User B)

4. CCA (initial, GSU)

Reserve units for  incoming CUG for user B

3. CCR (initial, service = CUG, ICID, RSU)

IMS-GWF

OCS

AS

S-CSCF

iFC for B

SIP signalling

9. 200 OK

new Units requested

10. CCR (update, USU)

11. CCA (update, GSU)

9. 200 OK

1.INVITE (User B, CUG information)

1.INVITE (User B, CUG information)

8.SIP signalling

9. 200 OK

3. CCA (initial, GSU)

Reserve units CDIV session for user B

2. CCR (initial, service = CDIV, RSU)

6. Reserve units f1. INVITE

towards User B (same ICID).

7.CCA (Initial, CC_not_applicable)

5. CCR (initial,  ICID, RSU )

1.INVITE (User B, CUG information)

1.INVITE (User B, CUG information)

5. 200 OK

CFU for user B

4. CCA (initial,GSU )

Reserve units for CUG towards user B

3. CCR (initial, service = CUG, ICID, RSU)

UE A

IMS-GWF

OCS

1.INVITE

AS

S-CSCF

Originating UE-A Home Network

2. Check on request validity regarding CUG

1.INVITE (User B)

iFC for A

OCS

1. INVITE (User B)

15. ACK

14.487 (Request Terminated)

13. More SIP signalling

12.CANCEL (User B)

18.200 OK

18.200 OK

11.200 OK

2. Check on request validity regarding CUG

11.200 OK

new Units requested

16. CCR (update, USU)

17. CCA (update, GSU)

UE-C answers

7. CCA (update, GSU)

)

5. 200 OK

AS

UE C

IMS-GWF

1. INVITE

UE B

AS

OCS

1. INVITE (User B, CUG Information)

115. Reserve units for session towards User B (same ICID).

. INVITE

S-CSCF

S-CSCF

UE-B Home Network

1. INVITE

“Pilot Identity” Home Network

10. Parallel scenario from step 3 to step 9 towards User C

iFC for B

2.UE-B and UE-C members of  FA group “Pilot Identity”

9 . SIP signalling : alerting phase between UE-A, S-CSCF, AS  and UE-B

5.INVITE (UE-B)

5. INVITE (UE-B)

5. INVITE (UE-B)

7. Reserve units for  session towards User B (same ICID-B).

8.CCA (Initial, CC_not_applicable)

6. CCR (initial,  ICID-B, RSU )

5. INVITE (UE-B)

4. CCA (initial,GSU )

Reserve units for FA  towards user B and user C

3. CCR (initial, service = FA, ICID-B, RSU)

AS

UE C

IMS-GWF

1. INVITE (Pilot Identity)

1. INVITE (Pilot Identity)

UE B

OCS

S-CSCF

6. SIP Signalling: alerting phase between UE-A, S-CSCF, AS and UE-B

“Pilot Identity” Home Network

iFC

8.200 OK

4. 200 OK

4. 200 OK

1. BYE

7. Parallel scenario from step 3 to step 6 towards User C

UE-C answers

5. INVITE (UE-B)

3. CCA (terminate)

End Credit Control

2. CCR (terminate, service = CDIV, USU)

OCS

1. BYE

AS

S-CSCF

UE-B Home Network

1. BYE (User C)

1. BYE

4. 200 OK

4. 200 OK

9. CANCEL (User B)

8.200 OK

5. INVITE (UE-B)

4. CCA (initial, GSU)

Reserve units for FA towards user B and user C

3. CCR (initial, service = FA, ICID-B, RSU)

AS

UE C

12. ACK

1. INVITE (Pilot Identity)

1. INVITE (Pilot Identity)

UE B

OCS

S-CSCF

“Pilot Identity” Home Network

iFC

11.487 (Request Terminated)

15.200 OK

New Units requested

13. CCR (update, USU)

14. CCA (update, GSU)

15.200 OK

SIP signalling

6. 200 OK

New Units requested

7. CCR (update, USU)

8. CCA (update, GSU)

6. 200 OK

1. INVITE (User B, CUG information)

1. INVITE (User B)

5. SIP signalling

6. 200 OK

2. Check on request validity regarding CUG

1. INVITE (User B, CUG Information)

1. INVITE (User B, CUG Information)

1. INVITE (User B, CUG information)

4. CCA (initial, GSU)

Reserve units for CUG towards user B

3. CCR (initial, service = CUG, RSU)

UE A

UE B

OCS

1. INVITE

AS

S-CSCF

Originating UE-A Home Network

2. Check on request validity regarding CUG

1. INVITE (User B)

iFC for A

Terminating UE-B Home Network

SIP signalling

6. 200 OK

New Units requested

7. CCR (update, USU)

8. CCA (update, GSU)

6. 200 OK

5. SIP signalling

6. 200 OK

1. INVITE (User B)

4. CCA (initial, GSU)

Reserve units for incoming CUG for user B

3. CCR (initial, service = CUG, RSU)

OCS

AS

S-CSCF

iFC for B