## Slide 1: Progress of SON in RAN3
RAN3-SA5 session on SON
January 20, 2010 Valencia, Spain
Dino Flore
RAN3 Chairman

## Slide 2: Outline
Rel-9 Progress on SON
Rel-10 Objectives on SON

## Slide 3: Rel-9 Progress
SON functionalities developed in Rel-9:
  Mobility Load Balancing (MLB)
  Mobility Robustness Optimization (MRO)
  RACH optimization
  Energy saving

## Slide 4: Rel-9 Progress: MLB
Intra-RAT
  Introduced the Composite Available Capacity concept allowing neighbor eNBs to exchange the overall available resource level over X2
  Introduced framework for mobility parameters negotiation over X2
    The functionality allows an eNB to communicate/request a change of mobilty parameters from/to its neighbors
    New X2-AP procedure: Mobility Settings Change
Inter-RAT
  Working assumption to use RIM to exchange load information across RATs
    Pending GERAN2/CT4/SA2 assessment on the feasibility of the approach
  For exchanges from E-UTRAN to GERAN/UTRAN the LTE load definition should be the same as for the intra-RAT case (Composite Available Capacity)
    Extension needed to RIM container (GERAN2)

## Slide 5: Rel-9 Progress: MRO
Introduced framework that allows neighbor eNBs to exchange information related to RLFs that occurred due to Too Early Handovers, Too Late Handovers or Handover to Wrong Cell
  Two new X2-AP procedures: Radio Link Failure Indication, Handover Report
This detection mechanism is carried out through the following procedures
  [Too Late HO] If the UE attempts to re-establish the radio link at eNB B after a RLF at eNB A then eNB B may report this RLF event to eNB A by means of the RLF Indication Procedure.
  [Too Early HO] eNB B may send a HANDOVER REPORT message indicating a Too Early HO event to eNB A when eNB B receives an RLF Indication from eNB A and if eNB B has sent the UE Context Release message to eNB A related to the completion of an incoming HO for the same UE within the last Tstore_UE_cntxt seconds.
  [HO to Wrong Cell] eNB B may send a HANDOVER REPORT message indicating a HO To Wrong Cell event to eNB A when eNB B receives an RLF Indication from eNB C, and if eNB B has sent the UE Context Release message to eNB A related to the completion of an incoming HO for the same UE within the last Tstore_UE_cntxt seconds. The indication may also be sent if eNB B and eNB C are the same and the RLF report is internal to this eNB

## Slide 6: Rel-9 Progress: RACH optimization
RACH optimization
  Signaling support was introduced to allow neighbor eNBs to exchange their used PRACH resources over X2
    RACH resources, including frequency and root sequences, should not be used in neighbor eNBs to avoid interference and RACH collisions
    No new procedure needed
      New IEs added to X2 Setup and eNB Configuration Update procedure
Energy saving
  Introduced a mechanism in UTRAN that allows an RNC to gradually swith‐on/off the cell TX (without deleting the cell configuration)
    Mechansim to be used to switch‐on/off capacity booster cells depending on network load
  Similar discussion took place for LTE but no conclusion was reached
    Discussion postponed to next quarter

## Slide 7: RAN WIs on SON for Rel-10
[DRAFT] SON WI (RP-091401)
  LTE only
  Status: postponed to RAN#47
  Leadership: RAN3
MDT WI (RP-091423):
  LTE and HSPA
  Status: Approved in RAN#46
  Leadership: RAN2 (secondary responsibility for RAN3)
Energy saving WI (RP-091439)
  HSPA
  Status: Approved in RAN#46
  Leadeship: RAN1 (secondary responsibility for RAN3)

## Slide 8: Rel-10 SON WI
Proposed Objectives (from RP-091401):
  Coverage and Capacity Optimisation (CCO)
  Mobility Robustness Optimisation (MRO) enhancements
  Mobility Load Balancing (MLB) enhancements
    NOTE: the enhancements are meant mainly for load information and inter-RAT solution. Any other improvements in the MLB solution must first be proven to be needed for correct operability of the MLB.
  Including HeNBs into the SON framework of MLB and MRO
    NOTE:where appropriate, the solutions for HeNBs should be based on the solutions for macro. However, applicability and feasibility of these solutions in femto world must be proved first.