3GPP TSG-SA5 (Telecom Management)	S5-101176

Meeting SA5#71, 10-14 May 2010, Montreal, Canada	revision of S5-100636

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 32.153 | CR | 0002 | ( rev | - | ( Current version: | 9.0.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network | X | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | New rule for WSDL namespace URIs |
| --- | --- |
| Source to WG: ( | Ericsson |
| Source to TSG: ( | SA5 |
| Work item code: ( | OAM10 |  | Date: ( | 10/05/2010 |
| Category: ( | F |  | Release: ( | Rel-10 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | An action was taken at SA5#69 (AP SA5-69/1) to update the template according to the agreement in S5-100092. |
| Summary of change: ( | The format of a WSDL namespace URI is defined. |
| Consequences if ( not approved: | Incorrectly defined namespace URIs may cause unecessary dependencies between specifications. |
| Clauses affected: ( | Annex C.1.2.x |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

1st Modified Section

#### C.1.2.x	Namespaces

The WSDL namespace URI shall follow the naming convention:

http://www.3gpp.org/ftp/specs/archive/32_series/IRPNumber#ResourceName

with:

- IRPNumber being the number before the 3GPP document version number, corresponding to the 3GPP document which describes the resource,

- ResourceName being a mnemonic for the resource.

Examples:

If the 3GPP document "3GPP TS 32.111-7 V9.0.0 (2009-12)" describes the resource “AlarmIRPSystem”, then the WSDL namespace URI shall be
http://www.3gpp.org/ftp/specs/archive/32_series/32.111-7#AlarmIRPSystem

If the 3GPP document "3GPP TS 32.127 V9.0.0 (2009-12)" describes the resource “AAMIRPData”, then the WSDL namespace URI shall be
http://www.3gpp.org/ftp/specs/archive/32_series/32.127#AAMIRPData

End of Modified Section

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.