3GPP TSG-SA5 (Telecom Management)	S5-101549

Meeting SA5#71, 10-14 May 2010, Montreal, Canada	revision of S5-101537

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 32.581 | CR | 0007 | ( rev | - | ( Current version: | 10.0.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network | X | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Missing Requirement for an operator’s defined time period at the HNB |
| --- | --- |
| Source to WG: ( | Nokia Siemens Networks |
| Source to TSG: ( | SA5 |
| Work item code: ( | OAM10 |  | Date: ( | 14/05/2010 |
| Category: ( | F |  | Release: ( | Rel-10 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | TS 22.220 requires in clause 5.2 for HNB: “If the connection between H(e)NB and the rest of the operator network is out of service, then it shall be possible within an operator’s defined time period for the H(e)NB to deactivate the air-interface.” A related requirement is missing in TS 32.581 |
| Summary of change: ( | The requirement »operator’s defined time period at the HNB to deactivate the air-interface in case of lost connection between HNB and the rest of the operator network« is added to TS 32.581 |
| Consequences if ( not approved: | Inconsistency with 3GPP standardization documents TS 22.220 and TS 33.320 |
| Clauses affected: ( | 2 and 6.1.1 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  | X |  | O&M Specifications | 32.581 |
| Other comments: ( |  |

1st Modified Section

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 32.821: "Study of Self-Organizing Network (SON) related OAM for Home NodeB".

[2] 	3GPP TS 25.467: "UTRAN architecture for 3G Home NodeB, stage 2".

[3] 	TR-069 Amendment 2, CPE WAN Management Protocol v1.1, Broadband Forum

[4] 	TR-106 Amendment 2 Data Model template for TR-069-Enabled Devices v1.1, Broadband Forum.

[5] 	TR-196 FAP Access Point Service Data Model v1.00, Broadband Forum.

[6] 	3GPP TS 32.435: "Performance Measurement, eXtensible Markup Language (XML) file format definition".

[7] 	3GPP TS 32.111-2: "Telecommunication management; Fault Management; Alarm Integration Reference Point (IRP): Information Service (IS) ".

[8]	3GPP TS 32.101: "Telecommunication management; Principles and high level requirements".

[9]	3GPP TS 32.102: "Telecommunication management; Architecture".

[10] 	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[11]	3GPP TS 22.220: " Service requirements for Home Node B (HNB) and Home eNode B (HeNB)".

End of 1st Modified Section

2nd Modified Section

### 6.1.1	Configuration Management

The requirements for configuration management are as follows:

REQ-OAMP_CM-FUN-001 The HNB configuration shall be administered by the HMS utilising the TR-069 CWMP Protocol, reference [3].

REQ-OAMP_CM-FUN-002 The HNB Information Model used by the HMS for Configuration Management shall be based on the following:

a. Broadband Forum TR-106 Amendment 2 Data Model [4]

b. FAP Access Point Service Data Model [5]

REQ-OAMP_CM-FUN-003 HMS shall be able to reboot the HNB.

REQ-OAMP_CM-FUN-004 HMS shall have remote access to the HNB to start/stop the radio transmission.

REQ-OAMP_CM-FUN-005 HMS shall have remote access to the HNB to start/stop the radio transmission on the frequencies specified by HMS.

REQ-OAMP_CM-FUN-006 HMS shall maintain the configuration data of the HNB.

REQ-OAMP_CM-FUN-007 When the HNB is initially powered up and connected to the HMS, HMS shall send the initially needed configuration data to the HNB.

REQ-OAMP_CM-FUN-008 If the inner IPsec tunnel IP address of the HNB changes and HNB is connected to HMS via IPsec Tunnel then the HNB shall notify the HMS using TR-069.

REQ-OAMP_CM-FUN-009 The HMS shall specify which parameters it needs to be notified of when the HNB changes their values through auto-configuration. The HNB shall notify the HMS of changes in the values of any such auto-configured parameters.

REQ-OAMP_CM-FUN-010 The HNB shall inform the HMS of its ability to auto-configure parameters or groups of parameters that are relevant to the HMS.

REQ-OAMP_CM-FUN-011 HMS shall be able to specify a value, or a valid range of values, for any parameter that is auto-configurable by the HNB.

REQ-OAMP_CM-FUN-012 Configuration management capability for the HNB shall be supported by means of TR-069 RPCs SetParameterValues, AddObject and DeleteObject. Optionally a bulk configuration management file may be supported. In this case the TR-069 manager uses the RPC download method to trigger a CM file download from a file server.

REQ-OAMP_CM-FUN-013 The HNB shall be able to inform the HMS of the changes in radio environment.

REQ-OAMP_CM-FUN-014 The HNB shall provide a capability allowing the HMS to manage downloading of HNB software/firmware image files and provide mechanisms for version identification and notification to the HMS of the success or failure of a file download.

REQ-OAMP_CM-FUN-015 The HNB shall support capabilities to inform the HMS about the results of specific actions triggered by the HMS.

REQ-OAMP_CM-FUN-016 It shall be possible to initiate a management connection at the request of either the HNB or the HMS.REQ-OAMP_CM-FUN-017 If the HNB is unable to offer service for an operator configured time period it will deactivate the air interfac.

End of 2nd Modified Section

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.