3GPP TSG-SA5 (Telecom Management)	S5e100039

Meeting SA5#71, 10-14 May 2010, Montreal, Canada	revision of S5e100020

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 32.594 | CR | 0001 | ( rev | - | ( Current version: | 9.0.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network | X | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Remove unused reference and wrong keyword, and modify editorial errors. |
| --- | --- |
| Source to WG: ( | ETRI |
| Source to TSG: ( | SA5 |
| Work item code: ( | OAM10 |  | Date: ( | 14/05/2010 |
| Category: ( | D |  | Release: ( | Rel-10 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | 1. Some abbreviations related to XML are missing. 2. Errors in abbreviation. 3. Obsolete keyword UMTS in keywords 4. Unused references in the main text and skipped reference number 5. 5. No reference to ISO 8601 in reference section 6. Other trivial editorial errors in Table 4.1 and Table 5.1 |
| Summary of change: ( | 1. Addition of some abbreviations related to XML. 2. Correction of errors in abbreviation. 3. Removal of obsolete keyword UMTS in keywords 4. Making void of unused reference and missing reference number 5. 5. Addition of new reference to ISI 8601 in reference section and related sentence. 6. Clean up of trivial editorial errors in Table 4.1 and Table 5.1. |
| Consequences if ( not approved: | Incomplete spec. with unused references, wrong keywords, and editorial errors. |
| Clauses affected: ( | Keywords, 2, 3.2, 4.1, 5.1 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

1st modifications

## 3.2	Abbreviations

For the purposes of the present document, the abbreviations given in TR 21.905 [1] and the following apply. An abbreviation defined in the present document takes precedence over the definition of the same abbreviation, if any, in TR 21.905 [1].

CM	Configuration Management

DM	Domain Manager

DTD	Document Type Definition

EM	Element Manager

HMS	Home NodeB Management System

HeMS	Home eNodeB Management System

HNB	Home NodeB

HeNB	Home eNodeB

IP	Internet Protocol

LTE	Long Term Evolution

MME	Mobility Management Entity

NGMN	Next Generation Mobile Networks

OAM	Operations, Administration and Maintenance

PM	Performance Management

PnP		Plug and Play

SAE	System Architecture Evolution

SON	Self-Organising Networks

UMTS	Universal Mobile Telecommunications System

UTC	Universal Time Coordinated

UTRAN	UMTS Radio Access Network

XML	eXtensible Markup Language

2nd modifications

Keywords

Management, LTE

3rd modifications

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	void

[3]	void

[4]	3GPP TS 32.300: "Telecommunication management; Configuration Management (CM); Name convention for Managed Objects".

[5]	void

[6]	void

[7]	void

[8]	3GPP TS 32.435: “Telecommunication management; Performance measurement: eXtensible Markup Language (XML) file format definition”

[9]	3GPP TS 32.592: “Information model for Type 1 interface HeNB to HeNB Management System (HeMS)”

[10]	void

[11]	void

[12]	void

[13]	W3C REC-xmlschema-2-20010502: "XML Schema Part 2: Datatypes".

void

[15]	WT-157, Component Objects for CWMP, Broadband Forum

[16] 		TR-098 Amendment 2, “Internet Gateway Device Data Model for TR-069”, Broadband Forum

[17]	void

[18]	TR-196 Amendment 1, “Femto Access Point Service Data Model”, Broadband Forum

[19]	ISO 8601:2004(E)  "Data elements and interchange formats — Information interchange — Representation of dates and times", ISO

4th modifications

## 4.1	File content description

Table 4.1 lists all the file content items, provides and explanation of the individual items, and maps the file content items to those used in the XML schema based file format definitions. XML tag attributes are useful where data values bind tightly to its parent element. They have been used where appropriate.

Table 4.1 File Content Description and Mapping of File Content Items to XML tags

| File Content Item | XML schema based XML tag | Description |
| --- | --- | --- |
| configDataCollection | configDataFile | This is the top-level tag, which identifies the file as a collection of config data. The file content is made up of a header ("configFileHeader"), the collection of configuration items ("configData"), and a configfile footer ("configFileFooter"). |
| configFileHeader | fileHeader | This is the configuration data file header to be inserted in each file. It includes a version indicator, the sender name, and vendor name of the sending network node. |
| configData | configData | The "configData" construct represents the sequence of zero or more configuration parameter items contained in the file. Each "configData" element contains the name of the NE ("nEId") and the list of parameters to be created, modified or deleted which pertaining to that NE The "configData" consists of DeviceData, DiagnosticsData, and FAPServiceData |
| configFileFooter | fileFooter | The configuration data file footer to be inserted in each file. It includes a time stamp, which refers to the time when the file is closed for sending to the NE. |
| fileFormatVersion | fileHeader fileFormatVersion | This parameter identifies the file format version applied by the sender. The format version defined in the present document shall be the abridged number and version of this 3GPP document (see below). The abridged number and version of a 3GPP document is constructed from its version specific full reference "3GPP […] (yyyy-mm)" by: - removing the leading "3GPP TS" - removing everything including and after the version third digit, representing editorial only changes, together with its preceding dot character - from the resulting string, removing leading and trailing white space, replacing every multi character white space by a single space character and changing the case of all characters to uppercase. e.g. "32.594 V9.0" |
| senderName | fileHeader senderName | The senderName uniquely identifies the NE or EM that assembled this alarm reporting file by its Distinguished Name (DN), according to the definitions in 3GPP TS 32.300 [4]. In the case of the NE-based approach, it is identical to the sender's "nEDistinguishedName". |
| vendorName | fileHeader vendorName | The "vendorName" identifies the vendor of the equipment that provided the measurement file. The string may be empty (i.e. string size =0) if the "vendorName" is not configured in the sender. For the XML schema based XML format, XML attribute specification "vendorName" may be absent in case the "vendorName" is not configured in the sender. |
| neId | managedElement |  |
| neUserName | managedElement userLabel | "userLabel" may be absent in case the "nEUserName" is not configured in the CM applications. |
| neDistinguishedName | managedElement localDn | The DN is split into the DN prefix and the Identifier of the Managed Object (see 3GPP TS 32.592 [9]). "localDn" may be absent in case the Identifier of the Managed Object is not configured in the CM applications |
| neSoftwareVersion | managedElement swVersion | "swVersion" may be absent in case the "nESoftwareVersion" is not configured in the CM applications. |
| Modifier | configData modifier | This element is present if the HMS is required to inform the NE whether the parameter information should be used to create, update or delete a specific object instance on the HNB. If not present the NE will assume the modification action is update |
| HNBDataParameters | configData DeviceInfo configData ManagementServer configData Time FAPService DNPrefix FAPService FAPControl FAPService AccessManagementParameters FAPService CellConfig FAPService TransportParameters FAPService LTEREMParameters FAPService GPS FAPService SecurityParameters FAPService LocationManagementParameters | These elements are present if the HMS requires to modify the specific configuration parameters The XML file format definitions implement the configuration structure and parameter definitions defined in 3GPP TS 32.592 [9] and broadband forum TR-098 Amendment 2 [16]. |
| timestamp | fileFooter dataTime |  |

5th modifications

## 5.1	Mapping table

Table 5.1 maps the PM file content items in the 3GPP TS 32.592 [9] document to those used in the XML schema based file format definitions. XML tag attributes are useful where data values bind tightly to its parent element. They have been used where appropriate.

Table 5.1 Mapping of File Content Items to XML tags

| File Content Item | XML schema based XML tag | Description |
| --- | --- | --- |
| measDataCollection | measCollecFile |  |
| measFileHeader | fileHeader |  |
| measData | measData |  |
| measFileFooter | fileFooter |  |
| fileFormatVersion | fileHeader fileFormatVersion |  |
| senderName | fileHeader dnPrefix and fileSender localDn | For the XML schema based XML format, the DN is split into the DN prefix and the Identifier of the Managed Object (see 3GPP TS 32.592 [9]). XML attribute specification "dnPrefix" may be absent in case the DN prefix is not configured in the sender. XML attribute specification "localDn" may be absent in case the Identifier of the Managed Object is not configured in the sender. |
| senderType | fileSender elementType | For the XML schema based XML format, XML attribute specification "elementType" may be absent in case the "senderType" is not configured in the sender. |
| vendorName | fileHeader vendorName | For the XML schema based XML format, XML attribute specification "vendorName" may be absent in case the "vendorName" is not configured in the sender. |
| collectionBeginTime | measCollec beginTime | 3GPP TS 32.592 [9] clause 6.3.2.1 Periodic Statistics “ReportStartTime” |
| neId | managedElement |  |
| neUserName | managedElement userLabel | For the XML schema based XML format, XML attribute specification "userLabel" may be absent in case the "nEUserName" is not configured in the CM applications. Not used in HeNB PM file |
| neDistinguishedName | fileHeader dnPrefix and managedElement localDn | For the XML schema based XML format, the DN is split into the DN prefix and the Identifier of the Managed Object (see 3GPP TS 32.592 [9]). XML attribute specification "localDn" may be absent in case the Identifier of the Managed Object is not configured in the CM applications. |
| neSoftwareVersion | managedElement swVersion | For the XML schema based XML format, XML attribute specification "swVersion" may be absent in case the "nESoftwareVersion" is not configured in the CM applications. Not used in HeNB PM file |
| measInfo | measInfo |  |
| measInfoId | measInfoId |  |
| measTimeStamp | granPeriod endTime | Calculated from the 3GPP TS 32.592 [9] clause 6.3.2.1 Periodic Statistics “ReportStartTime” + accumulation of the 3GPP TS 32.592 [9] clause 6.3.2.1 Periodic Statistics “SampleSeconds” |
| jobId | Job jobId | Not used in HeNB PM file |
| granularityPeriod | granPeriod duration | For the XML schema based XML format, the value of XML attribute specification "duration" shall use the truncated representation "PTnS" (see [13]). 3GPP TS 32.592 [9] clause 6.3.2.1 Periodic Statistics “SampleInterval” |
| reportingPeriod | repPeriod duration | For the XML schema based XML format, the value of XML attribute specification "duration" shall use the truncated representation "PTnS" (see [13]). 3GPP TS 32.592 [9] clause 6.3.1 Periodic Statistics “PeriodicUploadInterval” |
| measTypes | measTypes or measType | For the XML schema based XML format, depending on sender's choice for optional positioning presence, either XML element "measTypes" or XML elements "measType" will be used. 3GPP TS 32.592 [9] clause 6.3.2.2 Periodic Statistics “Reference” |
| measValues | measValue |  |
| measObjInstId | measValue measObjLdn | Identifier of the Managed Object (see 3GPP TS 32.592 [9]) |
| measResults | measResults or r | For the XML schema based XML format, depending on sender's choice for optional positioning presence, either XML element "measResults" or XML elements "r" will be used. Broadband Forum data Model WT-157 [15] PeriodicStatistics.SampleSet.{i}. Parameter.{i}.Values |
| suspectFlag | Suspect | Not used in HeNB PM file |
| timeStamp | measCollec endTime | 3GPP TS 32.592 [9] clause 6.3.2.1 Periodic Statistics “ReportEndTime” |
| There is no corresponding File Content Item. | measType p | An optional positioning XML attribute specification of XML element "measType" (XML schema based), used to identify a measurement type for the purpose of correlation to a result. The value of this XML attribute specification is expected to be a non-zero, non-negative integer value that is unique for each instance of XML element "measType" that is contained within the measurement data collection file. Not used in HeNB PM file |
| There is no corresponding File Content Item. | r p | An optional positioning XML attribute specification of XML element "r", used to correlate a result to a measurement type. The value of this XML attribute specification should match the value of XML attribute specification "p" of the corresponding XML element "measType" (XML schema based). Not used in HeNB PM file |

The representation of all timestamps in PM files shall follow the representations allowed by the ISO 8601 [19].

The precise format for timestamp representation shall be determined by the technology used for encoding the PM file (e.g. XML DTD, XML Schema). The choice of technology should ensure that this representation is derived from ISO 8601 [19]. Based on the representation used, the timestamp shall refer to either UTC time or local time or local time with offset from UTC.

End of modifications

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.