3GPP TSG-SA5 (Telecom Management)	S5-110411

SA5#75, 24 - 28 Jan 2011; Sorrento, Italy	revision of S5-110165

| CR-Form-v9.7 |
| --- |
| CHANGE REQUEST |
| ( | 32.426 | CR | 0037 | ( rev | 1 | ( Current version: | 10.2.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Add combined TA/LA update related measurements |
| --- | --- |
| Source to WG: ( | ZTE |
| Source to TSG: ( | S5 |
| Work item code: ( | OAM10 |  | Date: ( | 28/01/2011 |
| Category: ( | B |  | Release: ( | Rel-10 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) |
| Reason for change: ( | The CS fallback (CSFB) in EPS enables the provision of voice and other CS-domain services by reuse of the CS infrastructure. When a CS fallback capable UE is EPS/IMSI attached, it initiates the combined TA/LA procedure based on the triggers specified in TS 23.401 and when a CS fallback and/or SMS over SGs capable UE is not EPS/IMSI attached, it may initiate a combined TA/LA procedure in order to use CS Fallback or SMS over SGs services. If a CSFB capable user fails to perform the combined TA/LA update procedure, the user may not be able to use the CS-domain services, and if the success rate is low the user experience would be bad. So it is necessary to define combined TA/LA update procedure related measurements to evaluate the combined TA/LA update performance of EPC network by calculating the success rate. |
| Summary of change: ( | 1) Add the related reference 2) Add combined TA/LA update related measurements 3) Add use case of combined TA/LA update related measurements |
| Consequences if ( not approved: |  |
| Clauses affected: ( | 2, 4.1.12(new), A.X(new) |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

First change

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication and/or edition number or version number) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TS 32.401: "Telecommunication management; Performance Management (PM); Concept and requirements".

[2]	3GPP TS 32.600: "Telecommunication management; Configuration Management (CM); Concept and high-level requirements".

[3]	3GPP TS 24.301: " Technical Specification Group Core Network and Terminals; Non-Access-Stratum (NAS) protocol for Evolved Packet System (EPS); Stage 3".

[4]	3GPP TS 29.274: "Evolved General Packet Radio Service (GPRS); Tunnelling Protocol for Control plane (GTPv2-C); Stage 3".

[5]	3GPP TS 23.401: "General Packet Radio Service (GPRS) enhancements for Evolved Universal Terrestrial Radio Access Network (E-UTRAN) access (Release 8)".

[6]	3GPP TS 29.274: " Tunnelling Protocol for Control plane (GTPv2-C)".

[7]	3GPP TS 29.281: "GPRS Tunnelling Protocol User Plane (GTPv1-U)".

[8]	3GPP TS 36.414: "Evolved Universal Terrestrial Access Network (E-UTRAN); S1 data transport".

[9]	3GPP TS 29.272: "Mobility Management Entity (MME) and Serving GPRS Support Node (SGSN) related interfaces based on Diameter protocol".

[10]	3GPP TS 23.203: "Policy and charging control architecture".

[11]	3GPP TS 36.413: "Evolved Universal Terrestrial Radio Access Network (E-UTRAN); S1 Application Protocol (S1AP)".

[12]	3GPP TS 36.412: "Evolved Universal Terrestrial Access Network (E-UTRAN);  S1 signaling transport".

[13]	3GPP TS 23.402: "Architecture enhancements for non-3GPP accesses".

[14]	IETF RFC 5136: "Defining Network Capacity".

[15]		3GPP TS 23.246: "Multimedia Broadcast Multicast Service (MBMS); Architecture and functional description".

[16]	3GPP TS 36.445: "Evolved Universal Terrestrial Radio Access Network (E-UTRAN); M1 data transport".

[X]	3GPP TS 23.272: Circuit Switched (CS) fallback in Evolved Packet System (EPS); Stage 2

Next change

### 4.1.12	Combined TA/LA update procedure

The three measurement types defined in this clause are subject to the "2 out of 3 approach".

#### 4.1.12.1	Attempted Combined TA/LA update `

- This measurement provides the number of attempted Combined TA/LA update procedures.

- CC.

- Receipt of "TRACKING AREA UPDATE REQUEST" message from a UE with the Update Type indicates that this is a combined Tracking Area/Location Area Update Request or a combined Tracking Area/Location Area Update with IMSI attach Request (TS 23.272 [17]).

- A single integer value per measurement type defined in e).

- MM.CmbTauLauAtt

- MMEFunction

- Valid for packet switching.

- EPS.

#### 4.1.12.2	Successful Combined TA/LA update

- This measurement provides the number of successfully performed Combined TA/LA update procedure.

- CC.

- Transmission of a "TRACKING AREA UPDATE ACCEPT" message with the LAI information element and without EMM cause information element to the UE, in response to a "TRACKING AREA UPDATE REQUEST" message in which the Update Type information element indicated to the MME that it is a Combined TA/LA update. If the "TRACKING AREA UPDATE ACCEPT" message is caused by a retransmission, this will not cause the counter to be increased. (TS 24.301 [3]).

- A single integer value per measurement type defined in e).

- MM. CmbTauLauSucc

- MMEFunction

- Valid for packet switching.

- EPS.

#### 4.1.12.3	Failed Combined TA/LA update

- This measurement provides the number of failed Combined TA/LA update procedure. The measurement is split into subcounters per the reject cause.

- CC

- Transmission of a “TRACKING AREA UPDATE REJECT” message to the UE; or Transmission of a "TRACKING AREA UPDATE ACCEPT" message with no EMM cause and LAI information element or with EMM cause information element to the UE, in response to a "TRACKING AREA UPDATE REQUEST" message in which the Update Type information element indicated to the MME that it is a Combined TA/LA update (TS 24.301 [3]).,

- A single integer value per measurement type defined in e).

- MM. CmbTauLauFail

- MMEFunction

- Valid for packet switching

- EPS.

Next change

# A.X	Use case for combined TA/LA update procedure related measurements

The CS fallback (CSFB) in EPS enables the provision of voice and other CS-domain services by reuse of the CS infrastructure. When a CS fallback capable UE is EPS/IMSI attached, it initiates the combined TA/LA procedure based on the triggers specified in TS 23.401 and when a CS fallback and/or SMS over SGs capable UE is not EPS/IMSI attached, it may initiate a combined TA/LA procedure in order to use CS Fallback or SMS over SGs services.If a CSFB capable user fails to perform the combined TA/LA update procedure, the user may not be able to use the CS-domain services, and if the success rate is low the user experience would be bad. So it is necessary to define combined TA/LA update procedure related measurements to evaluate the combined TA/LA update performance of EPC network by calculating the success rate.

End of changes

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.