3GPP TSG-SA5 (Telecom Management)	S5-110441

SA5#75, 24 - 28 Jan 2011; Sorrento, ITALY	revision of S5-110206

| CR-Form-v9.7 |
| --- |
| CHANGE REQUEST |
| ( | 32.551 | CR | 0003 | ( rev | 1 | ( Current version: | 10.0.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network | X | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Modify the requirements about traffic threshold and time duration for Energy Saving Management (ESM) |
| --- | --- |
| Source to WG: ( | ZTE |
| Source to TSG: ( | S5 |
| Work item code: ( | OAM-ES |  | Date: ( | 28/01/2011 |
| Category: ( | F |  | Release: ( | Rel-10 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) |
| Reason for change: ( | The thresholds mentioned in requirements REQ-DIES-FUN-06 and REQ-DIES-FUN-07 shall work together, putting them in separate requirements will lead to misunderstanding. |
| Summary of change: ( | Merge the requirements REQ-DIES-FUN-06 and REQ-DIES-FUN-07. |
| Consequences if ( not approved: | The user of the specification will be misled. |
| Clauses affected: ( | 6.1.4 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

First change

### 6.1.4	Requirements for Distributed ES

REQ-DIES-FUN-01

The IRP Agent shall be able to allow the IRPManager to define a list of cells to prevent them from going into energySaving state.

REQ-DIES-FUN-02

The IRPAgent shall provide the IRPManager the possibility to define that a cell is prohibited to be reconfigured for Energy Saving purposes.

Note: This requirement applies for the capacity limited use case.

REQ-DIES-FUN-03

The IRPAgent should support a capability allowing the IRPManager to define a traffic threshold and a time duration: If the traffic in the active neighbor cells is above this threshold longer than this time duration, then the cell can leave the energySaving state.

REQ-DIES-FUN-04

The IRPAgent shall provide the capability to allow the IRPManager to configure one or more related cells as the candidate cells to take over the coverage when the original cell is going into energySaving state.

This requirement applies for the eNodeB overlaid use case.

REQ-DIES-FUN-05

The IRPAgent shall provide a capability to allow the IRPManager to indicate cell outage of an overlay cell that is a candidate cell that can take over the coverage for another cell.

This requirement applies for the use case eNodeB overlaid.

REQ-DIES-FUN-06

The IRPAgent should support a capability allowing the IRPManager to define a traffic threshold (threshold1) for the cell, a traffic threshold (threshold2) for the neighbour cells and a time duration; if the traffic in the cell is below this threshold1 longer than this time duration and the traffic in active neighbor cells is below this threshold2 longer than this time duration, then the cell can enter the energySaving state.

Editor’s note: 
Details of the traffic thresholds will be defined in stage 2.

REQ-DIES-FUN-07

Void

REQ-DIES-FUN-08

The IRPAgent should support a capability allowing the IRPManager to define in a uniform way on subnetwork level or for many cells the circumstances when entering or leaving the energy saving is allowed.

REQ-DIES-FUN-09

IRPManager shall be able to enable and disable energy saving for a selected part of the network.

End of changes

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.