Third Generation Partnership Project (3GPP™)

Meeting Report
for
TSG SA WG5
meeting: 93

Guangzhou, China, 20/01/2014 to 24/01/2014

this draft:  Tuesday, (2014-02-04) 10:34  [date/time according to secretary's PC time zone setting]

TABLE OF CONTENTS

1	Opening of the meeting	3

2	Approval of the agenda	3

3	IPR declaration	3

4	Meetings and activities reports	3

4.1	Last SA5 meeting report	3

4.2	Last SA meeting report	4

4.3	Inter-organizational reports	4

5	Cross-SWG issues	5

5.1	Administrative issues at SA5 level	5

5.2	Technical issues at SA5 level	7

5.3	Liaison statements at SA5 level	7

5.4	SA5 meeting calendar	7

5.5	Review of the Work Plan	7

5.6	Joint meeting SA1/SA5 on RAN sharing	8

6	OAM&P	8

6.1	OAM&P Plenary	8

6.2	New Work Item proposals - OAM&P & Converged Management	9

6.3	Maintenance and Rel-12 small Enhancements - OAM&P & Converged Management	11

6.4	OAM&P 12 Network Infrastructure Management	18

6.4.1	Network Management for 3GPP Interworking WLAN - NIM part	18

6.4.2	Alarm quality improvements	18

6.5	OAM&P 12 Performance Management	18

6.5.1	Network Management for 3GPP Interworking WLAN - PM part	18

6.5.2	Energy Efficiency related Performance Measurements	19

6.6	OAM&P 12 Self-Organizing Networks (SON) - OAM aspects	19

6.6.1	TR Study on Enhanced Network Management (NM) centralized Coverage and Capacity Optimization	19

6.6.2	Enhanced Network Management (NM) centralized Coverage and Capacity Optimization	24

6.7	OAM&P 12 WLAN Management	24

6.7.1	TR on WLAN impacts to Type-2 management interface to the 3GPP Network Manager	24

6.7.2	WLAN Network Resource Model for Type-2 interface	26

6.7.3	WLAN measurements defined in IEEE and IETF WLAN performance measurements for use on Type-2 interface	26

6.8	OAM&P 12 Network Sharing	26

6.8.1	OAM aspects of Network Sharing - Concepts and requirements (Stage 1)	27

6.8.2	OAM aspects of Network Sharing - Stage 2/3	28

6.9	OAM&P Studies	28

6.9.1	Study on management of Heterogeneous Networks	28

6.9.2	Study on Enhancements of OAM aspects of Distributed Mobility Load Balancing (MLB) SON function	30

6.9.3	Study on Application and Partitioning of Itf-N	33

7	Converged Management	34

7.1	Converged Management Plenary	34

7.2	OAM&P 12 Compliance of 3GPP SA5 specifications to the NGMN Top OPE Recommendations	36

7.2.1	TR on compliance of 3GPP SA5 specifications to the NGMN Top OPE Recommendations	37

7.2.2	TS work on Compliance of 3GPP SA5 specifications to the NGMN Top OPE Recommendations	39

7.3	OAM&P 12 Compliance of 3GPP SA5 specifications to the NGMN NGCOR Requirements	41

7.3.1	TR on compliance of 3GPP SA5 specifications to the NGMN NGCOR Requirements	41

7.3.2	Converged Management Model alignment Phase 2	42

7.3.3	Converged Management PM Interface definitions	42

8	Charging	43

8.1	Charging Plenary	43

8.2	New Charging Work Item proposals	48

8.3	Charging Maintenance and Rel-12 small Enhancements	48

8.4	Rel-12 Charging	60

8.4.1	Short Message Service - Service Centre (SMS-SC) Offline Charging	60

8.4.2	Charging per IP-Connectivity Access Network (IP-CAN) Session	63

8.4.3	Charging using an Alternative Roaming Provider	63

8.4.4	Charging for IMS centralized service (ICS) control (Stage 2/3)	66

8.5	Application Based Charging	67

8.5.1	Charging for Application Based Charging	67

8.6	BB1: Policy and Charging Control for supporting traffic from fixed terminals and NSWO (Non Seamless WLAN Offload) traffic from 3GPP UEs in fixed broadband access networks	69

8.6.1	Policy and Charging Enforcement Function (PCEF) based Charging for traffic from fixed terminals and NSWO traffic from 3GPP UEs in fixed broadband access networks	69

8.6.2	Traffic Detection Function (TDF) based Charging for traffic from fixed terminals and NSWO traffic from 3GPP UEs in fixed broadband access networks	72

8.7	Charging Studies	72

8.7.1	Study on Charging aspects on Roaming End-to-end scenarios with VoLTE IMS and interconnecting networks	72

9	Any Other Business	74

10	Closing of the meeting	74

Annex A: List of contribution documents	75

Annex B: List of change requests	88

Annex C: Lists of liaisons	96

C1: Incoming liaison statements	96

C2: Outgoing liaison statements	96

Annex D: List of agreed/approved new and revised Work Items	97

Annex E: List of action items	98

Annex F: List of decisions	99

Annex G: List of participants	100

Annex H: List of future meetings	102

Note: Hyperlinks to tdocs will work only if the present report is in a subdirectory named "report" and the tdocs themselves are in a parallel subdirectory names "docs".

## 1	Opening of the meeting

## 2	Approval of the agenda

S5-140000	Agenda
					Source: WG Chairman

Abstract:

-

Decision: 		The document was approved.

## 3	IPR declaration

S5-140039	IPR declaration
					Source: WG Chairman

Abstract:

-

Decision: 		The document was noted.

## 4	Meetings and activities reports

### 4.1	Last SA5 meeting report

S5-140001	Report from last SA5 meeting
					Source: MCC

Abstract:

-

Discussion:

Review of Action Points from SA5#92:

Chair: Error: All APs have the same number (92/1). MCC to remedy error.

Chair: APs 2,3 closed all the other remain ONGOING.

Closed APs:

92/1	Update draft TS of TS 28.601 to remove the editor’s notes, and send for email approval	Gang Chen

92/1	Update draft TS of TS 28.611 to remove the editor’s notes, and send for email approval	Gang Chen

Decision: 		The document was approved.

### 4.2	Last SA meeting report

S5-140002	SA5 status report at last SA meeting
					Source: WG Chairman

Decision: 		The document was noted.

S5-140003	SA5 results at last SA meeting
					Source: WG Chairman

Abstract:

SA#62:

SP 130685 LS from SA5 to ETSI ISG NFV on Management of Virtualized Network

The TSG SA Chairman outlined the intention to have 3GPP presence at the NFV meeting and to try to have a holistic overview of the NFV work in different bodies. An invitation to the NFV leadership to attend the next TSG SA meeting will also be extended. Delegates were asked to come prepared for discussion on this topic at TSG SA#63. This was then noted.

Discussion:

The 3GPP TSG SA and SA5 Chairs will attend the NFV meeting  in Feb 2014 and will try to have a holistic overview of the NFV work in different bodies.

Decision: 		The document was noted.

### 4.3	Inter-organizational reports

S5-140042	SA5 presentation at M-SDO plenary on Dec 6th 2013
					Source: WG Chairman

Abstract:

-

Decision: 		The document was noted.

S5-140043	Minutes M-SDO plenary on Dec 6th 2013 WG Chairman
					Source: WG Chairman

Abstract:

-

Decision: 		The document was noted.

S5-140216	Other presentations at M-SDO plenary on Dec 6th 2013
					Source: WG Chairman

Abstract:

-

Decision: 		The document was noted.

## 5	Cross-SWG issues

### 5.1	Administrative issues at SA5 level

S5-140007	Leaders meeting agenda
					Source: WG Chairman

Abstract:

1 - Quality

•	CR quality checks (S5-140017).

•	Compliance with 3GPP TR 21.801 “Specification drafting rules”: status of ongoing draft TSs/TRs and planning of quality check sessions.

•	Figures in specs should be editable (UML diagram format & tools): follow-up from the discussion with MCC at SA5#89 (see S5-131044 from SA#89). AP MCC to check available free UML tools (ongoing).

•	Definition of action plan for references to external and non-public documents in 3GPP specs (see S5-131044 from SA#89).First step: make an inventory and list issues (chair helped by TS Rapporteurs and MCC). Second step: fix issues (TS Rapporteurs produce CRs).

2 - Working procedures

•	IS-SS version link (general principles, contradicting CRs, etc): organization of breakout session.

•	Process for allocation of spec number.

3 - SA

•	Deliverables to next SA meeting (S5-140018).

4 - Meeting calendar

•	Aruba meeting.

•	SA5 meeting calendar (S5-140013).

5 - NGCOR/Multi-SDO

•	Debriefing M-SDO F2F plenary December 2013.

•	M-SDO meeting calendar.

6 - AOB

•	CH SWG will start on Monday 08:45 until mid-2014 (after this the need will have to be confirmed). SA5 Chair sent this information for SA5 #93, #94, #95, and #96.

•	SA5 checklist on MCC/chair work split: update to be done for SA5#94.

Decision: 		The document was noted.

S5-140008	Leaders meeting minutes
					Source: WG Chairman

Abstract:

-

Decision: 		The document was noted.

S5-140014	SA5 Working Procedures
					Source: WG Chairman

Abstract:

-

Decision: 		The document was noted.

S5-140015	SA5 Meeting Facility Requirements
					Source: WG Chairman

Abstract:

-

Decision: 		The document was noted.

S5-140016	Process for management of draft TSs/TRs
					Source: WG ViceChair

Abstract:

-

Decision: 		The document was noted.

S5-140017	CR Quality Check
					Source: MCC (az)

Abstract:

-

Decision: 		The document was noted.

S5-140028	Reserved
					Source: MCC

Abstract:

-

Decision: 		The document was [not addressed].

### 5.2	Technical issues at SA5 level

### 5.3	Liaison statements at SA5 level

### 5.4	SA5 meeting calendar

S5-140013	SA5 Meeting Calendar
					Source: WG Chairman

Abstract:

-

Decision: 		The document was noted.

### 5.5	Review of the Work Plan

S5-140018	Deliverables due for the NEXT SA Plenary
					Source: MCC

Abstract:

-

Decision: 		The document was revised to S5-140222.

S5-140222	Deliverables due for the NEXT SA Plenary
					Source: MCC

(Replaces S5-140018)

Decision: 		The document was noted.

S5-140019	SA5 WIDs
					Source: WG Chairman

Abstract:

-

Decision: 		The document was noted.

S5-140020	SA5 3GPP Work Plan
					Source: MCC

Abstract:

-

Decision: 		The document was noted.

S5-140219	SA5 work plan status after SA5#93
					Source: WG Chairman

Abstract:

-

Decision: 		The document was [not addressed].

### 5.6	Joint meeting SA1/SA5 on RAN sharing

## 6	OAM&P

### 6.1	OAM&P Plenary

S5-140004	Time Plan for OAM&P and Converged Management SWGs
					Source: WG Chairman

Abstract:

-

Decision: 		The document was revised to S5-140225.

S5-140225	Time Plan for OAM&P and Converged Management SWGs
					Source: WG Chairman

(Replaces S5-140004)

Discussion:

S5-140225d4 is the final version

Decision: 		The document was noted.

S5-140005	OAM Executive Report from THIS Meeting
					Source: OAM SWG Chair

Abstract:

-

Decision: 		The document was revised to S5-140297.

S5-140297	OAM Executive Report from THIS Meeting
					Source: OAM SWG Chair

(Replaces S5-140005)

Decision: 		The document was noted.

S5-140021	Minutes of OAM&P Plenary
					Source: Rapporteur

Abstract:

-

Discussion:

MCC to remove from the next meeting's ADN the "Minutes of OAM&P Plenary" was postponed for the next leaders' meeting in SA5#94.

Decision: 		The document was withdrawn.

S5-140191	Reply LS from GSMA IREG to 3GPP CT4 cc SA5 on FQDNs to support Multi-vendor Plug and Play (MvPnP) feature
					Source: GSMA IREG

Abstract:

Reply LS from GSMA IREG to CT4 (cc: SA5) on FQDNs to support Multi-vendor Plug and Play (MvPnP) feature.

CT4 requested GSMA IREG to endorse new FQDN formats defined in 23.003CR#0365.

GSMA IREG endorsed these new FQDNs and observed that the proposed sub-domains belong to OAM System Realm/Domain which CT4 has specified earlier, but is not yet formally endorsed by GSMA IREG and captured in IR.67.

GSMA IREG concluded to define only the OAM System realm in IR.67 and to specify its sub-domains for specific usage in TS 23.003.

CT4 may define new usages of the “oam” sub-domain without the need to inform GSMA IREG

Decision: 		The document was noted.

S5-140241	Report from Breakout session on IS-SS link
					Source: WG Chairman

Decision: 		The document was noted.

S5-140242	Reply to 3GPP/SA5 Liaison Questions Regarding Performance Measurements Architecture
					Source: Broadband Forum

Decision: 		The document was noted.

### 6.2	New Work Item proposals - OAM&P & Converged Management

S5-140022	Minutes of New Work Item proposals - OAM&P & Converged Management
					Source: Rapporteur

Abstract:

-

Decision: 		The document was noted.

S5-140136	New WID Radio Planning Tool interface (OAM-RPT)
					Source: NSN

Abstract:

-

Decision: 		The document was revised to S5-140259.

S5-140259	New WID Radio Planning Tool interface (OAM-RPT)
					Source: NSN

(Replaces S5-140136)

Decision: 		The document was revised to S5-140278.

S5-140278	New WID Radio Planning Tool interface (OAM-RPTi)
					Source: NSN

(Replaces S5-140259)

Decision: 		The document was revised to S5-140363.

S5-140363	New WID Radio Planning Tool interface (OAM-RPT)
					Source: NSN

(Replaces S5-140278)

Decision: 		The document was agreed.

S5-140138	DP on New proposed WID on Radio Planning Tool interface
					Source: NSN

Abstract:

-

Discussion:

Ericsson (Robert): Some functionalities are repeated (e.g. SON capabilities).

NSN (Olaf): Additional capabilities are out of scope.

Ericsson (Robert): Is this a one-way interface (download only) ?

NSN (Olaf): Yes.

NSN (Anatoly): The intention is to standardize only the data format.

NSN (Olaf): The request is coming from the NSN people in the field rolling out equipment. Only the interface should be standardized.

ALU (Padma): Is the intention to standardize the Data format/flow and Data content ?

NSN (Olaf): Yes.

Orange (JM): How does this fit in the OAM Reference Model ? Is this a Type 4 interface or ?

Ericsson (Thomas):

Orange (JM):

Decision: 		The document was noted.

### 6.3	Maintenance and Rel-12 small Enhancements - OAM&P & Converged Management

S5-140023	Minutes of Maintenance and Rel-12 small Enhancements - OAM&P & Converged Management
					Source: MCC

Abstract:

-

Decision: 		The document was noted.

S5-140057	Rel-12 CR 32752 Add mMEForMTC attribute
					32.752	  CR-0017  (Rel-12) v..
					Source: Intel

Abstract:

-

Discussion:

NSN (Anatoly): SA5 gets here an action from an SA2, RAN3 LS exchange without SA5 involvement/consultation. The problem was not well understood based on RAN3 colleagues' opinion.

Ericsson (Robert): There is no need to add the new mMEForMTC attribute.

NSN (Anatoly):

Decision: 		The document was noted.

S5-140058	Rel-12 CR 32753 Add mMEForMTC attribute
					32.753	  CR-0010  (Rel-12) v..
					Source: Intel

Abstract:

-

Decision: 		The document was noted.

S5-140059	Rel-12 CR 32755 Add mMEForMTC attribute
					32.755	  CR-0009  (Rel-12) v..
					Source: Intel

Abstract:

-

Decision: 		The document was noted.

S5-140089	Rel-10 CR 32.766 Add missing XML elements for SON Control and SON Targets
					32.766	  CR-0060  (Rel-10) v..
					Source: Huawei

Abstract:

-

Discussion:

NSN (Yizhi): proposed change

Huawei (Kai): agree

Decision: 		The document was revised to S5-140228.

S5-140228	Rel-10 CR 32.766 Add missing XML elements for SONControl and SONTargets
					32.766	  CR-0060  rev 1 (-) v..
					Source: Huawei

(Replaces S5-140089)

Decision: 		The document was agreed.

S5-140090	Rel-11 CR 32.422 Add missing figure for RCEF reporting example scenario
					32.422	  CR-0261  (Rel-11) v..
					Source: Huawei

Abstract:

-

Discussion:

NSN (Anatoly): The figure disappeared due to a CR implementation error. This CR is re-introducing the missing figure.

Decision: 		The document was revised to S5-140229.

S5-140229	Rel-11 CR 32.422 Add missing figure for RCEF reporting example scenario
					32.422	  CR-0261  rev 1 (-) v..
					Source: Huawei

(Replaces S5-140090)

Decision: 		The document was agreed.

S5-140091	Rel-12 CR 32.422 Add missing figure for RCEF reporting example scenario
					32.422	  CR-0262  (Rel-12) v..
					Source: Huawei

Abstract:

-

Discussion:

NSN (Anatoly): The figure disappeared due to a CR implementation error. This CR is re-introducing the missing figure.

Decision: 		The document was revised to S5-140230.

S5-140230	Rel-12 CR 32.422 Add missing figure for RCEF reporting example scenario
					32.422	  CR-0262  rev 1 (-) v..
					Source: Huawei

(Replaces S5-140091)

Decision: 		The document was agreed.

S5-140096	Rel-12 CR 32.300 Removal of DN max length for 28 series (Converged Management)
					32.300	  CR-0016  (Rel-12) v..
					Source: Ericsson

Abstract:

-

Discussion:

Ericsson (Robert):

Decision: 		The document was revised to S5-140231.

S5-140231	Rel-12 CR 32.300 Removal of DN max length for 28 series  (Converged Management)
					32.300	  CR-0016  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140096)

Decision: 		The document was revised to S5-140279.

S5-140279	Rel-12 CR 32.300 Removal of DN max length for 28 series  (Converged Management)
					32.300	  CR-0016  rev 2 (-) v..
					Source: Ericsson

(Replaces S5-140231)

Decision: 		The document was agreed.

S5-140121	Rel-10 CR 32.762 Add new member in blacklist
					32.762	  CR-0101  (Rel-10) v..
					Source: Ericsson

Abstract:

This was approved as S5-131770, but was not implemented due to CR contradicting CRs.

Decision: 		The document was agreed.

S5-140122	Rel-10 CR 32.766 Add new member in blacklist
					32.766	  CR-0061  (Rel-10) v..
					Source: Ericsson

Abstract:

This contribution was agreed as S5-131771, but was not implemented due to CR contradiction.

Decision: 		The document was agreed.

S5-140126	Rel-11 CR 28.702 Correct reference and attribute properties
					28.702	  CR-0002  (Rel-11) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140234.

S5-140234	Rel-11 CR 28.702 Correct reference and attribute properties
					28.702	  CR-0002  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140126)

Decision: 		The document was agreed.

S5-140127	Rel-11 CR 28.703 Correct proceduralState attribute mapping and datatype
					28.703	  CR-0001  (Rel-11) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140235.

S5-140235	Rel-11 CR 28.703 Correct proceduralState attribute mapping and datatype
					28.703	  CR-0001  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140127)

Decision: 		The document was agreed.

S5-140156	Rel-12 CR 32.851 Editorial Cleanup
					32.851	  CR-0002  (-) v..
					Source: Alcatel-Lucent

Abstract:

-

Decision: 		The document was withdrawn.

S5-140157	Rel-12 CR 32.851 Remove hanging paragraph
					32.851	  CR-0003  (Rel-12) v..
					Source: Alcatel-Lucent

Abstract:

-

Decision: 		The document was revised to S5-140240.

S5-140240	Rel-12 CR 32.851 Remove hanging paragraph
					32.851	  CR-0003  rev 1 (-) v..
					Source: Alcatel-Lucent

(Replaces S5-140157)

Decision: 		The document was agreed.

S5-140158	Rel-9 CR 32.423 Trace Session Reference
					32.423	  CR-0077  (Rel-9) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140236.

S5-140236	Rel-9 CR 32.423 Trace Session Reference
					32.423	  CR-0077  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140158)

Decision: 		The document was agreed.

S5-140159	Rel-10 CR 32.423 Trace Session Reference
					32.423	  CR-0078  (Rel-10) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140237.

S5-140237	Rel-10 CR 32.423 Trace Session Reference
					32.423	  CR-0078  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140159)

Decision: 		The document was agreed.

S5-140160	Rel-11 CR 32.423 Trace Session Reference
					32.423	  CR-0079  (Rel-11) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140238.

S5-140238	Rel-11 CR 32.423 Trace Session Reference
					32.423	  CR-0079  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140160)

Decision: 		The document was agreed.

S5-140161	Rel-10 CR 32.423 MNC/MCC Optional
					32.423	  CR-0080  (Rel-10) v..
					Source: Ericsson

Abstract:

-

Discussion:

Need CR also for 32.422. Submit package at next meeting

Decision: 		The document was noted.

S5-140162	Rel-11 CR 32.423 MNC/MCC Optional
					32.423	  CR-0081  (Rel-11) v..
					Source: Ericsson

Abstract:

-

Discussion:

Need CR also for 32.422. Submit package at next meeting

Decision: 		The document was noted.

S5-140163	Rel-11 CR 32.423 TRSR
					32.423	  CR-0082  (Rel-11) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140239.

S5-140239	Rel-11 CR 32.423 TRSR
					32.423	  CR-0082  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140163)

Decision: 		The document was agreed.

S5-140226	Rel-11 CR 32.762 Addition of not implemented parts of S5-131772 Add new member in blacklist
					32.762	  CR-0102  (-) v..
					Source: Ericsson

Decision: 		The document was revised to S5-140232.

S5-140232	Rel-11 CR 32.762 Addition of not implemented parts of S5-131772 Add new member in blacklist
					32.762	  CR-0102  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140226)

Decision: 		The document was revised to S5-140280.

S5-140280	Rel-11 CR 32.762 Addition of not implemented parts of S5-131772 Add new member in blacklist
					32.762	  CR-0102  rev 2 (-) v..
					Source: Ericsson

(Replaces S5-140232)

Decision: 		The document was agreed.

S5-140227	Rel-11 CR 32.766 Addition of not implemented parts of S5-131772 Add new member in blacklist
					32.766	  CR-0062  (-) v..
					Source: Ericsson

Decision: 		The document was revised to S5-140233.

S5-140233	Rel-11 CR 32.766 Addition of not implemented parts of S5-131772 Add new member in blacklist
					32.766	  CR-0062  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140227)

Decision: 		The document was agreed.

### 6.4	OAM&P 12 Network Infrastructure Management

#### 6.4.1	Network Management for 3GPP Interworking WLAN - NIM part

S5-140024	Minutes for Network Management for 3GPP Interworking WLAN - NIM part (530050)
					Source: Rapporteur

Abstract:

-

Decision: 		The document was withdrawn.

#### 6.4.2	Alarm quality improvements

S5-140037	Minutes for Alarm Quality Improvements
					Source: Rapporteur

Abstract:

-

Discussion:

SWG Chair: progress 0% to 5% complete

Decision: 		The document was noted.

S5-140165	pCR for Super CR on 32111-1 Alarm mgmt definitions
					Source: Ericsson

Abstract:

-

Discussion:

Make the changes on the Rel-12 and not Rel-11 TS.

Remove in references discontinued parts 3 CORBA, & SOAP and add part 6 SS.

Do not re-use voided Reference numbers (like 15), etc.

Decision: 		The document was noted.

### 6.5	OAM&P 12 Performance Management

#### 6.5.1	Network Management for 3GPP Interworking WLAN - PM part

S5-140025	Minutes for Network Management for 3GPP Interworking WLAN - PM part (530150)
					Source: Rapporteur

Abstract:

-

Decision: 		The document was withdrawn.

#### 6.5.2	Energy Efficiency related Performance Measurements

S5-140026	Minutes for Energy Efficiency related Performance Measurements (600044)
					Source: Rapporteur

Abstract:

-

Discussion:

progress 15% to 20% complete

Decision: 		The document was noted.

S5-140187	LS from ETSI EE to SA5 on Cooperation for Energy Efficiency Measurements
					Source: ETSI EE

Abstract:

Following the ETSI EE LS to 3GPP and the SA5 reply to SP-120449 (LS on Global KPIs for energy efficiency of deployed broadband) on “Cooperation for Energy Efficiency Measurements” (S5-122600) and a joint meeting in Sophia Antipolis (29 May 2013), a constant update on the activity of the WI EEPS DES00005 was agreed.

A first liaison was sent by ETSI EE in July 2013 (EE(13)000021).

The reply from SA5 received on 25 Oct 2013 (S5-131830) indicates counters for Data Volume (DV) and states that Energy Consumption (EC) counters are not a matter to be dealt within 3GPP.

ETSI EE has positively accepted the SA5 statements, by adopting DV counters in ES 203 228 and considering that it is reasonable not to have 3GPP Energy Consumption (EC) measurements, even if it could be useful to have EC counters.

Following the agreement on SA5 request to receive the most up-to-date ES drafts together with an indication on the stable clauses, the latest draft ES 203 228 version 003 was attached

ACTION:	Resubmit at next SA5 meeting
	(action on: MCC / due by: 2014-04-01)

Decision: 		The document was postponed.

### 6.6	OAM&P 12 Self-Organizing Networks (SON) - OAM aspects

#### 6.6.1	TR Study on Enhanced Network Management (NM) centralized Coverage and Capacity Optimization

S5-140056	Rel-12 CR 32425 Add UE distribution measurements
					32.425	  CR-0147  (Rel-12) v..
					Source: Intel

Abstract:

-

Discussion:

Converted into a pCR for draft TR 32.841

Decision: 		The document was revised to S5-140246.

S5-140246	Converted to pCR TR 32.841 (was Rel-12 CR 32.425 Add UE distribution measurements)
					Source: Intel

(Replaces S5-140056)

Discussion:

Converted into a pCR for draft TR 32.841

Decision: 		The document was approved.

S5-140088	DP of 2D UE distribution
					Source: Intel

Abstract:

-

Decision: 		The document was noted.

S5-140150	pCR to TR 32.836 Study on NM CCO SON Function: measurements in 2-dim bins
					Source: Cisco

Abstract:

-

Decision: 		The document was noted.

S5-140173	Revised WID  Study on Enhanced NM Centralised Coverage and Capacity Optimisation
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140275.

S5-140275	Revised WID  Study on Enhanced NM Centralised Coverage and Capacity Optimisation
					Source: Ericsson

(Replaces S5-140173)

Decision: 		The document was revised to S5-140283.

S5-140283	Revised WID  Study on Enhanced NM Centralised Coverage and Capacity Optimisation
					Source: Ericsson

(Replaces S5-140275)

Discussion:

SWG Chair: Start with S5-140283d1 the Email approval

Decision: 		The document was for Email approval.

S5-140365	New WID on Enhanced NM Centralised Coverage and Capacity Optimisation
					Source: Ericsson

(Replaces S5-140275)

Discussion:

It was decided to split the WID into a Study in REl-12 (containing a TR) and a Rel-13 WID for the normative work.

Decision: 		The document was for Email approval and approved.

S5-140174	pCR on CCO bin evaluation for TR 32.836 Study on NM CCO SON Function
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140243.

S5-140243	pCR on CCO bin evaluation for TR 32.836 Study on NM CCO SON Function
					Source: Ericsson

(Replaces S5-140174)

Decision: 		The document was revised to S5-140281.

S5-140281	pCR on CCO bin evaluation for TR 32.836 Study on NM CCO SON Function
					Source: Ericsson

(Replaces S5-140243)

Discussion:

SWG Chair: Start with S5-140281d1 the Email approval

Decision: 		The document was for Email approval and noted.

S5-140175	pCR on Extending CCO actions for TR 32.836 Study on NM CCO SON Function
					Source: Ericsson

Abstract:

-

Decision: 		The document was noted.

S5-140176	pCR to TR 32.836 Add CCO PM triggering action
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140248.

S5-140248	pCR to TR 32.836 Add CCO PM triggering action
					Source: Ericsson

(Replaces S5-140176)

Decision: 		The document was approved.

S5-140177	pCR on Privacy clarifications for TR 32.836 Study on NM CCO SON Function
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140273.

S5-140273	pCR on Privacy clarifications for TR 32.836 Study on NM CCO SON Function
					Source: Ericsson

(Replaces S5-140177)

Decision: 		The document was approved.

S5-140178	pCR Recommendation for GERAN in TR 32.836 v1.2.1 Study on NM CCO SON Function
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140247.

S5-140247	pCR Recommendation for GERAN in TR 32.836 v1.2.1 Study on NM CCO SON Function
					Source: Ericsson

(Replaces S5-140178)

Decision: 		The document was approved.

S5-140180	pCR TR 32.836 Evaluation of correlation methods
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140282.

S5-140282	pCR TR 32.836 Evaluation of correlation methods
					Source: Ericsson

(Replaces S5-140180)

Discussion:

SWG Chair: Start with S5-140282d1 the Email approval

Decision: 		The document was for Email approval.

S5-140182	pCR TR 32.836 MLB use case recommendation
					Source: Ericsson

Abstract:

-

Decision: 		The document was noted.

S5-140185	pCR on Clarification on impact of user consent on data collection for TR 32.836 Study on NM CCO SON Function
					Source: Huawei

Abstract:

-

Decision: 		The document was revised to S5-140274.

S5-140274	pCR on Clarification on impact of user consent on data collection for TR 32.836 Study on NM CCO SON Function
					Source: Huawei

(Replaces S5-140185)

Decision: 		The document was approved.

S5-140190	Clarification on impact of user consent on data collection
					Source: Huawei

Abstract:

-

Decision: 		The document was noted.

S5-140287	Draft TR 32.836 Telecommunication management; Study on Network Management (NM) centralized Coverage and Capacity Optimization (CCO) Self-Organizing Networks (SON) function
					Source: Ericsson

Discussion:

SWG Chair: Start with S5-140287d1 the Email approval

Decision: 		The document was for Email approval and approved.

#### 6.6.2	Enhanced Network Management (NM) centralized Coverage and Capacity Optimization

S5-140027	Minutes for Enhanced NM Centralised Coverage and Capacity Optimisation (560032)
					Source: Rapporteur

Abstract:

-

Decision: 		The document was noted.

### 6.7	OAM&P 12 WLAN Management

S5-140029	Minutes for OAM&P 12 WLAN Management (560036)
					Source: Rapporteur

Abstract:

-

Discussion:

Percentage of completion:

Study on WLAN impacts to Type-2 management (560336): 75% to 80%

WLAN Network Resource Model for Type-2 interface (560136): 5% to 10%

WLAN performance measurements on Type-2 interface (560236): 5% to 5%

Decision: 		The document was noted.

#### 6.7.1	TR on WLAN impacts to Type-2 management interface to the 3GPP Network Manager

S5-140083	DP on remote monitoring
					Source: Intel

Abstract:

-

Decision: 		The document was withdrawn.

S5-140084	pCR TR 32.841 WLAN alarm notification
					Source: Intel

Abstract:

-

Discussion:

NSN (Anatoly): Annex X (informative) is not allowed, because the entire TR is an informative document and consequently cannot contain normative text. By default, the entire TR content is informative, there is no need to specify this in an annex header..

Decision: 		The document was noted.

S5-140085	pCR TR 32.841 WLAN use cases
					Source: Intel

Abstract:

-

Decision: 		The document was withdrawn.

S5-140131	pCR TR 32.841  Use Alarm IRP for reporting WLAN AP alarm
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140276.

S5-140276	pCR TR 32.841 Use Alarm IRP for reporting WLAN AP alarm
					Source: Ericsson

(Replaces S5-140131)

Decision: 		The document was revised to S5-140284.

S5-140284	pCR TR 32.841 Use Alarm IRP for reporting WLAN AP alarm
					Source: Ericsson

(Replaces S5-140276)

Decision: 		The document was approved.

S5-140220	pCR TR 32.841 WLAN use cases
					Source: Intel

Abstract:

-

Decision: 		The document was noted.

S5-140285	Draft TR 32.841 WLAN impacts on Type-2 management
					Source: Intel

Discussion:

SWG Chair: Start with S5-140285d1 the Email approval

Decision: 		The document was for Email approval and approved.

#### 6.7.2	WLAN Network Resource Model for Type-2 interface

S5-140086	pCR on 28680-001 WLAN Requirement
					Source: Intel

Abstract:

-

Decision: 		The document was revised to S5-140277.

S5-140277	pCR TS 28.680-001 WLAN Requirement
					Source: Intel

(Replaces S5-140086)

Discussion:

SWG Chair: Start with S5-140277d1 the Email approval

Decision: 		The document was for Email approval and approved.

S5-140286	Draft TS 28.680 WLAN Requirements
					Source: Intel

Discussion:

SWG Chair: Start with S5-140286d1 the Email approval

Decision: 		The document was for Email approval and approved.

#### 6.7.3	WLAN measurements defined in IEEE and IETF WLAN performance measurements for use on Type-2 interface

S5-140087	pCR on 28403-001 WLAN PM
					Source: Intel

Abstract:

-

Decision: 		The document was noted.

### 6.8	OAM&P 12 Network Sharing

S5-140038	Minutes for Network Sharing
					Source: Rapporteur

Abstract:

-

Decision: 		The document was noted.

#### 6.8.1	OAM aspects of Network Sharing - Concepts and requirements (Stage 1)

S5-140151	pCR 32.130 on definitions
					Source: Orange

Abstract:

-

Decision: 		The document was revised to S5-140254.

S5-140254	pCR 32.130 on definitions
					Source: Orange

(Replaces S5-140151)

Decision: 		The document was approved.

S5-140152	pCR 32.130 on concepts and background
					Source: Orange

Abstract:

-

Decision: 		The document was revised to S5-140249.

S5-140249	pCR 32.130 on concepts and background
					Source: Orange

(Replaces S5-140152)

Decision: 		The document was approved.

S5-140153	pCR 32.130 on requirements
					Source: Orange

Abstract:

-

Decision: 		The document was revised to S5-140250.

S5-140250	pCR 32.130 on requirements
					Source: Orange

(Replaces S5-140153)

Decision: 		The document was approved.

S5-140288	Draft TS 32.130 Network sharing; Concepts and requirements
					Source: Orange

Discussion:

SWG Chair: Start with S5-140288d1 the Email approval

Decision: 		The document was for Email approval and approved.

#### 6.8.2	OAM aspects of Network Sharing - Stage 2/3

### 6.9	OAM&P Studies

#### 6.9.1	Study on management of Heterogeneous Networks

S5-140030	Minutes for Study on management of Heterogeneous Networks (510046)
					Source: Rapporteur

Abstract:

-

Decision: 		The document was noted.

S5-140164	pCR TR 32.835 Reduction of PM data
					Source: Ericsson

Abstract:

-

Decision: 		The document was noted.

S5-140189	pCR on Rapporteur clean up for TR 32.835 Study of Heterogeneous Networks Management
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140251.

S5-140251	pCR on Rapporteur clean up for TR 32.835 Study of Heterogeneous Networks Management
					Source: Ericsson

(Replaces S5-140189)

Decision: 		The document was approved.

S5-140192	pCR TR 32.835 Completing the analysis of classification
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140253.

S5-140253	pCR TR 32.835 Completing the analysis of classification
					Source: Ericsson

(Replaces S5-140192)

Decision: 		The document was revised to S5-140289.

S5-140289	pCR TR 32.835 Completing the analysis of classification
					Source: Ericsson

(Replaces S5-140253)

Decision: 		The document was revised to S5-140293.

S5-140293	pCR TR 32.835 Completing the analysis of classification
					Source: Ericsson

(Replaces S5-140289)

Decision: 		The document was approved.

S5-140195	pCR on Recommendations for TR 32.835 Study of Heterogeneous Networks Management
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140252.

S5-140252	pCR on Recommendations for TR 32.835 Study of Heterogeneous Networks Management
					Source: Ericsson

(Replaces S5-140195)

Decision: 		The document was approved.

S5-140256	Revised WID SP-130046 Study on management of Heterogeneous Networks
					Source: Ericsson

Discussion:

agreed (not to go to SA for approval): changed only completion date to Jun 2014

Decision: 		The document was agreed (not to go to SA).

S5-140290	Draft TR 32.835 Study on management of Heterogeneous Networks
					Source: Ericsson

Discussion:

SWG Chair: Start with S5-140290d1 the Email approval

Decision: 		The document was for Email approval and approved.

#### 6.9.2	Study on Enhancements of OAM aspects of Distributed Mobility Load Balancing (MLB) SON function

S5-140031	Minutes for Study on Enhancements of OAM aspects of Distributed Mobility Load Balancing (MLB) SON function
					Source: Rapporteur

Abstract:

-

ACTION:	Email approval of TR 32.860
	(action on: Cisco / due by: 2014-04-01)

Decision: 		The document was revised to S5-140291.

S5-140291	Minutes for Study on Enhancements of OAM aspects of Distributed Mobility Load Balancing (MLB) SON function
					Source: Rapporteur

(Replaces S5-140031)

Decision: 		The document was noted.

S5-140062	pCR to TR 32.8xy Study on Enhancements of OAM aspects of distributed Self-Organizing Networks (SON) functions: MLB parameters alignment
					Source: Cisco

Abstract:

Additional use cases proposed for MLB

Discussion:

S5-140062 split into 2 pCRs S5-140258/S5-140262 for TR 32.860

Decision: 		The document was revised to S5-140258.

S5-140258	pCR TR 32.860 MLB Algorithms – Problem Statement (S5-140062 split into 2 pCRs S5-140258/S5-140262)
					Source: Cisco

(Replaces S5-140062)

Discussion:

S5-140062 split into 2 pCRs S5-140258/S5-140262 for TR 32.860

Decision: 		The document was approved.

S5-140262	pCR to TR 32.860 FS_D_MLB_SON_OAM (S5-140062 split into 2 pCRs S5-140258/S5-140262): MLB parameters alignment
					Source: Cisco

(Replaces S5-140062)

Discussion:

S5-140062 split into 2 pCRs S5-140258/S5-140262 for TR 32.860

Decision: 		The document was withdrawn.

S5-140065	pCR to TR 32.8xy Study on Enhancements of OAM aspects of distributed Self-Organizing Networks (SON) functions: Additional load information for MLB
					Source: Cisco

Abstract:

Additional use case proposed for Clause 4

Decision: 		The document was revised to S5-140260.

S5-140260	pCR TR 32.860 Problem statement – information of non-neighbours (S5-140065 split into 2 pCRs S5-140260/S5-140261)
					Source: Cisco

(Replaces S5-140065)

Discussion:

S5-140065 split into 2 pCRs S5-140260/S5-140261 for TR 32.860

Decision: 		The document was revised to S5-140292.

S5-140261	pCR to TR 32.860 FS_D_MLB_SON_OAM (S5-140065 split into 2 pCRs S5-140260/S5-140261): Additional load information for MLB
					Source: Cisco

(Replaces S5-140065)

Discussion:

S5-140065 split into 2 pCRs S5-140260/S5-140261 for TR 32.860

Decision: 		The document was withdrawn.

S5-140292	pCR TR 32.860 Problem statement – information of non-neighbours (S5-140065 split into 2 pCRs S5-140260/S5-140261)
					Source: Cisco

(Replaces S5-140260)

Discussion:

SWG Chair: Start with S5-140292d1 the Email approval

Decision: 		The document was for Email approval and approved.

S5-140098	pCR on TR 32.8xy on MLB
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140223.

S5-140223	pCR to TR 32.860 FS_D_MLB_SON_OAM
					Source: Ericsson

(Replaces S5-140098)

Decision: 		The document was revised to S5-140263.

S5-140263	pCR to TR 32.860 FS_D_MLB_SON_OAM
					Source: Ericsson

(Replaces S5-140223)

Decision: 		The document was withdrawn.

S5-140099	pCR to TR 32.8xy Study on Enhancements of OAM aspects of distributed Self-Organizing Networks (SON) functions: CAC definition
					Source: Cisco

Abstract:

-

Decision: 		The document was withdrawn.

S5-140120	pCR to TR 32.8xy Study on Enhancements of OAM aspects of distributed Self-Organizing Networks (SON) functions: HO Parameters Negotiation issues
					Source: NEC

Abstract:

-

Decision: 		The document was noted.

S5-140124	Revised WID SP-130430 Study on Enhancements of OAM aspects of Distributed MLB SON function
					Source: Cisco, Rapporteur

Abstract:

-

Decision: 		The document was revised to S5-140257.

S5-140257	Revised WID SP-130430 Study on Enhancements of OAM aspects of Distributed MLB SON function
					Source: Cisco

(Replaces S5-140124)

Discussion:

MCC allocated number is TR 32.860 for FS_D_MLB_SON_OAM

approved (not to go to SA for approval): changed only WI acronym, set TR#, for SA Info => Jun 2014

Decision: 		The document was agreed (not to go to SA).

S5-140202	pCR to TR 32.8xy Study on Enhancements of OAM aspects of distributed Self-Organizing Networks (SON) functions: CAC definition
					Source: Cisco, NEC

Abstract:

-

Decision: 		The document was noted.

S5-140296	Draft TR 32.860 Study on Enhancements of OAM aspects of Distributed Mobility Load Balancing (MLB) SON function
					Source: Cisco

Discussion:

SWG Chair: Start with S5-140296d1 the Email approval

Decision: 		The document was for Email approval and approved.

#### 6.9.3	Study on Application and Partitioning of Itf-N

S5-140036	Minutes for Study on Application and Partitioning of Itf-N
					Source: Rapporteur

Abstract:

-

Decision: 		The document was noted.

S5-140154	Draft TR 32.8xy Study on Application and Partitioning of Itf-N
					Source: China Mobile

Abstract:

-

Discussion:

Chair: Change TS to TR. Add URL for the NGMN reference.

MCC allocated TR 32.861 for Study on Application and Partitioning of Itf-N

Decision: 		The document was revised to S5-140264.

S5-140264	Draft TR 32.861 Study on Application and Partitioning of Itf-N
					Source: China Mobile

(Replaces S5-140154)

Discussion:

MCC allocated TR 32.861 for Study on Application and Partitioning of Itf-N.

SWG Chair: Start with S5-140264d1 the Email approval

ACTION:	Email approval of TR 32.861
	(action on: China Mobile / due by: 2014-04-01)

Decision: 		The document was for Email approval and approved.

## 7	Converged Management

### 7.1	Converged Management Plenary

S5-140006	Converged Management Executive report from THIS meeting
					Source: Converged Management SWG Chair

Abstract:

-

Decision: 		The document was noted.

S5-140097	TD Plan CRs upgrade XSD
					Source: Ericsson, Huawei

Abstract:

-

Discussion:

MCC: It is not allowed to replace Reference 8 by 13.

Reference 8 should become "Void" and reference 13 should remain as it is.

MCC: There are errors in References:

a) duplicates - see [3] and [12] ITU-T Recommendation X.721 - see 28.626;

b) styles in 2 References ("normal" instead of "EW");

c) Contradiction between TS body text in "3.1 Definitions" 32.672 [2] and in "2 References" TS 28.625 [2] - see 28.626

Chair: All to review the 28-series before preparing the CRs proposed by the document

ACTION:	All to review the 28-series (errors in References) before preparing the CRs
	(action on: SA5, MCC / due by: 2014-04-01)

Decision: 		The document was approved.

S5-140166	Open Action Items for Converged Management SWG
					Source: CMAN SWG chair

Abstract:

-

Decision: 		The document was withdrawn.

S5-140172	Open Action Items for Converged Management SWG
					Source: CMAN SWG chair

Abstract:

Replaces S5-140166, S5-140172

Discussion:

CMAN SWG chair (Thomas) reviewed the list of actions

Decision: 		The document was revised to S5-140265.

S5-140265	Open Action Items for Converged Management SWG
					Source: CMAN SWG chair

(Replaces S5-140172)

Decision: 		The document was noted.

S5-140179	LS from NGMN Project NGCOR to SA5 on Publication of Deliverables
					Source: NGMN NGCOR

Abstract:

LS from NGMN Project NGCOR on Publication of Deliverables

to SA1, SA5, ETSI, ITU-T, OIF, MEF, BBF, ONF, IETF, TMF.

1.

The NGMN (Next Generation Mobile Networks) Alliance was founded by leading international network operators in 2006. Its objective is to ensure that the functionality and performance of next generation mobile network infrastructure, service platforms and devices will meet the requirements of operators and, ultimately, will satisfy end user demand and expectations. The NGMN Alliance will drive and guide the development of all future mobile broadband technology enhancements focusing on LTE & EPC and its evolution The objective of the NGMN project NGCOR (Next Generation Converged Operations Requirements) is to reduce complexity and integration costs in the area of network management by achieving standardised interfaces between the Telco infrastructure and the OSS (Operations Support Systems). NGCOR aims to obtain more flexibility and reduced time-to-market in the introduction of services through standardised network management functionalities for converged fixed and mobile networks. The task of NGCOR is to provide high level requirements from operator point of view and feed these into the standardisation process of the SDOs. Note: Although the “M” in NGMN means Mobile, the main scope of NGCOR is convergence of management for mobile and fixed networks. Phase 1 of NGCOR focused on requirements for Fault Management, Resource Inventory and Modelling & Tooling. and Business Scenarios for Converged Operations from Multi-Domain & MultiTechnology perspective. Main aspects of Phase 2 were requirements for Configuration Management, Performance Management, Service Inventory Management and Business scenarios for Converged Operations (RAN Sharing Operations & Core Network Sharing Operations).

2. Publication of Deliverables

NGMN has published the requirements from Project NGCOR phase 1&2 in one document with the following chapters:  Generic Next Generation Converged Operational Requirements  Requirements for NGCOR Modelling and Tooling  High Level Requirements for Converged Operations  Requirements for Fault Management Interface  Requirements for Configuration Management  Requirements for Performance Management Interface  Requirements for Resource and Service Inventory Management  Business Scenarios for Network Sharing

The document is publicly available for download from the NGMN website: http://www.ngmn.org/uploads/media/NGMN_Next_Generation_Converged_Operations_Requirements_-_Final_Deliverable.pdf.

3. Expected Outcome of this Liaison

SA1, SA5, ITU-T WP2/2, ETSI-ISG-AFI, OIF, MEF, BBF, ONF, IETF, TMF are asked to review, provide feedback and take the requirements into consideration in their work.

Discussion:

Resubmit at next SA5 meeting

ACTION:	Resubmit at next SA5 meeting
	(action on: MCC / due by: 2014-04-01)

Decision: 		The document was postponed.

S5-140224	Multi-SDO meeting calendar
					Source: WG Chairman

Decision: 		The document was noted.

### 7.2	OAM&P 12 Compliance of 3GPP SA5 specifications to the NGMN Top OPE Recommendations

S5-140032	Minutes for Compliance of 3GPP SA5 specifications to the NGMN Top OPE Recommendations (560034)
					Source: Rapporteur

Abstract:

-

Discussion:

Changed agenda item to 7.2 as the Minutes should cover the entire work (both TR and TS parts).

Changed Title from:

"Minutes for TR on compliance of 3GPP SA5 specifications to the NGMN Top OPE Recommendations"

to

"Minutes for Compliance of 3GPP SA5 specifications to the NGMN Top OPE Recommendations"

Decision: 		The document was noted.

#### 7.2.1	TR on compliance of 3GPP SA5 specifications to the NGMN Top OPE Recommendations

S5-140112	pCR to TR 32.838 Northbound Interface for SON related parameters
					Source: Cisco

Abstract:

-

Decision: 		The document was revised to S5-140266.

S5-140266	pCR to TR 32.838 Northbound Interface for SON related parameters
					Source: Cisco

(Replaces S5-140112)

Decision: 		The document was revised to S5-140272.

S5-140272	pCR to TR 32.838 Northbound Interface for SON related parameters
					Source: Cisco

(Replaces S5-140266)

Decision: 		The document was withdrawn.

S5-140113	pCR to TR 32.838 SON controlled implementation: eICIC patterns
					Source: Cisco

Abstract:

-

Decision: 		The document was revised to S5-140267.

S5-140267	pCR to TR 32.838 SON controlled implementation: eICIC patterns
					Source: Cisco

(Replaces S5-140113)

Decision: 		The document was approved.

S5-140114	pCR to TR 32.838 SON controlled implementation: eNBs association
					Source: Cisco

Abstract:

-

Decision: 		The document was revised to S5-140268.

S5-140268	pCR to TR 32.838 SON controlled implementation: eNBs association
					Source: Cisco

(Replaces S5-140114)

Decision: 		The document was approved.

S5-140115	pCR to TR 32.838 SON controlled implementation, Interference Control
					Source: Cisco

Abstract:

-

Decision: 		The document was revised to S5-140269.

S5-140269	pCR to TR 32.838 SON controlled implementation, Interference Control
					Source: Cisco

(Replaces S5-140115)

Decision: 		The document was withdrawn.

S5-140116	pCR to TR 32.838 SON controlled implementation eICIC
					Source: Cisco

Abstract:

-

Decision: 		The document was revised to S5-140270.

S5-140270	pCR to TR 32.838 SON controlled implementation eICIC
					Source: Cisco

(Replaces S5-140116)

Decision: 		The document was withdrawn.

S5-140117	pCR to TR 32.838 SON controlled implementation: ICIC
					Source: Cisco

Abstract:

-

Decision: 		The document was revised to S5-140271.

S5-140271	pCR to TR 32.838 SON controlled implementation: ICIC
					Source: Cisco

(Replaces S5-140117)

Decision: 		The document was revised to S5-140294.

S5-140294	pCR to TR 32.838 SON controlled implementation: ICIC
					Source: Cisco

(Replaces S5-140271)

Discussion:

SWG Chair: Start with S5-140294d1 the Email approval

Decision: 		The document was for Email approval and approved.

S5-140188	Template for Clause 13 Automatic Inventory
					Source: Huawei

Abstract:

-

Decision: 		The document was agreed.

S5-140295	Draft TR 32.838 Study on Compliance of 3GPP OAM specifications to the NGMN Top OPE Recommendations
					Source: Ericsson

Discussion:

SWG Chair: Start with S5-140295d1 the Email approval

ACTION:	Email approval of TR 32.838
	(action on: Ericsson / due by: 2014-04-01)

Decision: 		The document was for Email approval and approved.

#### 7.2.2	TS work on Compliance of 3GPP SA5 specifications to the NGMN Top OPE Recommendations

S5-140092	Rel-9 CR 32.522 Add missing performance measurement support for HO
					32.522	  CR-0143  (Rel-9) v..
					Source: Huawei

Abstract:

-

Decision: 		The document was noted.

S5-140093	Rel-10 CR 32.522 Add missing performance measurement support for HO
					32.522	  CR-0144  (Rel-10) v..
					Source: Huawei

Abstract:

-

Decision: 		The document was noted.

S5-140094	Rel-11 CR 32.522 Add missing performance measurement support for HO
					32.522	  CR-0145  (Rel-11) v..
					Source: Huawei

Abstract:

-

Decision: 		The document was noted.

S5-140095	Rel-11 CR 28.628 Add missing performance measurement support for HO
					28.628	  CR-0006  (Rel-11) v..
					Source: Huawei

Abstract:

-

Discussion:

NSN (Anatoly): both 32-series and 28-series (for Converged Management) should be mentioned in the body text of the CR

Decision: 		The document was noted.

S5-140197	Clarification on the relation between RRC connection re-establishment measurement and HO optimization
					Source: Huawei

Abstract:

-

Decision: 		The document was noted.

S5-140198	Enhancements for HO optimization performance evaluation
					Source: Huawei

Abstract:

-

Decision: 		The document was noted.

### 7.3	OAM&P 12 Compliance of 3GPP SA5 specifications to the NGMN NGCOR Requirements

#### 7.3.1	TR on compliance of 3GPP SA5 specifications to the NGMN NGCOR Requirements

S5-140033	Minutes for TR on compliance of 3GPP SA5 specifications to the NGMN NGCOR Requirements (560435)
					Source: Rapporteur

Abstract:

-

Discussion:

Nothing has been agreed

Decision: 		The document was noted.

S5-140199	Discussion paper on Comparison of NGCOR V1.3 and V1.4 and way forward for NGCOR compliance WID
					Source: Huawei

Abstract:

-

Decision: 		The document was noted.

S5-140200	pCR Add introduction section to TR 32.837
					Source: Huawei

Abstract:

-

Decision: 		The document was noted.

S5-140201	Revised WID Compliance to NGMN NGCOR Requirements
					Source: Huawei

Abstract:

-

Decision: 		The document was noted.

#### 7.3.2	Converged Management Model alignment Phase 2

S5-140034	Minutes for Converged Management Model alignment Phase 2 (560135)
					Source: Rapporteur

Abstract:

-

Discussion:

Nothing has been approved

Decision: 		The document was noted.

S5-140215	MultiSDO-JWG-ModelAlignment-Status And Next Steps
					Source: Rapporteur

Abstract:

-

Decision: 		The document was noted.

S5-140217	Umbrella Operation Model (UOM) Version 5.1 Draft
					Source: Editor

Abstract:

-

Decision: 		The document was noted.

S5-140244	Minutes 21st meeting Multi-SDO Converged Management Model Alignment JWG
					Source: SWG Chair

Decision: 		The document was noted.

S5-140245	Minutes 22nd meeting Multi-SDO Converged Management Model Alignment JWG
					Source: SWG Chair

Decision: 		The document was noted.

#### 7.3.3	Converged Management PM Interface definitions

S5-140035	Minutes for Converged Management PM Interface definitions (560235)
					Source: Rapporteur

Abstract:

-

Discussion:

Nothing has been approved

Decision: 		The document was noted.

S5-140155	DP on gap analysis of performance requirements
					Source: China Mobile

Abstract:

-

Decision: 		The document was noted.

S5-140214	Status on Multi-SDO Converged Management PM Interface definitions JWG
					Source: Rapporteur

Abstract:

-

Decision: 		The document was noted.

## 8	Charging

### 8.1	Charging Plenary

S5-140009	CH Agenda and Time Plan
					Source: CH SWG Chair

Abstract:

-

Decision: 		The document was revised to S5-140301.

S5-140301	CH Agenda and Time Plan
					Source: CH SWG Chair

(Replaces S5-140009)

Decision: 		The document was approved.

S5-140010	CH Detailed Report from LAST Meeting
					Source: CH SWG Chair

Abstract:

-

Discussion:

Wrong file. S5-140041 contains CH Detailed Report from LAST Meeting

Decision: 		The document was withdrawn and replaced by S5-140041.

S5-140041	CH Detailed Report from LAST Meeting
					Source: CH SWG Chair

Abstract:

-

Decision: 		The document was approved.

S5-140011	CH Executive Report from THIS Meeting
					Source: CH SWG Chair

Abstract:

-

Decision: 		The document was revised to S5-140361.

S5-140361	CH Executive Report from THIS Meeting
					Source: CH SWG Chair

(Replaces S5-140011)

Decision: 		The document was noted.

S5-140012	CH Detailed Report from THIS Meeting
					Source: CH SWG Chair

Abstract:

-

Decision: 		The document was [not addressed].

S5-140181	Reply LS from CT1 to SA5 on Availability of SIP Instance Identifier
					Source: C1-135196

Abstract:

Reply LS from CT1 to SA5 (S5-131804) on Availability of SIP Instance Identifier (Rel-12, Work Item: CH12).

CT1 was requested to confirm the availability of the Instance Id in all requests and responses from the served user at each of the IMS nodes listed.

CT1 points out that the use of Instance Id in SIP signalling has privacy issues and is allowed: 1) in REGISTER requests & responses, 2) in requests & responses for the Emergency Call scenario, and 3) when the UE knows the Instance Id will be removed by a network entity.

According to the current IETF documentation, any new usages of Instance ID over what is already defined would require an IETF RFC to address the privacy issues.

CT1 asks SA5 to take this into account. If SA5 needs the information to be available beyond what is described above, CT1 would need a clear description of the requirements.

Decision: 		The document was noted.

S5-140184	Reply LS from CT3 cc SA5 on support for user location age or timestamp
					Source: C3-131852

Abstract:

Reply LS from CT3 to CT4 (cc: SA5, CT1) on support for User Location age or timestamp (Rel-11, Work Item: NWK-PL2IMS-CT).

CT4 has identified different formats of User Location timestamp in TS 29.274 and TS 29.212.

CT3 considers sufficient 32-bit format for providing time (in seconds) of the last known location of the end user. In this case, the 32 LSB for the fraction of seconds in the 64-bit format is not used any more.

CT3 has checked the definition of Age-Of-Location-Information AVP over Diameter based S6a (TS 29.272): it uses Unsigned32 type to represent a relative time in minutes.

CT3 asks CT4 to update the ULI timestamp definition to an Unsigned32 type in TS 29.274 correspondingly.

If however CT4 prefers to keep Unsigned64 type for ULI timestamp unchanged, the PGW would need to convert the time format between the GTP based interfaces and Diameter based interfaces.

Decision: 		The document was noted.

S5-140186	LS out to CT1 Reply LS on Availability of SIP Instance Identifier
					Source: Ericsson

Abstract:

-

Discussion:

S5-140181/C1-135196

Decision: 		The document was noted.

S5-140193	LS from SA2 to SA5 on the provision of IPv6 prefix length to SGW/SGSN
					Source: S2-133832

Abstract:

LS from SA2 to SA5 on Provision of IPv6 prefix length to SGW/SGSN (Rel-11, Work Item: TEI10, SAES).

SA2 has observed that in SA5 TS 32.251 the SGW/SGSN includes the IPv6 prefix length into the CDR field, I.e. “Served PDP/PDN Address prefix length”, when the IPv6 prefix length is less than 64 bits.

However, PGW/GGSN does not return IPv6 prefix length for GTPV1, but only sends fixed IPv6 prefix length of 64 bits for GTPV2 back to SGW/SGSN. Thus the requirement for CDR generation can not be fulfilled.

SA2 asks SA5 update the relevant specifications accordingly if necessary.

Decision: 		The document was noted.

S5-140196	LS from SA2 to SA5 on Charging aspects for Network Sharing (MOCN GWCN)
					Source: S2-134589

Abstract:

Reply LS from SA2 to SA5, CT4 on LS (S2-133875/S5-131380) SA5's questions related to Charging aspects for Network Sharing : MOCN - GWCN (Multi-Operator Core Network - Gateway Core Network Sharing).

SA5 target Rel-8, Work Item CH8.

SA5 question 1: SA5 noted in TS 23.251 clause 4.4: “An exception to this is that the HPLMN operator may specify in the inter-operator roaming/sharing agreement that for non-supporting UEs the Common PLMN ID is reported to the HPLMN”. It is unclear to SA5 whether this exception is supported in the protocol, and if so, how.

SA5 question 2: SA5 discussed TS 23.251 clause 6 statement: “whether the core network operator was selected by a supporting UE or allocated by the network to a UE shall be included in the CDR”, and concluded more clarification on use of such indicator in CDRs was needed. Especially whether it is intended for the Operator owning the shared CN or for the HPLMN and how it is expected to be described by the protocol.

In its answer SA2 has attached two Rel-12 Cat F 23.060CR#1819, 23.251CR#0096 under WI code TEI12, SAES, and asks SA5, CT4 to take this into account.

Decision: 		The document was noted.

S5-140203	LS out to SA2, CT3 on credit control failure handling
					Source: Openet

Abstract:

-

Decision: 		The document was revised to S5-140319.

S5-140319	LS out to SA2, CT3 on credit control failure handling
					Source: Openet

(Replaces S5-140203)

Discussion:

MCC post meeting notes:

David Shrader (Ericsson) informed on 26 Jan 2014 that S5-140319 does NOT contain the LS that was approved at the close of the charging session. This contains an earlier draft that was completely rewritten during the Thursday afternoon session.

Maryse Gardella (ALU), SWG CH Chair, confirmed that by mistake d1 was considered for the final version of S5-140319 and proposed to provide d2 with a new Tdoc# in a clean version. Maryse confirmed that S5-140319 was not opened during the SWG CH Closing Plenary.

I will share with all of you this final version before official announcement for this change. Btw what is the best way then to report such changes occurring after Closing Plenary? Announcement of revision for detailed report from Plenary? Dedicated Per-change email on exploder?

Decision: 		The document was revised to S5-140364.

S5-140364	LS out to SA2, CT3 on credit control failure handling
					Source: Openet

(Replaces S5-140319)

Decision: 		The document was for Email approval and approved.

S5-140218	Resubmitted LS from CT1 to SA5 on transit IOI exchange over ISC interface
					Source: C1-131748

Abstract:

LS from CT1 to SA5 on Transit IOI exchange over ISC interface (Rel-11, Work Item: IOI_IMS_CH).

CT1 asks SA5 to clarify a misalignment between CT1 TS 24.229(v11.7.0) and SA5 TS 32.240(v11.6.0)

Decision: 		The document was postponed.

S5-140221	Reply LS from GSMA SOLU to SA5 on Transit IOI clarification
					Source: GSMA SOLU

Abstract:

Reply LS from GSMA SOLU to SA5 on  “Clarification of transit IOI exchange over ISC interface” (S5-131393).

SOLU has discussed the SA5 question whether transit networks could exist between HPLMN S-CSCF and 3rd party AS.

SOLU could not find reasonable existing use cases that would match with the described situation.

SOLU thinks that this might happen in very rare cases for Enterprise services, despite no one could confirm a concrete example.

Even considering those Enterprise services, it appears that transport mode would be used and therefore the transit IOI is not needed.

Decision: 		The document was noted.

S5-140255	Reply LS from SA3 to SA5 (S5-132105) (cc: GSMA IREG) on securing Gy/Gyn interfaces for EPC Roaming LBO scenario
					Source: S3-140208

Decision: 		The document was noted.

S5-140336	LS out to BBF
					Source: SA5 SWG CH

Discussion:

ALU

Decision: 		The document was revised to S5-140362.

S5-140362	LS out to BBF
					Source: SA5 SWG CH

(Replaces S5-140336)

Discussion:

WG Chair: Start with S5-140362d1 the Email approval

Decision: 		The document was for Email approval and noted.

### 8.2	New Charging Work Item proposals

### 8.3	Charging Maintenance and Rel-12 small Enhancements

S5-140068	Rel-11 CR 32.260 Correction for SIP Route header transmitted in TF CDR
					32.260	  CR-0242  (Rel-11) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was agreed.

S5-140070	Rel-12 CR 32.260 Correction for SIP Route header transmitted in S-CSCF CDR
					32.260	  CR-0243  (Rel-12) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140351.

S5-140351	Rel-12 CR 32.260 Correction for SIP Route header transmitted in S-CSCF CDR
					32.260	  CR-0243  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140070)

Decision: 		The document was agreed.

S5-140071	Rel-8 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier
					32.299	  CR-0571  (Rel-8) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140337.

S5-140337	Rel-8 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier
					32.299	  CR-0571  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140071)

Decision: 		The document was agreed.

S5-140072	Rel-9 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier
					32.299	  CR-0572  (Rel-9) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140338.

S5-140338	Rel-9 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier
					32.299	  CR-0572  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140072)

Decision: 		The document was agreed.

S5-140073	Rel-10 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier
					32.299	  CR-0573  (Rel-10) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140339.

S5-140339	Rel-10 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier
					32.299	  CR-0573  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140073)

Decision: 		The document was agreed.

S5-140074	Rel-11 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier
					32.299	  CR-0574  (Rel-11) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140340.

S5-140340	Rel-11 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier
					32.299	  CR-0574  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140074)

Decision: 		The document was agreed.

S5-140075	Rel-12 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier
					32.299	  CR-0575  (Rel-12) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140341.

S5-140341	Rel-12 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier
					32.299	  CR-0575  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140075)

Decision: 		The document was agreed.

S5-140076	Rel-11 CR 32.298 Correction for User Location Information Time
					32.298	  CR-0427  (Rel-11) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140352.

S5-140352	Rel-11 CR 32.298 Correction for User Location Information Time
					32.298	  CR-0427  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140076)

Decision: 		The document was agreed.

S5-140077	Rel-12 CR 32.298 Correction for User Location Information Time
					32.298	  CR-0428  (Rel-12) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140353.

S5-140353	Rel-12 CR 32.298 Correction for User Location Information Time
					32.298	  CR-0428  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140077)

Decision: 		The document was agreed.

S5-140078	Rel-11 CR 32.251  Application based charging in case of PCEF enhanced with ADC-alignment with TS 23.203
					32.251	  CR-0342  (Rel-11) v..
					Source: Alcatel-Lucent

Abstract:

-

Decision: 		The document was revised to S5-140354.

S5-140354	Rel-11 CR 32.251 Application based charging in case of PCEF enhanced with ADC - alignment with TS 23.203
					32.251	  CR-0342  rev 1 (-) v..
					Source: Alcatel-Lucent

(Replaces S5-140078)

Decision: 		The document was agreed.

S5-140079	Rel-12 CR 32.251 Application based charging in case of PCEF enhanced with ADC - alignment with TS 23.203
					32.251	  CR-0343  (Rel-12) v..
					Source: Alcatel-Lucent

Abstract:

-

Decision: 		The document was revised to S5-140355.

S5-140355	Rel-12 CR 32.251 Application based charging in case of PCEF enhanced with ADC - alignment with TS 23.203
					32.251	  CR-0343  rev 1 (-) v..
					Source: Alcatel-Lucent

(Replaces S5-140079)

Decision: 		The document was agreed.

S5-140081	Rel-8 CR 32.298 Correction on Serving Node PLMN Identifier ASN.1 value in SGSN record
					32.298	  CR-0430  (Rel-8) v..
					Source: Alcatel-Lucent

Abstract:

-

Decision: 		The document was agreed.

S5-140100	CR Required MBMS Bearer Capabilities
					Source: ZTE

Abstract:

-

Decision: 		The document was withdrawn.

S5-140101	Rel-9 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging
					32.251	  CR-0345  (Rel-9) v..
					Source: ZTE

Abstract:

-

Decision: 		The document was revised to S5-140347.

S5-140347	Rel-9 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging
					32.251	  CR-0345  rev 1 (-) v..
					Source: ZTE

(Replaces S5-140101)

Decision: 		The document was agreed.

S5-140102	Rel-10 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging
					32.251	  CR-0346  (Rel-10) v..
					Source: ZTE

Abstract:

-

Decision: 		The document was revised to S5-140348.

S5-140348	Rel-10 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging
					32.251	  CR-0346  rev 1 (-) v..
					Source: ZTE

(Replaces S5-140102)

Decision: 		The document was agreed.

S5-140103	Rel-11 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging
					32.251	  CR-0347  (Rel-11) v..
					Source: ZTE

Abstract:

-

Decision: 		The document was revised to S5-140349.

S5-140349	Rel-11 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging
					32.251	  CR-0347  rev 1 (-) v..
					Source: ZTE

(Replaces S5-140103)

Decision: 		The document was agreed.

S5-140104	Rel-12 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging
					32.251	  CR-0348  (Rel-12) v..
					Source: ZTE

Abstract:

-

Decision: 		The document was revised to S5-140350.

S5-140350	Rel-12 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging
					32.251	  CR-0348  rev 1 (-) v..
					Source: ZTE

(Replaces S5-140104)

Decision: 		The document was agreed.

S5-140105	Rel-9 CR 32.298 Correction for Comment line of RequiredMBMSBearerCapabilities in eMBMS Charging
					32.298	  CR-0431  (Rel-9) v..
					Source: ZTE

Abstract:

-

Decision: 		The document was noted.

S5-140106	Rel-10 CR 32.298 Correction for Comment line of RequiredMBMSBearerCapabilities in eMBMS Charging
					32.298	  CR-0432  (Rel-10) v..
					Source: ZTE

Abstract:

-

Decision: 		The document was noted.

S5-140107	Rel-11 CR 32.298 Correction for Comment line of RequiredMBMSBearerCapabilities in eMBMS Charging
					32.298	  CR-0433  (Rel-11) v..
					Source: ZTE

Abstract:

-

Decision: 		The document was noted.

S5-140108	Rel-12 CR 32.298 Correction for Comment line of RequiredMBMSBearerCapabilities in eMBMS Charging
					32.298	  CR-0434  (Rel-12) v..
					Source: ZTE

Abstract:

-

Decision: 		The document was noted.

S5-140109	Rel-9 CR 32.251 Correction for QoS Negotiation in eMBMS charging
					32.251	  CR-0349  (Rel-9) v..
					Source: ZTE

Abstract:

-

Decision: 		The document was noted.

S5-140110	Rel-9 CR 32.273 Correction for QoS Negotiation in eMBMS charging
					32.273	  CR-0026  (Rel-9) v..
					Source: ZTE

Abstract:

-

Decision: 		The document was noted.

S5-140111	Rel-9 CR 32.298 Correction for QoS Negotiation in eMBMS charging
					32.298	  CR-0435  (Rel-9) v..
					Source: ZTE

Abstract:

-

Decision: 		The document was noted.

S5-140132	Rel-8 CR 32.298 Correction for S-GW change cause for record closing
					32.298	  CR-0436  (Rel-8) v..
					Source: Ericsson, Vodafone

Abstract:

-

Decision: 		The document was revised to S5-140342.

S5-140342	Rel-8 CR 32.298 Correction for S-GW change cause for record closing
					32.298	  CR-0436  rev 1 (-) v..
					Source: Ericsson, Vodafone

(Replaces S5-140132)

Decision: 		The document was agreed.

S5-140133	Rel-9 CR 32.298 Correction for S-GW change cause for record closing
					32.298	  CR-0437  (Rel-9) v..
					Source: Ericsson, Vodafone

Abstract:

-

Decision: 		The document was revised to S5-140343.

S5-140343	Rel-9 CR 32.298 Correction for S-GW change cause for record closing
					32.298	  CR-0437  rev 1 (-) v..
					Source: Ericsson, Vodafone

(Replaces S5-140133)

Decision: 		The document was agreed.

S5-140134	Rel-10 CR 32.298 Correction for S-GW change cause for record closing
					32.298	  CR-0438  (Rel-10) v..
					Source: Ericsson, Vodafone

Abstract:

-

Decision: 		The document was revised to S5-140344.

S5-140344	Rel-10 CR 32.298 Correction for S-GW change cause for record closing
					32.298	  CR-0438  rev 1 (-) v..
					Source: Ericsson, Vodafone

(Replaces S5-140134)

Decision: 		The document was agreed.

S5-140135	Rel-11 CR 32.298 Correction for S-GW change cause for record closing
					32.298	  CR-0439  (Rel-11) v..
					Source: Ericsson, Vodafone

Abstract:

-

Decision: 		The document was revised to S5-140345.

S5-140345	Rel-11 CR 32.298 Correction for S-GW change cause for record closing
					32.298	  CR-0439  rev 1 (-) v..
					Source: Ericsson, Vodafone

(Replaces S5-140135)

Decision: 		The document was agreed.

S5-140137	Rel-12 CR 32.298 Correction for S-GW change cause for record closing
					32.298	  CR-0440  (Rel-12) v..
					Source: Ericsson, Vodafone

Abstract:

-

Decision: 		The document was revised to S5-140346.

S5-140346	Rel-12 CR 32.298 Correction for S-GW change cause for record closing
					32.298	  CR-0440  rev 1 (-) v..
					Source: Ericsson, Vodafone

(Replaces S5-140137)

Decision: 		The document was agreed.

S5-140139	Rel-8 CR 32.299 Correction for S-GW change in Change-Condition AVP
					32.299	  CR-0577  (Rel-8) v..
					Source: Ericsson, Vodafone

Abstract:

-

Decision: 		The document was agreed.

S5-140140	Rel-9 CR 32.299 Correction for S-GW change in Change-Condition AVP
					32.299	  CR-0578  (Rel-9) v..
					Source: Ericsson, Vodafone

Abstract:

-

Decision: 		The document was agreed.

S5-140141	Rel-10 CR 32.299 Correction for S-GW change in Change-Condition AVP
					32.299	  CR-0579  (Rel-10) v..
					Source: Ericsson, Vodafone

Abstract:

-

Decision: 		The document was agreed.

S5-140142	Rel-11 CR 32.299 Correction for S-GW change in Change-Condition AVP
					32.299	  CR-0580  (Rel-11) v..
					Source: Ericsson, Vodafone

Abstract:

-

Decision: 		The document was agreed.

S5-140143	Rel-12 CR 32.299 Correction for S-GW change in Change-Condition AVP
					32.299	  CR-0581  (Rel-12) v..
					Source: Ericsson, Vodafone

Abstract:

-

Decision: 		The document was agreed.

S5-140146	Rel-12 CR 32.299 Remove clause 6.3 Editor's Notes
					32.299	  CR-0582  (Rel-12) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was noted.

S5-140148	Rel-11 CR 32.251 Correction of CDR generated for SMS in the MME
					32.251	  CR-0352  (Rel-11) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was agreed.

S5-140149	Rel-12 CR 32.251 Correction of CDR generated for SMS in the MME
					32.251	  CR-0353  (Rel-12) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was agreed.

S5-140204	Rel-11 CR 32.260 Correction for SRVCC PS to CS transfer Flows through ATCF
					32.260	  CR-0245  (Rel-11) v..
					Source: China Mobile, Huawei

Abstract:

-

Decision: 		The document was revised to S5-140356.

S5-140356	Rel-11 CR 32.260 Correction for SRVCC PS to CS transfer Flows through ATCF
					32.260	  CR-0245  rev 1 (-) v..
					Source: China Mobile, Huawei

(Replaces S5-140204)

Decision: 		The document was postponed.

S5-140205	Rel-12 CR 32.260 Correction for SRVCC PS to CS transfer Flows through ATCF
					32.260	  CR-0246  (Rel-12) v..
					Source: China Mobile, Huawei

Abstract:

-

Decision: 		The document was revised to S5-140357.

S5-140357	Rel-12 CR 32.260 Correction for SRVCC PS to CS transfer Flows through ATCF
					32.260	  CR-0246  rev 1 (-) v..
					Source: China Mobile, Huawei

(Replaces S5-140205)

Decision: 		The document was postponed.

S5-140206	Rel-11 CR 32.260 Correction for SRVCC CS to PS transfer Flows through ATCF
					32.260	  CR-0247  (Rel-11) v..
					Source: China Mobile, Huawei

Abstract:

-

Decision: 		The document was revised to S5-140358.

S5-140358	Rel-11 CR 32.260 Correction for SRVCC CS to PS transfer Flows through ATCF
					32.260	  CR-0247  rev 1 (-) v..
					Source: China Mobile, Huawei

(Replaces S5-140206)

Decision: 		The document was postponed.

S5-140207	Rel-12 CR 32.260 Correction for SRVCC CS to PS transfer Flows through ATCF
					32.260	  CR-0248  (Rel-12) v..
					Source: China Mobile, Huawei

Abstract:

-

Decision: 		The document was revised to S5-140359.

S5-140359	Rel-12 CR 32.260 Correction for SRVCC CS to PS transfer Flows through ATCF
					32.260	  CR-0248  rev 1 (-) v..
					Source: China Mobile, Huawei

(Replaces S5-140207)

Decision: 		The document was postponed.

S5-140209	Rel-12 CR 32.260 Correction of Subscriber Equipment Number and Instance Id for privacy concerns
					32.260	  CR-0244  (Rel-12) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was noted.

S5-140210	Rel-12 CR 32.298 Correction of Subscriber Equipment Number and Instance Id for privacy concerns
					32.298	  CR-0441  (Rel-12) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was noted.

S5-140213	Rel-12 CR 32.251 Functional update
					32.251	  CR-0358  (rel-12) v..
					Source: NSN

Abstract:

-

Decision: 		The document was revised to S5-140316.

S5-140316	Rel-12 CR 32.251 Functional update
					32.251	  CR-0358  rev 1 (-) v..
					Source: NSN

(Replaces S5-140213)

Decision: 		The document was noted.

S5-140314	DP on Availability of SIP Instance Identifier
					Source: SWG CH

Decision: 		The document was agreed.

### 8.4	Rel-12 Charging

#### 8.4.1	Short Message Service - Service Centre (SMS-SC) Offline Charging

S5-140060	Rel-12 CR 32274 SCS Identity identified as Originator for Device Triggering
					32.274	  CR-0027  (Rel-12) v..
					Source: Alcatel-Lucent

Abstract:

-

Decision: 		The document was agreed.

S5-140061	Rel-12 CR 32274 Introduction of new SC-SMO and SC-SMT CDRs description
					32.274	  CR-0028  (Rel-12) v..
					Source: Alcatel-Lucent

Abstract:

-

Decision: 		The document was revised to S5-140302.

S5-140302	Rel-12 CR 32274 Introduction of new SC-SMO and SC-SMT CDRs description
					32.274	  CR-0028  rev 1 (-) v..
					Source: Alcatel-Lucent

(Replaces S5-140061)

Decision: 		The document was agreed.

S5-140063	Rel-12 CR 32274 Introduction of information for SMS offline Charging
					32.274	  CR-0024  (Rel-12) v..
					Source: Alcatel-Lucent

Abstract:

-

Discussion:

Incorporated in S5-140303

Decision: 		The document was revised to S5-140303.

S5-140064	Rel-12 CR 32274 Introduction of supported fields for SMS online Charging
					32.274	  CR-0025  (Rel-12) v..
					Source: Alcatel-Lucent

Abstract:

-

Discussion:

Incorporated in S5-140303

Decision: 		The document was revised to S5-140303.

S5-140303	Rel-12 CR 32274 Introduction of information for SMS offline Charging
					32.274	  CR-0024  rev 1 (-) v..
					Source: Alcatel-Lucent

(Replaces S5-140063)

Decision: 		The document was agreed.

S5-140304	Rel-12 CR 32274 Introduction of supported fields for SMS online Charging
					32.274	  CR-0025  rev 1 (-) v..
					Source: Alcatel-Lucent

(Replaces S5-140064)

Decision: 		The document was withdrawn.

S5-140066	Rel-10 CR 32298 Introduction of new SC-SMO and SC-SMT CDRs description
					32.298	  CR-0429  (Rel-10) v..
					Source: Alcatel-Lucent

Abstract:

-

Decision: 		The document was agreed.

S5-140067	Rel-12 CR 32.299 Introduction of information for SMS offline Charging
					32.299	  CR-0576  (Rel-12) v..
					Source: Alcatel-Lucent

Abstract:

-

Decision: 		The document was revised to S5-140305.

S5-140305	Rel-12 CR 32.299 Introduction of information for SMS offline Charging
					32.299	  CR-0576  rev 1 (-) v..
					Source: Alcatel-Lucent

(Replaces S5-140067)

Decision: 		The document was agreed.

S5-140069	Rel-12 CR 32274 Improve References specifications list
					32.274	  CR-0026  (Rel-12) v..
					Source: Alcatel-Lucent

Abstract:

-

Decision: 		The document was withdrawn.

S5-140082	Rel-12 CR 32.297 Add File transfer for SMS CDRs from SMS-SC - Bsm Interface
					32.297	  CR-0014  (Rel-12) v..
					Source: Alcatel-Lucent

Abstract:

-

Decision: 		The document was agreed.

S5-140167	Revised WID Short Message Service - Service Center (SMS-SC) Offline Charging
					Source: Alcatel-Lucent

Abstract:

-

Decision: 		The document was revised to S5-140306.

S5-140306	Revised WID SP-120775 Short Message Service - Service Center (SMS-SC) Offline Charging
					Source: Alcatel-Lucent

(Replaces S5-140167)

Decision: 		The document was revised to S5-140360.

S5-140360	Revised WID SP-120775 Short Message Service - Service Center (SMS-SC) Offline Charging
					Source: Alcatel-Lucent

(Replaces S5-140306)

Discussion:

agreed without presentation

Decision: 		The document was agreed.

#### 8.4.2	Charging per IP-Connectivity Access Network (IP-CAN) Session

S5-140147	Rel-12 CR 32.251 Corrections for CHIPS
					32.251	  CR-0351  (Rel-12) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140307.

S5-140307	Rel-12 CR 32.251 Corrections for CHIPS
					32.251	  CR-0351  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140147)

Decision: 		The document was agreed.

#### 8.4.3	Charging using an Alternative Roaming Provider

S5-140040	pCR 32.276 Change to functional protocol names
					32.276 v..
					Source: Ericsson, Alcatel-Lucent, NSN

Abstract:

-

Decision: 		The document was agreed.

S5-140044	pCR 32.276 Correction of offline charging sections
					32.276 v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was agreed.

S5-140045	pCR 32.276 Additional requirements and limitations for VCS charging
					32.276 v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140308.

S5-140308	pCR 32.276 Additional requirements and limitations for VCS charging
					32.276 v..
					Source: Ericsson

(Replaces S5-140045)

Decision: 		The document was approved.

S5-140046	DP Analysis of charging information for VCS
					Source: Ericsson

Abstract:

-

Decision: 		The document was noted.

S5-140047	pCR 32.276 Charging information for VCS
					32.276 v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140300.

S5-140300	pCR 32.276 Charging information for VCS
					32.276 v..
					Source: Ericsson

(Replaces S5-140047)

Discussion:

Incorporation of S5-140047 and S5-140168

Decision: 		The document was approved.

S5-140168	pCR Definition of Charging Information for Voice Call Service Charging
					Source: Alcatel-Lucent

Abstract:

-

Discussion:

Incorporate  with S5-140047 in S5-140300

Decision: 		The document was revised to S5-140300.

S5-140048	pCR 32.276 Relationship of VCS chargeable events to CAMEL events
					32.276 v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140309.

S5-140309	pCR 32.276 Relationship of VCS chargeable events to CAMEL events
					32.276 v..
					Source: Ericsson

(Replaces S5-140048)

Decision: 		The document was approved.

S5-140049	TD Presentation of Spec 32.276 to TSG
					32.276 v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was noted.

S5-140050	Rel-12 CR 32.299 Introduction of charging information for VCS
					32.299	  CR-0568  (Rel-12) v..
					Source: Ericsson

Abstract:

-

Decision: 		The document was revised to S5-140313.

S5-140313	Rel-12 CR 32.299 Introduction of charging information for VCS
					32.299	  CR-0568  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140050)

Decision: 		The document was noted.

S5-140208	pCR 32.293 The examples of message flow for Proxy Function
					Source: Huawei

Abstract:

-

Decision: 		The document was revised to S5-140311.

S5-140311	pCR 32.293 The examples of message flow for Proxy Function
					Source: Huawei

(Replaces S5-140208)

Decision: 		The document was approved.

S5-140310	Draft TS 32.276 Telecommunication management; Charging management; Voice call service charging
					Source: Ericsson

Discussion:

SWG Chair: Start with S5-140310d1 the Email approval

Decision: 		The document was for Email approval and approved.

S5-140312	Draft TS 32.293 Telecommunication management; Charging management; Proxy function
					Source: Ericsson

Discussion:

SWG Chair: Start with S5-140312d1 the Email approval

Decision: 		The document was for Email approval and approved.

#### 8.4.4	Charging for IMS centralized service (ICS) control (Stage 2/3)

S5-140211	Rel-12 CR 32.250 Charging management for IMS Centralized Services (ICS)
					32.250	  CR-0038  (Re-12) v..
					Source: NSN

Abstract:

-

Decision: 		The document was revised to S5-140315.

S5-140315	Rel-12 CR 32.250 Charging management for IMS Centralized Services (ICS)
					32.250	  CR-0038  rev 1 (-) v..
					Source: NSN

(Replaces S5-140211)

Decision: 		The document was revised to S5-140327.

S5-140327	Rel-12 CR 32.250 Charging management for IMS Centralized Services (ICS)
					32.250	  CR-0038  rev 2 (-) v..
					Source: NSN

(Replaces S5-140315)

Decision: 		The document was agreed.

S5-140212	Rel-12 CR 32.298 Charging management for IMS Centralized Services (ICS)
					32.298	  CR-0442  (Re-12) v..
					Source: NSN

Abstract:

-

Decision: 		The document was revised to S5-140328.

S5-140328	Rel-12 CR 32.298 Charging management for IMS Centralized Services (ICS)
					32.298	  CR-0442  rev 1 (-) v..
					Source: NSN

(Replaces S5-140212)

Decision: 		The document was agreed.

### 8.5	Application Based Charging

#### 8.5.1	Charging for Application Based Charging

S5-140053	Rel-12 CR 32.251 Requirements and parameters alignment for application based charging
					32.251	  CR-0340  (Rel-12) v..
					Source: Allot

Abstract:

Resolutions for Open Issues and some alignments are introduced for application based charging.

Discussion:

Incorporate S5-140053 with S5-140145 in S5-140317

Decision: 		The document was revised to S5-140317.

S5-140145	Rel-12 CR 32.251 Corrections for ABC
					32.251	  CR-0350  (Rel-12) v..
					Source: Ericsson

Abstract:

-

Discussion:

Incorporate  S5-140145 with S5-140053 in S5-140317

Decision: 		The document was revised to S5-140317.

S5-140317	Rel-12 CR 32.251 Requirements and parameters alignment for application based charging
					32.251	  CR-0340  rev 1 (-) v..
					Source: Allot

(Replaces S5-140053)

Abstract:

Merged S5-140053 with S5-140145 in S5-140317

Decision: 		The document was agreed.

S5-140054	Rel-12 CR 32.298 Additional AVPs definitions and clarifications for application based charging
					32.298	  CR-0426  (Rel-12) v..
					Source: Allot

Abstract:

Alignment with TS 32.251 for ABC related AVPs is introduced

Decision: 		The document was noted.

S5-140055	Rel-12 CR 32.299 Additional AVPs definitions and clarifications for application based charging
					32.299	  CR-0570  (Rel-12) v..
					Source: Allot

Abstract:

Alignment with TS 32.251 for ABC related AVPs is introduced.

Decision: 		The document was noted.

S5-140080	Rel-12 32.251 Clarify Application based charging chapters apply to TDF
					32.251	  CR-0344  (Rel-12) v..
					Source: Alcatel-Lucent

Abstract:

-

Decision: 		The document was withdrawn.

S5-140144	DP on Rel-12 issues on ABC in TS 32.251
					Source: Ericsson

Abstract:

-

Decision: 		The document was noted.

S5-140194	Reply LS from SA2 to SA5 on providing Charging Characteristics to TDF
					Source: S2-134575

Abstract:

Reply LS from SA2 to SA5, CT3 on providing Charging Characteristics (CC) to TDF (Rel-12, Work Item: ABC)

SA2 informs that in order to transfer CC to TDF, the PCEF shall send CC to PCRF at session establishment if CC are available.

Then the PCRF shall transfer CC to TDF if charging is applicable for TDF and if this information is received from the PCEF in previous step. The PCRF may modify CC received from PCEF based on operator policies.

In case TDF receives both CC and Charging Information (CI) & Default charging method parameters, the CI & Default charging method shall supersede the values received in CC.

23.203CR#0855 attached

Decision: 		The document was noted.

S5-140318	Rel-12 CR 32.251 Add support for TDF into Failure Situations
					32.251	  CR-0359  (-) v..
					Source: Openet, Allot

Decision: 		The document was agreed.

### 8.6	BB1: Policy and Charging Control for supporting traffic from fixed terminals and NSWO (Non Seamless WLAN Offload) traffic from 3GPP UEs in fixed broadband access networks

#### 8.6.1	Policy and Charging Enforcement Function (PCEF) based Charging for traffic from fixed terminals and NSWO traffic from 3GPP UEs in fixed broadband access networks

S5-140051	Rel-12 CR 32.299 Addition of Fixed User Subscription Identifier
					32.299	  CR-0569  (Rel-12) v..
					Source: Allot

Abstract:

Subscription Id for fixed user is introduced and reference is added to Broadband Forum TR

Decision: 		The document was revised to S5-140335.

S5-140335	Rel-12 CR 32.299 Addition of Fixed User Subscription Identifier
					32.299	  CR-0569  rev 1 (-) v..
					Source: Allot

(Replaces S5-140051)

Decision: 		The document was agreed.

S5-140052	Rel-12 CR 32.251 Resolution for Open Issues, alignments and corrections for Fixed Broadband Access Annex
					32.251	  CR-0341  (Rel-12) v..
					Source: Allot

Abstract:

Resolutions for Open Issues and some alignments are introduced for Fixed Broadband Access coverage.

Decision: 		The document was revised to S5-140334.

S5-140334	Rel-12 CR 32.251 Resolution for Open Issues, alignments and corrections for Fixed Broadband Access Annex
					32.251	  CR-0341  rev 1 (-) v..
					Source: Allot

(Replaces S5-140052)

Decision: 		The document was agreed.

S5-140169	Rel-12 CR 32.251 Use of Bp Reference Point for CDR files transfer
					32.251	  CR-0354  (Rel-12) v..
					Source: Alcatel-Lucent

Abstract:

-

Decision: 		The document was revised to S5-140329.

S5-140329	Rel-12 CR 32.251 Use of Bp Reference Point for CDR files transfer
					32.251	  CR-0354  rev 1 (-) v..
					Source: Alcatel-Lucent

(Replaces S5-140169)

Decision: 		The document was agreed.

S5-140170	Rel-12 CR 32.251 Add requirements and clarify miscellaneous charging information
					32.251	  CR-0355  (Rel-12) v..
					Source: Alcatel-Lucent

Abstract:

-

Discussion:

Merged S5-140183 with S5-140170 in S5-140330

Decision: 		The document was revised to S5-140330.

S5-140183	Rel-12 CR 32.251 Corrections for Fixed Broadband Access
					32.251	  CR-0357  (12) v..
					Source: Ericsson

Abstract:

-

Discussion:

Merged S5-140183 with S5-140170 in S5-140330

Decision: 		The document was revised to S5-140330.

S5-140330	Rel-12 CR 32.251 Add requirements and clarify miscellaneous charging information
					32.251	  CR-0355  rev 1 (-) v..
					Source: Alcatel-Lucent

(Replaces S5-140170)

Abstract:

Merger of S5-140183 with S5-140170 in S5-140330

Decision: 		The document was agreed.

S5-140171	Rel-12 CR 32.251 Introduce IPE-CDR description and PS Charging information
					32.251	  CR-0356  (Rel-12) v..
					Source: Alcatel-Lucent

Abstract:

-

Decision: 		The document was revised to S5-140331.

S5-140331	Rel-12 CR 32.251 Introduce IPE-CDR description and PS Charging information
					32.251	  CR-0356  rev 1 (-) v..
					Source: Alcatel-Lucent

(Replaces S5-140171)

Decision: 		The document was agreed.

S5-140332	Rel-12 CR 32.251 Corrections for Fixed Broadband Access
					32.251	  CR-0357  rev 1 (-) v..
					Source: Ericsson

(Replaces S5-140183)

Decision: 		The document was withdrawn.

S5-140333	Rel-12 CR 32.251 Requirements and parameters alignment for application based charging for online scenarios
					32.251	  CR-0360  rev (-) v..
					Source: Allot Communications, Openet , Orange, Ericsson

Decision: 		The document was agreed.

#### 8.6.2	Traffic Detection Function (TDF) based Charging for traffic from fixed terminals and NSWO traffic from 3GPP UEs in fixed broadband access networks

### 8.7	Charging Studies

#### 8.7.1	Study on Charging aspects on Roaming End-to-end scenarios with VoLTE IMS and interconnecting networks

S5-140118	Draft TR 32.8xy Study on Charging aspects on Roaming End-to-end scenarios with VoLTE IMS and interconnecting networks (FS_REVOLTE_IMS_CH)
					TR 32.8xy Study on Charging aspects on Roaming End-to-end 	scenarios with VoLTE IMS and interconnecting networks v..
					Source: Deutsche Telekom

Abstract:

Skeleton of TR

Discussion:

MCC allocated TR 32.849 for FS_REVOLTE_IMS_CH

Decision: 		The document was revised to S5-140321.

S5-140321	Draft TR 32.849 Study on Charging aspects on Roaming End-to-end scenarios with VoLTE IMS and interconnecting networks (FS_REVOLTE_IMS_CH)
					32.849 v..
					Source: Deutsche Telekom

(Replaces S5-140118)

Decision: 		The document was agreed.

S5-140119	pCR Proposed general sections for TR32.8xy FS_REVOLTE_IMS_CH
					TR32.8xy FS_REVOLTE_IMS_CH v..
					Source: Deutsche Telekom

Abstract:

-

Decision: 		The document was revised to S5-140322.

S5-140322	pCR Proposed general sections for TR 32.849 FS_REVOLTE_IMS_CH
					32.849 v..
					Source: Deutsche Telekom

(Replaces S5-140119)

Decision: 		The document was approved.

S5-140123	pCR Proposed section Overview TR32.8xy FS_REVOLTE_IMS_CH
					 TR32.8xy Study on Charging aspects on Roaming End-to-end scenarios with VoLTE IMS and interconnecting networks v..
					Source: Deutsche Telekom

Abstract:

-

Decision: 		The document was revised to S5-140323.

S5-140323	pCR Proposed section Overview TR32.849 FS_REVOLTE_IMS_CH
					32.849 v..
					Source: Deutsche Telekom

(Replaces S5-140123)

Decision: 		The document was approved.

S5-140125	pCR Proposed Section for CDR Generation TR32.8xy FS_REVOLTE_IMS_CH
					TR 32.8xy Study on Charging aspects on Roaming End-to-end scenarios with VoLTE IMS and interconnecting networks v..
					Source: Deutsche Telekom

Abstract:

-

Decision: 		The document was revised to S5-140324.

S5-140324	pCR Proposed Section for CDR Generation TR 32.849 FS_REVOLTE_IMS_CH
					32.849 v..
					Source: Deutsche Telekom

(Replaces S5-140125)

Decision: 		The document was approved.

S5-140128	pCR Section on Logical LinkID TR 32.8xy FS_REVOLTE_IMS_CH
					TR 32.8xy v..
					Source: Deutsche Telekom

Abstract:

-

Decision: 		The document was revised to S5-140325.

S5-140325	pCR Section on Logical LinkID TR 32.849 FS_REVOLTE_IMS_CH
					32.849 v..
					Source: Deutsche Telekom

(Replaces S5-140128)

Decision: 		The document was approved.

S5-140129	pCR Proposed Section on Description of Scenarios TR 32.8xy FS_REVOLTE_IMS_CH
					TR 32.8xy v..
					Source: Deutsche Telekom

Abstract:

-

Decision: 		The document was noted.

S5-140130	pCR Proposed Section on ioi TR 32.8xy FS_REVOLTE_IMS_CH
					TR32.8xy v..
					Source: Deutsche Telekom

Abstract:

-

Decision: 		The document was revised to S5-140326.

S5-140326	pCR Proposed Section on ioi TR 32.849 FS_REVOLTE_IMS_CH
					32.849 v..
					Source: Deutsche Telekom

(Replaces S5-140130)

Decision: 		The document was approved.

S5-140320	Draft TR 32.849 Study on Charging aspects on Roaming End-to-end scenarios with VoLTE IMS and interconnecting networks (FS_REVOLTE_IMS_CH)
					Source: Deutsche Telekom

Discussion:

SWG Chair: Start with S5-140320d1 the Email approval

ACTION:	Email approval of TR 32.849
	(action on: Deutsche Telekom / due by: 2014-04-01)

Decision: 		The document was for Email approval and approved.

## 9	Any Other Business

SA5 celebrated its #100th meeting (counting with the adhoc meetings as well).

A great party was organized by the host (Huawei).

## 10	Closing of the meeting

## Annex A: List of contribution documents

| Document | Title | Source | Decision | Replaces | Replaced by |
| --- | --- | --- | --- | --- | --- |
| S5-140000 | Agenda | WG Chairman | approved | - | - |
| S5-140001 | Report from last SA5 meeting | MCC | approved | - | - |
| S5-140002 | SA5 status report at last SA meeting | WG Chairman | noted | - | - |
| S5-140003 | SA5 results at last SA meeting | WG Chairman | noted | - | - |
| S5-140004 | Time Plan for OAM&P and Converged Management SWGs | WG Chairman | revised | - | S5-140225 |
| S5-140005 | OAM Executive Report from THIS Meeting | OAM SWG Chair | revised | - | S5-140297 |
| S5-140006 | Converged Management Executive report from THIS meeting | Converged Management SWG Chair | noted | - | - |
| S5-140007 | Leaders meeting agenda | WG Chairman | noted | - | - |
| S5-140008 | Leaders meeting minutes | WG Chairman | noted | - | - |
| S5-140009 | CH Agenda and Time Plan | CH SWG Chair | revised | - | S5-140301 |
| S5-140010 | CH Detailed Report from LAST Meeting | CH SWG Chair | withdrawn | - | S5-140041 |
| S5-140011 | CH Executive Report from THIS Meeting | CH SWG Chair | revised | - | S5-140361 |
| S5-140012 | CH Detailed Report from THIS Meeting | CH SWG Chair | [not addressed] | - | - |
| S5-140013 | SA5 Meeting Calendar | WG Chairman | noted | - | - |
| S5-140014 | SA5 Working Procedures | WG Chairman | noted | - | - |
| S5-140015 | SA5 Meeting Facility Requirements | WG Chairman | noted | - | - |
| S5-140016 | Process for management of draft TSs/TRs | WG ViceChair | noted | - | - |
| S5-140017 | CR Quality Check | MCC (az) | noted | - | - |
| S5-140018 | Deliverables due for the NEXT SA Plenary | MCC | revised | - | S5-140222 |
| S5-140019 | SA5 WIDs | WG Chairman | noted | - | - |
| S5-140020 | SA5 3GPP Work Plan | MCC | noted | - | - |
| S5-140021 | Minutes of OAM&P Plenary | Rapporteur | withdrawn (remove for future meetings from AND) | - | - |
| S5-140022 | Minutes of New Work Item proposals - OAM&P & Converged Management | Rapporteur | noted | - | - |
| S5-140023 | Minutes of Maintenance and Rel-12 small Enhancements - OAM&P & Converged Management | MCC | noted | - | - |
| S5-140024 | Minutes for Network Management for 3GPP Interworking WLAN - NIM part (530050) | Rapporteur | withdrawn | - | - |
| S5-140025 | Minutes for Network Management for 3GPP Interworking WLAN - PM part (530150) | Rapporteur | withdrawn | - | - |
| S5-140026 | Minutes for Energy Efficiency related Performance Measurements (600044) | Rapporteur | noted | - | - |
| S5-140027 | Minutes for Enhanced NM Centralised Coverage and Capacity Optimisation (560032) | Rapporteur | noted | - | - |
| S5-140028 | Reserved | MCC | [not addressed] | - | - |
| S5-140029 | Minutes for OAM&P 12 WLAN Management (560036) | Rapporteur | noted | - | - |
| S5-140030 | Minutes for Study on management of Heterogeneous Networks (510046) | Rapporteur | noted | - | - |
| S5-140031 | Minutes for Study on Enhancements of OAM aspects of Distributed Mobility Load Balancing (MLB) SON function | Rapporteur | revised | - | S5-140291 |
| S5-140032 | Minutes for Compliance of 3GPP SA5 specifications to the NGMN Top OPE Recommendations (560034) | Rapporteur | noted | - | - |
| S5-140033 | Minutes for TR on compliance of 3GPP SA5 specifications to the NGMN NGCOR Requirements (560435) | Rapporteur | noted | - | - |
| S5-140034 | Minutes for Converged Management Model alignment Phase 2 (560135) | Rapporteur | noted | - | - |
| S5-140035 | Minutes for Converged Management PM Interface definitions (560235) | Rapporteur | noted | - | - |
| S5-140036 | Minutes for Study on Application and Partitioning of Itf-N | Rapporteur | noted | - | - |
| S5-140037 | Minutes for Alarm Quality Improvements | Rapporteur | noted | - | - |
| S5-140038 | Minutes for Network Sharing | Rapporteur | noted | - | - |
| S5-140039 | IPR declaration | WG Chairman | noted | - | - |
| S5-140040 | pCR 32.276 Change to functional protocol names | Ericsson, Alcatel-Lucent, NSN | agreed | - | - |
| S5-140041 | CH Detailed Report from LAST Meeting | CH SWG Chair | approved | - | - |
| S5-140042 | SA5 presentation at M-SDO plenary on Dec 6th 2013 | WG Chairman | noted | - | - |
| S5-140043 | Minutes M-SDO plenary on Dec 6th 2013 WG Chairman | WG Chairman | noted | - | - |
| S5-140044 | pCR 32.276 Correction of offline charging sections | Ericsson | agreed | - | - |
| S5-140045 | pCR 32.276 Additional requirements and limitations for VCS charging | Ericsson | revised | - | S5-140308 |
| S5-140046 | DP Analysis of charging information for VCS | Ericsson | noted | - | - |
| S5-140047 | pCR 32.276 Charging information for VCS | Ericsson | revised | - | S5-140300 |
| S5-140048 | pCR 32.276 Relationship of VCS chargeable events to CAMEL events | Ericsson | revised | - | S5-140309 |
| S5-140049 | TD Presentation of Spec 32.276 to TSG | Ericsson | noted | - | - |
| S5-140050 | Rel-12 CR 32.299 Introduction of charging information for VCS | Ericsson | revised | - | S5-140313 |
| S5-140051 | Rel-12 CR 32.299 Addition of Fixed User Subscription Identifier | Allot | revised | - | S5-140335 |
| S5-140052 | Rel-12 CR 32.251 Resolution for Open Issues, alignments and corrections for Fixed Broadband Access Annex | Allot | revised | - | S5-140334 |
| S5-140053 | Rel-12 CR 32.251 Requirements and parameters alignment for application based charging | Allot | revised | - | S5-140317 |
| S5-140054 | Rel-12 CR 32.298 Additional AVPs definitions and clarifications for application based charging | Allot | noted | - | - |
| S5-140055 | Rel-12 CR 32.299 Additional AVPs definitions and clarifications for application based charging | Allot | noted | - | - |
| S5-140056 | Rel-12 CR 32425 Add UE distribution measurements | Intel | revised | - | S5-140246 |
| S5-140057 | Rel-12 CR 32752 Add mMEForMTC attribute | Intel | noted | - | - |
| S5-140058 | Rel-12 CR 32753 Add mMEForMTC attribute | Intel | noted | - | - |
| S5-140059 | Rel-12 CR 32755 Add mMEForMTC attribute | Intel | noted | - | - |
| S5-140060 | Rel-12 CR 32274 SCS Identity identified as Originator for Device Triggering | Alcatel-Lucent | agreed | - | - |
| S5-140061 | Rel-12 CR 32274 Introduction of new SC-SMO and SC-SMT CDRs description | Alcatel-Lucent | revised | - | S5-140302 |
| S5-140062 | pCR to TR 32.8xy Study on Enhancements of OAM aspects of distributed Self-Organizing Networks (SON) functions: MLB parameters alignment | Cisco | revised | - | S5-140258 |
| S5-140063 | Rel-12 CR 32274 Introduction of information for SMS offline Charging | Alcatel-Lucent | revised | - | S5-140303 |
| S5-140064 | Rel-12 CR 32274 Introduction of supported fields for SMS online Charging | Alcatel-Lucent | revised | - | S5-140303 |
| S5-140065 | pCR to TR 32.8xy Study on Enhancements of OAM aspects of distributed Self-Organizing Networks (SON) functions: Additional load information for MLB | Cisco | revised | - | S5-140260 |
| S5-140066 | Rel-10 CR 32298 Introduction of new SC-SMO and SC-SMT CDRs description | Alcatel-Lucent | agreed | - | - |
| S5-140067 | Rel-12 CR 32.299 Introduction of information for SMS offline Charging | Alcatel-Lucent | revised | - | S5-140305 |
| S5-140068 | Rel-11 CR 32.260 Correction for SIP Route header transmitted in TF CDR | Ericsson | agreed | - | - |
| S5-140069 | Rel-12 CR 32274 Improve References specifications list | Alcatel-Lucent | withdrawn | - | - |
| S5-140070 | Rel-12 CR 32.260 Correction for SIP Route header transmitted in S-CSCF CDR | Ericsson | revised | - | S5-140351 |
| S5-140071 | Rel-8 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | revised | - | S5-140337 |
| S5-140072 | Rel-9 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | revised | - | S5-140338 |
| S5-140073 | Rel-10 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | revised | - | S5-140339 |
| S5-140074 | Rel-11 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | revised | - | S5-140340 |
| S5-140075 | Rel-12 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | revised | - | S5-140341 |
| S5-140076 | Rel-11 CR 32.298 Correction for User Location Information Time | Ericsson | revised | - | S5-140352 |
| S5-140077 | Rel-12 CR 32.298 Correction for User Location Information Time | Ericsson | revised | - | S5-140353 |
| S5-140078 | Rel-11 CR 32.251 Application based charging in case of PCEF enhanced with ADC-alignment with TS 23.203 | Alcatel-Lucent | revised | - | S5-140354 |
| S5-140079 | Rel-12 CR 32.251 Application based charging in case of PCEF enhanced with ADC - alignment with TS 23.203 | Alcatel-Lucent | revised | - | S5-140355 |
| S5-140080 | Rel-12 32.251 Clarify Application based charging chapters apply to TDF | Alcatel-Lucent | withdrawn | - | - |
| S5-140081 | Rel-8 CR 32.298 Correction on Serving Node PLMN Identifier ASN.1 value in SGSN record | Alcatel-Lucent | agreed | - | - |
| S5-140082 | Rel-12 CR 32.297 Add File transfer for SMS CDRs from SMS-SC - Bsm Interface | Alcatel-Lucent | agreed | - | - |
| S5-140083 | DP on remote monitoring | Intel | withdrawn | - | - |
| S5-140084 | pCR TR 32.841 WLAN alarm notification | Intel | noted | - | - |
| S5-140085 | pCR TR 32.841 WLAN use cases | Intel | withdrawn | - | - |
| S5-140086 | pCR on 28680-001 WLAN Requirement | Intel | revised | - | S5-140277 |
| S5-140087 | pCR on 28403-001 WLAN PM | Intel | noted | - | - |
| S5-140088 | DP of 2D UE distribution | Intel | noted | - | - |
| S5-140089 | Rel-10 CR 32.766 Add missing XML elements for SONControl and SONTargets | Huawei | revised | - | S5-140228 |
| S5-140090 | Rel-11 CR 32.422 Add missing figure for RCEF reporting example scenario | Huawei | revised | - | S5-140229 |
| S5-140091 | Rel-12 CR 32.422 Add missing figure for RCEF reporting example scenario | Huawei | revised | - | S5-140230 |
| S5-140092 | Rel-9 CR 32.522 Add missing performance measurement support for HO | Huawei | noted | - | - |
| S5-140093 | Rel-10 CR 32.522 Add missing performance measurement support for HO | Huawei | noted | - | - |
| S5-140094 | Rel-11 CR 32.522 Add missing performance measurement support for HO | Huawei | noted | - | - |
| S5-140095 | Rel-11 CR 28.628 Add missing performance measurement support for HO | Huawei | noted | - | - |
| S5-140096 | Rel-12 CR 32.300 Removal of DN max length for 28 series (Converged Management) | Ericsson | revised | - | S5-140231 |
| S5-140097 | TD Plan CRs upgrade XSD | Ericsson, Huawei | approved | - | - |
| S5-140098 | pCR on TR 32.8xy on MLB | Ericsson | revised | - | S5-140223 |
| S5-140099 | pCR to TR 32.8xy Study on Enhancements of OAM aspects of distributed Self-Organizing Networks (SON) functions: CAC definition | Cisco | withdrawn | - | - |
| S5-140100 | CR Required MBMS Bearer Capabilities | ZTE | withdrawn | - | - |
| S5-140101 | Rel-9 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging | ZTE | revised | - | S5-140347 |
| S5-140102 | Rel-10 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging | ZTE | revised | - | S5-140348 |
| S5-140103 | Rel-11 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging | ZTE | revised | - | S5-140349 |
| S5-140104 | Rel-12 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging | ZTE | revised | - | S5-140350 |
| S5-140105 | Rel-9 CR 32.298 Correction for Comment line of RequiredMBMSBearerCapabilities in eMBMS Charging | ZTE | noted | - | - |
| S5-140106 | Rel-10 CR 32.298 Correction for Comment line of RequiredMBMSBearerCapabilities in eMBMS Charging | ZTE | noted | - | - |
| S5-140107 | Rel-11 CR 32.298 Correction for Comment line of RequiredMBMSBearerCapabilities in eMBMS Charging | ZTE | noted | - | - |
| S5-140108 | Rel-12 CR 32.298 Correction for Comment line of RequiredMBMSBearerCapabilities in eMBMS Charging | ZTE | noted | - | - |
| S5-140109 | Rel-9 CR 32.251 Correction for QoS Negotiation in eMBMS charging | ZTE | noted | - | - |
| S5-140110 | Rel-9 CR 32.273 Correction for QoS Negotiation in eMBMS charging | ZTE | noted | - | - |
| S5-140111 | Rel-9 CR 32.298 Correction for QoS Negotiation in eMBMS charging | ZTE | noted | - | - |
| S5-140112 | pCR to TR 32.838 Northbound Interface for SON related parameters | Cisco | revised | - | S5-140266 |
| S5-140113 | pCR to TR 32.838 SON controlled implementation: eICIC patterns | Cisco | revised | - | S5-140267 |
| S5-140114 | pCR to TR 32.838 SON controlled implementation: eNBs association | Cisco | revised | - | S5-140268 |
| S5-140115 | pCR to TR 32.838 SON controlled implementation, Interference Control | Cisco | revised | - | S5-140269 |
| S5-140116 | pCR to TR 32.838 SON controlled implementation eICIC | Cisco | revised | - | S5-140270 |
| S5-140117 | pCR to TR 32.838 SON controlled implementation: ICIC | Cisco | revised | - | S5-140271 |
| S5-140118 | Draft TR 32.8xy Study on Charging aspects on Roaming End-to-end scenarios with VoLTE IMS and interconnecting networks (FS_REVOLTE_IMS_CH) | Deutsche Telekom | revised | - | S5-140321 |
| S5-140119 | pCR Proposed general sections for TR32.8xy FS_REVOLTE_IMS_CH | Deutsche Telekom | revised | - | S5-140322 |
| S5-140120 | pCR to TR 32.8xy Study on Enhancements of OAM aspects of distributed Self-Organizing Networks (SON) functions: HO Parameters Negotiation issues | NEC | noted | - | - |
| S5-140121 | Rel-10 CR 32.762 Add new member in blacklist | Ericsson | agreed | - | - |
| S5-140122 | Rel-10 CR 32.766 Add new member in blacklist | Ericsson | agreed | - | - |
| S5-140123 | pCR Proposed section Overview TR32.8xy FS_REVOLTE_IMS_CH | Deutsche Telekom | revised | - | S5-140323 |
| S5-140124 | Revised WID SP-130430 Study on Enhancements of OAM aspects of Distributed MLB SON function | Cisco, Rapporteur | revised | - | S5-140257 |
| S5-140125 | pCR Proposed Section for CDR Generation TR32.8xy FS_REVOLTE_IMS_CH | Deutsche Telekom | revised | - | S5-140324 |
| S5-140126 | Rel-11 CR 28.702 Correct reference and attribute properties | Ericsson | revised | - | S5-140234 |
| S5-140127 | Rel-11 CR 28.703 Correct proceduralState attribute mapping and datatype | Ericsson | revised | - | S5-140235 |
| S5-140128 | pCR Section on Logical LinkID TR 32.8xy FS_REVOLTE_IMS_CH | Deutsche Telekom | revised | - | S5-140325 |
| S5-140129 | pCR Proposed Section on Description of Scenarios TR 32.8xy FS_REVOLTE_IMS_CH | Deutsche Telekom | noted | - | - |
| S5-140130 | pCR Proposed Section on ioi TR 32.8xy FS_REVOLTE_IMS_CH | Deutsche Telekom | revised | - | S5-140326 |
| S5-140131 | pCR TR 32.841 Use Alarm IRP for reporting WLAN AP alarm | Ericsson | revised | - | S5-140276 |
| S5-140132 | Rel-8 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | revised | - | S5-140342 |
| S5-140133 | Rel-9 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | revised | - | S5-140343 |
| S5-140134 | Rel-10 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | revised | - | S5-140344 |
| S5-140135 | Rel-11 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | revised | - | S5-140345 |
| S5-140136 | New WID Radio Planning Tool interface (OAM-RPT) | NSN | revised | - | S5-140259 |
| S5-140137 | Rel-12 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | revised | - | S5-140346 |
| S5-140138 | DP on New proposed WID on Radio Planning Tool interface | NSN | noted | - | - |
| S5-140139 | Rel-8 CR 32.299 Correction for S-GW change in Change-Condition AVP | Ericsson, Vodafone | agreed | - | - |
| S5-140140 | Rel-9 CR 32.299 Correction for S-GW change in Change-Condition AVP | Ericsson, Vodafone | agreed | - | - |
| S5-140141 | Rel-10 CR 32.299 Correction for S-GW change in Change-Condition AVP | Ericsson, Vodafone | agreed | - | - |
| S5-140142 | Rel-11 CR 32.299 Correction for S-GW change in Change-Condition AVP | Ericsson, Vodafone | agreed | - | - |
| S5-140143 | Rel-12 CR 32.299 Correction for S-GW change in Change-Condition AVP | Ericsson, Vodafone | agreed | - | - |
| S5-140144 | DP on Rel-12 issues on ABC in TS 32.251 | Ericsson | noted | - | - |
| S5-140145 | Rel-12 CR 32.251 Corrections for ABC | Ericsson | revised | - | S5-140317 |
| S5-140146 | Rel-12 CR 32.299 Remove clause 6.3 Editor's Notes | Ericsson | noted | - | - |
| S5-140147 | Rel-12 CR 32.251 Corrections for CHIPS | Ericsson | revised | - | S5-140307 |
| S5-140148 | Rel-11 CR 32.251 Correction of CDR generated for SMS in the MME | Ericsson | agreed | - | - |
| S5-140149 | Rel-12 CR 32.251 Correction of CDR generated for SMS in the MME | Ericsson | agreed | - | - |
| S5-140150 | pCR to TR 32.836 Study on NM CCO SON Function: measurements in 2-dim bins | Cisco | noted | - | - |
| S5-140151 | pCR 32.130 on definitions | Orange | revised | - | S5-140254 |
| S5-140152 | pCR 32.130 on concepts and background | Orange | revised | - | S5-140249 |
| S5-140153 | pCR 32.130 on requirements | Orange | revised | - | S5-140250 |
| S5-140154 | Draft TR 32.8xy Study on Application and Partitioning of Itf-N | China Mobile | revised | - | S5-140264 |
| S5-140155 | DP on gap analysis of performance requirements | China Mobile | noted | - | - |
| S5-140156 | Rel-12 CR 32.851 Editorial Cleanup | Alcatel-Lucent | withdrawn | - | - |
| S5-140157 | Rel-12 CR 32.851 Remove hanging paragraph | Alcatel-Lucent | revised | - | S5-140240 |
| S5-140158 | Rel-9 CR 32.423 Trace Session Reference | Ericsson | revised | - | S5-140236 |
| S5-140159 | Rel-10 CR 32.423 Trace Session Reference | Ericsson | revised | - | S5-140237 |
| S5-140160 | Rel-11 CR 32.423 Trace Session Reference | Ericsson | revised | - | S5-140238 |
| S5-140161 | Rel-10 CR 32.423 MNC/MCC Optional | Ericsson | noted | - | - |
| S5-140162 | Rel-11 CR 32.423 MNC/MCC Optional | Ericsson | noted | - | - |
| S5-140163 | Rel-11 CR 32.423 TRSR | Ericsson | revised | - | S5-140239 |
| S5-140164 | pCR TR 32.835 Reduction of PM data | Ericsson | noted | - | - |
| S5-140165 | pCR for Super CR on 32111-1 Alarm mgmt definitions | Ericsson | noted | - | - |
| S5-140166 | Open Action Items for Converged Management SWG | CMAN SWG chair | withdrawn | - | - |
| S5-140167 | Revised WID Short Message Service - Service Center (SMS-SC) Offline Charging | Alcatel-Lucent | revised | - | S5-140306 |
| S5-140168 | pCR Definition of Charging Information for Voice Call Service Charging | Alcatel-Lucent | revised | - | S5-140300 |
| S5-140169 | Rel-12 CR 32.251 Use of Bp Reference Point for CDR files transfer | Alcatel-Lucent | revised | - | S5-140329 |
| S5-140170 | Rel-12 CR 32.251 Add requirements and clarify miscellaneous charging information | Alcatel-Lucent | revised | - | S5-140330 |
| S5-140171 | Rel-12 CR 32.251 Introduce IPE-CDR description and PS Charging information | Alcatel-Lucent | revised | - | S5-140331 |
| S5-140172 | Open Action Items for Converged Management SWG | CMAN SWG chair | revised | - | S5-140265 |
| S5-140173 | Revised WID Study on Enhanced NM Centralised Coverage and Capacity Optimisation | Ericsson | revised | - | S5-140275 |
| S5-140174 | pCR on CCO bin evaluation for TR 32.836 Study on NM CCO SON Function | Ericsson | revised | - | S5-140243 |
| S5-140175 | pCR on Extending CCO actions for TR 32.836 Study on NM CCO SON Function | Ericsson | noted | - | - |
| S5-140176 | pCR to TR 32.836 Add CCO PM triggering action | Ericsson | revised | - | S5-140248 |
| S5-140177 | pCR on Privacy clarifications for TR 32.836 Study on NM CCO SON Function | Ericsson | revised | - | S5-140273 |
| S5-140178 | pCR Recommendation for GERAN in TR 32.836 v1.2.1 Study on NM CCO SON Function | Ericsson | revised | - | S5-140247 |
| S5-140179 | LS from NGMN Project NGCOR to SA5 on Publication of Deliverables | NGMN NGCOR | postponed | - | - |
| S5-140180 | pCR TR 32.836 Evaluation of correlation methods | Ericsson | revised | - | S5-140282 |
| S5-140181 | Reply LS from CT1 to SA5 on Availability of SIP Instance Identifier | C1-135196 | noted | - | - |
| S5-140182 | pCR TR 32.836 MLB use case recommendation | Ericsson | noted | - | - |
| S5-140183 | Rel-12 CR 32.251 Corrections for Fixed Broadband Access | Ericsson | revised | - | S5-140330 |
| S5-140184 | Reply LS from CT3 cc SA5 on support for user location age or timestamp | C3-131852 | noted | - | - |
| S5-140185 | pCR on Clarification on impact of user consent on data collection for TR 32.836 Study on NM CCO SON Function | Huawei | revised | - | S5-140274 |
| S5-140186 | LS out to CT1 Reply LS on Availability of SIP Instance Identifier | Ericsson | noted | - | - |
| S5-140187 | LS from ETSI EE to SA5 on Cooperation for Energy Efficiency Measurements | ETSI EE | postponed | - | - |
| S5-140188 | Template for Clause 13 Automatic Inventory | Huawei | agreed | - | - |
| S5-140189 | pCR on Rapporteur clean up for TR 32.835 Study of Heterogeneous Networks Management | Ericsson | revised | - | S5-140251 |
| S5-140190 | Clarification on impact of user consent on data collection | Huawei | noted | - | - |
| S5-140191 | Reply LS from GSMA IREG to 3GPP CT4 cc SA5 on FQDNs to support Multi-vendor Plug and Play (MvPnP) feature | GSMA IREG | noted | - | - |
| S5-140192 | pCR TR 32.835 Completing the analysis of classification | Ericsson | revised | - | S5-140253 |
| S5-140193 | LS from SA2 to SA5 on the provision of IPv6 prefix length to SGW/SGSN | S2-133832 | noted | - | - |
| S5-140194 | Reply LS from SA2 to SA5 on providing Charging Characteristics to TDF | S2-134575 | noted | - | - |
| S5-140195 | pCR on Recommendations for TR 32.835 Study of Heterogeneous Networks Management | Ericsson | revised | - | S5-140252 |
| S5-140196 | LS from SA2 to SA5 on Charging aspects for Network Sharing (MOCN GWCN) | S2-134589 | noted | - | - |
| S5-140197 | Clarification on the relation between RRC connection re-establishment measurement and HO optimization | Huawei | noted | - | - |
| S5-140198 | Enhancements for HO optimization performance evaluation | Huawei | noted | - | - |
| S5-140199 | Discussion paper on Comparison of NGCOR V1.3 and V1.4 and way forward for NGCOR compliance WID | Huawei | noted | - | - |
| S5-140200 | pCR Add introduction section to TR 32.837 | Huawei | noted | - | - |
| S5-140201 | Revised WID Compliance to NGMN NGCOR Requirements | Huawei | noted | - | - |
| S5-140202 | pCR to TR 32.8xy Study on Enhancements of OAM aspects of distributed Self-Organizing Networks (SON) functions: CAC definition | Cisco, NEC | noted | - | - |
| S5-140203 | LS out to SA2, CT3 on credit control failure handling | Openet | revised | - | S5-140319 |
| S5-140204 | Rel-11 CR 32.260 Correction for SRVCC PS to CS transfer Flows through ATCF | China Mobile, Huawei | revised | - | S5-140356 |
| S5-140205 | Rel-12 CR 32.260 Correction for SRVCC PS to CS transfer Flows through ATCF | China Mobile, Huawei | revised | - | S5-140357 |
| S5-140206 | Rel-11 CR 32.260 Correction for SRVCC CS to PS transfer Flows through ATCF | China Mobile, Huawei | revised | - | S5-140358 |
| S5-140207 | Rel-12 CR 32.260 Correction for SRVCC CS to PS transfer Flows through ATCF | China Mobile, Huawei | revised | - | S5-140359 |
| S5-140208 | pCR 32.293 The examples of message flow for Proxy Function | Huawei | revised | - | S5-140311 |
| S5-140209 | Rel-12 CR 32.260 Correction of Subscriber Equipment Number and Instance Id for privacy concerns | Ericsson | noted | - | - |
| S5-140210 | Rel-12 CR 32.298 Correction of Subscriber Equipment Number and Instance Id for privacy concerns | Ericsson | noted | - | - |
| S5-140211 | Rel-12 CR 32.250 Charging management for IMS Centralized Services (ICS) | NSN | revised | - | S5-140315 |
| S5-140212 | Rel-12 CR 32.298 Charging management for IMS Centralized Services (ICS) | NSN | revised | - | S5-140328 |
| S5-140213 | Rel-12 CR 32.251 Functional update | NSN | revised | - | S5-140316 |
| S5-140214 | Status on Multi-SDO Converged Management PM Interface definitions JWG | Rapporteur | noted | - | - |
| S5-140215 | MultiSDO-JWG-ModelAlignment-Status And Next Steps | Rapporteur | noted | - | - |
| S5-140216 | Other presentations at M-SDO plenary on Dec 6th 2013 | WG Chairman | noted | - | - |
| S5-140217 | Umbrella Operation Model (UOM) Version 5.1 Draft | Editor | noted | - | - |
| S5-140218 | Resubmitted LS from CT1 to SA5 on transit IOI exchange over ISC interface | C1-131748 | postponed | - | - |
| S5-140219 | SA5 work plan status after SA5#93 | WG Chairman | [not addressed] | - | - |
| S5-140220 | pCR TR 32.841 WLAN use cases | Intel | noted | - | - |
| S5-140221 | Reply LS from GSMA SOLU to SA5 on Transit IOI clarification | GSMA SOLU | noted | - | - |
| S5-140222 | Deliverables due for the NEXT SA Plenary | MCC | noted | S5-140018 | - |
| S5-140223 | pCR to TR 32.860 FS_D_MLB_SON_OAM | Ericsson | revised | S5-140098 | S5-140263 |
| S5-140224 | Multi-SDO meeting calendar | WG Chairman | noted | - | - |
| S5-140225 | Time Plan for OAM&P and Converged Management SWGs | WG Chairman | noted | S5-140004 | - |
| S5-140226 | Rel-11 CR 32.762 Addition of not implemented parts of S5-131772 Add new member in blacklist | Ericsson | revised | - | S5-140232 |
| S5-140227 | Rel-11 CR 32.766 Addition of not implemented parts of S5-131772 Add new member in blacklist | Ericsson | revised | - | S5-140233 |
| S5-140228 | Rel-10 CR 32.766 Add missing XML elements for SONControl and SONTargets | Huawei | agreed | S5-140089 | - |
| S5-140229 | Rel-11 CR 32.422 Add missing figure for RCEF reporting example scenario | Huawei | agreed | S5-140090 | - |
| S5-140230 | Rel-12 CR 32.422 Add missing figure for RCEF reporting example scenario | Huawei | agreed | S5-140091 | - |
| S5-140231 | Rel-12 CR 32.300 Removal of DN max length for 28 series (Converged Management) | Ericsson | revised | S5-140096 | S5-140279 |
| S5-140232 | Rel-11 CR 32.762 Addition of not implemented parts of S5-131772 Add new member in blacklist | Ericsson | revised | S5-140226 | S5-140280 |
| S5-140233 | Rel-11 CR 32.766 Addition of not implemented parts of S5-131772 Add new member in blacklist | Ericsson | agreed | S5-140227 | - |
| S5-140234 | Rel-11 CR 28.702 Correct reference and attribute properties | Ericsson | agreed | S5-140126 | - |
| S5-140235 | Rel-11 CR 28.703 Correct proceduralState attribute mapping and datatype | Ericsson | agreed | S5-140127 | - |
| S5-140236 | Rel-9 CR 32.423 Trace Session Reference | Ericsson | agreed | S5-140158 | - |
| S5-140237 | Rel-10 CR 32.423 Trace Session Reference | Ericsson | agreed | S5-140159 | - |
| S5-140238 | Rel-11 CR 32.423 Trace Session Reference | Ericsson | agreed | S5-140160 | - |
| S5-140239 | Rel-11 CR 32.423 TRSR | Ericsson | agreed | S5-140163 | - |
| S5-140240 | Rel-12 CR 32.851 Remove hanging paragraph | Alcatel-Lucent | agreed | S5-140157 | - |
| S5-140241 | Report from Breakout session on IS-SS link | WG Chairman | noted | - | - |
| S5-140242 | Reply to 3GPP/SA5 Liaison Questions Regarding Performance Measurements Architecture | Broadband Forum | noted | - | - |
| S5-140243 | pCR on CCO bin evaluation for TR 32.836 Study on NM CCO SON Function | Ericsson | revised | S5-140174 | S5-140281 |
| S5-140244 | Minutes 21st meeting Multi-SDO Converged Management Model Alignment JWG | SWG Chair | noted | - | - |
| S5-140245 | Minutes 22nd meeting Multi-SDO Converged Management Model Alignment JWG | SWG Chair | noted | - | - |
| S5-140246 | Converted to pCR TR 32.841 (was Rel-12 CR 32.425 Add UE distribution measurements) | Intel | approved | S5-140056 | - |
| S5-140247 | pCR Recommendation for GERAN in TR 32.836 v1.2.1 Study on NM CCO SON Function | Ericsson | approved | S5-140178 | - |
| S5-140248 | pCR to TR 32.836 Add CCO PM triggering action | Ericsson | approved | S5-140176 | - |
| S5-140249 | pCR 32.130 on concepts and background | Orange | approved | S5-140152 | - |
| S5-140250 | pCR 32.130 on requirements | Orange | approved | S5-140153 | - |
| S5-140251 | pCR on Rapporteur clean up for TR 32.835 Study of Heterogeneous Networks Management | Ericsson | approved | S5-140189 | - |
| S5-140252 | pCR on Recommendations for TR 32.835 Study of Heterogeneous Networks Management | Ericsson | approved | S5-140195 | - |
| S5-140253 | pCR TR 32.835 Completing the analysis of classification | Ericsson | revised | S5-140192 | S5-140289 |
| S5-140254 | pCR 32.130 on definitions | Orange | approved | S5-140151 | - |
| S5-140255 | Reply LS from SA3 to SA5 (S5-132105) (cc: GSMA IREG) on securing Gy/Gyn interfaces for EPC Roaming LBO scenario | S3-140208 | noted | - | - |
| S5-140256 | Revised WID SP-130046 Study on management of Heterogeneous Networks | Ericsson | agreed (not to go to SA) | - | - |
| S5-140257 | Revised WID SP-130430 Study on Enhancements of OAM aspects of Distributed MLB SON function | Cisco | agreed (not to go to SA) | S5-140124 | - |
| S5-140258 | pCR TR 32.860 MLB Algorithms – Problem Statement (S5-140062 split into 2 pCRs S5-140258/S5-140262) | Cisco | approved | S5-140062 | - |
| S5-140259 | New WID Radio Planning Tool interface (OAM-RPT) | NSN | revised | S5-140136 | S5-140278 |
| S5-140260 | pCR TR 32.860 Problem statement – information of non-neighbours (S5-140065 split into 2 pCRs S5-140260/S5-140261) | Cisco | revised | S5-140065 | S5-140292 |
| S5-140261 | pCR to TR 32.860 FS_D_MLB_SON_OAM (S5-140065 split into 2 pCRs S5-140260/S5-140261): Additional load information for MLB | Cisco | withdrawn | S5-140065 | - |
| S5-140262 | pCR to TR 32.860 FS_D_MLB_SON_OAM (S5-140062 split into 2 pCRs S5-140258/S5-140262): MLB parameters alignment | Cisco | withdrawn | S5-140062 | - |
| S5-140263 | pCR to TR 32.860 FS_D_MLB_SON_OAM | Ericsson | withdrawn | S5-140223 | - |
| S5-140264 | Draft TR 32.861 Study on Application and Partitioning of Itf-N | China Mobile | approved | S5-140154 | - |
| S5-140265 | Open Action Items for Converged Management SWG | CMAN SWG chair | noted | S5-140172 | - |
| S5-140266 | pCR to TR 32.838 Northbound Interface for SON related parameters | Cisco | revised | S5-140112 | S5-140272 |
| S5-140267 | pCR to TR 32.838 SON controlled implementation: eICIC patterns | Cisco | approved | S5-140113 | - |
| S5-140268 | pCR to TR 32.838 SON controlled implementation: eNBs association | Cisco | approved | S5-140114 | - |
| S5-140269 | pCR to TR 32.838 SON controlled implementation, Interference Control | Cisco | withdrawn | S5-140115 | - |
| S5-140270 | pCR to TR 32.838 SON controlled implementation eICIC | Cisco | withdrawn | S5-140116 | - |
| S5-140271 | pCR to TR 32.838 SON controlled implementation: ICIC | Cisco | revised | S5-140117 | S5-140294 |
| S5-140272 | pCR to TR 32.838 Northbound Interface for SON related parameters | Cisco | withdrawn | S5-140266 | - |
| S5-140273 | pCR on Privacy clarifications for TR 32.836 Study on NM CCO SON Function | Ericsson | approved | S5-140177 | - |
| S5-140274 | pCR on Clarification on impact of user consent on data collection for TR 32.836 Study on NM CCO SON Function | Huawei | approved | S5-140185 | - |
| S5-140275 | Revised WID Study on Enhanced NM Centralised Coverage and Capacity Optimisation | Ericsson | revised | S5-140173 | S5-140283 |
| S5-140276 | pCR TR 32.841 Use Alarm IRP for reporting WLAN AP alarm | Ericsson | revised | S5-140131 | S5-140284 |
| S5-140277 | pCR TS 28.680-001 WLAN Requirement | Intel | approved | S5-140086 | - |
| S5-140278 | New WID Radio Planning Tool interface (OAM-RPTi) | NSN | revised | S5-140259 | S5-140363 |
| S5-140279 | Rel-12 CR 32.300 Removal of DN max length for 28 series (Converged Management) | Ericsson | agreed | S5-140231 | - |
| S5-140280 | Rel-11 CR 32.762 Addition of not implemented parts of S5-131772 Add new member in blacklist | Ericsson | agreed | S5-140232 | - |
| S5-140281 | pCR on CCO bin evaluation for TR 32.836 Study on NM CCO SON Function | Ericsson | noted | S5-140243 | - |
| S5-140282 | pCR TR 32.836 Evaluation of correlation methods | Ericsson | for Email approval | S5-140180 | - |
| S5-140283 | Revised WID Study on Enhanced NM Centralised Coverage and Capacity Optimisation | Ericsson | approved | S5-140275 | - |
| S5-140284 | pCR TR 32.841 Use Alarm IRP for reporting WLAN AP alarm | Ericsson | approved | S5-140276 | - |
| S5-140285 | Draft TR 32.841 WLAN impacts on Type-2 management | Intel | approved | - | - |
| S5-140286 | Draft TS 28.680 WLAN Requirements | Intel | approved | - | - |
| S5-140287 | Draft TR 32.836 Telecommunication management; Study on Network Management (NM) centralized Coverage and Capacity Optimization (CCO) Self-Organizing Networks (SON) function | Ericsson | approved | - | - |
| S5-140288 | Draft TS 32.130 Network sharing; Concepts and requirements | Orange | approved | - | - |
| S5-140289 | pCR TR 32.835 Completing the analysis of classification | Ericsson | revised | S5-140253 | S5-140293 |
| S5-140290 | Draft TR 32.835 Study on management of Heterogeneous Networks | Ericsson | approved | - | - |
| S5-140291 | Minutes for Study on Enhancements of OAM aspects of Distributed Mobility Load Balancing (MLB) SON function | Rapporteur | noted | S5-140031 | - |
| S5-140292 | pCR TR 32.860 Problem statement – information of non-neighbours (S5-140065 split into 2 pCRs S5-140260/S5-140261) | Cisco | approved | S5-140260 | - |
| S5-140293 | pCR TR 32.835 Completing the analysis of classification | Ericsson | approved | S5-140289 | - |
| S5-140294 | pCR to TR 32.838 SON controlled implementation: ICIC | Cisco | approved | S5-140271 | - |
| S5-140295 | Draft TR 32.838 Study on Compliance of 3GPP OAM specifications to the NGMN Top OPE Recommendations | Ericsson | for Email approval | - | - |
| S5-140296 | Draft TR 32.860 Study on Enhancements of OAM aspects of Distributed Mobility Load Balancing (MLB) SON function | Cisco | approved | - | - |
| S5-140297 | OAM Executive Report from THIS Meeting | OAM SWG Chair | noted | S5-140005 | - |
| S5-140300 | pCR 32.276 Charging information for VCS | Ericsson | approved | S5-140047 | - |
| S5-140301 | CH Agenda and Time Plan | CH SWG Chair | approved | S5-140009 | - |
| S5-140302 | Rel-12 CR 32274 Introduction of new SC-SMO and SC-SMT CDRs description | Alcatel-Lucent | agreed | S5-140061 | - |
| S5-140303 | Rel-12 CR 32274 Introduction of information for SMS offline Charging | Alcatel-Lucent | agreed | S5-140063 | - |
| S5-140304 | Rel-12 CR 32274 Introduction of supported fields for SMS online Charging | Alcatel-Lucent | withdrawn | S5-140064 | - |
| S5-140305 | Rel-12 CR 32.299 Introduction of information for SMS offline Charging | Alcatel-Lucent | agreed | S5-140067 | - |
| S5-140306 | Revised WID SP-120775 Short Message Service - Service Center (SMS-SC) Offline Charging | Alcatel-Lucent | revised | S5-140167 | S5-140360 |
| S5-140307 | Rel-12 CR 32.251 Corrections for CHIPS | Ericsson | agreed | S5-140147 | - |
| S5-140308 | pCR 32.276 Additional requirements and limitations for VCS charging | Ericsson | approved | S5-140045 | - |
| S5-140309 | pCR 32.276 Relationship of VCS chargeable events to CAMEL events | Ericsson | approved | S5-140048 | - |
| S5-140310 | Draft TS 32.276 Telecommunication management; Charging management; Voice call service charging | Ericsson | approved | - | - |
| S5-140311 | pCR 32.293 The examples of message flow for Proxy Function | Huawei | approved | S5-140208 | - |
| S5-140312 | Draft TS 32.293 Telecommunication management; Charging management; Proxy function | Ericsson | approved | - | - |
| S5-140313 | Rel-12 CR 32.299 Introduction of charging information for VCS | Ericsson | noted | S5-140050 | - |
| S5-140314 | DP on Availability of SIP Instance Identifier | SWG CH | agreed | - | - |
| S5-140315 | Rel-12 CR 32.250 Charging management for IMS Centralized Services (ICS) | NSN | revised | S5-140211 | S5-140327 |
| S5-140316 | Rel-12 CR 32.251 Functional update | NSN | noted | S5-140213 | - |
| S5-140317 | Rel-12 CR 32.251 Requirements and parameters alignment for application based charging | Allot | agreed | S5-140053 | - |
| S5-140318 | Rel-12 CR 32.251 Add support for TDF into Failure Situations | Openet, Allot | agreed | - | - |
| S5-140319 | LS out to SA2, CT3 on credit control failure handling | Openet | revised | S5-140203 | S5-140364 |
| S5-140320 | Draft TR 32.849 Study on Charging aspects on Roaming End-to-end scenarios with VoLTE IMS and interconnecting networks (FS_REVOLTE_IMS_CH) | Deutsche Telekom | approved | - | - |
| S5-140321 | Draft TR 32.849 Study on Charging aspects on Roaming End-to-end scenarios with VoLTE IMS and interconnecting networks (FS_REVOLTE_IMS_CH) | Deutsche Telekom | agreed | S5-140118 | - |
| S5-140322 | pCR Proposed general sections for TR 32.849 FS_REVOLTE_IMS_CH | Deutsche Telekom | approved | S5-140119 | - |
| S5-140323 | pCR Proposed section Overview TR32.849 FS_REVOLTE_IMS_CH | Deutsche Telekom | approved | S5-140123 | - |
| S5-140324 | pCR Proposed Section for CDR Generation TR 32.849 FS_REVOLTE_IMS_CH | Deutsche Telekom | approved | S5-140125 | - |
| S5-140325 | pCR Section on Logical LinkID TR 32.849 FS_REVOLTE_IMS_CH | Deutsche Telekom | approved | S5-140128 | - |
| S5-140326 | pCR Proposed Section on ioi TR 32.849 FS_REVOLTE_IMS_CH | Deutsche Telekom | approved | S5-140130 | - |
| S5-140327 | Rel-12 CR 32.250 Charging management for IMS Centralized Services (ICS) | NSN | agreed | S5-140315 | - |
| S5-140328 | Rel-12 CR 32.298 Charging management for IMS Centralized Services (ICS) | NSN | agreed | S5-140212 | - |
| S5-140329 | Rel-12 CR 32.251 Use of Bp Reference Point for CDR files transfer | Alcatel-Lucent | agreed | S5-140169 | - |
| S5-140330 | Rel-12 CR 32.251 Add requirements and clarify miscellaneous charging information | Alcatel-Lucent | agreed | S5-140170 | - |
| S5-140331 | Rel-12 CR 32.251 Introduce IPE-CDR description and PS Charging information | Alcatel-Lucent | agreed | S5-140171 | - |
| S5-140332 | Rel-12 CR 32.251 Corrections for Fixed Broadband Access | Ericsson | withdrawn | S5-140183 | - |
| S5-140333 | Rel-12 CR 32.251 Requirements and parameters alignment for application based charging for online scenarios | Allot Communications, Openet , Orange, Ericsson | agreed | - | - |
| S5-140334 | Rel-12 CR 32.251 Resolution for Open Issues, alignments and corrections for Fixed Broadband Access Annex | Allot | agreed | S5-140052 | - |
| S5-140335 | Rel-12 CR 32.299 Addition of Fixed User Subscription Identifier | Allot | agreed | S5-140051 | - |
| S5-140336 | LS out to BBF | SA5 SWG CH | revised | - | S5-140362 |
| S5-140337 | Rel-8 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | agreed | S5-140071 | - |
| S5-140338 | Rel-9 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | agreed | S5-140072 | - |
| S5-140339 | Rel-10 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | agreed | S5-140073 | - |
| S5-140340 | Rel-11 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | agreed | S5-140074 | - |
| S5-140341 | Rel-12 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | agreed | S5-140075 | - |
| S5-140342 | Rel-8 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | agreed | S5-140132 | - |
| S5-140343 | Rel-9 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | agreed | S5-140133 | - |
| S5-140344 | Rel-10 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | agreed | S5-140134 | - |
| S5-140345 | Rel-11 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | agreed | S5-140135 | - |
| S5-140346 | Rel-12 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | agreed | S5-140137 | - |
| S5-140347 | Rel-9 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging | ZTE | agreed | S5-140101 | - |
| S5-140348 | Rel-10 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging | ZTE | agreed | S5-140102 | - |
| S5-140349 | Rel-11 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging | ZTE | agreed | S5-140103 | - |
| S5-140350 | Rel-12 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging | ZTE | agreed | S5-140104 | - |
| S5-140351 | Rel-12 CR 32.260 Correction for SIP Route header transmitted in S-CSCF CDR | Ericsson | agreed | S5-140070 | - |
| S5-140352 | Rel-11 CR 32.298 Correction for User Location Information Time | Ericsson | agreed | S5-140076 | - |
| S5-140353 | Rel-12 CR 32.298 Correction for User Location Information Time | Ericsson | agreed | S5-140077 | - |
| S5-140354 | Rel-11 CR 32.251 Application based charging in case of PCEF enhanced with ADC - alignment with TS 23.203 | Alcatel-Lucent | agreed | S5-140078 | - |
| S5-140355 | Rel-12 CR 32.251 Application based charging in case of PCEF enhanced with ADC - alignment with TS 23.203 | Alcatel-Lucent | agreed | S5-140079 | - |
| S5-140356 | Rel-11 CR 32.260 Correction for SRVCC PS to CS transfer Flows through ATCF | China Mobile, Huawei | postponed | S5-140204 | - |
| S5-140357 | Rel-12 CR 32.260 Correction for SRVCC PS to CS transfer Flows through ATCF | China Mobile, Huawei | postponed | S5-140205 | - |
| S5-140358 | Rel-11 CR 32.260 Correction for SRVCC CS to PS transfer Flows through ATCF | China Mobile, Huawei | postponed | S5-140206 | - |
| S5-140359 | Rel-12 CR 32.260 Correction for SRVCC CS to PS transfer Flows through ATCF | China Mobile, Huawei | postponed | S5-140207 | - |
| S5-140360 | Revised WID SP-120775 Short Message Service - Service Center (SMS-SC) Offline Charging | Alcatel-Lucent | agreed | S5-140306 | - |
| S5-140361 | CH Executive Report from THIS Meeting | CH SWG Chair | noted | S5-140011 | - |
| S5-140362 | LS out to BBF | SA5 SWG CH | noted | S5-140336 | - |
| S5-140363 | New WID Radio Planning Tool interface (OAM-RPT) | NSN | agreed | S5-140278 | - |
| S5-140364 | LS out to SA2, CT3 on credit control failure handling | Openet | approved | S5-140319 | - |
| S5-140365 | WID Enhanced NM Centralised Coverage and Capacity Optimisation | Ericsson | approved | - | - |

## Annex B: List of change requests

| Document | Title | Source | Spec | CR | Rev | Rel | Cat | WI | Decision |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| S5-140100 | CR Required MBMS Bearer Capabilities | ZTE | - | - | - | - | - | - | withdrawn |
| S5-140095 | Rel-11 CR 28.628 Add missing performance measurement support for HO | Huawei | 28.628 | 0006 | - | Rel-11 | - | - | noted |
| S5-140126 | Rel-11 CR 28.702 Correct reference and attribute properties | Ericsson | 28.702 | 0002 | - | Rel-11 | - | - | revised |
| S5-140234 | Rel-11 CR 28.702 Correct reference and attribute properties | Ericsson | 28.702 | 0002 | 1 | - | - | - | agreed |
| S5-140127 | Rel-11 CR 28.703 Correct proceduralState attribute mapping and datatype | Ericsson | 28.703 | 0001 | - | Rel-11 | - | - | revised |
| S5-140235 | Rel-11 CR 28.703 Correct proceduralState attribute mapping and datatype | Ericsson | 28.703 | 0001 | 1 | - | - | - | agreed |
| S5-140211 | Rel-12 CR 32.250 Charging management for IMS Centralized Services (ICS) | NSN | 32.250 | 0038 | - | Re-12 | C | CHICS | revised |
| S5-140315 | Rel-12 CR 32.250 Charging management for IMS Centralized Services (ICS) | NSN | 32.250 | 0038 | 1 | - | C | CHICS | revised |
| S5-140327 | Rel-12 CR 32.250 Charging management for IMS Centralized Services (ICS) | NSN | 32.250 | 0038 | 2 | - | C | CHICS | agreed |
| S5-140053 | Rel-12 CR 32.251 Requirements and parameters alignment for application based charging | Allot | 32.251 | 0340 | - | Rel-12 | B | ABC | revised |
| S5-140317 | Rel-12 CR 32.251 Requirements and parameters alignment for application based charging | Allot | 32.251 | 0340 | 1 | - | B | ABC | agreed |
| S5-140052 | Rel-12 CR 32.251 Resolution for Open Issues, alignments and corrections for Fixed Broadband Access Annex | Allot | 32.251 | 0341 | - | Rel-12 | B | P4C-F-CH_T, P4C-F-CH_P | revised |
| S5-140334 | Rel-12 CR 32.251 Resolution for Open Issues, alignments and corrections for Fixed Broadband Access Annex | Allot | 32.251 | 0341 | 1 | - | B | P4C-F-CH_T, P4C-F-CH_P | agreed |
| S5-140078 | Rel-11 CR 32.251 Application based charging in case of PCEF enhanced with ADC-alignment with TS 23.203 | Alcatel-Lucent | 32.251 | 0342 | - | Rel-11 | - | - | revised |
| S5-140354 | Rel-11 CR 32.251 Application based charging in case of PCEF enhanced with ADC - alignment with TS 23.203 | Alcatel-Lucent | 32.251 | 0342 | 1 | - | - | - | agreed |
| S5-140079 | Rel-12 CR 32.251 Application based charging in case of PCEF enhanced with ADC - alignment with TS 23.203 | Alcatel-Lucent | 32.251 | 0343 | - | Rel-12 | - | - | revised |
| S5-140355 | Rel-12 CR 32.251 Application based charging in case of PCEF enhanced with ADC - alignment with TS 23.203 | Alcatel-Lucent | 32.251 | 0343 | 1 | - | - | - | agreed |
| S5-140080 | Rel-12 32.251 Clarify Application based charging chapters apply to TDF | Alcatel-Lucent | 32.251 | 0344 | - | Rel-12 | - | - | withdrawn |
| S5-140101 | Rel-9 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging | ZTE | 32.251 | 0345 | - | Rel-9 | - | - | revised |
| S5-140347 | Rel-9 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging | ZTE | 32.251 | 0345 | 1 | - | - | - | agreed |
| S5-140102 | Rel-10 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging | ZTE | 32.251 | 0346 | - | Rel-10 | - | - | revised |
| S5-140348 | Rel-10 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging | ZTE | 32.251 | 0346 | 1 | - | - | - | agreed |
| S5-140103 | Rel-11 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging | ZTE | 32.251 | 0347 | - | Rel-11 | - | - | revised |
| S5-140349 | Rel-11 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging | ZTE | 32.251 | 0347 | 1 | - | - | - | agreed |
| S5-140104 | Rel-12 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging | ZTE | 32.251 | 0348 | - | Rel-12 | - | - | revised |
| S5-140350 | Rel-12 CR 32.251 Correction for Partial Record Closure Reason in eMBMS Charging | ZTE | 32.251 | 0348 | 1 | - | - | - | agreed |
| S5-140109 | Rel-9 CR 32.251 Correction for QoS Negotiation in eMBMS charging | ZTE | 32.251 | 0349 | - | Rel-9 | - | - | noted |
| S5-140145 | Rel-12 CR 32.251 Corrections for ABC | Ericsson | 32.251 | 0350 | - | Rel-12 | F | ABC | revised |
| S5-140147 | Rel-12 CR 32.251 Corrections for CHIPS | Ericsson | 32.251 | 0351 | - | Rel-12 | F | CHIPS | revised |
| S5-140307 | Rel-12 CR 32.251 Corrections for CHIPS | Ericsson | 32.251 | 0351 | 1 | - | F | CHIPS | agreed |
| S5-140148 | Rel-11 CR 32.251 Correction of CDR generated for SMS in the MME | Ericsson | 32.251 | 0352 | - | Rel-11 | F | SIMTC-CH | agreed |
| S5-140149 | Rel-12 CR 32.251 Correction of CDR generated for SMS in the MME | Ericsson | 32.251 | 0353 | - | Rel-12 | A | SIMTC-CH | agreed |
| S5-140169 | Rel-12 CR 32.251 Use of Bp Reference Point for CDR files transfer | Alcatel-Lucent | 32.251 | 0354 | - | Rel-12 | - | - | revised |
| S5-140329 | Rel-12 CR 32.251 Use of Bp Reference Point for CDR files transfer | Alcatel-Lucent | 32.251 | 0354 | 1 | - | - | - | agreed |
| S5-140170 | Rel-12 CR 32.251 Add requirements and clarify miscellaneous charging information | Alcatel-Lucent | 32.251 | 0355 | - | Rel-12 | - | - | revised |
| S5-140330 | Rel-12 CR 32.251 Add requirements and clarify miscellaneous charging information | Alcatel-Lucent | 32.251 | 0355 | 1 | - | - | - | agreed |
| S5-140171 | Rel-12 CR 32.251 Introduce IPE-CDR description and PS Charging information | Alcatel-Lucent | 32.251 | 0356 | - | Rel-12 | - | - | revised |
| S5-140331 | Rel-12 CR 32.251 Introduce IPE-CDR description and PS Charging information | Alcatel-Lucent | 32.251 | 0356 | 1 | - | - | - | agreed |
| S5-140183 | Rel-12 CR 32.251 Corrections for Fixed Broadband Access | Ericsson | 32.251 | 0357 | - | 12 | F | P4C-F-CH_P | revised |
| S5-140332 | Rel-12 CR 32.251 Corrections for Fixed Broadband Access | Ericsson | 32.251 | 0357 | 1 | - | F | P4C-F-CH_P | withdrawn |
| S5-140213 | Rel-12 CR 32.251 Functional update | NSN | 32.251 | 0358 | - | rel-12 | F | CH12 | revised |
| S5-140316 | Rel-12 CR 32.251 Functional update | NSN | 32.251 | 0358 | 1 | - | F | CH12 | noted |
| S5-140318 | Rel-12 CR 32.251 Add support for TDF into Failure Situations | Openet, Allot | 32.251 | 0359 | - | - | B | ABC | agreed |
| S5-140333 | Rel-12 CR 32.251 Requirements and parameters alignment for application based charging for online scenarios | Allot Communications, Openet , Orange, Ericsson | 32.251 | 0360 | - | - | B | ABC | agreed |
| S5-140068 | Rel-11 CR 32.260 Correction for SIP Route header transmitted in TF CDR | Ericsson | 32.260 | 0242 | - | Rel-11 | F | RAVEL-CH | agreed |
| S5-140070 | Rel-12 CR 32.260 Correction for SIP Route header transmitted in S-CSCF CDR | Ericsson | 32.260 | 0243 | - | Rel-12 | F | RAVEL-CH | revised |
| S5-140351 | Rel-12 CR 32.260 Correction for SIP Route header transmitted in S-CSCF CDR | Ericsson | 32.260 | 0243 | 1 | - | F | RAVEL-CH | agreed |
| S5-140209 | Rel-12 CR 32.260 Correction of Subscriber Equipment Number and Instance Id for privacy concerns | Ericsson | 32.260 | 0244 | - | Rel-12 | F | CH12 | noted |
| S5-140204 | Rel-11 CR 32.260 Correction for SRVCC PS to CS transfer Flows through ATCF | China Mobile, Huawei | 32.260 | 0245 | - | Rel-11 | - | - | revised |
| S5-140356 | Rel-11 CR 32.260 Correction for SRVCC PS to CS transfer Flows through ATCF | China Mobile, Huawei | 32.260 | 0245 | 1 | - | - | - | postponed |
| S5-140205 | Rel-12 CR 32.260 Correction for SRVCC PS to CS transfer Flows through ATCF | China Mobile, Huawei | 32.260 | 0246 | - | Rel-12 | - | - | revised |
| S5-140357 | Rel-12 CR 32.260 Correction for SRVCC PS to CS transfer Flows through ATCF | China Mobile, Huawei | 32.260 | 0246 | 1 | - | - | - | postponed |
| S5-140206 | Rel-11 CR 32.260 Correction for SRVCC CS to PS transfer Flows through ATCF | China Mobile, Huawei | 32.260 | 0247 | - | Rel-11 | - | - | revised |
| S5-140358 | Rel-11 CR 32.260 Correction for SRVCC CS to PS transfer Flows through ATCF | China Mobile, Huawei | 32.260 | 0247 | 1 | - | - | - | postponed |
| S5-140207 | Rel-12 CR 32.260 Correction for SRVCC CS to PS transfer Flows through ATCF | China Mobile, Huawei | 32.260 | 0248 | - | Rel-12 | - | - | revised |
| S5-140359 | Rel-12 CR 32.260 Correction for SRVCC CS to PS transfer Flows through ATCF | China Mobile, Huawei | 32.260 | 0248 | 1 | - | - | - | postponed |
| S5-140110 | Rel-9 CR 32.273 Correction for QoS Negotiation in eMBMS charging | ZTE | 32.273 | 0026 | - | Rel-9 | - | - | noted |
| S5-140063 | Rel-12 CR 32274 Introduction of information for SMS offline Charging | Alcatel-Lucent | 32.274 | 0024 | - | Rel-12 | - | - | revised |
| S5-140303 | Rel-12 CR 32274 Introduction of information for SMS offline Charging | Alcatel-Lucent | 32.274 | 0024 | 1 | - | - | - | agreed |
| S5-140064 | Rel-12 CR 32274 Introduction of supported fields for SMS online Charging | Alcatel-Lucent | 32.274 | 0025 | - | Rel-12 | - | - | revised |
| S5-140304 | Rel-12 CR 32274 Introduction of supported fields for SMS online Charging | Alcatel-Lucent | 32.274 | 0025 | 1 | - | - | - | withdrawn |
| S5-140069 | Rel-12 CR 32274 Improve References specifications list | Alcatel-Lucent | 32.274 | 0026 | - | Rel-12 | - | - | withdrawn |
| S5-140060 | Rel-12 CR 32274 SCS Identity identified as Originator for Device Triggering | Alcatel-Lucent | 32.274 | 0027 | - | Rel-12 | - | - | agreed |
| S5-140061 | Rel-12 CR 32274 Introduction of new SC-SMO and SC-SMT CDRs description | Alcatel-Lucent | 32.274 | 0028 | - | Rel-12 | - | - | revised |
| S5-140302 | Rel-12 CR 32274 Introduction of new SC-SMO and SC-SMT CDRs description | Alcatel-Lucent | 32.274 | 0028 | 1 | - | - | - | agreed |
| S5-140082 | Rel-12 CR 32.297 Add File transfer for SMS CDRs from SMS-SC - Bsm Interface | Alcatel-Lucent | 32.297 | 0014 | - | Rel-12 | - | - | agreed |
| S5-140054 | Rel-12 CR 32.298 Additional AVPs definitions and clarifications for application based charging | Allot | 32.298 | 0426 | - | Rel-12 | B | ABC | noted |
| S5-140076 | Rel-11 CR 32.298 Correction for User Location Information Time | Ericsson | 32.298 | 0427 | - | Rel-11 | F | CH11 | revised |
| S5-140352 | Rel-11 CR 32.298 Correction for User Location Information Time | Ericsson | 32.298 | 0427 | 1 | - | F | CH11 | agreed |
| S5-140077 | Rel-12 CR 32.298 Correction for User Location Information Time | Ericsson | 32.298 | 0428 | - | Rel-12 | A | CH11 | revised |
| S5-140353 | Rel-12 CR 32.298 Correction for User Location Information Time | Ericsson | 32.298 | 0428 | 1 | - | A | CH11 | agreed |
| S5-140066 | Rel-10 CR 32298 Introduction of new SC-SMO and SC-SMT CDRs description | Alcatel-Lucent | 32.298 | 0429 | - | Rel-10 | - | - | agreed |
| S5-140081 | Rel-8 CR 32.298 Correction on Serving Node PLMN Identifier ASN.1 value in SGSN record | Alcatel-Lucent | 32.298 | 0430 | - | Rel-8 | - | - | agreed |
| S5-140105 | Rel-9 CR 32.298 Correction for Comment line of RequiredMBMSBearerCapabilities in eMBMS Charging | ZTE | 32.298 | 0431 | - | Rel-9 | - | - | noted |
| S5-140106 | Rel-10 CR 32.298 Correction for Comment line of RequiredMBMSBearerCapabilities in eMBMS Charging | ZTE | 32.298 | 0432 | - | Rel-10 | - | - | noted |
| S5-140107 | Rel-11 CR 32.298 Correction for Comment line of RequiredMBMSBearerCapabilities in eMBMS Charging | ZTE | 32.298 | 0433 | - | Rel-11 | - | - | noted |
| S5-140108 | Rel-12 CR 32.298 Correction for Comment line of RequiredMBMSBearerCapabilities in eMBMS Charging | ZTE | 32.298 | 0434 | - | Rel-12 | - | - | noted |
| S5-140111 | Rel-9 CR 32.298 Correction for QoS Negotiation in eMBMS charging | ZTE | 32.298 | 0435 | - | Rel-9 | - | - | noted |
| S5-140132 | Rel-8 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | 32.298 | 0436 | - | Rel-8 | F | CH8 | revised |
| S5-140342 | Rel-8 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | 32.298 | 0436 | 1 | - | F | CH8 | agreed |
| S5-140133 | Rel-9 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | 32.298 | 0437 | - | Rel-9 | A | CH8 | revised |
| S5-140343 | Rel-9 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | 32.298 | 0437 | 1 | - | A | CH8 | agreed |
| S5-140134 | Rel-10 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | 32.298 | 0438 | - | Rel-10 | A | CH8 | revised |
| S5-140344 | Rel-10 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | 32.298 | 0438 | 1 | - | A | CH8 | agreed |
| S5-140135 | Rel-11 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | 32.298 | 0439 | - | Rel-11 | A | CH8 | revised |
| S5-140345 | Rel-11 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | 32.298 | 0439 | 1 | - | A | CH8 | agreed |
| S5-140137 | Rel-12 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | 32.298 | 0440 | - | Rel-12 | A | CH8 | revised |
| S5-140346 | Rel-12 CR 32.298 Correction for S-GW change cause for record closing | Ericsson, Vodafone | 32.298 | 0440 | 1 | - | A | CH8 | agreed |
| S5-140210 | Rel-12 CR 32.298 Correction of Subscriber Equipment Number and Instance Id for privacy concerns | Ericsson | 32.298 | 0441 | - | Rel-12 | F | CH12 | noted |
| S5-140212 | Rel-12 CR 32.298 Charging management for IMS Centralized Services (ICS) | NSN | 32.298 | 0442 | - | Re-12 | C | CHICS | revised |
| S5-140328 | Rel-12 CR 32.298 Charging management for IMS Centralized Services (ICS) | NSN | 32.298 | 0442 | 1 | - | C | CHICS | agreed |
| S5-140050 | Rel-12 CR 32.299 Introduction of charging information for VCS | Ericsson | 32.299 | 0568 | - | Rel-12 | B | CHARP | revised |
| S5-140313 | Rel-12 CR 32.299 Introduction of charging information for VCS | Ericsson | 32.299 | 0568 | 1 | - | B | CHARP | noted |
| S5-140051 | Rel-12 CR 32.299 Addition of Fixed User Subscription Identifier | Allot | 32.299 | 0569 | - | Rel-12 | B | P4C-F-CH_T, P4C-F-CH_P | revised |
| S5-140335 | Rel-12 CR 32.299 Addition of Fixed User Subscription Identifier | Allot | 32.299 | 0569 | 1 | - | B | P4C-F-CH_T, P4C-F-CH_P | agreed |
| S5-140055 | Rel-12 CR 32.299 Additional AVPs definitions and clarifications for application based charging | Allot | 32.299 | 0570 | - | Rel-12 | B | ABC | noted |
| S5-140071 | Rel-8 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | 32.299 | 0571 | - | Rel-8 | F | CH8 | revised |
| S5-140337 | Rel-8 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | 32.299 | 0571 | 1 | - | F | CH8 | agreed |
| S5-140072 | Rel-9 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | 32.299 | 0572 | - | Rel-9 | A | CH8 | revised |
| S5-140338 | Rel-9 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | 32.299 | 0572 | 1 | - | A | CH8 | agreed |
| S5-140073 | Rel-10 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | 32.299 | 0573 | - | Rel-10 | A | CH8 | revised |
| S5-140339 | Rel-10 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | 32.299 | 0573 | 1 | - | A | CH8 | agreed |
| S5-140074 | Rel-11 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | 32.299 | 0574 | - | Rel-11 | A | CH8 | revised |
| S5-140340 | Rel-11 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | 32.299 | 0574 | 1 | - | A | CH8 | agreed |
| S5-140075 | Rel-12 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | 32.299 | 0575 | - | Rel-12 | A | CH8 | revised |
| S5-140341 | Rel-12 CR 32.299 Correction of data type for Time-Usage and applicability of Service-Specific-Info and AF-Charging-Identifier | Ericsson | 32.299 | 0575 | 1 | - | A | CH8 | agreed |
| S5-140067 | Rel-12 CR 32.299 Introduction of information for SMS offline Charging | Alcatel-Lucent | 32.299 | 0576 | - | Rel-12 | - | - | revised |
| S5-140305 | Rel-12 CR 32.299 Introduction of information for SMS offline Charging | Alcatel-Lucent | 32.299 | 0576 | 1 | - | - | - | agreed |
| S5-140139 | Rel-8 CR 32.299 Correction for S-GW change in Change-Condition AVP | Ericsson, Vodafone | 32.299 | 0577 | - | Rel-8 | F | CH8 | agreed |
| S5-140140 | Rel-9 CR 32.299 Correction for S-GW change in Change-Condition AVP | Ericsson, Vodafone | 32.299 | 0578 | - | Rel-9 | A | CH8 | agreed |
| S5-140141 | Rel-10 CR 32.299 Correction for S-GW change in Change-Condition AVP | Ericsson, Vodafone | 32.299 | 0579 | - | Rel-10 | A | CH8 | agreed |
| S5-140142 | Rel-11 CR 32.299 Correction for S-GW change in Change-Condition AVP | Ericsson, Vodafone | 32.299 | 0580 | - | Rel-11 | A | CH8 | agreed |
| S5-140143 | Rel-12 CR 32.299 Correction for S-GW change in Change-Condition AVP | Ericsson, Vodafone | 32.299 | 0581 | - | Rel-12 | A | CH8 | agreed |
| S5-140146 | Rel-12 CR 32.299 Remove clause 6.3 Editor's Notes | Ericsson | 32.299 | 0582 | - | Rel-12 | F | CH12 | noted |
| S5-140096 | Rel-12 CR 32.300 Removal of DN max length for 28 series (Converged Management) | Ericsson | 32.300 | 0016 | - | Rel-12 | - | - | revised |
| S5-140231 | Rel-12 CR 32.300 Removal of DN max length for 28 series (Converged Management) | Ericsson | 32.300 | 0016 | 1 | - | - | - | revised |
| S5-140279 | Rel-12 CR 32.300 Removal of DN max length for 28 series (Converged Management) | Ericsson | 32.300 | 0016 | 2 | - | - | - | agreed |
| S5-140090 | Rel-11 CR 32.422 Add missing figure for RCEF reporting example scenario | Huawei | 32.422 | 0261 | - | Rel-11 | - | - | revised |
| S5-140229 | Rel-11 CR 32.422 Add missing figure for RCEF reporting example scenario | Huawei | 32.422 | 0261 | 1 | - | - | - | agreed |
| S5-140091 | Rel-12 CR 32.422 Add missing figure for RCEF reporting example scenario | Huawei | 32.422 | 0262 | - | Rel-12 | - | - | revised |
| S5-140230 | Rel-12 CR 32.422 Add missing figure for RCEF reporting example scenario | Huawei | 32.422 | 0262 | 1 | - | - | - | agreed |
| S5-140158 | Rel-9 CR 32.423 Trace Session Reference | Ericsson | 32.423 | 0077 | - | Rel-9 | - | - | revised |
| S5-140236 | Rel-9 CR 32.423 Trace Session Reference | Ericsson | 32.423 | 0077 | 1 | - | - | - | agreed |
| S5-140159 | Rel-10 CR 32.423 Trace Session Reference | Ericsson | 32.423 | 0078 | - | Rel-10 | - | - | revised |
| S5-140237 | Rel-10 CR 32.423 Trace Session Reference | Ericsson | 32.423 | 0078 | 1 | - | - | - | agreed |
| S5-140160 | Rel-11 CR 32.423 Trace Session Reference | Ericsson | 32.423 | 0079 | - | Rel-11 | - | - | revised |
| S5-140238 | Rel-11 CR 32.423 Trace Session Reference | Ericsson | 32.423 | 0079 | 1 | - | - | - | agreed |
| S5-140161 | Rel-10 CR 32.423 MNC/MCC Optional | Ericsson | 32.423 | 0080 | - | Rel-10 | - | - | noted |
| S5-140162 | Rel-11 CR 32.423 MNC/MCC Optional | Ericsson | 32.423 | 0081 | - | Rel-11 | - | - | noted |
| S5-140163 | Rel-11 CR 32.423 TRSR | Ericsson | 32.423 | 0082 | - | Rel-11 | - | - | revised |
| S5-140239 | Rel-11 CR 32.423 TRSR | Ericsson | 32.423 | 0082 | 1 | - | - | - | agreed |
| S5-140056 | Rel-12 CR 32425 Add UE distribution measurements | Intel | 32.425 | 0147 | - | Rel-12 | - | - | revised |
| S5-140092 | Rel-9 CR 32.522 Add missing performance measurement support for HO | Huawei | 32.522 | 0143 | - | Rel-9 | - | - | noted |
| S5-140093 | Rel-10 CR 32.522 Add missing performance measurement support for HO | Huawei | 32.522 | 0144 | - | Rel-10 | - | - | noted |
| S5-140094 | Rel-11 CR 32.522 Add missing performance measurement support for HO | Huawei | 32.522 | 0145 | - | Rel-11 | - | - | noted |
| S5-140057 | Rel-12 CR 32752 Add mMEForMTC attribute | Intel | 32.752 | 0017 | - | Rel-12 | - | - | noted |
| S5-140058 | Rel-12 CR 32753 Add mMEForMTC attribute | Intel | 32.753 | 0010 | - | Rel-12 | - | - | noted |
| S5-140059 | Rel-12 CR 32755 Add mMEForMTC attribute | Intel | 32.755 | 0009 | - | Rel-12 | - | - | noted |
| S5-140121 | Rel-10 CR 32.762 Add new member in blacklist | Ericsson | 32.762 | 0101 | - | Rel-10 | F | OAM10 | agreed |
| S5-140226 | Rel-11 CR 32.762 Addition of not implemented parts of S5-131772 Add new member in blacklist | Ericsson | 32.762 | 0102 | - | - | - | - | revised |
| S5-140232 | Rel-11 CR 32.762 Addition of not implemented parts of S5-131772 Add new member in blacklist | Ericsson | 32.762 | 0102 | 1 | - | - | - | revised |
| S5-140280 | Rel-11 CR 32.762 Addition of not implemented parts of S5-131772 Add new member in blacklist | Ericsson | 32.762 | 0102 | 2 | - | - | - | agreed |
| S5-140089 | Rel-10 CR 32.766 Add missing XML elements for SONControl and SONTargets | Huawei | 32.766 | 0060 | - | Rel-10 | - | - | revised |
| S5-140228 | Rel-10 CR 32.766 Add missing XML elements for SONControl and SONTargets | Huawei | 32.766 | 0060 | 1 | - | - | - | agreed |
| S5-140122 | Rel-10 CR 32.766 Add new member in blacklist | Ericsson | 32.766 | 0061 | - | Rel-10 | F | OAM10 | agreed |
| S5-140227 | Rel-11 CR 32.766 Addition of not implemented parts of S5-131772 Add new member in blacklist | Ericsson | 32.766 | 0062 | - | - | - | - | revised |
| S5-140233 | Rel-11 CR 32.766 Addition of not implemented parts of S5-131772 Add new member in blacklist | Ericsson | 32.766 | 0062 | 1 | - | - | - | agreed |
| S5-140156 | Rel-12 CR 32.851 Editorial Cleanup | Alcatel-Lucent | 32.851 | 0002 | - | - | - | - | withdrawn |
| S5-140157 | Rel-12 CR 32.851 Remove hanging paragraph | Alcatel-Lucent | 32.851 | 0003 | - | Rel-12 | - | - | revised |
| S5-140240 | Rel-12 CR 32.851 Remove hanging paragraph | Alcatel-Lucent | 32.851 | 0003 | 1 | - | - | - | agreed |

## Annex C: Lists of liaisons

### C1: Incoming liaison statements

| Document | Original | Title | From | Decision | Reply in |
| --- | --- | --- | --- | --- | --- |
| S5-140179 | 131206_NGMN | LS from NGMN Project NGCOR to SA5 on Publication of Deliverables | NGMN NGCOR | postponed |  |
| S5-140181 | C1-135196 | Reply LS from CT1 to SA5 on Availability of SIP Instance Identifier | C1-135196 | noted |  |
| S5-140184 | C3-131852 | Reply LS from CT3 cc SA5 on support for user location age or timestamp | C3-131852 | noted |  |
| S5-140187 | EE(14)000051 | LS from ETSI EE to SA5 on Cooperation for Energy Efficiency Measurements | ETSI EE | postponed |  |
| S5-140191 | packet_doc_69_001 | Reply LS from GSMA IREG to 3GPP CT4 cc SA5 on FQDNs to support Multi-vendor Plug and Play (MvPnP) feature | GSMA IREG | noted |  |
| S5-140193 | S2-133832 | LS from SA2 to SA5 on the provision of IPv6 prefix length to SGW/SGSN | S2-133832 | noted |  |
| S5-140194 | S2-134575 | Reply LS from SA2 to SA5 on providing Charging Characteristics to TDF | S2-134575 | noted |  |
| S5-140196 | S2-134589 | LS from SA2 to SA5 on Charging aspects for Network Sharing (MOCN GWCN) | S2-134589 | noted |  |
| S5-140218 | C1-131748 | Resubmitted LS from CT1 to SA5 on transit IOI exchange over ISC interface | C1-131748 | postponed |  |
| S5-140221 | SOLU63 Doc_006 | Reply LS from GSMA SOLU to SA5 on Transit IOI clarification | GSMA SOLU | noted |  |
| S5-140242 | bbf2014 023 01 (2) | Reply to 3GPP/SA5 Liaison Questions Regarding Performance Measurements Architecture | Broadband Forum | noted |  |
| S5-140255 | S3-140208 | Reply LS from SA3 to SA5 (S5-132105) (cc: GSMA IREG) on securing Gy/Gyn interfaces for EPC Roaming LBO scenario | S3-140208 | noted |  |

### C2: Outgoing liaison statements

| Document | Title | To | Cc | reply to i/c LS |
| --- | --- | --- | --- | --- |
| S5-140364 | LS out to SA2, CT3 on credit control failure handling | SA2, CT3 | - | - |

## Annex D: List of agreed/approved new and revised Work Items

| Document | Title | Source | new/revised |
| --- | --- | --- | --- |
| S5-140363 | New WID Radio Planning Tool interface (OAM-RPT) | NSN | new WID |
| S5-140360 | Revised WID SP-120775 Short Message Service - Service Center (SMS-SC) Offline Charging | Alcatel-Lucent | revised WID |
| S5-140365 | New WID on Enhanced NM Centralised Coverage and Capacity Optimisation` | Ericsson | new WID |
| S5-140283 | Revised WID Study on Enhanced NM Centralised Coverage and Capacity Optimisation` | Ericsson | revised WID |

## Annex E: List of action items

| Meeting/Number | Agenda item | Document | Details | Responsible | Due by |
| --- | --- | --- | --- | --- | --- |
| 93/1 |  |  | Add IS-SS link management to SA5 working procedure | SA5 Chair | SA5#94 |
| 93/2 |  |  | Facilitate the detection of conflict between CRs | All | SA5#94 |
| 93/3 |  |  | A mapping table and extension rules for XML Solution Sets should be proposed. | All | SA5#94 |
| 93/4 |  |  | The interpretation of “Null” combined with an empty list, for a multi-valued attribute (like theIubLink in TN NRM) which has isNullable=True. Consider to create a “User’s guide” for this. | Ericsson | SA5#94 |
| 93/5 |  |  | General AP for the group to check the necessity of “id” for all the 28/32 series IOCs (general OAM action item) | All | SA5#94 |
| 93/6 | 7.1 | S5-140097 | All to review the 28-series (errors in References) before preparing the CRs | SA5, MCC | 2014-04-01 |
| 93/7 | 6.9.3 | S5-140264 | Email approval of TR 32.861 | China Mobile | 2014-04-01 |
| 93/8 | 6.9.2 | S5-140031 | Email approval of TR 32.860 | Cisco | 2014-04-01 |
| 93/9 | 7.2.1 | S5-140295 | Email approval of TR 32.838 | Ericsson | 2014-04-01 |
| 93/10 | 8.7.1 | S5-140320 | Email approval of TR 32.849 | Deutsche Telekom | 2014-04-01 |
| 92/1 |  |  | Remove the service trace features from Rel-11 after the corresponding specs are upgraded to Rel-12. | OAM SWG |  |
| 92/2 |  |  | Clarify the guidance for mapping of inherited attributes in SS for 28 series (whether the inherited attributes are repeated in SS mapping table and idl) | CMAN Chair (Thomas Tovinger) |  |
| 90/1 |  |  | Clarify the “Import” semantics in IS - Identified from 6.3 (CR session) | OAM SWG |  |
| 90/2 |  |  | Contact BBF (informally) about status of alignment on performance measurements (original LS S5-121387 out to BBF ) | SA5 Chair |  |

## Annex F: List of decisions

| Meeting/Number | Agenda item | Document | Details |
| --- | --- | --- | --- |
| 93/1 | 6.9.3 | S5-140154 | allocated TR 32.861 for Study on Application and Partitioning of Itf-N |
| 93/2 | 6.9.2 | S5-140257 | allocated TR 32.860 for FS_D_MLB_SON_OAM |

## Annex G: List of participants

| Name | Representing | Status-Partner |
| --- | --- | --- |
| Al-kanani, Hassan (Dr.) | NEC Technologies (UK) LTD | 3GPPMEMBER (ETSI) |
| Andrianov, Anatoly (Mr.) | NSN | 3GPPMEMBER (ETSI) |
| Berggren, Tommy (Mr.) | TeliaSonera AB | 3GPPMEMBER (ETSI) |
| Bizzarri, Simone (Mr.) | TELECOM ITALIA S.p.A. | 3GPPMEMBER (ETSI) |
| Chou, Joey (Mr.) | Intel Corporation (UK) Ltd | 3GPPMEMBER (ETSI) |
| Cornily, Jean Michel (Mr.) | Orange Spain | 3GPPMEMBER (ETSI) |
| Gardella, Maryse (Mrs.) | Alcatel-Lucent | 3GPPMEMBER (ETSI) |
| Goermer, Gerald (Mr.) | NSN Oy | 3GPPMEMBER (ETSI) |
| Guo, Wenjie (Miss) | ZTE Corporation | 3GPPMEMBER (ETSI) |
| Heskin, Eamon (Mr.) | Deutsche Telekom AG | 3GPPMEMBER (ETSI) |
| Hubinette, Ulf (Mr.) | Ericsson | 3GPPMEMBER (ETSI) |
| Huo, Xiaoning (Mr.) | China Mobile Com. Corporation | 3GPPMEMBER (CCSA) |
| Jesske, Roland (Mr.) | Deutsche Telekom AG | 3GPPMEMBER (ETSI) |
| Lagha, Naceur (Mr.) | Amdocs Software Systems Ltd | 3GPPMEMBER (ETSI) |
| Li, Gang (Mr.) | Nanjing Ericsson Panda Com Ltd | 3GPPMEMBER (CCSA) |
| Li, Hui (Mr.) | HUAWEI Technologies Japan K.K. | 3GPPMEMBER (ARIB) |
| Li, Li (Miss) | HiSilicon Technologies Co. Ltd | 3GPPMEMBER (CCSA) |
| Liang, Shuangchun (Dr.) | China Mobile Com. Corporation | 3GPPMEMBER (CCSA) |
| McNamee, Alan (Mr.) | Openet Telecom | 3GPPMEMBER (ETSI) |
| Oueslati, Lina (Miss) | ORANGE | 3GPPMEMBER (ETSI) |
| Petersen, Robert (Mr.) | Ericsson Japan K.K. | 3GPPMEMBER (ARIB) |
| Pollakowski, Olaf (Dr.) | NSN | 3GPPMEMBER (ETSI) |
| Schnell, Christof (Ing.) | Vodafone GmbH | 3GPPMEMBER (ETSI) |
| Shrader, David (Mr.) | Ericsson Inc. | 3GPPMEMBER (ATIS) |
| Sudarsan, Padma (Ms.) | Alcatel-Lucent Deutschland AG | 3GPPMEMBER (ETSI) |
| Toche, Christian (Mr.) | Huawei Technologies France | 3GPPMEMBER (ETSI) |
| Tovinger, Thomas (Mr.) | Ericsson | 3GPPMEMBER (ETSI) |
| Tse, Edwin (Mr.) | Ericsson Inc. | 3GPPMEMBER (ATIS) |
| Yanover, Vladimir (Dr.) | Cisco Systems Belgium | 3GPPMEMBER (ETSI) |
| Yao, Yizhi (Mr.) | NSN | 3GPPMEMBER (ETSI) |
| Zhang, Kai (Mr.) | HUAWEI TECHNOLOGIES Co. Ltd. | 3GPPMEMBER (ETSI) |
| Zhang, Zhuoyun (Miss) | China Unicom | 3GPPMEMBER (CCSA) |
| Zhu, Weihong (Mr.) | ZTE Corporation | 3GPPMEMBER (CCSA) |
| Zoicas, Adrian (Mr.) | ETSI | 3GPPORG_REP (ETSI) |

## Annex H: List of future meetings

| Title | Start date | End date (OP) | Town | Country | Reference |
| --- | --- | --- | --- | --- | --- |
| 3GPPSA5#94 | 24/03/2014 09:00:00 | 28/03/2014 17:30:00 | Oranjestad | Aruba | S5-94 |
| 3GPPSA5#95 | 12/05/2014 09:00:00 | 16/05/2014 17:30:00 | Sapporo | JP | S5-95 |
| 3GPPSA5#96 | 18/08/2014 09:00:00 | 22/08/2014 17:30:00 | Sophia Antipolis | FR | S5-96 |
| 3GPPSA5#97 | 20/10/2014 09:00:00 | 24/10/2014 17:30:00 | Venice | IT | S5-97 |
| 3GPPSA5#98 | 17/11/2014 09:00:00 | 21/11/2014 17:30:00 | US | US | S5-98 |