## Slide 1: Offline Charging Architecture
Scenarios to be considered

## Slide 2: Problem Description
current 3GPP offline charging architecture implies costly, high correlation effort of CDRs
offline charging scenario may be based on S-CSCF CDR parameter Application Server Involvement. This information is derived from Application Server subscription information within iFCs which determines only the need to forward SIP requests to Application Servers. This AS could provide accounting information.
instead seperate information shall be exchanged and recorded by each involved applications, if accounting information is provided.

## Slide 3: Scenario 1: MMTel
Vast majority of users Abasic are only subscribed to Multimedia Telephony Service (TS 22.173)
‚Calling Party Pays‘ charging model is applicable (TS 22.115)
MMTel AS CDR provide sufficient accounting information
Still high effort as 3GPP offline charging architecture requires correlation of at least 2 CDRs.
Determination of charging scenario is feasable based on S-CSCF CDR parameter Application Servers Information

## Slide 4: Scenario 2: TelCo VPN
Minor group of users Avpn are subscribed to Multimedia Telephony Service (TS 22.173) and additionally to VPN Service.
VPN Service enables:
  Private Numbering Plan (User, VPN-specific)
  Charging of session and service to 3rd party („VPN owner“) (TS 22.115)
Both MMTel AS and VPN AS provide accounting-relevant information.
High effort as 3GPP offline charging architecture requires correlation of at least 3 CDRs.
Determination of charging scenario is feasable based on S-CSCF CDR parameter Application Servers Information

## Slide 5: Scenario 3: Enhanced Multimedia Telephony
User Aemt is subscribed to Multimedia Telephony Service (TS 22.173)
Additionally User Aemt is subscribed to EMT Service. Here tailored services are applied.
  App1: Filtering/manipulation of costumer-specific headers
  App2: Tailored implementation of call transfer (soap i/f instead sip REFER)
In case of involvement of App1, MMTel AS provide sufficient accounting information
In case of involvement of App2, accounting information of both services must be correlated
Determination of charging scenario is NOT feasable based on S-CSCF CDR parameter Application Servers Information.