## Slide 1: 3GPP SA5 status on NFV
Christian Toche
3GPP SA5 chairman
ETSI NFV ISG, OPNFV, 3GPP SA5, TM Forum
Joint workshop, Prague
February 27th, 2015

## Slide 2: Contents
Introduction of 3GPP SA5
Objectives of the 3GPP SA5 study on NFV
Current status of the 3GPP SA5 study on NFV
Contents of the 3GPP SA5 study on NFV
Alignment of ETSI NFV Terms and 3GPP SA5 Terms
Mixed network management architecture
An ensemble in one network deployment example
Possible areas for involvement of 3GPP SA5
  VNF PM & FM flows
Considerations on cooperation process
Annex: E2E procedure flows for mobile networks

## Slide 3: 3GPP SA5 Telecom Management ToR
SA WG5 will specify the requirements, architecture and solutions for provisioning and management of the network (RAN, CN, IMS) and its services. The WG will define charging solutions in alignment with the related charging requirements developed by the relevant WGs, and will specify the architecture and protocols for charging of the network and its services.
The WG will ensure its work is also applicable to the management and charging of converged networks, and potentially applicable to fixed networks. The WG will coordinate with other 3GPP WGs and all relevant SDOs to achieve the specification work pertinent to the provisioning, charging and management of the network and its services.
http://www.3gpp.org/Specifications-groups/sa-plenary/56-sa5-telecom-management

## Slide 4: 3GPP SA5 leadership
SA5
Christian Toche (Huawei) Chair since 08/2005 Jean-Michel Cornily (Orange) VC since 08/2013 Thomas Tovinger (Ericsson) VC since 08/2007
Charging Sub-Working Group (SWG)
Maryse Gardella (Alcatel-Lucent) Chair since 08/2013 David Shrader (Ericsson) VC since 08/2013 Li Li (Huawei) VC since 08/2014
OAM&P Sub-Working Group (SWG) Yizhi Yao (Nokia Networks) Chair since 01/2013
Converged Management Sub-Working Group (SWG) Thomas Tovinger (Ericsson) Chair since 08/2013 Lan Zou (Huawei) VC since 05/2012

## Slide 5: Objectives of the 3GPP SA5 study on NFV
Study the use cases and concepts for the network management of virtualized networks, taking into account the relevant use cases from ETSI NFV ISG.
Analyse and classify the scenarios when all or some instances of 3GPP-defined network elements in a subsystem/domain are virtualized (i.e. respectively fully virtualized networks and mixed networks)
Identify the requirements for potential solutions to the scenarios above. Study whether or not a single management system for mixed networks is required.
Identify the potential impacts on the existing 3GPP Management reference model.
Analyse the existing 3GPP Management reference model, interfaces, protocols and procedures to determine what can be re-used, adapted or extended, and whether new IRPs are needed.
Propose enhancements or extensions to the 3GPP Management reference model, if an impact is foreseen. If needed, solution(s) for a single management system for mixed networks should be studied.
Provide recommendations for the normative work, based on the result of the analyses and the potentially identified impacts, enhancements or extensions.
SA5 will take in account the work done by ETSI NFV ISG and cooperate with ETSI NFV ISG as necessary.
Study Item Description: http://www.3gpp.org/ftp/TSG_SA/TSG_SA/TSGS_64/Docs/SP-140398.zip

## Slide 6: Status of the 3GPP SA5 study on NFV
The output of the study is recorded in a Technical Report: TR 32.842.
The target for delivery of TR 32.842 is June 2015.
The latest version of the draft TR 32.842 is v0.4.0 (February 2015).
The TR 32.842 will be sent for information to TSG SA#67 (March 11-13 2015).
The TR 32.842 will provide recommendations for normative work to be started after June 2015.
http://www.3gpp.org/DynaReport/32842.htm

## Slide 7: Contents of the 3GPP SA5 study on NFV
Fault Management for NFV
  Failure management when VNF detects VNF failure
  Failure management when the alarm is generated by NFVI
  Failure management when the EM detects VNF failure
  Failure management when the alarm is generated by VNFC
  Notification of VNFCs impacted due to scheduled NFVI maintenance
  VM failure is detected by VNF application
  VNF snapshot capture
Configuration Management for NFV
  VNF instantiation and configuration for mixed network
  NFV configuration management
  VNF configuration management by EM in mixed network
  Automatic re-connection of eNBs after lifecycle management of vMME
Performance Management for NFV
  VNF performance measurements reporting to EM
Core Network Lifecycle Management for NFV
  Instantiation of core network service
  Network Service instance scaling
  Network Service instance update due to VNF instance modification
  Termination of core network service
  VNF package on-boarding
  VNF package enable
  VNF package disable
  VNF package update
  VNF expansion
  VNF contraction
  Termination of Core VNF instance
Other use cases
  Information collection prior to capacity expansion

## Slide 8
Mixed network management architecture
Figure 7.1-1 from draft TR 32.842 (work in progress)

## Slide 9
An ensemble in one network deployment example
This ensemble includes EM, VNFM, PNF and VNF as one package.
The package of this ensemble is provided by the same vendor as shown in the following figure.
Provide fast time to market implementation and simplify interoperability provisioning and testing in multiple vendors environment.
Provide a migration path which minimizes the level of disruption of service when introducing virtualized entities (functional blocks) into operator’s networks, whereby existing network management processes and tools can be reused.
Assembling EM with VNFM would allow the use of the same set of network management processes and tools to manage non-virtualized and virtualized network functions.
Assembling EM, VNFM, VNF and NE (PNF) would allow leveraging vendor’s expertise on assembling existing EM and NE to coordinate with the new required VNF and VNFM functionality.
Support of this ensemble would focus towards interoperability of one vendor’s VNFM with other vendors VIMs and NFVOs.
More ensembles will be addressed in future meetings.

## Slide 10
Roles & responsibilities
P: Primary responsibility
  The work is to be initiated by SA5 and coordinated with other SDOs.
  The start of the work can be either triggered by SA5 itself or by request from another relevant SDO.
  How to coordinate with other SDOs will be based on the cooperation process to be jointly defined by the relevant SDOs.
S: Secondary responsibility
  The work is to be initiated by another SDO.
  SA5 will be involved via the cooperation process which will be jointly defined by the relevant SDOs.
  The SDO with primary responsibility will start the work (if it does not exist yet).
I: Informed
  SA5 needs to be informed about the approval of the proposals and specifications.
  SA5 will check if SA5 requirements on Mobile Network NFV management can be supported. In case they are not supported, SA5 could request the other SDO to make some changes.

## Slide 11
Criteria for allocating the roles
For the interfaces connected to 3GPP nodes, including NM/OSS, EM and VNF
  The lifecycle management, which is mostly generic for all kinds of networks (but not really specific to Mobile Networks), SA5 is allocated as “S”.
  FCAPS of VNF, which is SA5 traditional expertise, SA5 is allocated as “P”.
  For SA5 initiated requirements, SA5 is allocated as “P”.
For the interfaces within ETSI MANO domain
  The lifecycle management, which is mostly generic for all kinds of networks (but not really specific to Mobile Networks), SA5 is allocated as “I”.
  FCAPS of VNF, which is the most VNF relevant, SA5 is allocated as “S”.
  For SA5 initiated requirements, SA5 is allocated as “S”.
For the interfaces within 3GPP domain
  SA5 is allocated as “P” for the relevant areas.
For the information model (data) specific to Mobile Networks (for all interfaces)
  SA5 is allocated as “P” for the relevant areas.

## Slide 12: Possible areas for involvement of SA5 (1/3)
SA5: P
Interfaces |  | Os-Ma-nfvo (OSS/BSS/NM - NFVO) | Ve-Vnfm-em (EM-VNFM) | Ve-Vnfm-vnf (VNF-VNFM) | Or-Vnfm (NFVO-VNFM) 9 | Vi-Vnfm (VIM-VNFM) | Or-Vi (NFVO-VIM) | Itf-N (OSS/BSS/NM - EM)
Functions |  |  |  |  |  |  |  | 
Lifecycle management (LCM) | Network service (NS)1 | For Mobile NS, 1. NM needs to trigger infra NS LCM when it is required for mobile NS. 2. NM needs to receive state/status information about the infra NS (supporting the mobile-NS) |  |  |  |  |  | Define the operations and models for Mobile NS LCM
 | VNF2 | For Mobile VNF, 1.NM needs to trigger Generic VNF LCM as part of the Mobile VNF LCM procedure. 2. NM needs to receive message about the outcome of Generic VNF LCM (supporting the mobile VNF.) | 1. EM needs to trigger mobile VNF LCM. 2.EM needs to receive message about the outcome of VNF LCM | Ensure the initial configuration data for mobile network connectivity to be configured from VNFM to VNF | Ensure the VNF LCM can satisfy the mobile VNF LCM needs |  |  | Define the operations and models for Mobile VNF LCM
SA5: I
SA5: S
(work in progress)

## Slide 13: Possible areas for involvement of SA5 (2/3)
Interfaces |  | Os-Ma-nfvo (OSS/BSS/NM - NFVO) | Ve-Vnfm-em (EM-VNFM) | Ve-Vnfm-vnf (VNF-VNFM) | Or-Vnfm (NFVO-VNFM) 9 | Vi-Vnfm (VIM-VNFM) | Or-Vi (NFVO-VIM) | Itf-N (OSS/BSS/NM - EM)
Functions |  |  |  |  |  |  |  | 
FCAPS | Network services (NS)3 | NM needs to collect Infra NS FCAPS for correlation with the mobile network application layer NS FCAPS |  |  |  |  |  | Define the operations and models for Mobile NS FCAPS
 | VNF4 | NM needs to collect Generic VNF FCAPS for correlation with the mobile network application layer VNF FCAPS | 1.EM collects VNF related VR’s FCAPS for correlation with mobile VNF FCAPS. 2. EM needs to trigger mobile VNF LCM 3.EM needs to receive message about the outcome of VNF LCM | Ensure the VNF whose VRs are impacted reports the VR data to VNFM |  | Ensure the VR data can be correlated with Mobile VNF data |  | Define the operations and models for Mobile VNF and mixed network FCAPS
SA5: P
SA5: I
SA5: S
(work in progress)

## Slide 14: Possible areas for involvement of SA5 (3/3)
Interfaces | Os-Ma-nfvo (OSS/BSS/NM - NFVO) | Ve-Vnfm-em (EM-VNFM) | Ve-Vnfm-vnf (VNF-VNFM) | Or-Vnfm (NFVO-VNFM) 9 | Vi-Vnfm (VIM-VNFM) | Or-Vi (NFVO-VIM) | Itf-N (OSS/BSS/NM - EM)
Functions |  |  |  |  |  |  | 
Virtualized Resource management (VRM)5 | NM needs to be able to trigger VRM |  |  |  |  |  | Make sure the VR data can be correlated with Mobile VNF data
Policy administration6 | NM needs to be able to configure the VRM policy |  |  | Forwarding of the VRM policy configuration |  | Ensure the operator defined policy are forwarded | Define Mobile VNF application level policy management
Architecture7 | Define Mobile VNF and mixed network management architecture based on the ETSI NFV architecture |  |  |  |  |  | 
E2E management procedures (mobile network) 8 | Define Mobile VNF and mixed network E2E management for the mobile dedicated features with the reference of common procedures defined in ETSI NFV |  |  |  |  |  | 
SA5: P
SA5: I
SA5: S
(work in progress)

## Slide 15: Notes
References are corresponding to ETSI GS NFV-MAN 001 V1.1.1 (2014-12)”:
1: "Life cycle management — Network Service": 7.1.1, 7.1.2, 7.1.3.
2: "Life cycle management — VNF" : 7.2.1 to 7.2.5.
3: "FCAPS — Network Service": 7.1.4, 7.1.5, 7.5.
4: "FCAPS — VNF": 7.2.6 to 7.2.8.
5: "Virtualized Resource management": 7.3.
6: "Policy administration": 7.4.
7: "Architecture": 5.
8: "E2E management procedures (mobile network)" means the end-to-end procedures for NFV management (of mobile networks), including the interactions among all the relevant management entities (OSS/BSS/NM, EM, NFVO, VNFM, VIM) and VNF/PNF, and if needed it will include the interactions between VNFs/PNFs too.
9: An interface has two elements: protocol and information. There are interface(s), e.g. NFVO-VNFM where 3GPP is secondary on protocol but primary on information (if the information is related to a) information model of 3GPP-defined-nodes, b) PM and FM data of 3GPP-defined-nodes or c) Mobile NSs (which is not the currently ETSI defined NS)).

## Slide 16
VNF PM & FM flows

## Slide 17: Discussion on PM & FM flows
Identify the purpose/motivation why VNFM/NFVO would need to receive VNF FM (Flow-1).
Identify the purpose/motivation why OSS/BSS would need to receive NS FM (Flow-6).
Identify the purpose/motivation why VNFM/NFVO would need to receive VNF PM (Flow-1).
Identify the purpose/motivation why OSS/BSS would need to receive NS PM (Flow-6).

## Slide 18
Considerations on cooperation process
Each SDO keeps their responsibility, i.e. no change in responsibility due to virtualisation.
ETSI NFV is responsible for virtualisation, 3GPP is responsible for mobile networks etc.
Identify the areas where responsibilities from different SDOs touches each other so that cooperation is needed (restrict list to high priority items).
Per area, agree on involved SDOs and define responsibilities (Primary, Secondary, Information).
Establish direct communication channel via limited size Joint Working Groups.
Based on agreements on way forward done at this meeting, a more detailed cooperation process will be drafted if needed.

## Slide 19: Annex
E2E procedure flows for mobile networks
  VNF instantiation & termination flows (examples)
  VNF expansion & contraction flows (examples)

## Slide 20
E2E VNF instantiation flows (examples)
Figure 7.3.1-1 VNF instantiation with resources allocated by VNFM
Figure 7.3.1-2 VNF instantiation with resources allocated by NFVO

## Slide 21
E2E VNF termination flows (examples)
Figure 7.3.x-1 Termination request is sent from NM to EM
Figure 7.3.x-2 Termination request is sent from NM directly to NFVO

## Slide 22
E2E VNF expansion & contraction flows (examples)
Figure 7.3.X-2: VNF instance contraction procedure triggered by NM/EM
Figure 7.3.X-1: VNF instance expansion procedure triggered by NM/EM

## Slide 23: Thank you!
ETSI ISG NFV
3GPP
SA5
OPNFV
TM
Forum