## Slide 1: Discussion on Way Forward on EEC context-related topics
Catalina Mladin, Convida Wireless

## Slide 2: Introduction
Several proposals at SA6#42-e (and earlier) can benefit from having informal decisions on way forward before new contributions are submitted at the next meeting.
The topics center on EEC context @EES, but related decisions include ACR and registration-related features

## Slide 3: Background on relevant contributions
The following contributions (content and email discussions) are relevant for this discussion.
  EEC Context – where two tracks have been requested:
    Track A (Granular): Where EEC context @EES is captured in 2 IEs EEC Registration context (Reg-Ctx) and Service Session Context (SSC)
      S6-210689 TRACK A, S6-210690 TRACK A, S6-210691 TRACK A
    Track B (Unified): Where EEC context @ EES is captured in 1 IE S6-210689 TRACK B, S6-210691 TRACK B
  Registration bypass mode S6-210664_rev1_was0467 edgeApp EEC registration clarification
  Discovery bypass mode: new contribution attached, alternative to S6-210692

## Slide 4: EEC Context at-a-glance
EEC Context
The information contained in the IEs (see the FINAL versions at SA6#42) is the same in the two tracks.
The context transfer procedures become multiple & dedicated (for granular option) vs. single (for unified option)
Reg CTX
Service Session Ctx (SSC)
Service Session Ctx (SSC)
Service Session Ctx (SSC)

## Slide 5
Granular approach vs.
Clearer delineation of info between elements i.e. per EEC (RegCtx) vs. per AC-EAS session (SSC)
Multiple dedicated/ specialized Push/Pull procedures specified
In ACR for regular mode, If Registration bypass mode agreed, in some cases only the dedicated Push/Pull procedure needed
Unified approach
Clearer understanding of overall EEC info/context available at EES
Single Push/Pull procedure, simplifies ACR flow
If Registration bypass mode agreed, the unified Push/Pull procedure used, IE details in request

## Slide 6: Registration Bypass Mode
What: EEC can do Discovery requests without having to register first
Why: ECSP policy flexibility
Consequences:
  EESs provide services to all authorized EECs, no gating possibility (if desired)
  EEC Context not established in EEL
    Info availability unclear
    Lifecycle management more difficult
    Affects baseline for following procedures
  Need to cover mixed deployments

## Slide 7: Discovery Bypass Mode
What: EEC can request EAS info provided in registration response
Why: ECSP policy flexibility, signalling optimization, EEC functionality offload
Consequences:
  Discovery and registration separate, indication of add-on functionality is explicit.
  No impact on other procedures, other than the bypassing of the discovery

## Slide 8: Proposals
Agree on focusing on a single approach for covering EEC context relocation, i.e. either Granular or Unified.
Discuss whether Registration bypass mode should be supported. If YES:
  Agree that Rel-17 should cover ACR with deployment restrictions, e.g. either:
      Only for regular mode deployments: This is the current paradigm. We can specify that the registration bypass mode exists, but additional functionality described in Rel-18.
      Only for homogeneous deployments. Finalize ACR assuming either “regular” or “registration bypass” deployments. Specify ACR (and other functionality) for heterogeneous deployments in Rel-18
  Agree that Discovery bypass mode should also be supported. There are no down-stream effects.