3GPP TSG-SA WG6 Meeting #43-e	S6-211348

e-meeting, 24th May – 2nd June 2021	(revision of S6-211162 rev 1)

Source:	Convida Wireless LLC

Title:	5GMARCH store and forward

Spec:	3GPP TS 23.554 v0.3.0

Agenda item:

Document for:	Approval

Contact:	Mladin.Catalina@convidawireless.com

1. Introduction

This contribution merges in the TR solution 21 on store-and-forward (S/F) which addresses the Key Issue13  on store-and-forward clause 5.13 and the following requirement:

TS 22.262 [R-5.1.2-005] The MSGin5G Service shall support storage of a message if a UE is unavailable (disconnected or power off) for future delivery once the UE becomes available.

The contribution proposes  the feature implementation for Application to point messaging based on Service Provider deployment S/F policy and message storage information.

2. Reason for Change

To enable the MSGin5G Service to provide store-and-forward monitoring capabilities in the 3GPP Network.

3. Proposal

It is proposed to agree the following changes to 3GPP TS 23.554 v0.3.0

* * * First Change * * * *

### 8.2.2	MSGin5G inbound messages into the MSGin5G Server

Figure 8.2.2-1 shows the procedure for a MSGin5G UE that initiates a MSGin5G message request.

# Figure 8.2.2-1: New MSGin5G Message Request from UE

Figure 8.2.2-2 shows the procedure for an Application Server that initiates an API request for sending a MSGin5G Message to UE.

Editor's note:	The APIs provided by MSGin5G Server to App Server is to be specified in another section of the TS.

# Figure 8.2.2-2: Application Server initiates a request for sending a MSGin5G message

Figure 8.2.2-3 shows the procedure for a Legacy 3GPP Message Gateway or a non-3GPP Message Gateway that sends a new MSGin5G message request to the MSGin5G Server on behalf of a Legacy 3GPP UE or Non-3GPP UE.

# Figure 8.2.2-3: New MSGin5G Message Request sending from Message Gateway

The following procedure applies to the above figures 8.2.2-1, 8.2.2-2 and 8.2.2-3 with the exception that step 1 only applies to figure 8.2.2-1.

1.	The Application Client-1 in the UE sends a request to the MSGin5G Client for invoking the MSGin5G Client to send a new MSGin5G Message to a recipient or to multiple recipients.

Editor's note:	Whether the APIs provided by the MSGin5G Client to the Application Client is to be specified in another section of the TS is FFS.

2.	As shown in figure 8.2.2-1 or 8.2.2-3, the MSGin5G Client or Message Gateway sends the MSGin5G Message Request to the MSGin5G Server and includes the IEs as listed in table 8.2.2-1 in the request; or as shown in figure 8.2.2-2, the Application Server sends an API request to the MSGin5G Server for sending a MSGin5G message, the API request includes the IEs as listed in table 8.2.2-1.

# Table 8.2.2-1: Request to MSGin5G Server for sending MSGin5G message

| Information element | Status | Description |
| --- | --- | --- |
| Originating MSGin5G Service ID | M | The service identity of the sending MSGin5G Client, Legacy 3GPP UE, Non-3GPP UE or the sending Application Server. |
| Recipient MSGin5G Service ID | O | The service identity of the receiving MSGin5G Client, Legacy 3GPP UE, Non-3GPP UE or the receiving Application Server. This IE is mandatory for point-to-point messaging, application-to-point messaging, AOMT messaging and MOAT messaging and is not present in other message scenarios. |
| Recipient Group Service ID | O | The service identifier of the target MSGin5G Group. This IE is mandatory for a Group Message and is not present in other message scenarios. |
| Recipient Broadcast Area ID | O | The service identifier of the Broadcast Service Area where the message needs to be broadcast. This IE is mandatory in the Broadcast Message and is not present in other message scenarios. |
| Messaging Topic | O | Indicates which messaging topic this message is related to. This IE is mandatory for a message distribution based on topic and is not present in other message scenarios. |
| Application ID | O | Identifies the application(s) for which the payload is intended. This list of Application IDs IE is required when the message is sent to one or multiple Application Clients served by same MSGin5G Client. This list of Application IDs IE may be included when the message is sent to an Application Server or to an Application Client. MSGin5G Server is unaware of the content. |
| Message ID | M | Unique identifier of this message. If the request is a Delivery Report (as shown in step 6) the Message ID IE is copied from the MSGin5G message that is being acknowledged. |
| Security Credentials | O | Security information required by the MSGin5G Server. This is a placeholder for SA3 security information. |
| Delivery Status Required | O | Indicates if delivery acknowledgement from the recipient is requested. This IE is not present if the MSGin5G message request is a Delivery Report (as shown in step 6). |
| Failure Cause | O | If the request is a Delivery Report (as shown in step 6) the Failure Cause indicates the failure reason, if applicable. |
| Payload | O | Payload of the message. MSGin5G Server/Client is unaware of the content. If the Request is a Delivery Report (as shown in step 6) the Payload IE is not included. If the request is sent from MSGin5G Client or Message Gateway to the MSGin5G server, the maximum size of this IE is a configurable value that shall not exceed 2048 octets. |
| Priority Type | O | Application priority level requested for this message. If the Request is a Delivery Report (as shown in step 6) the Priority Type IE is copied from the message that is being acknowledged. |
| Message is segmented | O | Indicates this message is part of a segmented message. |
| Segmentation Set Identifier | O | All segmented messages associated within the same set of segmented messages (i.e. associated with the same MSGin5G message) are assigned the same unique identifier. Mandatory IE to be present in every segmented message. |
| Total number of message segments | O | Indicates the total number of segments for the message. The Total Segments needs to be included only in the first segment of the message. |
| Message segment number | O | An incrementing message segment number that indicates segmented message number of each segmented message within a set of segmented messages |
| Last Segment Flag | O | An indicator of whether this segmented message is the last segment in the set of segmented messages or not. The Last Segment Flag needs to be included only in the last segment of the message. Message segment number of the segment with "Last Segment Flag" set can be considered as total segments. |
| Message expiration time | O | Time duration used by MSGin5G Server for providing store-and-forward services if the destination is not available for communications. The MSGin5GServer attempts delivery at or before the message expiration time, or when the recipient becomes available. (NOTE 1) |
| NOTE 1: MSGin5G Service Provider policies may indicate whether the store-and-forward feature is enabled or not in the deployment. If the feature is disabled and the information element is present, the value is ignored and an appropriate failure cause is provided to the sender. |

3.	The MSGin5G Server determines if the recipients are available to receive the message or if the message needs to be stored for deferred delivery. The MSGin5G Server may use e.g. UE reachability status monitoring or the recipient’s Communication Availability information to determine whether the recipients are available. How the MSGin5G server makes this determination is out of scope of the current specification.

4.	If the message needs to be stored for deferred delivery, the MSGin5G Server shall store the message request with the relevant delivery information and shall attempt delivery at or before the message expiration time, or when the recipient becomes available.

5.	The MSGin5G Server shall return a response to the originating entity and includes the IEs as listed in table 8.1.2-2 in the response.

# Table 8.2.2-2: Information Elements in Response

| Information element | Status | Description |
| --- | --- | --- |
| Originating MSGin5G service ID | M | The identity of the MSGin5G Client, Legacy 3GPP UE, Non-3GPP UE or the identity of the Application Server that initiated the previous Request. |
| Message ID | M | Identifier of the initiating Request. |
| Delivery Status | O | Indicates if delivery is a failure, or if the message is stored for deferred delivery. |
| Failure Cause | O | The reason for failure |

6. If requested, the MSGin5G Server may provide a MSGin5G Message Delivery report to the Message Gateway.