3GPP TSG-SA WG6 Meeting #48-e	S6-220zzz

e-meeting, 5th – 14th April 2022	(revision of S6-220zzz)

Source:	InterDigital

Title:	Solution for KI#19 – ACR selection and coordination

Spec:	3GPP TR 23.700-98

Agenda item:	x.x

Document for:	Approval

Contact:	Atle Monrad (atle.monrad@interdigital.com)

1. Introduction

This pCR proposes a solution for Key issue #19: ACR scenario combination.

More specifically, Key Issue #19 explains that using a single ACR scenario or using multiple ACR scenarios should be possible.

TR 23.700-98: Different combinations of utilizing ACR scenarios by Applications should be enabled by the Edge Enabler Layer (e.g. only one ACR scenario allowed or several ACR scenarios allowed).

2. Reason for Change

Rel-17 TS 23.558 defines information elements and procedures to learn about ACR capabilities (e.g. service continuity support) of EEL participants and to discover EEL participants with compatible ACR capabilities.

There is no procedure defined for selecting and initiating the ACR scenario(s) to use when an EEC chooses to use an EAS; or defining when such ACR scenario(s) should be initiated (e.g. when to start ACR detection phase).

Aditionally, ACR scenarios defined in Rel-17 EEL have incompatible ACR execution phases that should not be performed concurrently.

Observation #1: AC, EAS and EES profiles include ACR capabilities while the EEC context does not.

The EEC can communicate its ACR capabilities via the optional EEC registration request procedure. However, the EEC Context stored at the EES does not have an information element to store the EEC ACR capabilities.

The EEC can communicate its ACR capabilities via the EAS discovery request or subscription; EEC ACR capabilities are used as a filter to discover EAS(s) supporting compatible ACR scenarios.

The AC/EEC capabilities can support multiple ACR scenarios; thus, the AC/EEC that supports multiple ACR scenerios can select an EES and EAS that supports multiple ACR scenerios.

Observation #2: The EEL does not specify a single entity for selecting one or multiple ACR scenarios to use for a given AC and EAS pair.

The ACR selection should happen before the AC uses a selected EAS.

When the EEC performs EAS selection it should also be able to select the ACR scenario(s) to be used; the EEC can make this ACR selection using the ACR capabilities that are already available at the EEC (e.g. using the EAS Profile, the EES Profile, the AC Profile and the EEC’s own ACR capabilities).

Observation #3: ACR scenarios are composed four phases as shown on figure 8.8.1.1-1 of in TS 23.558; we’ll refer to these four phases as ACR detection, ACR decision, ACR execution and ACR cleanup in this paper.

Selecting multiple ACR scenarios to run concurrently for a given AC and EAS pair can provide benefits; for example performing ACR detection concurrently at the EEC and at the EAS. Using concurrent ACR scenarios is only possible during the ACR detection and the ACR decision phases.

The ACR execution phase for different ACR scenarios must not happen concurrently; the steps defined in the ACR execution phase of different ACR scenarios contain procedures and messaging that can result in service continuity failure if allowed to happen concurrently for a given AC and EAS pair.

Therefore when multiple ACR scenarios are selected for one AC and EAS pair, it is mandatory to gate the ACR execution phase to ensure that only one ACR scenario can enter the ACR execution phase and perform application context relocation.

3. Conclusions

<Conclusion part (optional)>

4. Proposal

This p-CR proposes a Key Issue #19 solution that is based on the following principles:

- The EEC selects ACR scenarios(s) to use for detection and decision for an AC and EAS pair when it selects the EAS

- The EEC communicates to the EES the selected ACR scenario list for detection and decision along with the selected EAS; the EES communicates the selected ACR scenario list for detection and decision to the selected EAS

- Each of the EEC/EES/EAS can begin the ACR detection and decision phases based on the selected ACR scenario list

- When ACR participant(s) perform an ACR decision, a coordination request is sent to the EES which ensures gating of the ACR execution to one of the deciding ACR entities.

It is proposed to agree the following changes to 3GPP TR 23.700-98 v0.5.1.

* * * * First Change * * * *

# 7	Solutions

## 7.0	Mapping of solutions to key issues

Table 7.0-1 Mapping of solutions to key issues

|  | KI # 1 | KI # 2 | KI # 3 | KI # 4 | KI # 5 | KI # 6 | KI # 7 | KI # 8 | KI # 9 | KI # 10 | KI # 11 | KI # 12 | KI # 13 | KI # 14 | KI # 15 | KI # 16 | KI # 17 | KI # 18 | KI # 19 | KI # 20 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Sol #1 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sol #2 |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sol #4 |  |  |  |  |  | X |  |  |  | X |  |  |  |  |  |  |  |  |  |  |
| Sol #5 |  |  |  |  |  | X |  |  |  | X |  |  |  |  |  |  |  |  |  |  |
| Sol #6 |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sol #7 |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sol #8 |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sol #9 |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |
| Sol #10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |
| Sol #11 |  | X |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sol #12 |  |  | X |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |
| Sol #13 |  |  |  |  |  | X |  |  |  | X |  |  |  |  |  |  |  |  |  |  |
| Sol #14 |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |
| Sol #15 |  |  |  |  |  |  |  | X |  |  |  |  |  | X |  |  |  |  |  |  |
| Sol #16 |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |
| Sol #17 |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |
| Sol #18 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |
| Sol #19 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |
| Sol #20 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sol #x |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |
| … |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

* * * * Next Change * * * *

## 7.x	Solution #x: EEC selected ACR scenarios with EES ACR coordination

### 7.x.1	Architecture enhancements

None

### 7.x.2	Solution description

#### 7.x.2.1	General

The following solution corresponds to the key issue #19 on ACR scenario combination.

#### 7.x.2.2	Procedure

This solution is based on the following principles:

-	The EEC selects ACR scenarios(s) to use for ACR detection and decision for an AC and EAS pair when it selects the EAS.

-	The EEC communicates to the EES the selected ACR scenario list for detection and decision along with the selected EAS; the EES communicates the selected ACR scenario list for detection and decision to the selected EAS.

-	Each of the EEC/EES/EAS can begin the ACR detection and decision phases based on the selected ACR scenario list.

-	When ACR participant(s) perform an ACR decision, a coordination request is sent to the EES which ensures gating of the ACR execution to one of the deciding ACR entities

In this solution, the EEC is responsible to determine the ACR scenario(s) that should be used for an AC and EAS pair. The EEC perfroms ACR selection at EAS selection time. Factors for selecting ACR procedures are out of scope of this solution.

The following ACR selection outcomes are possible:

-	The EEC can select no ACR scenario which indicates that service continuity is not supported or needed.

-	The EEC can select one ACR scenario which indicates that service continuity is supported and needed, and that ACR coordination at the EES is not supported or needed.

-	The EEC can select two or more more ACR scenarios which indicates that service continuity is supported and needed, and that ACR coordination at the EES is supported and needed.

The EES is responsible to perform ACR coordination when multiple ACR scenarios are selected by the EEC during ACR selection. ACR coordination ensures that only one of the selected ACR scenarios proceeds to the ACR execution phase. When an ACR decision is sent to the EES for ACR coordination, the EES can decide to allow or deny the ACR scenario to proceed to the ACR execution phase. The criteria for deciding which ACR scenario should proceed to ACR execution is out of scope of this solution.

Figure 7.x.2.2-1 presents an overview of the procedures for ACR selection at the EEC and ACR coordination at the EES.

Figure 7.x.2.2-1 EEC selected ACR scenarios with EES ACR coordination

- The EEC performs EAS discovery using procedures defined in 3GPP TS 23.558 [2] clause 8.5 to obtain a list of discovered EAS(s).

The discovered EAS list contains EAS(s) that are compatible with the AC and EEC ACR capabilities provided in the EAS discovery request or subscription.

- The EEC (or AC and EEC) selects one EAS from the discovered EAS list.

Additionally, the EEC selects the ACR scenario(s) that should be used for the given AC and selected EAS and assigns a unique ACR identifier (ACRID) to each ACR scenario in the list. ACR selection can result in zero or more ACR scenarios being selected.

NOTE 1:	ACR selection criteria are out of scope of the current solution.

- The EEC sends the selected EAS declaration request to the EES indicating which EAS was selected. If the EEC selected one or more ACR scenarios, the EEC includes the list of selected ACR scenario(s) to be used for the ACR detection and ACR decision phases.

- The EES sends an ACR selection notification to the selected EAS providing the selected ACR scenario list. Not shown on the figure, the EAS had to previously subscribe to receive ACR notifications.

- The EES sends the selected EAS declaration response to the EEC indicating success or failure of the EAS and ACR selection.

6.	Each of the EEC, the EES and the EAS determines if it should perform ACR detection and/or ACR decision based on the ACR scenario(s) in the selected ACR scenario list. This can result in one or more of the EEC, EES or EAS performing ACR detection and/or ACR decision.

7.	Depending on whether the ACR detection and ACR decision processing is performed in step 6. Each of the EEC, the EES and the EAS can concurrently detect UE mobility and decide that ACR is needed. Upon detection and decision of an ACR, the EEC and/or EAS can send an ACR coordination request to the EES. ACR coordination requests can be sent concurrently. Additionally (not shown on the figure) depending on the selected ACR list, the EES itself can have been performing ACR detection and decision; the EES considers this during ACR coordination. The ACRID of the ACR scenario that made the ACR decision is included in the ACR coordination request.

8.	The EES selects only one ACR scenario to proceed to the ACR execution phase. The EES considers ACRs that were indicated by the EEC and/or EES and/or EAS.

NOTE 2:	ACR coordination criteria used to select an ACR scenario are out of scope of the current solution.

9.	The EES sends an ACR coordination response to each ACR coordination request that it received. The ACR coordination response includes the ACRID of the ACR scenario that is allowed to proceed to the ACR execution phase.

10.	Each of the EEC, the EES and/or the EAS compares the ACRID from the ACR coordination response with the ACRID it provided in the ACR coordination request; only the ACR participant with matching ACRID is allowed to proceed to the ACR execution phase.

### 7.x.3	Solution evaluation

This clause provides an evaluation of the solution.

* * * * Next Change * * * *