3GPP TSG-SA WG6 Meeting #49-e	S6-221311 rev1

e-meeting, 16th – 25th May 2022	(revision of S6-221183 rev 2)

Source:	Convida Wireless LLC

Title:	AC Association aware service provisioning

Spec:	3GPP TR 23.700-98 v.0.6.0

Agenda item:	9.8

Document for:	Approval

Contact:	Catalina Mladin, mladin.catalina@convidawireless.com

1. Introduction

This pCR provides a solution in support KI #17 for use cases requiring multiple ACs to use services from a single common EAS (e.g., to meet strict latency requirements).

The solution defines enhancements to the service provisioning procedure that enables ACs/EECs of different UEs to share information with an ECS indicating an association between the ACs requires a common EAS. Based on this AC association information, an ECS can provision the EECs of the associated ACs with information for establishing a connection to a common EES. Via the common EES, the associated ACs/EECs can in turn discover and use services from a common EAS.

Rev 2 changes are highlighted in yellow. In rev 2 the document has also been updated with green highlights for the changes that had been made in rev 1. Both rev1 and rev2 changes are track-marked as “catalina rev” (in case rev 1 changes are not all highlighted).

For June 1st conf call, addressed the following comments:

- In step 2, Figure 7.27.2.4-1, it says: “If a match is not found, the ECS further compares…” In release 17, it was agreed to have minimum EAS info in the ECS. Now with this pCR, the ECS needs to maintain a lot of not supposed to managed info for AC association info. This is not ECS job.

[cm] changed, see blue highlights

- For step 3, Figure 7.27.2.4-1, Why to anchor in the same EES? CAAR can have the common EAS being used so any EES can query CAAR.

- [cm] unclear question, but in this solution EES uses CARR for storage, ECS makes EES choice

- Don’t understand the requirement for EEC registration impact.

- [cm] to discuss registration. It is not a requirement. The procedure can be deleted.

- 7.27.2.Y, don’t understand the need to maintain AC associations in the CAAR.

- [cm] to discuss in conf call

- The EEC registration part is not for the common EAS discovery, the detailed reason I provided in the email discussion.

[cm] to discuss at conf call. The registration procedure can be deleted, but we should clarify first

- why add Central AC Association Repository (CAAR)? It is out of SA6's scope.

[cm] because of impacts on ECS, if information is stored there

- why ECS will select multiple EES(s), if different EEC choose different EES, how to ensure select same EAS?

[cm] by using ACR. This has been explained via precious emailse.

- as for EES Store of AC Associations, ECS Query of AC Associations part, don’t see the value of these two procedure.

[cm] to discuss at conf call.

2. Reason for Change

Address Key Issue #17 discovery of a common EAS

3. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-98

* * * First Change * * * *

#### 7.27.2.4	Procedure for determining common EES

In this procedure, an EEC sends a service provisioning request to an ECS including an AC association Profile. Included in the AC association Profile is information regarding an association between AC(s) requiring use of a common EAS. Based on the AC association Profile, the ECS provisions the EEC with information for a common EES suitable for the AC association.  Pre-conditions:

- EEC has been pre-configured with rules for discovering the address (e.g. URI) of an ECS which can enable services for an AC association, i.e. has access to a Central AC Association Repository (CAAR);

- An AC association Profile has been provided to the EEC.

Figure 7.27.2.4-1 AC Association aware service provisioning

- EEC sends a service provisioning request to the ECS. The service provisioning request includes an AC association Profile. Included in the AC association Profile is information regarding an association between AC(s) on this UE and other ACs indicating that the use of a common EAS is required.

- Upon receiving the request, the ECS uses the AC association Profile information (e.g., association ID, associated UEs) to query the EES profile, AC Association tuples stored by CAAR to determine whether an EES is already servicing the AC association. If a match is not found, the ECS queries CARR using the procedure in 7.27.2.Z to determine if any of the EES(s) storing AC association at CARR are candidates to service the AC association (e.g., have registered EAS(s) meeting the requirements of the AC association).

- If the processing of the request with AC association Profile information was successful, the ECS responds to the EEC with a service provisioning response which includes information of the EES already servicing the AC association or information for EES(s) that are candidates to service the AC association.

If the ECS is unable to determine EES(s) to service the AC association, the ECS rejects the service provisioning request and responds with an appropriate failure cause.

If the ECS determines multiple EES(s) to service the AC association, the ECS provides an EES list to the EEC and may include parameters used to evaluate the AC association-related service.

Editor’s Note: The parameters used to evaluate the AC association-related service to be included in the response are FFS. They may include, for example, the number of ACs in the association which are being served by the EES, etc. Any such parameters are to be provided by the EES to the CAAR.

* * * Next Change * * * *

#### 7.27.2.X	EEC Registration Enhancements for AC Associations

Compared to the EEC registration procedure specified in 3GPP TS 23.558 clause  8.4.2.2.2 the following differences are captured below:

- The registration request sent from the EEC to the EES includes AC association profile information.

Compared to the EEC registration update procedure specified in 3GPP TS 23.558 clause  8.4.2.2.3 the following differences are captured below:

- The registration update request sent from the EEC to the EES includes AC association profile information.

#### 7.27.2.Y	EES Store of AC Associations

The EES procedure for storing its AC Associatiation at CAAR  uses a storage request in which the following information is provided to the CAAR: EES Profile, list of AC Associations Profiles being served, registrar ECS information including list of EDNs. This information is updated by EES when any of this information changes or is about to change (e.g. in advance of EES de-registration).

#### 7.27.2.Z	ECS Query of AC Associations

The ECS procedure for quering the AC Associatiation information at CAAR uses the AC Association Profiles recieived, and its own ECS information. The response provides a list of its registered EESs which serve the AC Association Profiles being queried for.

Editor’s Note: It is FFS whether and how the CAAR query may be used to direct EECs to a different ECS for the purpose of receiving services consistent with the AC Association