3GPP TSG-SA WG6 Meeting #49-BIS-e	S6-22xxxx

e-meeting, 22nd June – 1st July 2022	(revision of S6-221382)

Source:	Qualcomm

Title:	Pseudo-CR on Requirements for common EAS

Spec:	3GPP TR 23.700-98 v1.0.0

Agenda item:	9.8

Document for:	Approval

Contact:	Nishant Gupta <gnishant@qti.qualcomm.com>

1. Introduction

This pCR specifies requirements for a common EAS discovery, such that a group of ACs get service from the same EAS.

2. Reason for Change

Key issue #17.

Different scenarios that should be considered and expected result in those scenarios:

- All UEs in same EDN 1 ( UEs should be provided with EAS 1 as common EAS

- UEs distributed in two (or more) EDNs, where EDNs don’t overlap ( UEs should be provided with a common EAS in their respective EDNs. For UEs in EDN 1, EAS 1 is the common EAS; for UEs in EDN 2, EAS 2 is the common EAS. There is no coordination between the EDNs to find the common EAS. However, as a separate procedure EASs in EDN 1 and EDN 2 can use solutions of Key Issue #13 (Edge enabler layer support for EAS synchronization) for EAS sync.

- UEs distributed in two (or more) EDNs, where atleast one EDN covers all UEs ( UEs should be provided with a common EAS from the EDN that covers all UEs.

- UEs distributed in two (or more) EDNs, where there is a partial overlap ( maximum number of UEs should be provided with a common EAS.

The scenarios above assume that an EAS that meets the AC KPI requirements is available.

3. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-98 v0.6.0.

* * * First Change * * * *

## 5.x	Common EAS

### 5.x.1	General

This clause specifies requirements for common EAS discovery, such that a group of ACs can get service from the same EAS.

### 5.x.2	Requirements

1.	Edge Enabler Layer shall enable a group of application clients to discover a common EAS i.e., same EASID, EAS endpoint and EDN.

2.	Edge Enabler Layer shall lookup for a common EAS such that the common EAS provides similar KPIs for all the application clients in the group, if required by the application.

NOTE 1:	What KPIs e.g. latency, bit rate etc. EEL uses and how will these KPIs are obtained to lookup for the common is subject of the solutions of this key issue.

3.	Edge Enabler Layer shall enable a group of application clients to be redirected to a different common EAS.

NOTE 2:	Redirection to a different common EAS can happen due to several reasons such as additional ACs requiring to connect to the common EAS, EAS unavailability etc.

NOTE 3:	Requirement of ACs to use a common EAS based on application client and EAS requirements is determined and managed at the application layer.

NOTE 4:	Application clients can be running on the same UE or different UEs.