3GPP TSG-SA WG6 Meeting #49-e	S6-221140

e-meeting, 16th – 25th May 2022	(revision of S6-22xxxx)

Source:	Ericsson

Title:	Solve EN for sol#18

Spec:	3GPP TS 23.700-98 v0.7.0

Agenda item:	9.8

Document for:	Approval

Contact:	Wenliang Xu; wenliang.xu@ericsson.com

1. Introduction

This contribution solves the EN in sol#18.

2. Reason for Change

In sol#18, there is an EN saying:

Editor's Note: Whether or not EEL can provide ACR support for ACR scenarios (clause 8.8.2.4 and clause 8.8.2.5 of 3GPP TS 23.558 [2]) is FFS

It is obvious that EEL’s support for ACR scenarios in cl.8.8.2.4 and 8.8.2.5 is base function in Rel-17. The EN can be simply removed.

For CC on 1st June:

During SA6#49e, there is a concern raised:

“Let’s move first from EES 1 to EES 2, and then to EES 3 as a second step. Without registration at EES 1, there is no context in EES 1, therefore EEC context relocation is not performed EES 1-> EES 2. When ACR between EES 2 and 3 needs to be performed, how does EES 2, now S-EES, perform T-EAS discovery? So without context you can go only one step for these 2 scenarios.”

Ericsson’s Answer: it is about whether the EEL entity in the 2nd ACR can have sufficient info to perform T-EAS discovery w/o having EEC context. After further investigation, it is not even a legacy issue.

For S-EAS decided ACR scenario, the S-EAS (let’s say S-EAS is EAS 2 which is registered in EES 2) has sufficient info to discover T-EAS, in the following steps:

- UE moves from EDN 1 to EDN 2, EEC registration is not performed in both EDNs (i.e. no EEC context maintained in EES 1 and EES 2)

- Then UE moves from EDN 2 to EDN 3, the EAS 2 in EDN 2 can discover T-EAS via EES 2 w/o requiring EEC context being maintained in EES 2.

For S-EES decided ACR scenario, the S-EES (let’s say S-EES is EES 2) also has sufficient info to discover T-EAS, in the following steps:

- UE moves from EDN 1 to EDN 2, EEC registration is not performed in both EDNs (i.e. no EEC context maintained in EES 1 and EES 2)

- Then UE moves from EDN 2 to EDN 3, the EES 2 in EDN 2 can discover T-EAS w/o requiring EEC context being maintained in EES 2. This is because EES 2 either receives “ACR determination” action with T-EAS info directly or being instructed by S-EAS in EELManagedACR/ACR facilitation. All those APIs or API operations have EAS characteristics (i.e. EAS discovery filters) included.

| EAS characteristics for ACR | O | Set of characteristics to determine required EAS as detailed in Table 8.5.3.2-2. Applicable for the "ACR monitoring" event and "ACR facilitation" event. |
| --- | --- | --- |

Hence, the EN can remove the 8.8.2.4 clause.

Of course, current proposal doesn’t preclude EEC registration (if required by EES) for constraint UE.

3. Conclusions

<Conclusion part (optional)>

4. Proposal

It is proposed to agree the following changes in TS 23.700-98.

* * * First Change * * * *

### 7.18.2	Solution description

This solution addresses KI#15. In this solution, in order to reduce power consumption in the UE, it specifies the EEC with Reduced Capabilities (RedEEC). The RedEEC skips EEC registration and the EAS discovery procedure is enhanced to delegate the EAS selection to EES. Figure 7.18.2-1 illustrates the details interactions.

Figure 7.18.2-1: service provisioning and EAS discovery for constraint device

In step 1, EEC performs service provisioning. For EAS discovery, the EEC sends the request to a selected EES from the candidate EES(s) and indicates UE type to EES in step 2. In step 3, the EES performs EAS discovery as described in clause 8.5.2.2 of 3GPP TS 23.558 [2] and in addition selects a suitable EAS from discovered candidate EAS(s) if UE type indicates constraint device, then the EES sends EAS discovery response to the EEC including the selected EAS information in the Discovered EAS list. In step 5, if the EAS discovery response contains successful result, the EEC sends to AC the received selected EAS information and the EAS discovery and selection procedure ends; otherwise, the EEC repeats step 2 with next selected candidate EES.

NOTE:	The EEC can interact with each candidate EES if no appropriate EAS can be selected by EES.

Table 7.18.2-1 and table 7.18.2-1 below show the detailed impact (highlighted with bold text) for EAS discovery request and response.

Table 7.18.2-1: EAS discovery request

| Information element | Status | Description |
| --- | --- | --- |
| Requestor identifier | M | The ID of the requestor (e.g. EECID) |
| UE Identifier | O | The identifier of the UE (i.e. GPSI or identity token) |
| Security credentials | M | Security credentials resulting from a successful authorization for the edge computing service. |
| EAS discovery filters | O | Set of characteristics to determine required EASs, as detailed in Table 8.5.3.2-2. |
| UE location | O | The location information of the UE. The UE location is described in clause 7.3.2. |
| Target DNAI (NOTE) | O | Target DNAI information which can be associated with potential T-EAS(s) |
| EEC Service Continuity Support | O | Indicates if the EEC supports service continuity or not. The IE also indicates which ACR scenarios are supported by the EEC or, if this message is sent by the EEC to discover a T-EAS, which ACR scenario(s) are intended to be used for the ACR. |
| EES Service Continuity Support (NOTE) | O | The IE indicates if the S-EES supports service continuity or not. The IE also indicates which ACR scenarios are supported by the S-EES or, if the EAS discovery is used for an S-EES executed ACR according to clause 8.8.2.5, which ACR scenario is to be used for the ACR. |
| EAS Service Continuity Support (NOTE) | O | The IE indicates if the S-EAS supports service continuity or not. The IE also indicates which ACR scenarios are supported by the S-EAS or, if the EAS discovery is used for an S-EAS decided ACR according to clause 8.8.2.4, which ACR scenario is to be used for the ACR. |
| UE type | O | Indicates UE or device type (e.g. constraint device) |
| NOTE: This IE shall not be included when the request originates from the EEC. |

Table 7.18.2-2: EAS discovery response

| Information element | Status | Description |
| --- | --- | --- |
| Successful response | O | Indicates that the EAS discovery request was successful. |
| > Discovered EAS list | O | List of discovered EAS(s). Each element includes the information described below. Based on UE type, only one EAS may be included. |
| >> EAS profile | M | Profile of the EAS. Each element is described in clause 8.2.4 |
| >> Lifetime | O | Time interval or duration during which the information elements in the EAS profile is valid and supposed to be cached in the EEC (e.g. time-to-live value for an EAS Endpoint) |
| Failure response | O | Indicates that the EAS discovery request failed. |
| > Cause | O | Indicates the cause of EAS discovery request failure. |

In service continuity, to offload UE from monitoring triggers (e.g. location change) to start ACR, EEC can announce its support for EDN side decided ACR scenarios (clause 8.8.2.4 and clause 8.8.2.5 of 3GPP TS 23.558 [2]) so that EEC only need to passively receive ACR information notifications.

### 7.18.3	Solution evaluation

This solution addresses KI#15 with EAS discovery and selection procedure for constrained device using EDGEAPP. The EEC relies on EES to select an appropriate EAS (the EEC does not need to select an EAS among discovered EAS list from candidate EESs).

* * * End of Changes * * * *

# Comments

tbu