## Slide 1: Discussion on FS_MCShAC
Jens Toobe, BDBOS
Supporting companies:
FirstNet, MINISTERE DE L'INTERIEUR, Nokia

## Slide 2: Outline
Discussion paper:
Intention of the WI
Further Background
Proposed functional model
User configuration exchange procedure
Agree way to progress the study
  Summary and next steps/discussion points

## Slide 3: Intention of WI
Transpose SA1 service requirements into architecture
  Gap in 3GPP specification identified and requirements added
  Based on a SA1 study (TR 22.881) requirements in 3GPP TS 22.280 were added. See clause 5.16.4 - Sharing of administrative configuration between Mission Critical Organizations.
No intention to standardize vendor specific/internal interfaces or processes
Allow standardized exchange of administrative information between MC systems via a separate interface

## Slide 4: Further Background
Public safety needs a standardized way to allow agencies/organizations that do not normally share personnel to be able to exchange information on first responders, who are sent to assist in a large incident, e.g., hurricane, earthquake or other operational scenarios.
European rails and other agencies need an automated way to send user information between MC systems to allow users to move between those systems.

## Slide 5: Proposed Generic Functional Model

## Slide 6: Simplified User Config Exchange Procedure
Primary MC system generates user configuration request and sends the information to a partner MC system for inclusion/addition/change or deletion of user configuration.
Partner MC system verifies and checks the request and its content. In case the request is validated and confirmed, the user configuration information is distributed to the relevant server entities within the partner MC system.
Should the validation of the user configuration information fail, optionally, the request is sent to an ACM client for further action.
The primary MC system is informed of the results.

## Slide 7: Summary
Service requirements have been identified and defined in SA1
There are requirements, clear mandate and strong support by PPDRs to have an Administrative Configuration Exchange (ACX) capability established and standardized by 3GPP
It cannot be assumed that MC systems operated by PPDR organizations that need to exchange MC users will have relevant MC server connections established, other than between ACX entities.
Technically viable solutions should be accepted into studies
Involvement of companies with experience in exchange of users, e.g., mutual aid, are invited to share their expertise.

## Slide 8: Next steps/discussion points
Agreement on architecture enhancements
Review/new solutions for SA6#50