## Slide 1: EDGEAPP_Ph2 work plan
Sapan Shah
Rapporteur, Samsung

## Slide 2: Outline
Current Status of WID Objectives
Aspects to be considered in Normative
Summary and Work Plan

## Slide 3: Current Status of WID Objectives
Work progressed for bringing concluded solutions from study to normative specification for KI# 1, 2, 3, 4, 7, 8, 9, 14, 19, 21

## Slide 4: Aspects to be considered in Normative
KI#1
“The above enhanced notification services utilizing push notification, application triggering via SMS over NAS and leveraging generic notification service from SEAL in lieu of Edge Notification Server will be addressed in the normative phase. ”
KI#2
“EES supporting EAS's and other entity's (e.g. ETSI MEP or MEC App.) access to service APIs exposed by other EAS, in the context of CAPIF, will be addressed in the normative phase. ”
KI#3
“Solution#6 addresses the open issue #3 by introducing a new procedure to modify ACR parameters. Specifying the signaling required for the procedure are to be addressed in the normative phase (without impacting AC).”
“Further investigation in normative work is required for sol#12 to evaluate backward compatibility issue inthis solution.”
KI#6
“Detailed signalling to provide ECS2 address to the requesting EEC or EES based on solution #4 is to be addressed in normative phase. Signalling between ECS1 and ECS2 to discover and retrieve provisioning to the requesting EEC or T-EES for the requesting EES will be addressed in normative phase according to solution #5. A new interface EDGE-10 between ECS1 and ECS2 is used in Solution #5. Also, in normative phase, if required, the additional optional IEs are added to ECS configuration information provided by ECS to 5GC according to Solution #13.”
KI#11
“What functionalities of EDGE-9 and EDGE-6 are to be reused for EDGE-14 and EDGE-15 respectively in clause 6.5 and the detailed differences for EDGE prime reference points and the cardinality rules in clause 6.6, will be addressed in the normative phase.”

## Slide 5: Aspects to be considered in Normative
KI#17
To Select one or more solution or to merge solutions
KI#22
To Select one or more solution or to merge solutions (Based on GSMA LS response)
Unresolved ENs
E.g. Solutions for KI#18

## Slide 6: Work Plan
Respect the overall evaluation and conclusions in the study
Contribution plan
  To complete discussion on solutions which has left overs from study
    KI #1, #2, #3, #6, #11, #17, #18, #22, #23
  To bring solutions which are concluded and has no left overs
    KI #5, #7, #8, #9, #10, #12, #13, #14, #15, #16, #20, #24
  Complete the solutions already agreed in normative
    KI #1, #2, #3, #4, #7, #8, #9, #14, #19, #21
Preparation before meeting
  Share solutions to interested companies to get early comments
  Remember: We are SA6 !!
    If a solution is shared to you, provide on time and constructive feedback to help the author.
    This should help progress in Rel-18 (only 2 meetings left), otherwise we have postpone few things to Rel-19.