## Slide 1: Discussion: Proposed Solution for UE Identifier API with NATed UE IP Address
Shahram Mohajeri
AT&T

## Slide 2: Contents
Overview of the NATed UE IP Address problem
Rel-18 EDGEAPP Study attempt in solving the problem
Background on existing EES UE Identifier API
Proposed solution description
Proposed solution – high level call flow

## Slide 3: Overview of the NATed UE IP Address problem
Nnef_UEId_Get opertion in Rel-17 doesn’t support NATed UE IP Address
  TS 23.502 clause 4.15.10:
    NOTE 3: The case where UE IP address provided by the AF to the NEF corresponds to an IP address that has been NATed (Network and Port Address Translation) is not supported in this release.
Recent LS (S6-221953) to SA2 and the LS reply from SA2 (S6-223087) reconfirmed the above
  SA6 Question: “Can SA2 support taking NATed UE IP address as input and then expose the UE External ID to EES?”
  SA2 Answer: states as per NOTE 3 in TS 23.502 above“…there is currently no specification support for exposure of UE External ID based on the NATed UE IP address.”
  In stage 3 (TS 29.522) Nnef_UEId_Get maps to the following endpoint
  EES requesting to “retrieve” AF-specific UEId using a NATed UE IP address as input would result in an error response (HTTP “404 Not Found“)

## Slide 4: Rel-18 EDGEAPP Study attempt in Solving the Problem
In Rel-18 EDGEAPP Study, solution #23 is based on having EES invoke the Nnef_UEID API with UE’s private IP address. However, for large network deployments due to private IP address reuse, solution #23 is not workable.
Related Q/A from the recent LS (S6-221953) to SA2 and the LS reply from SA2 (S6-223087) as shown below is not promising:
  SA6 Question: “In certain deployment when multiple UEs are allocated with the same private IP address, can SA2 support addressing IPv4 address overlap issue?”
  SA2 Answer:
    “when this same private IP address is allocated to different UE(s) for different DNN and S-NSSAI(s) by associating the AF with a DNN and S-NSSAI
    Otherwise and furthermore, the "ipDomain" attribute as defined in TS 29.514 clause 4.2.2.2 Note 3 may be leveraged
    The above DNN/S-NSSAI or ipDomain attribute is not expected to be exposed outside the 5GC network.”
  ”

## Slide 5: Background on existing EES UE Identifier API
Rel-17, TS 23.558 has defined Eees_UEIdentifier API with a single operation called “Eees_UEIdentifier_Get” which can be used by EAS to retrieve the AF-specific UEId for a given IP Address (aka User Info.)
This operation is a direct RESTful API call between the EAS and the EES
In stage 3 (TS 29.558) “Eees_UEIdentifier_Get” maps to the following endpoint:
e.g. POST https://example.com/eees-ueidentifier/v1/fetch

## Slide 6: Proposed solution description
An IPv4 EAS instead of making a direct RESTful API call (i.e. POST ../fetch) to the EES
  Would take advantage of the UE’s dual-stack and
  Redirect the UE (via HTTP 302) to a newly introduced EES endpoint:
    {apiRoot}/eees-ueidentifier/<apiVersion>/redirectedFetch
EES “redirectedFetch” is an IPv6 endpoint registered in DNS
  Causes, the UE to switch to its IPv6 stack (i.e. UE is assigned an IPv6 address by 5GC as it redirects to EES’s “redirectedFetch” endpoint)
Net result: EES sees the UE’s IPv6 address and uses it to invoke Nnef_UEId_Get service which will successfully return the AF-specific UEId
In stage 3 “Eees_UEIdentifier” API would introduce an additional new endpoint (as highlighted):
{apiRoot}/eees-ueidentifier/<apiVersion>
/fetch
/redirectedFetch

## Slide 7: Proposed solution description (Cont’d)
EES in stage 2 (TS 23.558) would introduce a new service endpoint
  i.e. a new operation in the existing Eees_UEIdentifier API called “Eees_UEIdentifier_RedirectedGet”
This new EES service endpoint is to be used only by IPv4 EASs for redirecting the UE’s (via HTTP 302) to this endpoint in order to retrieve the UEId
  i.e. an IPv4 EAS, in MNO networks where NAT is used, would be informed (at onboarding) to use this new “Eees_UEIdentifier_RedirectedGet” operation (as opposed to “Eees_UEIdentifier_Get” operation) to retrieve the UEId
  At onboarding, EAS also provides a redirect-URI and a notification-URI which will be used by EES to return the UEId either via an in-band redirect (HTTP 302) or an out-of-band notification method
Note: The new API request is an indirect call from EAS to EES through the UE
  While the reply from EES to EAS carrying the UEId can be indirect through the UE or direct via notification
API Name | API Operations | Operation Semantics | Consumer(s)
Eees_UEIdentifier | Get | Request/Response | EAS
 | RedirectedGet | Request/Response | EAS via UE redirect (HTTP 302)
23.558: Table 8.6.5.4.1-1

## Slide 8
App client
on UE
EAS
(IPv4)
1. GET (some application request) SourceIP addr = NATed IPv4
3. HTTP 302 redirect: GET {apiRoot}/eees-ueidentifier/v1/redirectedFetch?Seq=xyz
2. EAS needs UEId (then will redirect the UE to get the UEId by pointing it to the EES’s redirectedFetch endpoint )
EES
{apiRoot}/eees-ueidentifier/v1/redirectedFetch
NEF
5. Nnef_UEId_Get ( UE-IPv6-addr, AFId)
6. Response (AF-specific-UEId=1234567abcd)
7. HTTP 302 redirect: GET EAS1.com?Seq=xyz, AF-specific-UEId=1234567abcd
Option “A”: return UEId to EAS via an EAS-registered redirect-URI
Option “B”: return UEId to EAS via notification at an EAS-registered notification-URI
4. UE’s source IP address is IPv6 =2001:db8:3333:4444:5555:6666:7777:8888
NOTE: Now EES can invoke a Nnef_UEId_Get service with UE’s IPv6 as input
8’. Notify (Seq=xyx, AF-specific-UEId=1234567abcd)
Proposed solution – high level call flow
7’. HTTP 302 redirect: GET EAS.com?Seq=xyz, ack-Ok