3GPP TSG-SA WG6 Meeting #52-bis-e	S6-22xxxx

e-meeting, 16th – 20th January 2023	(revision of S6-22xxxx)

Source:	BDBOS

Title:	MCShAC – use of functional alias

Agenda Item:	9.2

Contact:	dania.azem@bdbos.bmi.bund.de

Introduction

During SA6#52 some approved solutions introduced the use of functional alias in the information flows.

For example in solution #8, the MC service user profile update request is defined as:

Table 7.10.1.2.1-1: MC service user profile update request

| Information element | Status | Description |
| --- | --- | --- |
| MC service ID | M | The identity of the MC service user at the primary MC system who triggers the request. |
| Functional alias | O | The functional alias of the MC service user at the primary MC system triggers request. |
| MC service ID | O (see NOTE) | The identity of the MC service user at the partner MC system towards which the request is sent |
| Functional alias | O (see NOTE) | The functional alias of the MC service user at the partner MC system towards which the request is sent |
| MC service ID | M | MC service ID of the migrated MC service user, which has been created by the partner MC system. |
| MC service user profile | M | The suggested updated MC service user profile on the partner MC system. |
| Additional Information | O | Additional information regarding the suggested updated MC service user profile on the partner MC system. |
| NOTE: Either the MC service ID or the functional alias must be present. |

Nevertheless, the use of functional alias for ACMX raised some concerns/questions:

- How to handle the request if the addressed FA is not active when the request is received, since the target MC system cannot store it and may/should deny this request.

- How to resolve the received FA at the MC system

Conclusion

The related procedures will be updated if required