## Slide 1: Authorization of MCX users at Location management server
Andreas Flander
BDBOS

## Slide 2: Outline
The postponed CRs in Tdoc S6-230308, S6-230309 and S6-230310 proposed adding authorization parameters for MCX users at LMS during SA6#52-Bis-e.
In TS 23.280 some procedures in clause 10.9 require such authorization prior to proceeding the requests.
For example the procedure Restrict location information dissemination (clause 10.9.3.11), has configurable parameter in each of MCX user profile configuration data which authorises MCX users or not.

## Slide 3: Outline
The discussed contributions propose to introduce in total 5 parameters to each MCX user profile configuration data:
  Authorised to request Location information
  Authorised to request Location information subscription
  Authorised to request Location information history
  Authorised to request Location information from an Partner MC System
  Authorised to request Location information subscription from an Partner MC System

## Slide 4: Proposed authorizations parameters
Authorised to request Location information: This parameter contains authorization for requests covering 3GPP TS 23.280 procedure below:
  10.9.3.3 Client triggered location reporting procedure
  10.9.3.6.2 On-demand usage of location information procedure
  10.9.3.8.1 Client-triggered one-time location information report
  10.9.3.8.2 Client-triggered periodic location information report

## Slide 5: Proposed authorizations parameters
Authorised to request Location information subscription: This authorization enables setup and cancellation of subscriptions. Procedures in 3GPP TS 23.280, clause 10.9 requiring this authorization:
  10.9.3.5 Location information subscription procedure
  10.9.3.7 Location information cancel subscription procedure

## Slide 6: Proposed authorizations parameters
Authorised to request Location information history: The history of location data is stored at the MCX user’s UE. Authorised Clients may request this data or status of this data from another Location management client. Related procedures in 3GPP TS 23.280, clause 10.9:
  10.9.3.9.2.1 On-demand report location history procedure
  10.9.3.9.3.1 On-demand status location history reporting procedure
  10.9.3.9.4.3 Cancel location history reporting procedure

## Slide 7: Proposed authorizations parameters
Authorised to request Location information from an Partner MC System: This parameter contains a list of partner MC systems. Related procedure in 3GPP TS 23.280, clause 10.9:
  10.9.3.10.2 On-demand request of location information procedure

## Slide 8: Proposed authorizations parameters
Authorised to request Location information subscription from an Partner MC System: The parameter contains a list of partner systems, where the subscription lasts until cancellation is requested. Related procedures in 3GPP TS 23.280, clause 10.9:
  10.9.3.10.4 Location information subscription procedure
  10.9.3.10.5 Location information cancel subscription procedure