## Slide 1: FRMCS Future Railway Mobile Communication System TR 22.889 Introduction
Martin Oettl
Nokia
Rapporteur
3GPP TSG-SA WG6 Meeting #16
Dali, China
Notes: 1

## Slide 2: High-level relation of FRMCS and legacy systems
Notes: 1

## Slide 3: Definitions
Controller (Train Controller): A Ground FRMCS User provided with special capabilities by the FRMCS System.
Driver (Train Driver): A Mobile FRMCS User provided with special capabilities by the FRMCS System.
External System(s): A general category of stationary FRMCS Users (e.g. external system monitoring trains passing a red light and initiate a railway emergency call).
FRMCS Application: The application on a 3GPP UE offering railway specific communication services to the FRMCS User by making use of the communication capabilities offer by a 3GPP UE and 3GPP network.
FRMCS Equipment Identity: The identity by which a FRMCS equipment can be addressed.
FRMCS Equipment Type: Indicates the purpose the FRMCS equipment which is being used, FRMCS equipment of different equipment type do have different capabilities.
Notes: 1

## Slide 4: Definitions – cont.
FRMCS Equipment: The FRMCS Equipment consists of a 3GPP UE and a FRMCS Application residing on it.
FRMCS Functional Identity: The identity related to a user or related to the equipment (e.g. as Driver of a specific train, usually a train number).
FRMCS System: The system providing railway specific communication constituted of the FRMCS Equipment (GSM-R is not part of the FRMCS System).
FRMCS User Identity: The identity by which a FRMCS User can be addressed.
FRMCS User: A human user or a machine making use of the railway specific communication.
Ground FRMCS User: A general category of FRMCS Users that are predominantly stationary.
Mobile FRMCS User: A general category of FRMCS Users that are mobile.
Role (Functional Role): The function a FRMCS User or a FRMCS Equipment is currently performing (e.g. driver, controller or shunting staff, etc.)
Notes: 1

## Slide 5: Grouping of FRMCS Applications
stable
To be defined
not stable
Notes: 1

## Slide 6: Basic functionality
Notes: 1

## Slide 7: Basic functionality
The basic functionality use cases describe the behavior of the FRMCS Equipment when powered up and down. For power up it takes the already powered up 3GPP UE as starting point conversely the same applies for power down.
Power on the UE
    The FRMCS Application shall be capable to perform a self-test and inform the user about the results.
Access to the FRMCS System
    When a FRMCS Equipment registers to the FRMCS System, the FRMCS Equipment capabilities are activated and the FRMCS Equipment shall be reachable by its FRMCS Equipment Identity.
Controlled power down UE
    When the UE is about to be powered down, a FRMCS-user logged into the FRMCS System shall be logged off first and deregistered from the FRMCS System. The FRMCS Equipment capabilities shall be deactivated and the FRMCS Equipment shall be removed from the FRMCS System.
Uncontrolled power down UE
    When the UE is uncontrolled powered down, a FRMCS-user logged into the FRMCS System shall be logged out from the FRMCS System and deregistered from the FRMCS System.
Notes: 1

## Slide 8: Critical communication applications
Notes: 1

## Slide 9: Critical communication applications
Critical communications applications are essential for train movements, safety, shunting, presence, trackside maintenance, legal aspects such as emergency communications, etc.
Multi-train voice communication for Drivers including Ground FRMCS User(s)
    A Driver and/or a Ground FRMCS User has a voice communication to other Drivers and/or Ground FRMCS Users.
On-train outgoing voice communication from the Driver towards the Controller(s) of the train
    A Driver has a voice communication to the Controller(s) that was, is, or will be responsible for the movement of the train.
Notes: 1

## Slide 10: Critical communication applications
Railway emergency communication
  Initiation of the Railway emergency alert
    An FRMCS-user is able to initiate a Railway emergency alert to another FRMCS-user, e.g. a mobile FRMCS User, a Driver, an External System, a Controller, maintenance staff or a member of a shunting team.
  New entry to the Railway emergency alert
    The FRMCS System shall continuously check if additional FRMCS Users meet the conditions of the Railway emergency alert. The additional FRMCS-users receive the Railway emergency alert.
  Changing of the Railway emergency alert
    The Controller or an External System is able to change the conditions selecting the appropriate recipients of the Railway emergency alert. The change may result in an expansion or a reduction of FRMCS Users that shall be informed about the emergency situation.
  Leaving of the Railway emergency alert
    The FRMCS System shall continuously check if FRMCS Users do match to the condition of the Railway emergency alert. If not, FRMCS System terminates the alert of the concerned FRMCS-user.
  Termination of the Railway emergency alert
    The Controller is able to terminate the Railway emergency alert.
Notes: 1

## Slide 11: Critical communication applications
Railway emergency communication
  Initiation of railway emergency voice communication
    Based on operational rules, additional information about the emergency situation can be exchanged using voice communication, e.g. the initiator of the railway emergency voice communication may inform other involved FRMCS-users about the emergency situation.
  Initiation of Data communication during Railway Emergency Alert
    Based on operational rules, additional information about the emergency situation can be exchanged using data communication, e.g. a system or a user is able to send the additional information like text or voice prompts.
  Service interworking and service continuation with GSM-R
    For migration purposes, the service interworking and service continuation between the GSM-R system and FRMCS System for Railway emergency alerts and Railway emergency voice communication needs to be defined.
  Interface to train borne recorder
    The FRMCS Equipment shall provide information about Railway emergency communication to the train borne recorder or other equipment via a dedicated interface.
Automatic Train Control (ATC) support by the FRMCS System
    For Automatic Train Control (ATC) the train transmits its information (such as current location, current speed, etc.) to a radio block center (RBC). The RBC uses the received information to decide about the movement of the train.
Notes: 1

## Slide 12: Performance communication applications
Notes: 1

## Slide 13: Performance communication applications
Transmission of real time video
    An FRMCS User requesting another FRMCS User to transmit real time video
    An FRMCS User receiving a real time video request to transmit real time video
    An FRMCS User accepting a request to transmit real time video
    An FRMCS User rejecting a request to transmit real time video
    An FRMCS User ignoring a request to transmit real time video
Transfer of CCTV archives
    CCTV archives are uploaded via bulk transfer from the on-board system to the ground system.
    Transfer of CCTV archives inside the train between different storages and through Inter-carriage links into the FRMCS node providing the uplink connection with the ground system.
Data transmission in real time
    Authorized FRMCS Users can exchange data in real time between each other, for example, health and status of train are transferred between intelligent on-train systems and train maintenance..
Notes: 1

## Slide 14: Business communication applications
Notes: 1

## Slide 15: Business communication applications
Live streaming of multimedia
    Live streaming of multimedia content from ground to train to allow passengers having access to live streaming services through the FRMCS System in the train.
Bulk transfer of multimedia data bases from ground to train
    The FRMCS System enables transfer of multimedia databases from ground to train while the train stops at the stations or is at the depot. The multimedia may contain movies, TV shows, cached webpages etc.
Notes: 1

## Slide 16: Critical support applications
Notes: 1

## Slide 17: Critical support applications
Critical applications are essential for train movements, safety, shunting, presence, trackside maintenance, legal aspects such as emergency communications, etc.
Assured voice communication (AVC)
    Assured Voice Communication (AVC) provides an indication to FRMCS-users as soon as a voice communication link is interrupted. It is invoked on an existing voice communication between two or more FRMCS-users:
    - Invocation of AVC
    - Stopping AVC
    - Interruption of a communication link
    - Extension of AVC to a new user
Notes: 1

## Slide 18: Critical support applications
Role management and presence
  Registration to a functional identity
    A FRMCS-user or the FRMCS Equipment shall be able to register to one or multiple functional identities. A functional identity can therefore be equipment related or user related.
  Deregistration of a functional identity
    A FRMCS-user or the FRMCS-equipment shall be able to deregister from one or multiple functional identities.
  User log-in to the FRMCS System
    The user is identified by the FRMCS System.
  User log-out from the FRMCS system
    The FRMCS-user is logged out of the FRMCS System.
  Presentation of identities
    A FRMCS-user or the FRMCS-equipment shall be able to be identified by the functional identity(ies) to other FRMCS-users.
  Interrogation of identities within a certain context
    A FRMCS-user or the FRMCS-equipment is able to recognize which other functional identities are present within a certain context (for example on a train, region, communication group, Railway Emergency Communication, all Drivers on a station, etc.).
Notes: 1

## Slide 19: Role management
Functional identities
Leading train driver
Driver 2
Driver 3
Shunting leader
Shunting member
Track side maintenance leader
Track side maintenance member
Primary train controller
Secondary train controller
Power controller
Shunting controller
Trackside maintenance controller
Platform inspector
Public announcement
Chief conductor
Second conductor
Third conductor
Catering staff chief
Diagnostics
Functional identity
A user can be authorized to be a train driver (functional Role) of a train.
The train running schedule assigns a specific train running number for this train, e.g. 123. The train driver uses his equipment to register himself as the leading train driver (functional Role) of train number 123 (Functional Identity).
After registration the train driver is registered to the system as the leading train driver of train 123 and known to other users by a specific Functional Identity.
Notes: 1

## Slide 20: Role management
Equipment type | Equipment Capabilities (Examples)
Cabin radio | Emergency button, external loudspeaker
Shunting radio | Loudspeaker, hands free
Trackside maintenance radio | 
Security staff radio | Emergency button, public emergency call button
Catering staff radio | 
Train controller device | Emergency button, call to maintenance staff button, call to power controllers button
Shunting controller device | 
Sensor | No HMI
FRMCS Equipment Type
The FRMCS Equipment is constituted of an UE and the FRMCS Application on this UE.
The FRMCS Equipment Type is relevant for the registration process of functional identities.
For example a train driver cannot perform registration as train driver of train 123 if he uses a catering staff FRMCS Equipment.
The FRMCS Equipment shall also be reachable based on the identity of the FRMCS Equipment. For example the cabin radio of a specific train can be reached by their FRMCS Equipment Identity.
FRMCS-user identity
The railway employee (a specific person) is also reachable even if no functional identity has been assigned.
This is done by using a unique FRMCS-user identity.
After the employee has performed the log-in procedure to the FRMCS System, the user is reachable via his individual FRMCS-user identity.
Notes: 1

## Slide 21: Role management
Equipment without MMI, without the possibility to be addressed via a functional identity related to the equipment (e.g. sensor in the track)
Equipment that can be registered to a functional identity related to the equipment (e.g. PA system on a train) but without other FRMCS-user login.
Equipment that can be registered to a functional identity and that allows a FRMCS User to login and register to functional identities related to the user (e.g. cabin radio)
Equipment that cannot register to a functional identity, but that allows a FRMCs user to login and to register to functional identities related to the user (e.g. a generic handheld device)
Notes: 1

## Slide 22: Critical support applications
Location services
  Provide location information
    The FRMCS Equipment provides its location information to the FRMCS System for further processing e.g. for automatic train operation. External systems can support providing additional location information.
  Request for location information
    A FRMCS-user, an application or an External System can request the location information of a functional identity, FRMCS-user identity or FRMCS Equipment Identity from the FRMCS System.
  Request for identities in a certain area
    A FRMCS-user, an application or an External System can request identities based on location information from the FRMCS System.
FRMCS-user communication handling
  Inviting-a-FRMCS-user to a voice communication
    A FRMCS-user can invite another FRMCS-user to a new or an existing voice communication.
  FRMCS-user receiving an invitation to a voice communication
    A FRMCS-user will receive the invitation originated by the inviting FRMCS-user.
  FRMCS-user accepting an invitation to a voice communication
    A FRMCS-user can accept the invitation sent by the inviting FRMCS-user.
  FRMCS-user rejecting an invitation to a voice communication
    A FRMCS-user can reject the invitation sent by the inviting FRMCS-user.
  FRMCS-user ignoring an invitation to a voice communication
    A FRMCS-user can ignore the invitation sent by the inviting FRMCS-user.
Notes: 1

## Slide 23: Critical support applications
End to End Prioritization
    This priority is an end to end priority to be applied on application layer. In certain cases priority on transport layer might be derived from this.
Multi user talker control (on and off network)
  Set the number of simultaneous talkers
    For multi user communication, i.e. when several users are involved in the same communication, the number of users that are granted the right to talk at the same time can be limited to either one, a limited number or unrestricted number.
  Set initial talker permissions and priorities
    One or multiple FRMCS-users can be granted with the permission to perform as talker in a certain communication. These FRMCS-users are able to request permission to talk during communication.
    Different FRMCS-users can be granted with a different talker priority. In case of parallel requests for permission to talk, the permission is granted to the FRMCS-user(s) with highest talker priority.
  Request permission to talk
    The FRMCS-user shall be able to request the permission to talk (raise the hand).
  Grant permission to talk
    The system shall be able to limit the number of simultaneous talkers in a voice communication.
    The list of FRMCS-users with permission to talk and those who have requested it, shall be available to the Multi User Talker Control application.
  Revoke permission to talk
    An entitled FRMCS-user who monitors the progress of the communication shall be able at any point to revoke the permission to talk of any of the FRMCS-users with permission to talk.
Notes: 1

## Slide 24: Critical support applications
Robust mission critical group communications
    Transformation of on-network railway service into off-network railway service (service continuity).
Authorisation of communication
    The system may restrict communication based on a configurable access matrix related to the FRMCS subscriber identity, the FRMCS Functional Identity of the equipment, the FRMCS User Identity, the FRMCS Functional Identity of the FRMCS-users considering the source and destination address.
Authorisation of application
    The FRMCS System shall enable / disable FRMCS Applications for a FRMCS User depending on subscriber identity, the functional identity of the FRMCS Equipment, the FRMCS User Identity or the functional identity/ies of the FRMCS User. Also context based criteria like location and other conditions are to be taken into account.
Sharing FRMCS Equipment by FRMCS Users
    FRMCS Users may share FRMCS Equipment, e.g. a trainborne UE. To use the shared equipment securely, it is needed to identify the user for the equipment.
FRMCS naming authority
    The FRMCS Naming Authority (NA) is a registry service provided by FRMCS System to facilitate the handling of various namespaces, number ranges or other information sets needed to support FRMCS services (user and equipment ID, no duplication etc.).
Notes: 1

## Slide 25: Critical support applications
Wayside-Centric Automatic Train Control
    One way to realize the moving block system is that a centralized server communicates with trains and manages the moving block based on the positions of the trains. The On-board Automatic Train Protection (OATP), which is on the train, report the position of the train to the Wayside Automatic Train Protection (WATP), and the WATP decides and provide the movement authority of the train to the OATP.
Autonomous Train Control and Operation
    Autonomous train control system whose service concept is aligned to the eV2X service, trains share its position by exchanging the information without any centralized server, and each train decides how far it can be authorized to move based on the position information.
Virtual Coupling
    On-board FRMCS UE for automatic train control shall be able to communicate through off-network with another on-board FRMCS UE.
Composite-based train operation
    The FRMCS System shall be able to assign and withdraw an FRMCS Equipment Identity common to several FRMCS Equipment, e.g. for trains being coupled together in order to be reachable under the same FRMCS Equipment Identity.
Notes: 1

## Slide 26: FRMCS system principles
Notes: 1

## Slide 27: FRMCS System principles
Legacy system interworking
TRS Trunked Radio System
Notes: 1

## Slide 28: Legacy System interworking
Area Broadcast Group Communication interworking between GSM-R and FRMCS Users
    Allows an area broadcast group communication between FRMCS User(s) and GSM-R User(s), and vice versa.
Location Service interworking between GSM-R and FRMCS Users
    Allows FRMCS System and GSM-R system to obtain and share the location information of their users.
    Presence interworking between GSM-R and FRMCS Users
    Allows FRMCS User(s) to see the status of GSM-R user(s), and vice versa. For example, FRMCS User(s) can see the status of a GSM-R user, including user ID, states (available, busy, etc.), vice versa.
    Point to Point communication between GSM-R and FRMCS Users
    Allows a FRMCS User to communicate with a GSM-R User, vice versa.
    Interworking with legacy systems (including GSM-R and) TRS
    Allows interworking with legacy system (including GSM-R and) TRS.
    Circuit Switched communication between GSM-R and FRMCS Users
    Circuit switched bearer services are used in GSM-R for voice and data communication. That encompasses user-to-user as well as multiuser voice communication.
    Provide call priority during interworking with LMR
    To make interworking between the networks to during provide FRMCS communication, it needs to manage call priority between calls which are made between the networks.
Notes: 1

## Slide 29: FRMCS System principles
Builds stable positioning framework for FRMCS services and devices including trainborne and handheld devices
    Stable positioning framework for FRMCS services and devices are placed in indoor and/or outdoor. The use case focuses covering “GPS shadow area” with ad-hoc positioning technology such as LTE location service.
    Bearer flexibility
    FRMCS envisages bearer flexibility to allow a certain level of independence between Railway Applications and the underlying transport system, including wireless and wireline access.
    QoS in a railway environment
    Application categories (voice, video, critical, non-critical etc.), Priority Level, Latency, Reliability, Session handling.
    Provide broadband and mission critical services with seamless connectivity
    The FRMCS shall provide the broadband and mission critical services with seamless connectivity (up to 500km/h).
    Offer railway services high-quality control functions with real-time train status monitoring
    The FRMCS System offers high-quality control functions for railway services with real-time train status monitoring (up to 500km/h).
Notes: 1

## Slide 30: FRMCS System principles
Builds stable positioning framework for FRMCS services and devices including trainborne and handheld devices
    Stable positioning framework for FRMCS services and devices are placed in indoor and/or outdoor. The use case focuses covering “GPS shadow area” with ad-hoc positioning technology such as LTE location service.
    FRMCS Positioning Accuracy
    Consolidate positioning information i.e. the location information resulting from the combination of all positioning sources available to the FRMCS System.
    FRMCS System security framework
    Identity management, authentication, authorization, key management, data protection (regarding integrity, confidentiality, privacy, non-reputation), prevention of attacks, detection of attacks, reaction on detected attacks.
Notes: 1

## Slide 31: Thank You!
3GPP TSG-SA WG6 Meeting #16
Dali, China
Notes: 1