3GPP TSG-SA WG6 Meeting #30	S6-190863

Newport Beach, CA, USA, 8th – 12th April 2019	(revision of S6-190821_S6-190723_S6-190629)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.282 | CR | 145 | rev | 3 | Current version: | 16.2.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Functional alias supplements for the MCData transmission and reception control procedures |
| --- | --- |
| Source to WG: | UIC |
| Source to TSG: | S6 |
| Work item code: | MONASTERY2 |  | Date: | 2019-04-10 |
| Category: | B |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | MCData transmission and reception control procedures use the respective MCData ID for the control tasks. If, in addition, the functional alias is used for the identification of the sending MCData client, functional alias addressing capabilities in the MCData transmission and reception control procedures are required accordingly. |
| Summary of change: | The change request address all the necessary changes in the context with the functional alias and MCData transmission and reception control for on-network mode captured in clause 7.6. |
| Consequences if not approved: | Limitations in the use of functional alias for MCData services. |
| Clauses affected: | 7.6.2.2.2, 7.6.2.3.2, 7.6.2.4.2 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: | None |

**********************************************1st Change*****************************************

#### 7.6.2.2	Automatic transmission for SDS

##### 7.6.2.2.1	General

When SDS message is sent, the data is transferred from the sending MCData client to the receiving MCData client without any request/grant procedure or any explicit actions on the part of the receiving MCData client.

##### 7.6.2.2.2	Procedure

The procedure in figure 7.6.2.2.2-1 describes the case where MCData SDS is automatically transmitted to the selected recipient user or affiliated members of the selected MCData group.

Pre-conditions:

1.	MCData user is configured with permission to transmit data.

2.	Optionally, MCData client may have an activated functional alias to be used.

3.	The MCData server may have subscribed to the MCData functional alias controlling server within the MC system for functional alias activation/de-activation updates.

Figure 7.6.2.2.2-1: Automatic transmission for SDS

1.	MCData user selects the data to transmit and the recipient MCData user or MCData group. The MCData user at MCData client 1 may include a functional alias used within the SDS data transmission.

2.	MCData client checks for MCData user's permission to transmit data and checks if the data size is less than the maximum data size for SDS. MCData client calculates the total transmission request size and determines to select one of the appropriate procedure described in subclause 7.4.2.2, 7.4.2.3, 7.4.2.5 or 7.4.2.6.

3.	Transmission control on the MCData server verifies if the MCData user is authorized to transmit and the data size in the received transmission request that this does not exceed the maximum data size for SDS. MCData server verifies whether the provided functional alias, if present, can be used and has been activated for the MCData user.

4.	MCData server may send one of the following MCData control indications:

a)	If the MCData user does not have permission to transmit data to another MCData user or MCData group then the "No permission to transmit data" control indication is sent.

b)	If the selected transmission is for a MCData group and there are no affiliated group members, then the transmission control on MCData server sends the "No affiliated members found to the selected MCData group" control indication.

Otherwise continue with step 5.

5.	MCData server automatically transmits the data and, if available, the functional alias of the originating MCData client 1 to the selected MCData user or the affiliated members of the selected MCData group according to the procedures selected in step 2.

**********************************************2nd Change*****************************************

#### 7.6.2.3	Send data with mandatory download

##### 7.6.2.3.1	General

The mandatory download procedure allows a sending MCData client to send data to a receiving MCData client, where the receiving MCData client is compelled to download the data.

##### 7.6.2.3.2	Procedure

The procedure in figure 7.6.2.3.2-1 describes the case where MCData user is using FD. The FD is subjected to transmission control prior to transmitting data to the selected recipient user or affiliated members of the selected MCData group for mandatory download.

Pre-conditions:

1.	MCData user is configured with permission to transmit data.

2.	MCData administrator has configured maximum data size for FD.

3.	Maximum amount of data that a MCData user can transmit in a single request is configured.

4.	Maximum amount of time that a MCData user can transmit in a single request is configured.

5.	Optionally, MCData client may have an activated functional alias to be used.

6.	The MCData server may have subscribed to the MCData functional alias controlling server within the MC system for functional alias activation/de-activation updates.

Figure 7.6.2.3.2-1: Send data with mandatory download

1.	MCData user selects the data to transmit, the recipient MCData user or MCData group and the indication for mandatory download. The MCData user at MCData client 1 may include a functional alias used within the FD data transfer.

2.	MCData client has checked for MCData user's permission to transmit data. MCData client calculates the total transmission request size and determines to select one of the appropriate procedures described in subclause 7.5.2.4, 7.5.2.5, 7.5.2.6 or 7.4.2.7 and including the mandatory download indication.

3.	Transmission control on the MCData server verifies if the MCData user is authorized to transmit and the data size in the received transmission request is within the maximum size allowed for FD transmission. MCData server verifies whether the provided functional alias, if present, can be used and has been activated for the MCData user.

4.	MCData server may send one of the following MCData control indications:

a)	If the MCData user does not have permission to transmit data to another MCData user or MCData group then the "No permission to transmit data" control indication is sent.

b)	If the data size requested to be transmitted is more than the maximum amount of data that an MCData user can transmit in a single request, the transmission control on MCData server rejects the data transmission request and sends the rejection control indication "Rejected due to exceeding data transmit size".

c)	If the data transmission time exceeds the maximum amount of time that an MCData user can transmit in a single request, the transmission control on MCData server rejects the data transmission request and sends the rejection control indication "Rejected due to exceeding data transmit time".

d)	If the selected transmission is for a MCData group and there are no affiliated group members, then the transmission control on MCData server sends the "No affiliated members found to the selected MCData group" control indication.

e)	MCData server may queue the data transmit request for later transmission with control indication "Request to transmit is queued".

Otherwise continue with step 5.

5.	MCData server transmits the data to the selected MCData user or the affiliated members of the selected MCData group according to the procedures selected in step 2 (where the recipient MCData client receives the data automatically).

**********************************************3rd Change*****************************************

#### 7.6.2.4	Send data without mandatory download

##### 7.6.2.4.1	General

The send data without mandatory download procedure allows the receiving MCData client to accept download, defer download (i.e. no response) or refuse (e.g. by the user deleting the notification item) the data sent from the sending MCData client.

##### 7.6.2.4.2	Procedure

The procedure in figure 7.6.2.4.2-1 describes the case where MCData user selected data is subjected to transmission control prior to transmitting data to the selected recipient user or affiliated members of the selected MCData group for downloading with recipient MCData user consent.

Pre-conditions:

1.	MCData user is configured with permission to transmit data.

2.	Maximum amount of data or time that an MCData user can transmit in a single request is configured.

3.	Time limit for the temporarily stored data waiting to be delivered to a receiving user is configured.

4.	Optionally, MCData client may have an activated functional alias to be used.

5.	The MCData server may have subscribed to the MCData functional alias controlling server within the MC system for functional alias activation/de-activation updates.

Figure 7.6.2.4.2-1: Send data without mandatory download

1.	MCData user selects the data to transmit and the recipient MCData user or MCData group and does not select the mandatory download indication. The MCData user at MCData client 1 may include a functional alias used within the data transmission.

2.	MCData client has checked for MCData user's permission to transmit data and the data size is within the maximum data size allowed. The MCData client calculates the total transmission request size and determines to select procedure described in subclause 7.5.2.4 or 7.5.2.6 and without including the mandatory download indication.

3.	Transmission control on the MCData server verifies if the MCData user is authorized to transmit and the data size in the received transmission request is within the maximum data size allowed. MCData server verifies whether the provided functional alias, if present, can be used and has been activated for the MCData user.

4.	MCData server sends control indication appropriate to trigger condition:

a)	If the MCData user does not have permission to transmit data to another MCData user or MCData group then the "No permission to transmit data" control indication is sent.

b)	If the selected transmission is for a MCData group and there are no affiliated group members, then the transmission control on MCData server sends the "No affiliated members found to the selected MCData group" control indication.

c)	If the data size requested to be transmitted is more than the maximum amount of data that an MCData user can transmit in a single request, the transmission control on MCData server rejects the data transmission requests and sends the rejection control indication "Rejected due to exceeding data transmit size".

d)	If the data transmission time exceeds the maximum amount of time that an MCData user can transmit in a single request (applies to DS only), the transmission control on MCData server rejects the data transmission request and sends the rejection control indication "Rejected due to exceeding data transmit time".

e)	MCData server may queue the data transmit request for later transmission with a control indication "Request to transmit is queued".

Otherwise, continue with step 5.

5.	If the temporarily stored data has not expired, the MCData server transmits the data to the selected MCData user or the affiliated members of the selected MCData group according to the procedures selected in step 2 (where the recipient MCData client may receive the data automatically).

6.	Otherwise, MCData server sends MCData control indication appropriate to trigger condition:

a)	If the timer expired for periodic announcement with the list of available recently invited data group communications, the recipient MCData client waiting to receive the temporarily stored data receives control indication with "List of available temporarily stored data waiting to download".

b)	If the temporarily stored data is expired, the data may be purged from the temporary store and the recipient MCData user is informed with control indication "Data expired and not available to download anymore".

**********************************************End of Changes*************************************