3GPP TSG-SA WG6 Meeting #30	S6-190884

Newport Beach, CA, USA, 8th – 12th April 2019	(revision of S6-190688, S6-190671)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.282 | CR | 0150 | rev | 2 | Current version: | 16.2.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | MCData File Distribution using the MBMS download delivery method |
| --- | --- |
| Source to WG: | Expway |
| Source to TSG: | S6 |
| Work item code: | eMCData2 |  | Date: | 2019-04-10 |
| Category: | B |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | xMB has been extended to allow the use of the MBMS download delivery method (3GPP TS 26.346) for MCData file distribution over MBMS, according to the gap analysis done in TR 23.792. |
| Summary of change: | New procedure “Group standalone file distribution using the MBMS download delivery method” |
| Consequences if not approved: | File distribution over MBMS cannot reuse the existing capabilities from the MBMS user service architecture. |
| Clauses affected: | 2, 4, 5.x (new), 6.4.3.1.2, 6.4.4.1.4, 6.6.4.1.3, 7.5.2.1.11, 7.3.3, 7.3.x (new), 7.3.x.1 (new), 7.3.x.2 (new), 7.3.x.2.1 (new), 7.3.x.3 (new), 7.3.x.3.1 (new), ), 7.3.x.3.1.1 (new), ), 7.3.x.3.1.2 (new), 7.3.x.3.2 (new), 7.5.2.1.x (new), 7.5.2.x (new), 7.5.2.x.1 (new), 7.5.2.x.2 (new) |
|  | Y | N |  |  |
| Other specs | X |  | Other core specifications | TS/TR ... CR … |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

**** First change ****

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TS 22.280: "Mission Critical Common Requirements (MCCoRe); Stage 1".

[3]	3GPP TS 22.282: "Mission Critical Data services".

[4]	3GPP TS 23.401: "General Packet Radio Service (GPRS) enhancements for Evolved Universal Terrestrial Radio Access Network (E-UTRAN) access".

[5]	3GPP TS 23.280: "Common functional architecture and information flows to support mission critical communication services; Stage 2".

[6]	3GPP TS 23.228: "IP Multimedia Subsystem (IMS); Stage 2".

[7]	3GPP TS 23.303: "Proximity-based services (ProSe); Stage 2".

[8]	3GPP TS 23.468: "Group Communication System Enablers for LTE (GCSE_LTE); Stage 2".

[9]	3GPP TS 23.237: "IP Multimedia Subsystem (IMS) Service Continuity; Stage 2".

[10]	3GPP TS 23.002: "Network Architecture".

[11]	3GPP TS 23.379: "Functional architecture and information flows to support Mission Critical Push To Talk (MCPTT); stage 2".

[12]	3GPP TS 29.283: "Diameter data management applications".

[13]	3GPP TS 33.180: "Security of the Mission Critical Service".

[14]	3GPP TS 23.203: "Policy and charging control architecture".

[15]	3GPP TS 36.331: "Evolved Universal Terrestrial Radio Access (E-UTRA); Radio Resource Control (RRC); Protocol specification".

[16]	3GPP TS 29.468: "Group Communication System Enablers for LTE (GCSE_LTE); MB2 reference point; Stage 3".

[17]	3GPP TS 29.214: "Policy and charging control over Rx reference point".

[18]	3GPP TS 23.283: "Mission Critical Communication Interworking with Land Mobile Radio Systems; Stage 2".

[x]	3GPP TS 26.348: "Northbound Application Programming Interface (API) for Multimedia Broadcast/Multicast Service (MBMS) at the xMB reference point".

[y]	3GPP TS 29.116: "Representational state transfer over xMB reference point between content provider and BM-SC ".

[z]	3GPP TS 26.346: "Multimedia Broadcast/Multicast Service (MBMS); Protocols and codecs".

**** Next change ****

# 4	Introduction

The MCData service suite provides a set of generic capabilities and specific services to enable one-to-one and group data communications between MCData users.

The MCData architecture utilises the common functional architecture to support mission critical services over LTE defined in 3GPP TS 23.280 [5] and aspects of the IMS architecture defined in 3GPP TS 23.228 [6], the Proximity-based Services (ProSe) architecture defined in 3GPP TS 23.303 [7], the Group Communication System Enablers for LTE (GCSE_LTE) architecture defined in 3GPP TS 23.468 [8], the MBMS User Service architecture defined in 3GPP TS 26.348 [x], the Security of the Mission Critical Service in 3GPP TS 33.180 [13] and the PS-PS access transfer procedures defined in 3GPP TS 23.237 [9] to enable support of the MCData service.

The MCData UE primarily obtains access to the MCData service via E-UTRAN, using the EPS architecture defined in 3GPP TS 23.401 [4]. Certain application functions of MCData service can be accessed using MCData UEs via non-3GPP access networks.

The MCData system provides the function to support interworking with LMR systems defined in 3GPP TS 23.283 [18].

**** Next change ****

### 5.x	MBMS user service architecture requirements

The MBMS user service architecture offers a set of delivery methods to applications. The MBMS download delivery method is used for the delivery of files over MBMS and provides reliability control by means of forward-error-correction techniques and associated delivery procedures such as file-repair.

For MCData FD, the MC service-on network architecture (subclause 5.2.6 from 3GPP TS 23.280 [5]) includes the MBMS user service architecture (3GPP TS 26.346 [z]), with the MCData server assuming the role of the content provider, as represented in figure 5.x-1:

Figure 5.x-1: MCData on-network architecture including the MBMS user service architecture

The MCData server creates MBMS user services over the xMB interface, assigning them a MBMS user service id (subclause 5.3 from 3GPP TS 26.348 [x]), and creates MBMS sessions for these MBMS user services (subclause 5.4 from 3GPP TS 26.348 [x]), with the type set to "Files" to use the MBMS download delivery method.

To control the QoS and the MBMS broadcast area of the MBMS user services, the MCData server uses the xMB mission critical extension, specified in 3GPP TS 26.348 [x]. The MCData server may determine the MBMS broadcast area based on the cell identities of the affiliated group members received over GC1.

The MCData server provides a file delivery manifest over xMB-C (see subclause 5.6.2 from 3GPP TS 26.348 [z]) describing the list of files to be broadcasted, and for each file, the target completion date, the number of repetitions.

The MBMS user service metada, which provides the delivery and schedule parameters, are returned to the MCData server after the MBMS session creation or update, under the form of a SA file (annex L.3A from 3GPP TS 26.346 [z]). The MCData server signals this SA file, together with the service id and the uri of the file to be received to the targeted MCData clients.

Editor's note: it is FFS how the service announcement channel (3GPP TS 26.346) to deliver the MBMS user service metadata can be used.

MCData clients can make use of a MBMS client (3GPP TS 26.347 [y], not shown on the figure), which provides API for the consumption of MBMS user services using the MBMS download delivery method (subclause 6.2 of 3GPP TS 26.347 [y]).

Editor's note: if appropriate security can not be added to prevent Denial of Service attack during file repair, use of xMB will be removed.

##### Editor's note: instantiation of MBMS user service and MBMS session will also be made possible within the MCData server for a transmission over MB2.**** Next change ****6.4.3.1.2	MCData server

The MCData server functional entity provides centralised support for MCData services suite. Conversation management, robots, enhanced status, database enquiries and secured internet MCData services requiring one-to-one or group data communication are realized using SDS, file distribution, data streaming and IP connectivity MCData communication capabilities.

All the MCData clients supporting users belonging to a single group are required to use the same MCData server for that group. An MCData client supporting a user involved in multiple groups can have relationships with multiple MCData servers.

The MCData server functional entity represents a specific instantiation of the GCS AS described in 3GPP TS 23.468 [8] to control multicast and unicast operations for group communications.

The MCData server functional entity represents a specific instantiation of the content provider as described in 3GPP TS 26.348 [x] to control multicast operations for file distribution.

The MCData server functional entity is supported by the SIP AS functional entity of the signalling control plane.

The MCData server shall support the controlling role and the participating role. The MCData server may perform the controlling role for one-to-one and group data communication. The MCData server performing the controlling role for a one-to-one or group data communication may also perform a participating role for the same one-to-one or group data communication. For each one-to-one and group data communication, there shall be only one MCData server assuming the controlling role, while one or more MCData servers in participating role may be involved.

The MCData server performing the controlling role is responsible for:

-	handling transmission and reception control (e.g. policy enforcement for participation in the MCData group communication) towards all the MCData users of the one-to-one and group data communication;

-	interfacing with the group management server for group policy and affiliation status information of this MCData server's served affiliated users; and

-	managing SDS and FD data distribution during MCData group communication.

The MCData server performing the participating role is responsible for:

-	handling transmission control (e.g. authorization for participation in the MCData group communication) to MCData users of the one-to-one and group data communication;

-	group affiliation support for MCData user, including enforcement of maximum Nc2 number of simultaneous group affiliations by a user;

-	interfacing with the group management server for group policy and affiliation status information of this MCData server's served affiliated users;

-	relaying the MCData communication messages between the MCData client and the MCData server performing the controlling role; and

-	handling reception control (e.g. temporarily storing the data to present to the MCData user as required) to its MCData users of the one-to-one and group data communication.

NOTE:	The MCData server in the controlling role and the MCData server in the participating role can belong to the same MCData system.

**** Next change ****

##### 6.4.4.1.4	Reference point MCData-6 (between the MCData server and the EPS)

The MCData-6 reference point, which exists between the MCData server and the EPS, is used to request the allocation and activation of multicast transport resources for MCData application usage. The MCData-6 reference point uses the MB2-C interface as defined in 3GPP TS 29.468 [16]. The MCData-6 reference point also the xMB-C interface as defined in 3GPP TS 29.116 [y] for file distribution.

**** Next change ****

##### 6.6.4.1.3	Reference point MCData-FD-3 (multicast between the FD functions of the MCData client and the MCData server)

The MCData-FD-3 reference point, which exists between the FD functions of the MCData client and the MCData server, is used by the FD function of the MCData server to send downlink multicast file data to the FD function of the MCData client. The MCData-FD-3 reference point uses the MB2-U interface defined in 3GPP TS 23.468 [8] or the xMB-U interface as defined in 3GPP TS 26.348 [y].

**** Next change ****

##### 7.5.2.1.11	MCData group standalone FD response (using HTTP or MBMS download delivery method)

Table 7.5.2.1.11-1 describes the information flow for the MCData group standalone FD response (in subclause 7.5.2.6.2) sent from the MCData client to the MCData server and from the MCData server to another MCData client.

Table 7.5.2.1.11-1: MCData group standalone FD response (using HTTP or MBMS download delivery method)

| Information element | Status | Description |
| --- | --- | --- |
| MCData ID | M | The identity of the MCData user sending FD request |
| MCData group ID | M | The MCData group ID to which the file is to be sent |
| MCData ID | M | The identity of the MCData user sending response |
| Conversation Identifier | M | Identifies the conversation |

**** Next change ****

### 7.3.3	Use of dynamic MBMS bearer establishment

The MCData service shall support the procedure for using pre-established MBMS bearers as specified 3GPP TS 23.280 [5] with the following clarifications:

-	The MC service client is the MCData client;

-	The MC service server is the MCData server; and

-	The MC service ID is the MCData ID.

The MCData service shall use the MCData-6, MCData-DS-1 and MCData-DS-3 reference points for this procedure.

MCData may use dynamic MBMS bearer for the MCData feature data streaming. The MBMS bearer can be used by any group. Depending on the capacity of the MBMS bearer, the bearer can be used to broadcast one or more services in parallel.

For file distribution using the media plane (7.5.2.7), the use of dynamic MBMS bearer is not supported.

Both the media packets as well as the transmission control messages to the receiving users may be sent on the MBMS bearer. Optionally a separate MBMS bearer could be used for the transmission control messages, due to different bearer characteristic requirements.

**** Next change ****

### 7.3.x	Use of MBMS user services for file distribution

### 7.3.x.1	General

This subclause defines information flows and procedures for usage of MBMS user services that applies to MCData file distribution. MBMS user services can be used for any MC service group.

### 7.3.x.2	Information flows for MBMS user service usage

#### 7.3.x.2.1	MBMS user service announcement

Table 7.3.x.2.1-1 describes the information flow MBMS bearer announcement from the MCData server to the MCData client.

Table 7.3.x.2.1-1: MBMS user service announcement

| Information element | Status | Description |
| --- | --- | --- |
| MBMS user service id | M | Id of the MBMS user service |
| SA file | M | The service announcement file as returned in the create/update session response (subclause 5.4 in 3GPP TS 26.348 [x]) (NOTE) |
| Monitoring state | O | The monitoring state is used to control if the client is actively monitoring the reception quality or the MBMS bearer used by the MBMS user service. |
| Unicast status | O | An indication that the listening status of the unicast bearer is requested. |
| NOTE: The SA file provides the TMGI, the list of MBMS service area identifiers, the frequency and the delivery parameters. |

### 7.3.x.3	Procedures for MBMS user service usage

### 7.3.x.3.1	Use of pre-established MBMS user services

##### 7.3.x.3.1.1	General

In this scenario, the MCData server pre-establishes MBMS user service(s) in certain pre-configured areas before the initiation of a group file distribution. When a user originates a request for a file distribution in one of these areas, the MCData server can use the pre-established MBMS user service(s) for the DL media transmission.

The MBMS user service can be announced prior to the file distribution or within the signalling message for the file distribution.

The MBMS user service does not transmit application level control signalling. An MBMS bearer could be used for the application level control messages according to the generic MBMS procedures defined in 3GPP TS 23.280 [5].

##### 7.3.x.3.1.2	Procedure

The procedure figure 7.3.x.3.1.2-1 shows only one of the receiving MCData clients using an MBMS user service.

Pre-conditions:

-	The participating users are already affiliated.

Figure 7.3.x.1.2-1: Use of pre-established MBMS user service

- The MCData server determines to create a MBMS user service with a given a MBMS user service id (subclause 5.3 from 3GPP TS 26.348 [x]).

NOTE 1:	The procedure to determine the creation of MBMS user services is implementation specific.

2. The MCData server creates a MBMS session for the MBMS user service (subclause 5.4 from 3GPP TS 26.348 [x]), with the type set to "Files" to use the MBMS download delivery method. This MBMS session will be used for file distribution. In response, the MCData server gets the TMGI of the MBMS bearer used for the MBMS session, and the SA file containing the metadata of the MBMS user service.

3.	The MCData server passes the MBMS user service info for the service description associated with the pre-established MBMS user service to the MCData client. The MCData client obtains the TMGI, identifying the MBMS bearer, from the SA file included in the MBMS user service description.

4.	The MCData client stores the information associated with the MBMS user service. The MCData client uses the TMGI and other MBMS user service related information to activate the monitoring of the MBMS bearer.

5.	The MCData client that enters or is in the service area of at least one announced TMGI indicates to the MCData server that the MCData client is able to receive file distributed over MBMS, whereby the MCData server may decide to use this MBMS user service instead of unicast bearer for MC communication sessions.

NOTE 2:	Step 4 is optional for the MCData UE on subsequent MBMS user service announcements.

NOTE 3:	The information flow is specified in subclause 10.7.2.2 from 3GPP TS 23.280 [5].

6.	When the MCData server wants to deliver a file to a group, the MCData server updates the MBMS session to provide the file location and its uri. The MCData server gets the updated SA file from the response.

### 7.	The MCData server signals the file transmission over the MBMS user service to the targetted MCData clients.

### 8.	The file, transmitted with the MBMS download delivery method, is received by the MCData clients.

#### 7.3.x.3.2	Use of dynamic MBMS user service establishment

In this scenario depicted in figure 7.3.x.3.2-1, the MCData server decides to establish an MBMS user service for the distribution of a given file. The MBMS user service is announced to the MCData client, together with the file information to be received.

NOTE 1:	The MCData server logic for determining when to establish the new MBMS user service is implementation specific. For example, the MCData server could decide to establish the MBMS delivery based on the location of the UE's that are a part of the targeted group.

Figure 7.3.x.3.2-1: Use of dynamic MBMS user service establishment

- An MCData group communication session is established.

- The MCData server creates a MBMS user service with a given a MBMS user service id (subclause 5.3 from 3GPP TS 26.348 [x]).

3. The MCData server creates a MBMS session for the MBMS user service (subclause 5.4 from 3GPP TS 26.348 [x]), with the type set to "Files" to use the MBMS download delivery method, and provide the file location and its uri. In response, the MCData server gets the TMGI of the MBMS bearer used for the MBMS session, and the SA file containing the metadata of the MBMS user service and the scheduling parameter for the file delivery.

4.	The MCData server passes the SA file to the MCData client. The MCData client obtains the TMGI, identifying the MBMS bearer, from the SA file included in the MBMS user service description.

5.	The MCData client stores the information associated with the MBMS user service. The MCData client uses the TMGI and other MBMS user service related information to activate the monitoring of the MBMS bearer.

6.	The MCData client that enters or is in the service area of at least one announced TMGI indicates to the MCData server that the MCData client is able to receive file distributed over MBMS, whereby the MCData server may decide to use this MBMS user service instead of unicast bearer for MC communication sessions.

7.	The MCData server signals the file transmission over the MBMS user service to the targetted MCData clients.

#### 8.	The file, transmitted with the MBMS download delivery method, is received by the MCData clients.

**** Next change ****

##### 7.5.2.1.x	MCData group standalone FD over MBMS request

Table 7.5.2.1.x-1 describes the information flow for the MCData group standalone FD request (in subclause 7.5.2.6.2) sent from from the MCData server to another MCData client.

Table 7.5.2.1.x-1: MCData group standalone FD over MBMS request

| Information element | Status | Description |
| --- | --- | --- |
| MCData ID | M | The identity of the MCData user sending file |
| MCData group ID | M | The MCData group ID to which the file is to be sent |
| Conversation Identifier | M | Identifies the conversation |
| Transaction Identifier | M | Identifies the MCData transaction |
| Reply Identifier | O | Identifies the original MCData transaction to which the current transaction is a reply to |
| Disposition indication | O | Indicates whether file download completed reported is expected or not |
| Download indication | M | Indicates mandatory download |
| Content reference | M | URL reference to the content and file metadata information (NOTE) |
| MBMS user service id | M | Id of the MBMS user service delivering the file |
| NOTE: the URL identifies the file delivered with the MBMS user service. |

**** Next change ****

#### 7.5.2.x	Group standalone file distribution using the MBMS download delivery method

##### 7.5.2.x.1	General

The initiation of a group standalone FD to a selected group results in affiliated group members receiving the file data over MBMS.

The first steps of the procedure are identical to the procedure Group standalone file distribution using HTTP (7.5.2.6). Based on the density and distribution of target group members, the MCData server may decide to deliver the file over MBMS.

##### 7.5.2.x.2	Procedure

The procedure in figure 7.5.2.x.2-1 describes the case where a MCData user is initiating group standalone data communication for sending file to multiple MCData users, with or without download completed report request.

Pre-conditions:

1.	The MCData users on the MCData client 1 to n belong to the same group and are already registered for receiving MCData service and affiliated.

2.	File to be distributed is uploaded to media storage function on MCData content server using the procedures defined in subclause 7.5.2.2.

Figure 7.5.2.x.2-1: Group standalone FD using the MBMS download delivery method

1-4.	Steps 1-4 are the same as in the procedure for Group standalone FD using HTTP (7.5.2.6).

5.	The MCData server executes the procedure described in subclause 7.3.x	Use of MBMS user services for file distribution. The MCData server provides, in the MBMS session properties (subclause 5.4 of 3GPP TS 26.348 [x]), the file location on the media storage function and sets the earlier fetch time with a long enough delay so that steps 6 to 8 are executed before the delivery over MBMS.

6.	MCData server initiates the MCData group standalone FD over MBMS request towards each MCData user determined in step 3. The request is sent over unicast or within an MBMS bearer for application level control signalling.

7.	The receiving MCData clients 2 to n notify the user about the incoming MCData group standalone FD request (including file metadata, if present).

8.	MCData client 2 to n automatically sends accepted MCData group standalone FD response when the incoming request included mandatory download indication.

NOTE:	When the UE is in idle mode, MCData clients may skip step 8.

9.	The MCData server forwards the MCData group standalone FD responses to the MCData client 1.

NOTE:	Step 8 can occur at any time following step 6, and prior to step 10 depending on the conditions to proceed with the file transmission.

10.	The MCData client receives the file delivered over MBMS, and executes the file repair procedure if losses occured.

NOTE:	If the MBMS reception quality is too bad, the Media storage client of the MCData client(s) downloads the file using the procedures defined in subclause 7.5.2.3.

11.	The MCData clients, after a successfully reception, initiate a MCData download completed reports for reporting file download completed, if requested by the user at MCData client 1.

12.	The MCData file download completed reports from MCData clients may be stored by the MCData server for download history interrogation from the authorized MCData users. The MCData file download completed report from each MCData user may be aggregated.

13.	Aggregated or individual MCData download completed report is sent by the MCData server to the MCData user at MCData client 1.