3GPP TSG-SA WG6 Meeting #32	S6-191464

Roma, Italy 8th – 12th July 2019	(revision of S6-191392)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.222 | CR | 0064 | rev | 1 | Current version: | 16.4.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Clarification and alignment with publish request information flows |
| --- | --- |
| Source to WG: | Huawei, Hisilicon |
| Source to TSG: | S6 |
| Work item code: | eCAPIF |  | Date: | 2019-06-20 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | 1) The information element “shareable indication information” in table 8.3.2.1 and table 8.25.2.1 indicates whether the service API information can be shared or not. If shared the CAPIF provider domain information is missing in table 8.3.2.1 while it is captured in 8.25.2.1. Hence, it is required to align table 8.3.2.1 with CAPIF provider domain informatin.. 2) Another issue identified in 8.25.3.1 ‘Service API publish for CAPIF interconnection’ is that in step 1, the service API to be published to the other CCF currently is only from the API publish function. However in fact, the service API may also from another CCF with the in case of multiple CCFs deployment as shown in figure 6.2.2-1 and figure 6.2.-2. |
| Summary of change: | - Update the description of information element “shareable indication information” - Update the corresponding procedures |
| Consequences if not approved: | Cause confusion to downstream working group |
| Clauses affected: | 8.3.2.1, 8.3.3, 8.25.2.1, 8.25.3.1 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

*********************** 1st change *******************

#### 8.3.2.1	Service API publish request

Table 8.3.2.1-1 describes the information flow service API publish request from the API publishing function to the CAPIF core function.

Table 8.3.2.1-1: Service API publish request

| Information element | Status | Description |
| --- | --- | --- |
| API publisher information | M | The information of the API publisher may include identity, authentication and authorization information |
| Service API information | M | The service API information includes the service API name, service API type, communication type, description, interface details (e.g. IP address, port number, URI), protocols, version numbers, and data format. |
| Shareable information | O (see NOTE) | Indicates whether the service API or the service API category can be published to other CCFs. And if sharing, a list of CAPIF provider domain information where the service API or the service API catetory can be published is contained. |
| NOTE: If the shareable information is not present, the service API is not allowed to be shared. |

*********************** Next change *******************

### 8.3.3	Procedure

Figure 8.3.3-1 illustrates the procedure for publishing the service APIs. The service API publish mechanism is supported by the CAPIF core function.

Pre-conditions:

1.	Authorization details of the APF are available with the CAPIF core function.

2.	API invokers may have subscribed with the CAPIF core function to obtain new service API information.

Figure 8.3.3-1: Publish service APIs

1.	The API publishing function sends a service API publish request to the CAPIF core function, with the details of the service API. If the service API is to be shared to other CAPIF core functions, the shareable information and the CAPIF provider domain information are included.

2.	Upon receiving the service API publish request, the CAPIF core function checks whether the API publishing function is authorized to publish service APIs. If the check is successful, the service API information provided by the API publishing function is stored at the CAPIF core function (API registry).

3.	The CAPIF core function provides a service API publish response to the API publishing function indicating success or failure result and triggers notifications to subscribed API invokers as described in subclause 8.8.4.

*********************** Next change *******************

#### 8.25.2.1	Interconnection API publish request

Table 8.25.2.1-1 describes the information flow interconnection API publish request from CAPIF core function to CAPIF core function.

Table 8.25.2.1-1: Interconnection API publish request

| Information element | Status | Description |
| --- | --- | --- |
| CCF information | M | The information of the CAPIF core function which publishes APIs, may include identity, authentication and authorization information |
| Service API information | O (see NOTE 1) | The service API information includes the service API name, service API type, communication type, description, interface details (e.g. IP address, port number, URI), protocols, version numbers, and data format. |
| Service API category | O (see NOTE 1) | The category of the service APIs to be published, (e.g.,V2X, IoT) |
| Shareable information | O (see NOTE 2) | Indicates whether the service API or the service API category can be published to other CCFs. And if sharing, a list of CAPIF provider domain information where the service API or the service API catetory can be published is contained. |
| CAPIF provider domain information | O (see NOTE 3) | Indicates the CAPIF provider domain of the service API to be published |
| NOTE 1: At least one of the Service API information and Service API category shall be present. NOTE 2: If the shareable information is not present, the service API is not allowed to be shared. NOTE 3: This is only presented when publish service API to a different CAPIF provider domain. |

*********************** Next change *******************

#### 8.25.3.1	Service API publish for CAPIF interconnection

This subclause describes the procedure for service API publish for CAPIF interoperation.

Pre-condition:

1.	CCF-A and CCF-B connect to each other, and either belong to the single trust domain of the same CAPIF provider or trust domains of different CAPIF providers.

2.	CCF-B is configured as the designated CAPIF core function in the trust domain of CAPIF provider A.

3.	When CCF-A and CCF-B belong to trust domains of different CAPIF providers, the two CAPIF providers have business agreement for service API sharing.

Figure 8.25.3.1-1: Interconnection API publish

1.	CCF-A gets the service APIs to be shared with CCF-B from the API publish function which is in the same CAPIF provider domain of CCF-A as described in subclause 8.3.3, or from another CCF as described in this procedure.

2.	Based on the shareable information for the service API or the service API category information, the CCF-A determines to publish the service API or the service API category information to the CCF-B. The CCF-A sends the interconnection API publish request to CCF-B with the details of service APIs or the category information of the service APIs, the identity information of CCF-A, shareable  information and CAPIF provider domain information if allowed to share. The API topology hiding may be enabled.

3.	CCF-B stores the service API information or service API category provided by the CCF-A.

4.	CCF-B provides an interconnection API publish response to the CCF-A indicating success or failure result and triggers notifications to subscribed API invokers as described in subclause 8.8.4.