3GPP TSG-SA WG6 Meeting #32	S6-191565

Roma, Italy 8th – 12th July 2019	(revision of S6-191504)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.280 | CR | 0218 | rev | 3 | Current version: | 16.3.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | IOPS architectural model |
| --- | --- |
| Source to WG: | Ericsson |
| Source to TSG: | S6 |
| Work item code: | MCIOPS |  | Date: | 2019-07-01 |
| Category: | B |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | For the case of a backhaul failure, MC services shall be supported based on the availability of an Isolated E-UTRAN operation for Public Safety (IOPS) system. During the IOPS mode of operation, the IOPS system shall provide local connectivity to public safety users under the coverage of the radio base station(s) forming the IOPS system, as described in 3GPP TS 23.401 Annex K. Therefore, the support of MC services on an IOPS system requires the description of the IOPS architectural model for the IOPS mode of operation. |
| Summary of change: | The application of the IOPS architectural model for the case of a backhaul failure is described. |
| Consequences if not approved: | MC services are not supported for the case of a backhaul failure. |
| Clauses affected: | New 9.X |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First change * * *

## 9.X	Architecture model for the IOPS mode of operation

### 9.X.1	IOPS architectural model

#### 9.X.1.1	Overview

The IOPS architectural model includes application functions at the IOPS MC system and UEs to support MC services on the IOPS mode of operation during a backhaul failure. The IOPS MC system provides MC service support via a single PLMN dedicated to the IOPS mode of operation, as described in 3GPP TS 23.401 Annex K [17].

The IOPS architectural model consists of an IOPS signalling control plane and an IOPS application plane. The IOPS signalling control plane provides the necessary signalling support for the related IOPS application layer transactions, e.g. the registration and discovery of UEs on the IOPS MC system. The IOPS application plane provides the necessary support for the transport of the IOPS operation related application data as well as the IP packets containing the MC service application data to be distributed over the IOPS MC system.

#### 9.X.1.2	IOPS architectural model diagram

Figure 9.X.1.2-1 shows the IOPS architectural model for the IOPS MC system solution in case of a backhaul failure.

Figure 9.X.1.2-1 IOPS architectural model

#### 9.X.1.3	IOPS application services support layer

The IOPS MC system is composed of the following functional entities for the support of MC services on the IOPS mode of operation:

-	an IOPS MC connectivity function as described in clause 7.4.2.X.2 and an IOPS distribution function as described in clause 7.4.2.X.3.

#### 9.X.1.4	SIP core

The SIP core supports the IOPS signalling control plane. It is described in clause 9.2.1.3.

#### 9.X.1.5	IOPS EPS

The IOPS EPS provides point-to-point and point-to-multipoint bearer services with QoS on the IOPS mode of operation. The IOPS mode of operation is described in 3GPP TS 23.401 Annex K [17].

#### 9.X.1.6	UE 5

The UE 5 is an MC service UE supporting the IOPS mode of operation. It supports bearer services and applications to support MC services over the IOPS MC system. The UE 5 is composed of the following functional entities:

-	for MC services over the IOPS MC system, MC service clients as described in subclause 7.4.2.3.1 with application functions of the specific MC service defined in the corresponding MC service TS; and

-	for IOPS application plane, an IOPS connectivity client as described in clause 7.4.2.X.1; and

-	for IOPS signalling control, a signalling user agent as described in subclause 7.4.3.1.1.

#### 9.X.1.7	UE 6

The UE 6 represents one or more UEs with the same functionality as UE 5.

* * * End of Change * * *