3GPP TSG-SA WG6 Meeting #36-BIS-e	S6-200526

# E-meeting, 31st March – 8th April 2020											(revision of S6-xxxxxx)

| CR-Form-v12.0 |
| --- |
| CHANGE REQUEST |
|  | 23.222 | CR | 0071 | rev | - | Current version: | 17.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Add obtaining routing info service API |
| --- | --- |
| Source to WG: | Ericsson |
| Source to TSG: | S6 |
| Work item code: | eCAPIF |  | Date: | 2020-03-26 |
| Category: | A |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | The dynamic routing of service API invocation procedure in clause 8.27 requires a dedicated API support in CAPIF core function, which is missing in API table 10.1. Since all CAPIF APIs are described in clause 10.1, it is proposed to add CAPIF_Routing_Info API to complete the CAPIF API. |
| Summary of change: | Add CAPIF_Routing_Info API and its service operation. |
| Consequences if not approved: | Inconsistency with the procedure in clause 8.27; Missing API and its service operation name to guide stage 3 implementation. |
| Clauses affected: | 10.1, 10.x (new), 10.x.1 (new), 10.x.2 (new) |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First Change * * * *

## 10.1	General

Table 10.1-1 illustrates the CAPIF core function APIs.

Table 10.1-1: List of CAPIF core function APIs

| API Name | API Operations | Known Consumer(s) | Communication Type |
| --- | --- | --- | --- |
| CAPIF_Discover_Service_API | Discover_Service_API | AP Invoker | Request/ Response |
|  | Subscribe_Event | API Invoker | Request/ Response |
|  | Notify_Event | API Invoker | Notify |
|  | Unsubscribe_Event | API Invoker | Request/ Response |
| CAPIF_Publish_Service_API | Publish_Service_API | API Publishing Function | Request/ Response |
|  | Unpublish_Service_API | API Publishing Function | Request/ Response |
|  | Update_Service_API | API Publishing Function | Request/ Response |
|  | Get_Service_API | API Publishing Function | Request/ Response |
|  | Subscribe_Event | API Publishing Function | Request/ Response |
|  | Notify_Event | API Publishing Function | Notify |
|  | Unsubscribe_Event | API Publishing Function | Request/ Response |
| CAPIF_Events API | Subscribe_Event | API Invoker, API Publishing Function, API Management Function, API Exposing Function | Request/ Response |
|  | Notify_Event | API Invoker, API Publishing Function, API Management Function, API Exposing Function | Notify |
|  | Unsubscribe_Event | API Invoker, API Publishing Function, API Management Function, API Exposing Function | Request/ Response |
| CAPIF_API_Invoker_management API | Onboard_API_Invoker | API Invoker | Request/ Response |
|  | Offboard_API_Invoker | API Invoker | Request/ Response |
|  | Subscribe_Event | API Management Function | Request/ Response |
|  | Notify_Event | API Management Function | Notify |
|  | Unsubscribe_Event | API Management Function | Request/ Response |
| CAPIF_Security API | Obtain_Security_Method | API Invoker | Request/ Response |
|  | Obtain_Authorization | API Invoker | Request/ Response |
|  | Obtain_API_Invoker_Info | API Exposing Function | Request/ Response |
|  | Revoke_Authorization | API Exposing Function | Request/ Response |
| CAPIF_Monitoring API | Subscribe_Event | API Management Function | Request/ Response |
|  | Notify_Monitoring_Service_Event | API Management Function | Notify |
|  | Unsubscribe_Event | API Management Function | Request/ Response |
| CAPIF_Logging_API_Invocation API | Log_API_Invocation | API exposing function | Request/ Response |
| CAPIF_Auditing API | Query_API_Invocation_Log | API management function | Request/ Response |
| CAPIF_Access_Control_Policy API | Obtain_Access_Control_Policy | API exposing function | Request/Response |
| CAPIF_Routing_Info API | Obtain_Routing_Info | API exposing function | Request/Response |

* * * Next Change * * * *

## 10.x	CAPIF_Routing_Info API

### 10.x.1	General

API description: This API enables the API exposing function to obtain the routing information to forward the API invocation to another API exposing function.

### 10.x.2	Obtain_Routing_Info operation

API operation name: Obtain_Routing_Info

Description: Allows obtaining the API routing information.

Known Consumers: API exposing function.

Inputs: Refer subclause 8.27.2.

Outputs: Refer subclause 8.27.2.

See subclause 8.27.3 for the details of usage of this API operation.

* * * End of Changes * * * *