## Slide 1: Discussion on new SID SEALDD_Ph2
Jian Zhang, Yanmei Yang
Huawei, Hisilicon

## Slide 2: <<FS_SEALDD_Ph2>> 1/4
Continuation or New Item: FS_SEALDD_Ph2
Study Item/Work Item/Both: SID
Source of requirements: SA1, SA2
Expected Output: new TR, content to be added to existing TS (23.433)
Anticipated start date/meeting: SA6#xx
Target Completion: SA6#xx
Estimated TUs: xx
Rapporteurship: xx
Supporting IMs: Huawei, HiSilicon

## Slide 3: <<FS_SEALDD_Ph2>> 2/4
Description:
Due to the limitation of Rel-18 time-window, there are some issues have not been treated and discussed, the lossless data delivery enhancement, the possible architecture enhancement, and the interaction of SEALDD-C interface could be further studied and discussed.
Furthermore, in SA1 and SA2, there are multiple application content/data delivery related services (e.g. XR and media service, industrial application). However, there are several data transmission issues that strongly depends on application layer, For example:
Regarding of XR and media service, the application layer should provide or encapsulate the media frame feature (e.g. the importance of PDU set or the dependency of PDU set), and used by 5GS to provide the different QoS handling.
For the TSN/TSC service in industrial application, the application layer should provide the traffic characteristics (e.g. survival time), and used by 5GS to perform the deterministic data transmission.
Therefore, the SEALDD layer can act as enablement service to provide the related operation (e.g. identifying the media frame feature, determining the traffic characteristics for industrial application), to further support by 5GS to perform the related network control.

## Slide 4: <<FS_SEALDD_Ph2>> 3/4
Goals:
- Study the enhancement of data delivery to support the XR and media service (e.g. identifying the media frame feature).
- Study the enhancement of data delivery to support the industrial application (e.g. determining the traffic characteristics for TSN/TSC service)
- Study the adaptive transport layer connection (e.g. transmission path or transmission parameter optimization)
- Study the lossless data delivery enhancement due to UE mobility (e.g. the connection management between SEALDD traffic and application traffic to ensure lossless transmission).
- Study the possible SEALDD architecture enhancement (e.g. the relationship with NRM server).
- Study the interaction of SEALDD-C interface between VAL client and SEALDD client.

## Slide 5: <<FS_SEALDD_Ph2>> 4/4
Dependency on other working groups:
- SA2
Impacts to 3GPP/Industry work if this is not accepted into Rel-19:
- The existing data delivery service cannot support multiple vertical applications.