## Slide 1: 3GPP Broadband Callout Feature A Discussion
Harish Negalaguli (Harish.Negalaguli@motorolasolutions.com)
Sudipto Biswas (Sudipto.biswas@motorolasolutions.com)
Motorola Solutions
Last Updated: 2023-11-07

## Slide 2: Tetra Callout Feature
Introduction
This is a high-level proposal for a 3GPP-standard-based Broadband Callout feature
Broadband Callout feature can be implemented like the Tetra Callout Feature; A simple scenario could be:
Control Room Operator receives emergency call from Public
Operator selects personnel to be alerted and sends a Callout Alert message to the personnel
Personnel can respond to the alert (Callout Accept or Standby or Reject)
The operator can send further Callout Message with text or voice message to Callout group
Personnel can also respond with Callout Message with text or voice
Control room sends a Callout End
More details available in ‘Broadband Callout’ presentation (S6-232258) by Hans Petter Naper in SA6#56 Gothenburg meeting.

## Slide 3: Broadband Callout Solution – Schematic Plan
Control Room MCX Client
Callout Feature Enhancement
Existing MCX Features
MCX Server
Existing MCX Features
UE MCX Clients
Callout Feature Enhancement
Existing MCX Features
No changes expected in MCX Server, except forwarding the Broadband Callout Application Id in the SDS Message
Callout Feature Enhancement required in MCX Clients in Control Room and in UE
Callout Feature uses existing underlying features like: SDS, Private and Group Communication

## Slide 4: Broadband Callout using 3GPP MCX Features
Existing 3GPP MCData Features can be used to realize Broadband Callout feature
Callout messages can be sent using MCData SDS feature as Application Payload Data * The SDS feature is a basic protocol carrying a limited size, but variable content, payload message. * SDS provides option to include a content payload of at least [1000] bytes of binary data to be used by a local running application and the necessary addressing detail to identify the intended application.
One to One or Group Communication can be initiated to reach out to MCX Users nearby * Ad hoc Group Communication allows the combination of a random set of MCX Users into groups * Alternately Group regrouping enables temporary combination of MCX Service Groups. * Private Communication enables authorized users to communicate with a selected MCX User

## Slide 5: 3GPP MCData Spec Impact Analysis 1/3
Stage-2 document already mentions architectural support for applications such as the Callout feature over MCData SDS feature.
Specification Number & Section | Relevant Extract/Summary | Analysis
23282-i50 - MCData Stage-2; Section 5.3 SDS Capability | This section states the Architectural Requirements associated with SDS | No changes expected

## Slide 6: 3GPP MCData Spec Impact Analysis 2/3
Specification Number & Section | Relevant Extract/Summary | Analysis
24.282-i40 – MCData Signaling Stage-3; 15.2.7 Application Id | * The purpose of the Application ID information element is to uniquely identify the application for which the payload is intended * ‘Application Id Value’ contains a number that uniquely identifies the destination application. | Changes proposed; 1. A specific value to be allocated to Callout feature so that MCData Client can pass the relevant messages to the Broadband Callout feature.
24.282-i40 - MCData-Signaling Stage-3; 6.2.2.1 Generating an SDS Message, and other sections | The value chosen for the ‘Application ID Value’ is decided by the mission critical organization. | 
In Stage-3 specification, addressing mechanism to be defined to identify Callout application for which SDS payload is intended

## Slide 7: 3GPP MCData Spec Change Requirement 3/3
Following Callout messages need to be defined: Alert, Accept, Standby, Reject, Message, Device Acknowledge, User Exit, User Availability Request, User Availability, Delivery Report, End.
Specification Number & Section | Relevant Extract/Summary | Analysis
24.282-i40 - MCData-Signalling Stage-3; 15.2.13 Payload | This section defines the Payload information element, which contains the payload intended for the recipient user or application; | Change proposed; An additional ‘Payload content type’ will be defined for ‘BROADBAND CALLOUT‘ Associated ‘Payload data’ will be encoded as defined in the TCCA Broadband Callout Service Overview, and Service Definition documents.

## Slide 8: Summary
Tetra Callout Feature helps to dispatch operations efficiently.
A similar 3GPP Broadband Callout Feature can be implemented on top of existing 3GPP MCX features like: MCData SDS, Private & Group Communication, Adhoc & Regroup Group-creation; Minimal changes would be required in 3GPP MCData Standards.
3GPP standard based Broadband Callout implementation should enable Interoperation of such solutions from different vendors.

## Slide 9: Thank You