## Slide 1: Discussion on EAS selection for UE group
Huawei, Hisilicon
Yajie

## Slide 2
EAS selection for UE group
There are two options of EAS selection for certain UE group
  OPTION#1: UE#1, UE#2 in the same group connect to the common EAS e.g. EAS#1
  OPTION#2: UE#1, UE#2 in the same group connect to the different EAS (e.g. EAS#1, EAS#2)
Either Select the common EAS or multiple EASs for certain UE group may provide a better service
  OPTION#1: UE#1 and UE#2 both be close to the EAS; thus connecting the common EAS can obtain the better service
  OPTION#2: UE#1 is close to the EAS#1, UE#2 is close to the EAS#2; thus group of UE select multiple EASs may obtain a better service
EAS#1
UE#1
UE#2
EAS#1
UE#1
UE#2
EAS#2
Application context synchronization
OPTION#1: common EAS
OPTION#2: multiple EASs
UE#1 and UE#2 both be close to the EAS;
thus connecting the common EAS can obtain the better service
Location A
Location A
Location B
Location A
Location A
Location B
UE#1 is close to the EAS#1, UE#2 is close to the EAS#2;
Thus, UE#1 connects to the EAS#1; UE#2 connects to the EAS#2 could obtain the better service (if the EAS synchronization duration time is short)
Notes: Observation#1
#2
Way forward

## Slide 3
Whether to select common EAS or multiple EAS
Case#1: selecting common EAS can provide better service for both UE#1 and UE#2
  Common EAS: UE#1 will suffer around 40ms delay; UE#2 will suffer around 50ms delay
  Multi EAS: UE#1 will suffer around 40ms+40ms delay; UE#2 will suffer around 50ms+40ms delay
Case#2: selecting multiple EASs can provide better service for both UE#1 and UE#2
  Common EAS: UE#1 will suffer around 20ms delay; however UE#2 will suffer around 80ms delay
  Multi EAS: UE#1 will suffer around 20ms+20ms delay; UE#2 will suffer around 10ms+20ms delay
Thus, for different deployment case selecting common EAS or multiple EASs may provide different service performance.
EAS#1
UE#1
UE#2
EAS#2
Case#1
40ms
40ms
50ms
60ms
EAS#1
UE#1
UE#2
EAS#2
20ms
20ms
10ms
80ms
Case#2

## Slide 4
Way Forward
Whether to select common EAS or multi EASs need to be considered based on the delay between UE &EAS and EAS synchronization delay
Thus the related procedure need to be enhanced
Notes: Observation#1
#2
Way forward

## Slide 5: The end