## Slide 1: Discussion paper on the slice alignment capability exposure
Rebecka Alfredsson
Ericsson

## Slide 2: Background – FS_NSCALE
FS_NSCALE - TR 23.700-99 v18.2.0
  5.11 - Key issue 11: Slice requirement alignment
    Mentions the need for slice requirement alignment
Open issues:
- “Whether and How the SEAL network slice capability management service supports better alignment between vertical needs and slice requirements parameters for initial service requirements and ongoing service conditions?”

## Slide 3: Background – FS_NSCALE
FS_NSCALE - TR 23.700-99 v18.2.0
  6.19 Solution 19: Slice requirements alignment capability
    Provides the solution to perform slice alignment
Clause 6.19.1.1
“To enable the VAL server to configure the optimal slice requirements parameters to align with the real vertical needs, the NSCE layer is able to monitor the network performance statistics and to evaluate whether the current slice requirements parameters are reasonable to achieve the maximum return of investment. To enable the slice/service self-management, the NSCE server may have the capability to generate and configure more reasonable slice requirements parameters. To avoid frequently reconfiguration of network slice requirements, the action of alignment is triggered by the evaluation of network performance statistics during a certain time period but not by a single event.”

## Slide 4: Background – FS_NSCALE
6.19 Solution 19:
Figure 6.19.1.2-1: Slice requirements alignment process

## Slide 5: Missing functionality – NSCALE TS 23.435
Clause 9.16 - Slice requirements verification and alignment capability exposure
  The NSCE server only performs verification and generates the optimal slice requirement
  Missing the self-service configuration of the optimal slice requirement - ”alignment capability exposure”
  Missing the mechanism to avoid frequent and unnecessary reconfiguration/reporting

## Slide 6: Proposed Solution(1)
Following changes to clause 9.16 in NSCALE TS 23.435
  Take input from the VAL server for slice auto alignment in the request in Step 1
  Verify the slice requirement within the verification range in Step 6
  Perform slice alignment based on the generated optimal slice configuration in Step 6
The proposed changes are in line with the solution mentioned in the cl. 6.19 TR 23.700-99

## Slide 7: Proposed Solution(2)
Step 1
Step 2
Step 2 – perform verification margin check and auto-alignment
  Use existing procedure clause 9.12.2.1.2 – Slice related Communication Service Reconfiguration mentioned in TS 23.435
Step 1 – take input from the VAL server for
  Slice Auto-alignment
  Slice QoS verification margin
Figure 9.16.2.1-1: Slice requirements verification and alignment process

## Slide 8: Solution
Step 1 – input from the VAL server
Information element | Status | Description
VAL server ID | M | The identifier of the VAL server
VAL service ID | M | The identifier of the VAL service for which the requirement request applies
VAL UE ID list | O | The list of VAL UE IDs for which the requirement request applies
Slice identifier | M | The slice identifier (S-NSSAI, NSI ID or ENSI) which is mapped to the VAL application, if known by the VAL server
Slice Requirements List | M | The list of the slice requirements which need to be aligned.
>sliceRequirement | M | The requirement which need to be aligned, this parameter refers to the attribute of serviceProfile defined in TS 28.531[5]
Slice QoS verification margin | O | Indicates the QoS verification margin in terms of percentage to check slice requirements are within the given margin during verification. For example, the Slice QoS margin indicates the X% margin or deviation of configured slice QoS for the configured sliceRequirement. If the configured slice QoS is within the X% margin during verification step then no need to send the notification/alignment to the VAL server.
Automatic alignment mode | O | Indicates the mode for automatic enforcement of the generated optimal slice requirements to meet the slice requirements. E.g OFF or ON
>automatic alignment range | O (See NOTE) | Indicates the acceptable range for the enforcement of the generated optimal slice requirements.
NOTE: This IE is present only if Automatic alignment mode is ON |  | 
Table 9.16.3.2-1: Slice requirements verification and alignment subscription
Providing verification margin to avoid frequent reconfiguration/reporting
Providing auto-alignment for self-service slice alignment capability
Automatic alignment range IE proposed by China Mobile

## Slide 9: Solution
Step 2 – perform verification margin check and auto-alignment
  Use existing procedure clause 9.12.2.1.2 – Slice related Communication Service Reconfiguration mentioned in TS 23.435 for slice requirement alignment

## Slide 10: Summary
This discussion paper proposes a solution to solve
  the missing functionality related in clause 9.16 TS 23.435 for
    slice requirement alignment capability exposure using auto-alignment
    Avoid unnecessary frequent notification and alignment using slice QoS verification margin
  The proposed solution is in line with the solution mentioned in clause 6.19 TR 23.700-99 v18.2.0