## Slide 1: EAS synchronization discussion
Convida Wireless LLC.
Catalina Mladin

## Slide 2: Rel-17 EAS synchronization
No explicit definition of “EAS synchronization”.
Rel-17:
  In service continuity planning, the Application Context may be duplicated and sent from the S‑EAS to the T‑EAS before the UE moves to the expected location. In this case, the Application Contexts in S‑EAS and T‑EAS are synchronized when the Application Context is updated until the AC connects to the T-EAS.
  NOTE 1: The information elements of the Application Context and how the Application Context is synchronized between the S‑EAS and the T‑EAS is up to implementation of the application.
  NOTE 2: In the case of EELManagedACR, the Application Context synchronization is accomplished using the same mechanism as when transferring the context from the S‑EES to the T‑EES.
Observation 1: Rel-17 understanding use linked to service continuity, specifically to provide "application context continuity” in addition to ACT

## Slide 3: Rel-18 EAS synchronization
No explicit definition of “EAS synchronization”.
“EAS synchronization” exact matches in text
  3 times describes “EAS synchronization support” in EAS profile and corresponding discovery filters
  1 time in 8.8.3.2 before T-EAS discovery procedure start:
    “T-EAS discovery procedure also supports EAS retrieval which enables a S-EAS to obtain T-EAS(s) serving the application group so that the S-EAS can start communication with obtained EAS(s) for EAS synchronization. “
    In this case it refers to EAS synchronization following ACT (same as previous slide)
  4 times in 8.8.3.2 within T-EAS discovery procedure (within steps 1 and 2)
    Both steps refer to finding suitable EASs for performing EAS synchronization in the context of a request containing application group ID.

## Slide 4: SA6 #58 Proposals
Current proposal for change to:
  EAS Synchronization: The capability of an EAS that supports content synchronization with other EAS(s) serving the same Application Group ID.
Observation 2: This definition is unclear about usecase, i.e. group mobi
Observation 3: Several current proposals address more complex usecases (Reselection of Common EAS, Combining Common EAS with EAS bundle, Reselection of EAS bundle ) or assuming that “Common EAS” is a state achieved nearly instantaneously.

## Slide 5: Questions
SA6 is kindly asked to address the following questions:
  Is EAS capability to synch S-EAS to T-EAS different than capability of Common EAS to synch ?
  Is the “black bucket” of information to be synchronized the same for the S-EAS to T-EAS case and between EASs in Common EAS case?
  For the definition on the previous slide: is there an unstated assumption that “Common EAS” usecase relies on a convergence time, when a group is served by more than one Common EAS? If yes, what are the usecases we consider leading to that condition.

## Slide 6: Cross-release impacts
SA6 is kindly asked to consider clarifying the above to fully address (or to ensure we have correctly addressed):
  “Composite” usecases such as: Reselection of Common EAS, Combining Common EAS with EAS bundle, Reselection of EAS bundle
  Mechanisms assuming that “Common EAS” is a state achieved nearly instantaneously.

## Slide 7: Thanks