## Slide 1: Way forward proposal for MCGWUE
Huawei

## Slide 2: Different level of access control at the GW UE
 | Non-3GPP Device/Non-3GPP RAT connection level control | User level control
Granularity | Per pair of node (i.e., Non-3GPP device and the gateway UE) | Per single user using the gateway UE
Purpose | Restrict the N3GPP device/N3GPP-device-gateway-connection to connect to the GW UE | Restrict the “traffic” through the GW UE to limited user (per user per service)
Result | Only the N3GPP device with the ‘set’ is allowed to connect to the gateway UE; After this, all the users using this Non-3GPP device/ Non-3GPP RAT connection is automatically allowed. | Only the authorized user can communicate with the MC servers via the GW UE. After this, the user is allowed to communicate with the MC server.
GW UE behavior | The GW UE DOSE NOT enforce any traffic filter, directly forward any traffic. | The GW UE DOES enforce the traffic filter, only allow the traffic of authorized user.
Scenarios applicability | Single case: Not required for the Non-3GPP cannot host the MC client | Both case: the Non-3GPP device hosting the MC client and not hosting the MC client
Mandatory | Yes The authorization is valid regardless of user’s login/logoff | No, it is optional.
Pros and Cons | Per node/n3GPP connection access control Waste of GW UE resource (e.g., Uu) if a user is not authorized by the MC server (IDM, MC service server) | The traffic can be initially controlled at the GW UE The Uu of GW UE is only used for authorized traffic.
Impact to SA6 work | No impact. Non-3GPP connection/device authentication and service authorization is guaranteed by the low layer e.g., WPA2-PSK | Has impact. The GW UE needs to filter the ‘traffic’, i.e., distinguish, forward or discard certain traffic (per user per traffic)
This is mandatory but guaranteed by low layer
This is optional within SA6 scope

## Slide 3: Controversial issues and way forward
Whether to have user level access control at the GW UE ?
  Yes from Rel-18
If the user level access control at the GW UE is needed, what is it used for:
  restrict the usage of GW UE resource, per user per service.
How ?
  3.1 The MC server needs know the GW UE used by the MC service user
  It is used for the MC server to request to open the gate for traffic of the MC service user
3.2 When the MC service server is aware of the GW UE information used by the MC service user and open the gate for the authorized user at the GW UE ?
  After the service authorization, the MC service user requests the connection authorization and uses the “MC service ID”. The gate at the MC gateway UE is opened as instructed by the MC service server.
Whether the GW UE and the MC service user use the same MC service server ?
Yes, by using the same configuration for the access control of the MC service server at the MC gateway UE and the enforcement of the following traffic of the MC service user.

## Slide 4: Proposals
Way forward proposal: user level control at the GW UE only for :
the configuration retrieve, affiliation, call control, floor control, media packet
Non-3GPP device
MC client
GW UE
Identity authentication, SIP registration/authorization, service authorization
MC server
Get intial UE configuration
Connect to the GW UE at low layer with security e.g., WiFi WPA2-PSK
Identity authentication, SIP registration/authorization, service authorization via the GW UE
GW UE only forward transparently
Get configurations” UE configuration, user profile, group configuration
MC service operation(s): affiliation, call establishment/release, floor control, media packet
MC service user logoff
Per service
In summary：
The GW-local (for the interaction of MBMS, location aspect) and GW-core (for the access control at the GW UE)
The connection authorization is performed for the following traffic b/w the client and server.
The GW UE enforce the traffic control (open the gate) per the configuration from the MC service server.
The MC client may not have to know the MC service ID of the MC gateway UE. In this way, the MC service user may use any GW UE without acquiring the MC service ID of the GW UE (currently no one know when and how it happened)
Some pre-conditions：
Non-3GPP connection is already established via security protection.
The GW UE and the MC Client on the N3GPP device share the same initial UE configuration (except the MC service UE label)
The GW UE is pre-configured the initial allowed traffic (identity authentication, service authorization).
Pre-configured traffic filter to allow certain traffic
Conn authorization (MC service ID, requested traffic filter)
Conn authorization (MC service ID, allowed traffic filter)
Get new allowed traffic filter, and enforce the traffic control.
Conn authorization (MC service ID, requested traffic filter, MC service ID of the GW UE)
Conn authorization (MC service ID, allowed traffic filter, GW-local identity for the user)