## Slide 1: CAPIF RNAA & OAuth’s Authorization Code Flow
Niranth
Nokia

## Slide 2: Background
High level functional architecture for CAPIF supporting RNAA
  Procedures for obtaining authorization from resource owner by API invoker from Authorization Function (CCF) is fully supported by CAPIF-1/CAPIF-1e.
  OAuth 2.0’s Authorization Code Flow procedure as specified in IETF RFC 6749 can be supported over CAPIF-1/1e.
  As per TS 23.222 (SA6), Role of CAPIF-8 for RNAA is FFS and is out of scope of Rel.18.
  As per TS 33.122 (SA3), Role of CAPIF-8 is out of scope of 3GPP.

## Slide 3: CAPIF RNAA and OAuth Auth Code Flow
CCF
API invoker
CAPIF-1/1e
CAPIF-1/1e
Authorization endpoint
Token endpoint
Information Flows | OAuth (RFC 6749 & RFC 7636) | CAPIF (TS 23.222, TS 33.122)
(A) – API invoker requesting Authorization Code for resource access via service API | Authorization Request from Client to Authorization Server. (Uses Authorization endpoint) | Supported by CCF (Authorization Function) over CAPIF-1/1e Use Authorization Request of OAuth
(B) – Resource Owner granting resource access | By implementation methods. Out of scope of RFC 6749 & RFC 7636. | Aligned with OAuth and a standardized method is out of scope of Rel.18
(C) – Authorization Code provided to API invoker by Authorization Function | Authorization Response from Authorization Server to Client (Uses Authorization endpoint) | Supported by CCF (Authorization Function) over CAPIF-1/1e Use Authorization Response of OAuth
(D) – API invoker request for Access Token with Auth Code | Access Token Request from Client to Authorization Server (Uses Token endpoint) | Supported by CCF (Authorization Function) over CAPIF-1/1e Use Access Token Request of OAuth
(E) – Authorization Function provides the Access Token to API invoker | Access Token Response from Authorization Server to Client (Uses Token endpoint) | Supported by CCF (Authorization Function) over CAPIF-1/1e Use Access Token Response of OAuth
OAuth’s Authorization Code Flow can be implemented over CAPIF-1/1e.

## Slide 4: CAPIF-8 interactions for RNAA
CCF
API invoker
CAPIF-1/1e
CAPIF-1/1e
Authorization endpoint
Token endpoint
OAuth’s Authorization Code Flow can be implemented over CAPIF-1/1e.
CAPIF-8 can be considered purely for step B (user authentication) which supports interactions between Authorization Server and Resource Owner for User Authentication and obtaining permission from Resource Owner (ie end user granting access).
CAPIF-8
ROC
End user interaction
UE

## Slide 5: Summary
For RNAA, SA3 is utilizing the mechanisms specified in IETF RFC 6749 & RFC 7636.
  Authorization Code Flow
  Authorization Code Flow with PKCE
  Enhanced version of Client Credentials Flow
In IETF RFC 6749 & RFC 7636 Authorization Code Flow does NOT specify a standard mechanism for the flow supporting step (B) – Interactions between Authorization Server and Resource Owner (via user-agent).
Considering the above, SA6 intends to specify standardized interactions for CAPIF-8 in future release. Hence, it should be clearly captured in TS 23.222 that CAPIF-8 is out of scope of Rel.18.
Following proposals are submitted to SA6#58
  Relevant updates to TS 23.222 about CAPIF-8 (see CR in S6-233722)
  Send LS to SA3 about the update related to CAPIF-8 (see LS in S6-233725)

## Slide 6: Thank You!