## Slide 1: FS_5GSAT_APP: KI discussion on Satellite Access impacts to communication experience
07 Nov, 2023
Basu Pattan (Samsung)

## Slide 2: Content
Background
Group communication
Application Service Delivery impacts due to UE Mobility
Application Service Delivery impacts due to Satellite in Motion

## Slide 3: Background
Three area types based on different access coverage:
  Only Satellite Access (NTN)
  Only Terrestrial Access (TN)
  Both TN and NTN
UE-A connects to TN only
UE-C connects to NTN only
Theoretically, UE-B can connect to both TN and NTN, however Rel-18 defines:
  UE-B does not connect to TN and NTN simultaneously, and
  UE-B may connect either to TN or NTN
RAT Type for satellite access in 5GS:
  NR(LEO), NR(MEO), NR(GEO) and NR(OTHERSAT)
RAT Type for satellite access in EPS:
  WB-E-UTRAN(LEO), WB-E-UTRAN(MEO), WB-E-UTRAN(GEO), WB-E-UTRAN(OTHERSAT), NB-IoT(LEO), NB-IoT(MEO), NB-IoT(GEO), NB-IoT(OTHERSAT), LTE-M(LEO), LTE-M(MEO), LTE-M(GEO) and LTE-M(OTHERSAT) for satellite access with WB-E-UTRAN, NB-IoT or LTE-M
Typical ground-satellite-ground round-trip-time delay e.g. ~540ms for GEO, ~42ms for LEO at 1200km, and ~26 ms for LEO at 600km
End-to-end Latency: includes latency at access network, backhaul, core network and inter-connected networks

## Slide 4: Satellite Access impacts to communication experience
Scenario: Mission Critical (MC) Group Members present across all 3 area types.
TS 23.501 defined 5QIs (related to Mission Critical):
MC KPIs (3GPP TS 22.179):
To take advantage of coverage enhancement, MC service shall consider all Group Members but added round-trip-time delays in Satellite Access impacts communication experience
Typical round-trip-time delay (ground-satellite-ground):
  ~540ms for GEO, ~42ms for LEO at 1200km, and ~26 ms for LEO at 600km

## Slide 5: 4.x Key issue #x: Satellite Access impacts to communication experience
4.x.1 Description
3GPP TS 23.501 defines 5QI for various services. For services to work as expected and to have better communication experience, service KPIs are defined by 3GPP, which are independent of the underlying access type. Until Rel-18, SA6 defined solutions, considering access provided by terrestrial network. When considering non-terrestrial network, SA6 defined services and application enablers are likely to be impacted due to large ground-satellite-ground round-trip-time delay introduced by the underlying satellite access. It is therefore necessary to analyse the application layer impacts due to satellite access, prior to identifying the approaches to mitigate such impacts. Awareness of satellite access to the applications could be used to optimize services and adjust the application layer behaviour.
4.x.2 Open issues
The open issues are:
Analyze application layer impacts due to Satellite access usage for 3GPP Services
How to make Mission Critical services aware of satellite access usage
3) How to make application enablers aware of satellite access usage
4) How to use satellite access characteristics to optimise Mission Critical services
5) How to use satellite access characteristics to optimise application layer enablement behaviour

## Slide 6
Thank You!