## Slide 1: Discussion on SEALDD server discovery for SEALDD client
Jian Zhang
Huawei, Hisilicon

## Slide 2: Outline
Background
CNAME-based DNS redirection
Conclusion and proposal

## Slide 3: Background
9.4.3 SEALDD server discovery and selection for SEALDD client
9.4.3.1 General
The VAL client can use existing mechanisms (e.g. DNS query mechanism, application layer signalling mechanism) to find an appropriate SEALDD server in non-EDN scenario and EDN scenario. The VAL client can provide the SEALDD server information to the SEALDD client when the SEALDD service is required.
NOTE: DNS query mechanism and application layer signalling mechanism are outside the scope of SA6.
The EAS registration procedure of 3GPP TS 23.558 [10] can be enhanced to enable VAL/SEALDD client to discover and select proper SEALDD server in EDN scenario.
In Rel-18, the SEALDD server discovery for SEALDD client has been specified as following:
There are two mechanisms to support the distributed SEALDD server discovery for SEALDD client in EDN scenario, i.e., DNS query, and EDGEAPP related method.
Regarding of the DNS query, the CNAME-based DNS mechanism has been standardized in the IETF and is widely used in the industry.

## Slide 4: CNAME-based DNS redirection
In CNAME-based DNS redirection, the authoritative server returns a CNAME response to the DNS request, telling the LDNS server to restart the name lookup using a new name. A CNAME is essentially a symbolic link in the DNS namespace, and like a symbolic link, redirection is transparent to the client; the LDNS server gets the CNAME response and re-executes the lookup. Only when the name has been resolved to an IP address does it return the result to the user. Note that DNAME would be preferable to CNAME if it becomes widely supported.
In IETF RFC 7336, the following CNAME-based DNS redirection to support the distributed server discovery for end user:
SEALDD client
VAL client
UE
SEALDD server
Local DNS server
Authoritative DNS server
DNS system
1. DNS query with VAL server FQDN
2. DNS query with VAL server FQDN
3. DNS response with FQDN with CNAME
4. DNS redirection query with FQDN with CNAME
5. DNS redirection response with SEALDD server IP address
6. DNS response with SEALDD server IP address
7. UE/client can retrieve data/content from SEALDD server (return in step 6)
High-level figure for CNAME-based DNS redirection mechanism

## Slide 5: Conclusion and Proposal
The CNAME-based DNS mechanism can be used to support the SEALDD server discovery and selection for the SEALDD client in EDN scenario
The related paper in S6-240269 should be agreed to make the DNS query mechanism more clear to support SEALDD server discovery and selection for the SEALDD client in EDN scenario
Notes: Mapping关系slide6对应CR被agreed