## Slide 1: Recap on signalling plane migration discussion
Ericsson

## Slide 2: Sequence for migration (fig. 10.1.1.2-1)
Observation 1: Migration happens only at the application layer
Observation 2: The MC service user is still connected to the SIP core of its home MC system

## Slide 3: 5.2.9.3 SIP core / IMS utilization
Migrated MC service users should utilise the SIP core / IMS of the partner MC system.
NOTE 1: The above recommendation ensures the security policy of the partner MC system is not compromised and ensures service‑level delay requirements are consistently met (which are especially at risk when the SIP core / IMS of the primary MC system and the SIP core / IMS of the partner MC system are far apart from a geographical point of view).
Where connectivity and security policies allow, the same SIP core / IMS can be utilised to connect to the primary MC system and one or more partner MC systems.
NOTE 2: Whether the same SIP core / IMS can be utilised to connect to the primary MC system and a partner MC system is left to business agreements between MC service providers, and is outside the scope of the present document.
For each partner MC system, MC service UEs of MC service users enabled for migration shall be provisioned with:
- configuration that controls whether the MC service UE shall connect to the SIP core / IMS of the primary MC system or a different SIP core / IMS (i.e. SIP core / IMS of the partner MC system); and
- where a different SIP core / IMS to the primary MC system's SIP core / IMS is to be connected to then the MC service UE shall also be configured with:
- configuration required for the MC service UE to access the SIP core / IMS; and
- credentials required for the MC service UE to register with the SIP core / IMS.
Editor's note: It is FFS how the MC service UE connects to the SIP core / IMS of the partner MC system to access MC services in the partner MC system.
FQDN of the SIP Proxy (P-CSCF) or its IP address (cl. 5.1.1.0 of TS 23.228)
Which credentials/ parameters?
FQDN: Fully Qualified Domain Name

## Slide 4: 5.2.9.2 PLMN utilization
Migrated MC service users should utilize the PLMN used by the partner MC system to access MC services in the partner MC system, however, utilizing the PLMN used by the primary MC system is not precluded.
NOTE 1: The above recommendation ensures the security policy of the partner MC system is not compromised, the expected QCIs are used on the RAN, and ensures service‑level delay requirements are consistently met (which are especially at risk when the HPLMN of the primary MC system and HPLMN of the partner MC system are far apart from a geographical point of view).
NOTE 2: Whether the PLMN used by the partner MC systems or the PLMN used by the primary MC system is used to access MC services in partner MC systems is left to business agreements between MC service providers and is outside the scope of the present document.
MC service users enabled for migration shall be provisioned with configuration that specifies which PLMNs may be used to migrate to other MC systems.
If the PLMN used by a partner MC system is different from the PLMN used by the primary MC system (i.e. migrating MC service user starts using the PLMN used by the partner MC system), then:
….
If the PLMN used by the partner MC system and the PLMN used by the primary MC system are the same (i.e. migrating MC service user continues to use the PLMN used by the primary MC system), then:
- the EPS subscriptions of the PLMN used by the primary MC system utilized by the MC service users who are allowed to migrate to the partner MC system need to be provisioned with the APNs specified in subclause 5.2.7 that identify the PDNs of the partner MC system.

## Slide 5: Observations
Migration on the MC service layer is accompanied with possible changes in any of the following layers:
  3GPP core layer
  SIP layer
The possible changes are:
  Partner 3GPP core, Partner SIP core
  Partner 3GPP core, Primary SIP core
  Primary 3GPP core, Partner SIP core
The MCx UE/ MCx client needs to be configured whether
  It must change the primary PLMN
  It must change the primary SIP core/IMS

## Slide 6: Proposals
Solution 1: eUICC based
  MCx user utilizes MCx UE device equipped with eUICC card (eSIM, eISIM)
  The eUICC card includes multiple profiles to select multiple PLMN and SIP core/ IMS
Solution 2: configuration based
  Allow the MCx client to store the IMS credentials (IMC) of the SIP core/ IMS of the partner MC system(s) despite being equipped with (e)ISIM
  Use SIP digest as the authentication mechanism towards the SIP core/IMS of the partner MC system(s)

## Slide 7: Solution 1:
Pros:
  Multiple profiles to select from by user
  eSIM selection is independent from MC application usage
Cons:
  SIP core is selected based on PLMN selection. This makes deployment option in Fig 9.2.2.1.4 difficult to achieve
  Migration is done per user (i.e. all MC clients concurrently used by a MC user are migrated simultaneously). This makes eSIM change on multiple devices difficult to coordinate
  Switching profile may need too much time (e.g., up to 1 minute), during which the MC user suffers service interruption
  QoS requests from MC service server needs multiple Rx integrations to different PLMNs

## Slide 8: Solution 2:
Pros:
  SIP core selection is controlled by the MC application configuration (similar to all MC clients using non 3GPP devices)
  Support for a coordinated SIP core change is triggered by a MC user migration for all multiple devices used by the MC user
  Simpler QoS implementation via one home PCRF (assuming HR roaming)
  Support for all deployment options in TS 23.280 clause 9.2.2.1
Cons:
  Authentication method change - support for SIP Digest (SA3 impact)

## Slide 9: 9.2.2.1 Administration of MC service, SIP core, and EPS
Figure 9.2.2.1.3-1: MC service provider administers MC service separately from SIP core and EPS
Figure 9.2.2.1.4-1: MC service provider provision of SIP core, separate domain from EPS

## Slide 10: MC service user migration
Scenario: MCx user simultaneously uses multiple MCx UE devices
MC system A
PLMN A
Core Network
PLMN B
Core Network
MCx user 1
UE 1
MC Client1
UE 2
MC Client2
MCx UE 1
MCx UE 2
SIP core/ IMS
SIP core/ IMS A
MC system B
SIP core/ IMS
SIP core/ IMS B
Observation: According to TS 23.280, clause 10.6.3.3.1, step 7, the primary MC service server marks the MC service user as having migrated. This means that all MCx clients that a single MC user uses need to be migrated simultaneously.
Figure 10.6.3.3.1-1: Service authorization for migration to partner MC system and subsequent service authorization
7. The primary MC service server marks the MC service user as having migrated, and records the partner MC system as the migrated MC system….
MCx user 1 migrates with MCx UE1 only
Change to PLMN B and SIP core/IMS B are needed

## Slide 11: Solution evaluation: Solution 1
MC system A
PLMN A
Core Network
PLMN B
Core Network
UE 1
MC Client1
MCx user 1
MCx user 1
UE 1
MC Client1
UE 2
MC Client2
PLMN A
Core Network
UE 2
MC Client2
MCx UE 1
MCx UE 2
MCx UE 2
MCx UE 1
SIP core/ IMS
MC system A
SIP core/ IMS
SIP core/ IMS A
SIP core/ IMS A
MC system B
SIP core/ IMS
SIP core/ IMS B
Both MCx client 1 and MCx client 2 need to be migrated simultaneously
Only MCx UE 1 changes its geographical location and is triggered to change eUICC profile due to changing to PLMN B (partner 3GPP core)
Consequently, the MCx client 1 will change to the SIP core/ IMS B (partner SIP core/IMS)
MCx UE 2 has not changed its geographical location, thus it is still connected to PLMN A
How would the MCx client 2 switch to SIP core/IMS A of the partner MC system in order to simultaneously get migrated?
MCx UE 1 and MCx client 1 are connected to PLMN B and SIP core/ IMS B, respectively
MCx UE 2 and MCx client 2 are connected to PLMN A and SIP core/ IMS A, respectively
MCx user 1 migrates with MCx UE1 only
Change to PLMN B and SIP core/IMS B are needed

## Slide 12: Solution evaluation: Solution 2
MC system A
PLMN A
Core Network
PLMN B
Core Network
UE 2
MC Client2
MCx user 1
MCx user 1
UE 1
MC Client1
UE 2
MC Client2
PLMN A
Core Network
MCx UE 1
MCx UE 2
MCx UE 2
SIP core/ IMS
MC system A
SIP core/ IMS
SIP core/ IMS A
SIP core/ IMS A
MC system B
SIP core/ IMS
SIP core/ IMS B
UE 1
MC Client1
MCx UE 1
Both MCx client 1 and MCx client 2 need to be migrated simultaneously
Both MCx UE1/ MCx client 1 and MCx UE2/ MCx client 2 are configured to change to the partner’s PLMN and partner’s SIP core/ IMS networks, and are equipped with the necessary parameters
MCx user 1 migrates with MCx UE1 only
Change to PLMN B and SIP core/IMS B are needed
MCx UE 1, MCx UE and MCx client 1, MCx client 2 are connected to PLMN B and SIP core/ IMS B, respectively as needed

## Slide 13: Way forward
An LS to SA3?

## Slide 14: Thank You!

## Slide 15: Background from TS 23.228 and TS 33.203
The necessary parameters to initiate registration to IMS system:
  The IMS private user identity (IMPI)
  One or more IMS public user identities (IMPU)
  The home network domain name used to address the SIP REGISTER request
  Any authentication key
In addition, the FQDN of the SIP proxy (P-CSCF) or its IP address
FQDN: Fully Qualified Domain Name

## Slide 16: Background from TS 33.203
IMS AKA achieves mutual authentication between ISIM (UICC card) and the home network
The identity used for authenticating a subscriber is the IMS private user identity (IMPI)
The HSS and the ISIM share a long-term key associated with the IMPI
The ISIM is capable of securely store one IMPI only (the IMPI of the primary MC system)

## Slide 17: Observations
An MC service UE is attached to only one PLMN at a time
An MC service UE is registered to only one SIP core/IMS network at a time
The IMPI of another IMS network (other than the primary MC system) is not included in the ISIM`s of the MC service UE
In case of migration: the IMPI (and necessary parameters to initiate SIP registration at the partner MC system) are missing

## Slide 18: Background from TS 23.228 and TS 23.203
For UEs supporting only non-3GPP access, if neither ISIM nor USIM is present, but IMC is present, the necessary information is stored in the IMC (clause 4.3.3 of TS 23.228)
IMC shall not be used if ISIM or USIM is present (clause 9 of TS 23.203)
TS 33.180 allows for MC service users over non-3GPP access (e.g., control room) to use SIP digest mechanism (clause 6.2.1 of TS 33.180)

## Slide 19: Background from TS 23.228 and TS 23.203
SIP digest achieves mutual authentication between the UE and home network
The identity used for authenticating a subscriber is the IMPI
The HSS and the UE share a password associated with the IMPI
FQDN of the SIP proxy (P-CSCF) or its IP address needs to be known

## Slide 20: 9.2.2.1 Administration of MC service, SIP core, and EPS (scenarios 3 &4)
Figure 9.2.2.1.3-1: MC service provider administers MC service separately from SIP core and EPS
Figure 9.2.2.1.4-1: MC service provider provision of SIP core, separate domain from EPS
Solution 1: eUICC based
Partner 3GPP core, Partner SIP core
Partner 3GPP core, Primary SIP core
Primary 3GPP core, Partner SIP core
Solution 1: eUICC based
Partner 3GPP core, Partner SIP core
Partner 3GPP core, Primary SIP core*
Primary 3GPP core, Partner SIP core*
eUICC cord concept, is to change PLMN instead of roaming over the PLMN layer.
By changing the PLMN, the SIP core/ IMS is automatically changed
eUICC does not support deployment scenario 4, because the profile change is triggered by changing the PLMN operator
* Our understanding is that eUICC does not include a profile that connects one Home PLMN to two different SIP cores/ IMS
eUICC card supports only deployment scenario 3
Due to geographical location change, the MCx UE is triggered to change the PLMN, i.e., select the profile that matches the partner’s PLMN.
As a result, the SIP core/ IMS will be changed (i.e., profile change is triggered by PLMN operator change, not by SIP core/IMS change)

## Slide 21: 9.2.2.1 Administration of MC service, SIP core, and EPS (scenarios 3 &4)
Figure 9.2.2.1.3-1: MC service provider administers MC service separately from SIP core and EPS
Figure 9.2.2.1.4-1: MC service provider provision of SIP core, separate domain from EPS
Solution 2: configuration based
Partner 3GPP core, Partner SIP core
Partner 3GPP core, Primary SIP core
Primary 3GPP core, Partner SIP core
Solution 2: configuration based
Partner 3GPP core, Partner SIP core
Partner 3GPP core, Primary SIP core
Primary 3GPP core, Partner SIP core
Solution 2 removes the dependency on having the SIP core/IMS change being dependent on PLMN change
It decouples the PLMN and SIP core/ IMS selection
The MCx UE/ MCx client is configured whether it to change the PLMN layer and/ or SIP core/IMS layer, and is configured with the necessary credentials